## Slide 1: Ring circumference
I. Chaikovska, V. Kubytskyi, V. Mytrochenko
A. Loulergue

## Slide 2: An unexpected find: shorter circumference
The RF frequency is found experimentally to be 0.3 - 0.4 MHz higher than the nominal. What is the reason?
Need explicit simulation!
Short and small-radius dipoles, long fringe fields
Nominal optics MCF 0.014
Measured orbits
Below 500.27 MHz the beam is lost

## Slide 3
Screenshot from 02/08/2023 16:50:56.
Beating frequency between FLO =500.32 MHz and turning frequency of the bunch freely circulating around the ring.
Result of screenshot processing.
Bunch circulating frequency vs time.
Experimental attempts to measure the ring frequency

## Slide 4
Part 1: Tracking in real field
Simplified dipole model in tracking codes: BEND/ SBEND (including the fringe field modeling)
Works for majority of the studies but fails in the circumference/frequency evaluation.
Tracking in realistic 3D fieldmaps is needed.

## Slide 5: “Experiment on the table” with RF-track (Method 1)
  It was found that the beam trajectory in the dipoles is shorter wrt. to the ideal path => shorter pathlength and so smaller total circumference
First study to measure ring frequency :
Lattice with dipoles represented by SBEND (usual way) : F = 500.02 MHz
Lattice with dipoles represented by VOLUME with realistic magnetic field : F =500.38 MHz, dispersive orbit. The same effect as in the experiment!
Big step in understanding of the problem
100 turns with realistic dipoles

## Slide 6: Measure track length in the dipole (Method 2)
Integration of equation of motion in magnetic field.
Compare with ideal orbit length.
Geometrical:
delta in half magnet -0.836117 ;
delta total 1.672234 mm ;
ring circumference delta (x8) -13.377869 mm
Comparing field integrals BL:
  ideal -66.934421 ; real -66.553028;
  ratio 0.994302;
  delta_l 1.688603 mm

## Slide 7
20165 elements vs 157 elements
Dipoles slicing and insert in the ring
Need to adjust element length according to track length.
Slow for matching;
Negative drifts - huge tunes. Cut fields and rescale.
Work done in AT and MADX in parallel for better understanding
Goal: develop the realistic model of the dipoles to be used in the tracking code (AT or MADX) to perform the tracking
Solution: perform the magnet slicing to fit the real magnetic field

## Slide 8: Part 2: AT simulation. Add Drifts
The realistic dipole modelling and electron tracking is understood and studied
Goal: study the solution to bring the ring to the nominal (or suitable for timing and FPC systems) RF frequency

## Slide 9
Problem: absence of the correct dipole simulation in AT
BEND model in AT (constant bending radius), which is not correct for the ThomX dipole
+6mm drifts
+6mm drifts
The exact drift length to be adjusted

## Slide 10: Refitted optics for the ring with the bigger circumference (optics matching)

## Slide 11
atsummary(r_optic)
************* Summary for '' ************
Energy: 0.05000 [GeV]
Gamma: 97.84756
Circumference: 17.99848 [m]
Revolution time: 60.03646 [ns] (16.65654 [MHz])
Betatron tune H: 0.17309 (2883.07420 [kHz])
V: 0.63365 (10554.45082 [kHz])
Momentum Compaction Factor: 1.42541e-02
Chromaticity H: +0.07212
V: -1.34426
atsummary(ring)
************* Summary for '' ************
Energy: 0.05000 [GeV]
Gamma: 97.84756
Circumference: 17.98672 [m]
Revolution time: 59.99723 [ns] (16.66744 [MHz])
Betatron tune H: 0.16998 (2833.12609 [kHz])
V: 0.64018 (10670.09816 [kHz])
Momentum Compaction Factor: 1.43393e-02
Chromaticity H: -0.00000
V: -0.00000
Name field before after variation
QP1 PolynomB -4.86169 -4.80669 0.0549962
QP2 PolynomB 9.44146 9.40109 -0.0403643
QP3 PolynomB -18.5428 -18.7781 -0.235302
QP4 PolynomB 16.4601 16.6294 0.169288
QP31 PolynomB -8.90015 -8.5712 0.328949
QP41 PolynomB 5.10745 4.8107 -0.296743
NOMINAL OPTICS
OPTICS WITH INSERTED DRIFTS
WITHOUT using QP1,QP2 (injection/extraction):
Name field before after variation
QP3 PolynomB -18.5428 -18.7993 -0.256462
QP4 PolynomB 16.4601 16.5988 0.1387
QP31 PolynomB -8.90015 -8.57761 0.322532
QP41 PolynomB 5.10745 4.88248 -0.224968
From RF-track (optics w/o matching)
Freq = 500.0689 with a drift of 0.0058813 m
Consistent results
Simulation/matching results
Lnom + 11.8 mm

## Slide 12
Exp [500.02 ; 500.25 ; 500.35 ; 500.38]
Model [499.69; 499.92; 500.02; 500.05]
Frequency offset in modelling and experiment
Nominal optics
In the current context, the experimental studies are in good agreement

## Slide 13
New optics with the inserted drifts
Current optics (nominal)
6D closed orbits @ ±10 kHz
Comparizon of two optics

## Slide 14
Simple scaling rule, suppose current nominal frequency is 500.35 MHz:
deltaF = 0.327e6;
circumference = 17.98672;
delta_L_theory = 1./2.*circumference*deltaF./500.023e+06;
Very approximately: 1 mm offset on each side of the ring corresponds to 50 kHz offset in frequency
Simple scaling to be used for estimations

## Slide 15: Part 3: Surround dipole with metallic plates
Goal: install the metallic plates for each of the dipole in the ring
Limitation of the fringe field will allow to increase the pathlength in the dipole.
Example: le dipole de l’anneau de soleil.
Etude magnetostatique 3d
n/ref. : dsm/dapnia/sacm/soleil-2002

## Slide 16: “Experiment on the table” with RF-track
Scaled fieldmap for dipoles with MP
Fieldmaps are provided by Fabrice (SOLEIL)
RF track simulations have been performed with the measured (ALBA) and OPERA dipole field. Difference in fieldmaps => difference: ~ 0.1 MHz
Correct scaling of magnetic field for the magnet with plates allows to reduce the ring RF frequency by ~200 kHz
More realistic design of the plates should be implemented.
OPERA
OPERA

## Slide 17: Summary
We developed the method to simulate the ThomX ring in AT.
We investigated the frequency/circumference difference and solution to elongate the ring.
With the inserted drifts up to 6 mm each, the rematched optics is close to nominal. Detailed studies in progress.
  The minimum possible drift value: avec des joints plus large le mini est 0,1mm. Si on met des pièces en plus le mini est 3 mm (info from Rodolphe).
The solution with the metallic plates seems very promising. Allowed spacing and realistic geometry studies in progress. Solution could be more difficult to implement.
Ideally: for model/real accelerator studies, it is important to have the correct dipole simulation in the tracking code. Solution: bring the dipole field as much as possible to the theoretical model of the dipole.
After the input from timing group, fix and validate the frequency change.

## Slide 18
Example of beam storage.
Processing of oscilloscope data
RefCurve_2023-06-13_3_152443.Wfm.csv
Beam storage in the beginning of the summer

## Slide 19: Data from 16/11/2023

## Slide 20: Data from 16/11/2023

## Slide 21: Data from 16/11/2023