## Slide 1: Improving the Energy Efficiency of Future Accelerators
1st iSAS Workshop, April 15, 2023, IJCLab
Mike Seidel
Paul Scherrer Institute (PSI) and École polytechnique fédérale de Lausanne (EPFL)

## Slide 2
nucl. plant 1.3 GW
cyclist
SLS, 2.6 MW
Power – Orders of Magnitude
Cyclist | 0.4 kW
Proton Therapy | 500 kW
Swiss Light Source 2.0 | 2.6 MW
Large Hadron Collider | 120 MW
FCC-ee, @ Higgs Energy | 282 MW
Nuclear Power Station | 1.3 GW
Earth Moon Dissipation | 3.8 TW
Mankind Total (all sources) | 19 TW
Earth
Moon
Tides
[Williams, Boggs, 2016: 3.8TW]
LHC
proton therapy

## Slide 3
Due to climate change and the overexploitation of many natural resources, sustainability and energy efficiency have become key aspects of all human activity.
This is also important for the next generation of research infrastructures (RI) for these reasons, but also to gain support by politics and society.
Energy efficiency is a key aspect, besides carbon footprint, lifecycle, heat recovery etc.
As a scientific community, we should be at the forefront, leading by example with innovative solutions.
School Strike for Climate
Wikipedia

## Slide 4: Community Activities on Sustainability
2014-17: EUCARD-2, WP Energy Efficient Accelerator Technologies
https://www.psi.ch/enefficient
2017–21: ARIES, Work Package Efficient Energy Management
https://www.psi.ch/aries-eem
2021–25: I.FAST, Work Package Sustainable Concepts
https://www.psi.ch/scat
ICFA panel on sustainable accelerators, chair: Thomas Roser (BNL)
https://icfa.hep.net/icfa-panel-on-sustainable-accelerators-and-colliders/
 consult websites for link collection to workshops and documentation

## Slide 5: Accelerator driven Research Infrastructures (RI)
grid power
primary beam
auxiliary systems
conversion target
undulators/magnets
colliding beam insertion
…
primary beam production
conversion to specific secondary radiation
electrons
protons
ions
X-rays
neutrons, muons, neutrinos
exotic particles
high level goal:
Science output per grid power, per operating/investment cost.
radiation to
experiments
accelerator

## Slide 6: Accelerator Concepts and Technologies
Proton Drivers with high intensity applications
Synchrotron Light Sources and FELs
Particle Colliders
Resonators and high Power RF Systems
Accelerator Magnets and Power Supplies
Cryogenic Systems
Component Cooling, Air Conditioning, Vacuum, Instrumentation … and other aux. systems
concepts, RI‘s
technologies

## Slide 7: Superconductivity in Accelerators
the main concepts in accelerators: bending of trajectories and energy gain by RF fields, profit from energy efficient superconducting technology
DC field: cooper pairs move frictionless
zero losses
example: MRI magnet with cold switch
RF field: cooper pairs move frictionless, but carry mass that is accelerated back and forth
 imperfect shielding of RF field in material
 dissipation from «normal» electrons in RF field
 very small but non-zero losses
Magnets
RF Resonators

## Slide 8: Proton Driver Accelerators [as example for high intensity applications]

## Slide 9: Comparison: Megawatt p-Drivers
Yakovlev, FNAL, invited talk, IPAC 2017
facility | accelerator type | Economy | Energy Reach | Power Reach | operational complexity | grid-to-beam Efficiency
SNS | superconducting linac | -- | ++ | ++ | ++ | 9%
J-PARC | rapid cycling synchrotron | ++ | ++ | - | - | 3%
PSI | isochronous cyclotron | + | -- | + | - | 18%
Workshop: Efficiency of Proton Driver Accelerators, 2016, PSI
https://indico.psi.ch/event/3848/
Megawatt class facilities operating today:
optimized for application, not efficiency
590 MeV, 1.4 MW

## Slide 10: Superconducting Linac : High Efficiency Potential example: PIP-II design of Fermilab
operating regime | avg. RF power | cryogenic power | avg. beam power | grid-to-beam Efficiency
PIP-II pulsed operation | 1.44MW | 1.19MW | 17.6kW | 0.7%
PIP-II CW operation | 9.10MW | 1.83MW | 1.60MW | 15%
PIP-II base parameters:
H-, 800MeV, 2.0mA, part of Fermilab complex
aim: neutrino production (1MW @ 60..120GeV)
CW operation as upgrade path
highest efficiency
[from presentation B.Chase, Y.Yakovlev, 2018]
not efficient in pulsed operation:

## Slide 11: Low Loss Superconducting Resonators
3‘000 church bell
50‘000 Cu resonator
21010 s.c. resonator
1
105
1010
Q0 = quality factor
 e-folding decay and resonance width
high Q resonators, 1.3GHz, 2K, FNAL
[A.Grassellino, A.Romanenko et al, 2013]
example:
Ua = 20MV, (R/Q) = 609, Q0 = 21010, Ib=2mA
Pdissip = 33 W
Pbeam = 40.000 W
dissipated power:
but: cryogenic efficiency!

## Slide 12: Cryogenic Efficiency
best possible coefficient of performance (COP):
Wc = amount of work required to remove heat Qin at cold temperature T
T0 = 293K
T = 2K
Qin
Wc
[S.Claudet et al, CERN 2013]
 lower COP is better !

## Slide 13: COP Factor: compare heating of houses
best possible coefficient of performance (COP):
T = 308K (35C)
T0 = 273K (0C)
Qout, Qin
W
in theory: COPCarnot = 8.8
in practice: COP = 3…5
in this case  higher COP is better !
heat pumps at MAX-4, using waste heat
[Björn Eldvall / E.ON,
Martin Gierow / Kraftringen]

## Slide 14: Powerflow s.c. Linac – Minimum System Example for a Single Cavity
GRID
AC/DC/RF/guide
RF  0.4 .. 0.6
cryogenics
COP  1000
beam
Pdissip
PRF
power balance:
regime | Ib [mA] | Q0 | RF | Pbeam [kW] | grid-to-beam Efficiency
TDR, CW | 2.0 | 21010 | 0.44 | 40.0 kW | 30%
high Q | 2.0 | 31010 | 0.44 | 40.0 kW | 33%
high current | 4.0 | 31010 | 0.65 | 80.0 kW | 50%
considered:
one 650MHz cavity
Ua = 20MV
l = 1.1m
ignored: cavity detuning, <1, regulation overhead, aux. systems …
extrapolation

## Slide 15: technical challenges of s.c. RF not discussed here:
low DC current requires high QL for matching  narrow bandwidth  stability/regulation problem
in optimum matched condition:
Lorentz force detuning 1Hz/MV2 -> extremely sensitive
high intensity  high power transfer through coupler; excitations of HOMs (damping required), etc.
ERL: deceleration of spent beams  losses from emittance growth

## Slide 16: Technology R&D: Efficient RF Power Sources
Example: SSA for Isotope production Cyclotron, 98.5MHz, 12x1kW units, D=93% (90% with regulation overhead)
Uppsala group, WP in I.FAST program
Magnetron, R&D at various groups, =60-80% within reach
e.g. Wang et al, J-Lab, IPAC 2019; A.Dexter, Lancaster U., LINAC-2014; B.Chase, Fermilab, JINST-2015
Klystrons, >70% within reach
e.g. CLIC two stage multi-beam klystron, J.Cai, I.Syratchev, IEEE Trans, 2020
Solid state amplifiers (SSA) at various groups, =60-90% depending of freq.
Example: study 1GHz for CLIC drive beam; 6 cavities, 30 beamlets; 25+140kV; sat=82%
https://indico.cern.ch/event/1138197/
I.FAST efficient RF workshop, July 4-6, 2022, Switzerland:

## Slide 17: Technology R&D: Superconducting RF at higher temperature
promising R&D: Nb3Sn coated cavities at Cornell
4.2 vs. 2.0K  efficiency
[M.Liepe, Cornell, IPAC‘19]
S Posen et al 2021 Supercond. Sci. Technol. 34 025007
record cw gradient in Nb3Sn-coated, Eacc = 24 MV/m
Cornell, FERMILAB
 simplicity, cost, efficiency, smaller size
To be published
DESY, Hamburg U.
aim for sustained SRF accelerator technology
10y Goal: >70 MV/m with a Q0 of 1x1010 and at 4K
contact: M.Wenskat, DESY
Marc Wenskat et al 2023 Supercond. Sci. Technol. 36 015010, DOI 10.1088/1361-6668/aca83f
SMART recipe leads to a Tc of 15.4 K on Nb-samples coated with 15 / 25 nm of AlN / NbTiN
overview: G.Bisoffi, RF Achievements and Plans
https://agenda.infn.it/event/35579/contributions/201871/

## Slide 18: Light Source Example

## Slide 19: Example Swiss Light Source SLS and its Upgrade @ PSI
Brilliance x 35 for users Less electricity consumption Key savings: Electromagnets  Permanent magnets Klystrons  Solid state amplifiers (63%) standard pumps  modern pumps for cooling
-29 %
 3.3MW
SLS2.0: Grid to user X-rays
Ptot = 2.4MW
PRF = 0.82MW
P (undulators) = 91kW
[M.Jörg, PSI]

## Slide 20: Particle Colliders

## Slide 21: Colliders - Concepts
MuonC
+/-
1
10
100
1000
m [MeV]
e

p
Next generation: high Luminosity, high Energy reach needed
Energy Efficiency: Luminosity per Grid Power
Ring
p/p
Linear
e+/e-
Ring
e+/e-
particle mass impacts synchrotron radiation and beamstrahlung (collision)
 scaling laws and grid power drivers are quite different for the concepts under discussion

## Slide 22: Colliders Types and Power Drivers
MuonC
+/-
Ring
p/p
Linear
e+/e-
Ring
e+/e-
FCC-ee 240GeV:
Pgrid = 282MW
CLIC 380GeV (3.0TeV):
Pgrid = 110MW (589MW)
ILC 250GeV (1TeV):
Pgrid = 111MW (300MW)
FCC-hh 100TeV:
Pgrid = 580MW
MAP 6.0TeV:
Pgrid = 270MW
+ beam recirculation
- synchrotron radiation
+ no synchrotron radiation
- no recirc., small beam needed
power drivers: cryo (ILC) vs RF (CLIC)
+ no Beamstrahlung-Limitation
- inefficient RCS, complexity
+ high energy reach
- SR deposited @50K, cryogenics

## Slide 23: Ring Collider
energy recirculated, thus efficient concept
however, SR losses at higher energies
LHC: burnup dominates beam loss
= „decay time of beam energy in number of turns due to SR“
quality factor storage ring:
bending radius
classical particle radius

## Slide 24: FCC-ee – Optimized Lepton Ring Collider
A. Milanese, Efficient twin aperture magnets for the future circular e+/e- collider,
Phys. Rev. Accel. Beams 19, 112401 (2016)
100km
K.Oide at al
Ecm = 240 GeV (H)
Pgrid = 282 MW
Egrid/y = 1.33 TWh
 dominated by RF (compensating SR losses)
similar as CERN total today
conceptual measures:
crab waist scheme (specific luminosity)
4 IP‘s instead 2
maximise bending fill factor (combined func. mag.)
technology measures:
high-efficiency klystrons (HEIKA collaboration)
4.5 K s.c. cavities, high Q (400 MHz Nb/Cu)
twin apertue dipoles (50% savings of bends)
HTS quads and sextupoles (M.Koratzinos et al, CHART)
M.Koratzinos et al, CHART, HTS Sextupole

## Slide 25: Overview Lepton Proposals
energy specific luminosity production:

## Slide 26: Ring vs. Linear Collider
Ring Collider
beams circulate
Linear Collider
beams collide once
beam reused
synchrotron radiation dominated
equilibrium beamsize  collision parameters limited
beam used only once
no synchrotron radiation
ambitious collision parameters possible (no ring dynamics)
 | FCC-ee 365GeV | CLIC 380GeV
x [nm] | 38‘000 | 150
y [nm] | 68 | 2
z [m] | 2‘500 | 70
N [109] | 230 | 5,2
fb [kHz] | 147 | 17,6
Pb[MW] | 988 | 2.8

## Slide 27: Combining Linear- and Ring-Collider using the ERL Concept
ERL
power circulates
P
P
acceleration
deceleration
I
I
power recirculated, beam recirc. at low E
benefit from better collision parameters
 high L per grid power, but higher investments & complexity
two ERL proposals published:
1) Circular Energy Recovery Collider
V. Litvinenko, T. Roser, M. Llatas, Physics Letter B 804 (2020) 135394
multi turn ERL, modification FCC-ee
2) Energy Recovery Linear Collider
V.I. Telnov 2021 JINST 16 P12025
twin s.c. linacs, beam recirculation, wiggler damping

## Slide 28: Muon Collider – Efficient at Highest Energies
Muon: E0 = 106 MeV,  = 2.2 s
low SR, low beamstrahlung during collisions!
scaling laws for muon collisions at varying E:
thus L/P is increasing with energy:
Beamstrahlung in e+/e- collider:
!

## Slide 29: Summary Efficient Particle Accelerators
Grid to Beam
State of the art 20%, up to 50% reachable for s.c. linacs & high beam power; cyclotrons provide solutions for E<1GeV, e.g. ADS systems
Colliders
e+/e- ring collider is a powerful yet simple scheme; advanced efficient schemes include energy recovery collider and muon collider
fluctuating sustainable energy: E management / dynamic operation
Technology
s.c. magnets & high Q cavities are efficient, higher temperature operation (HTS)
efficient RF sources, permanent magnets, heat recovery & photovoltaics
other: water & He consumption, critical materials, managed lifecycle, carbon footprint, energy procurement, advanced energy production

## Slide 30: Thank you for your attention.
Many thanks for discussions and input:
V.Yakovlev (Fermilab), V.Ziemann (U.Uppsala), M.Jörg (PSI), H.Schlarb (DESY), D.Schulte, F.Zimmermann (CERN),
M.Bylac (CNRS), P.Williams (STFC).

## Slide 31: spare slides on Light Sources, Dynamic Operation

## Slide 32: Synchrotron Light Sources and Free Electron Lasers
GRID
AC/DC/RF/beam
magnets, AC, aux.systems…
radiation for users
unwanted radiation
over the history ring light sources have improved the brilliance by more than 10 orders of magnitude, the last step is made using multi bend achromat lattices and miniaturization using permanent magnets
power consumption of ring light sources is in the range of a few Megawatt and often not a critical factor; however, s.c. FELs might use O(20MW)
the production of tailored radiation – spectral distribution, coherence, ultrashort pulses etc. is in the focus today
possible efficiency measure:
SLS2.0 magnet structure

## Slide 33: Free Electron Laser
longitudinal,  z², O(30m)
energy loss, E/E
streaked beam, SwissFEL
no lasing lasing
O(10-3)
best demonstrated energy extraction: E/E = 30%
(Ek=65MeV, Laser seeded FEL)
Facility | Technology | Pgrid (typ) | Pbeam (typ) | Photon Power
SwissFEL | n.c., 6 GHz, pulsed |  3.0 MW | 100 W | up to 0.2 W
EXFEL | s.c., 1.3 GHz, pulsed |  10 MW | 40‘000 W | up to 40 W
FEL process
 ?
RF, Linac
Grid Power Consumption
(order of magnitude)
examples: n.c. / s.c.
FEL: P  N2 (coherence length)

## Slide 34: The Future – Fluctuating Energy Sources
courtesy: FRAUNHOFER-INSTITUT FÜR SOLARE ENERGIESYSTEME ISE, Karlsruhe (2020)
residual power
production of power
solar, wind
release from storage
variation: x5!
use of power
industry, traffic etc
energy storage
simulation: April 2050, sustainable energy system Germany
Grid
O(GWh)
Collider
collider dynamic operation – possible at all?
low intensity pilot beam (ca . factor 2 grid power reduction needed)
or: standby mode with fast L recovery concepts
or: local energy storage, gas power