## Slide 1
Heavy Ion Accelerators in the world/ in France
B. Jacquot CNRS,

## Slide 2
Overview
Heavy Ions (HI) in the world of particle Accelerators
Technologies and Challenges, specificity
Leading Facilities HI in the world
Medical Applications of HI
French Heavy Ions Facilities
What to do with GdR SCiPAC?

## Slide 3
Very Large Accelerators in the world
Very Large accelerator facilities (>0.5 billion Euros)
? Heavy Ion Accelerators Versus p-Accelerators, electrons-Accerators ?
Higher Power:PSI
Higher luminonisity
The largest
KEK
CERN(Pb-Pb), Fermilab, XFEL, J-PARC /Super KEKB, BNL(RHIC),
SNS, Los Alamos, RIBF, FRIB, PSI, GSI, RAON, HIRFL
+ 70 Synchrotron light sources
Projects : ESS, GSI_FAIR, HIAF, EIC@RHIC, PIPII, MYRRHA
Futur : CERN_FCCee, FCChh, ILC
Biggest facility are proton accelerators and electron accelerators
But Heavy Ion accelerators are however well represented

## Slide 4
Large Accelerators in the world and science
Large protons accelerators:
  Particle physics, Applications with neutrons, Nuclear physics
    Anti protons, bosons,exotic mesons hadrons, Neutrino(FERMILAB,PSI, J-PARK),
    Hadron structure and dynamics (FAIR, LHC, RHIC)
    Neutrons (SNS,ESS,PSI,CERN, Los Alamos), Acc. Driven System (MYRRHA)
    Muons (FERMILAB,PSI),
Large Heavy Ion accelerators :
Nuclear Physics (…), Atomic physics, Material science, Biophysics,
Nuclear structure with RadioActive Ion Beams (Fragmentation, Fission, Isol )
QG Plasma (LHC_ALICE,RHIC)

## Slide 5
Heavy ion Accelerator Technologies
Heavy Ion accelerators ~ protons accelerators : few specifities
Technology
High Voltage (DC) :
Tandem Van de Graff, deflector
Magnet (Normal and Superconducting)
SPECIFIC : ECRIS Source
« Low RF » frequency (10-88 MHz)
High Power solid target :1kW-100kWatts
Accelerator Types
Linac , Synchrotron => medium/large machine
Cyclotrons => small/ medium machine
Van de Graaf & Tandem=> small machine
Heavy Ion Beams
large A/Q, higher Brho, small b <<1, cost~ Q/A,
No Synchrotron radiation
All Time structures : Continuous (electrostatic),
Cw (100% duty cycle linac, cyclotron), Pulsed (synchrotron) SPECIFIC : Charge state, STRIPPING

## Slide 6
Leading facilities with Heavy ions
RIBF (Japan)
2023: 9kW U @ 340MeV/A
2032: >100 kW U beam
FRIB (USA)
2023: 10kW 28Si @ 298MeV/A,…
2028 : U @ 400 MeV/A
400kW for all beams
FAIR (Germany)
U28+ @ 1200 MeV/A, p 29 GeV
Beam energy GeV/u
A/Q . < I> mA
J. Wei
FRIB
FRIB
RIBF
RIBF
Spiral2

## Slide 7
Leading facilities with Heavy ions : RIBF
Rare Isotopes Beam Facility (RIBF Riken)
150 New isotopes discovered
From 2007 to 2024 : impressive evolution. 2024 : 9 kW 238U

## Slide 8
Leading facilities with Heavy ions : RIBF
238U 35+/64+/86+ 340 MeV/A
Too high power for C foil
Helium gas stripper
50 cm long : no window
Differential gas pumping system
RIBF, Rare Isotopes Beam Facility (Riken) : U acceleration

## Slide 9
Uranium Beam 238U @ 340 MeV/A
Superconducting Ring Cyclotron (SRC)
8300 tons, Bmax 3.8 T
World Strongest Cyclotron
K factor= 2600 MeV E/A =K (Q/A)2
Leading facilities with Heavy Ions : RIBF

## Slide 10
Leading facilities with Heavy Ions : RIBF
RIBF: optimizing stripping from e=5% (2024) to 65%
50 m isochronous ring : recirculate unused charge states

## Slide 11
Leading facilities with Heavy ions : FRIB
FRIB : Linac 238U 200 MeV/A (2022) then 400MeV/A
Linac : 4 cavity families 80.5 MHz ‘QWR) & 322 Mhz (HWR)
Multi charge state operation : increase acceleration efficiency

## Slide 12
Leading facilities with Heavy Ions : FRIB
FRIB : High power target , C Multi-Slices > 100kWatts
RIB production ~ <Beam Intensity> x Target Thickness
~ < I > x beam Energy 2

## Slide 13
Leading facilities with Heavy Ions : FAIR @ GSI
FAIR : Facility Antiprotons and Ion Research ; A very ambitious scientific program
Facility in construction
Civil engineering
many components constructed
Main synchrotron assembling will start
PANDA: p-pbar annhilation (after 2028) Collector ring + H.E. ring+ detector
APPA : Atomic, Plasma, Applications, biophysics
SFRS, CRYRING,HITRAP,…
NUSTAR : Nuclear structure , N. Astrophysics
Super FRS
CBM : Compressed baryonic matter
CBM detector

## Slide 14
SiS100 : 110 Superconducting dipole magnets
Circumference ~ 1.1 km
1.5 GeV/u for U28+ cycle : 0.5 Hz ions per cycle : ~ 4. 1011
29 GeV for protons : ~ 1011 pps
Leading facilities with Heavy Ions : FAIR project

## Slide 15
Heavy Ion Accelerators : What is the best for R.I.B.
For Radioactive Ion Beam production in flight method : « thin Target »
RIB production in flight :
~ s .<Beam Intensity> x Target Thickness x Separator Transmission
Optimal prod. 30% energy loss in target
dE/dx~ (Ztarget. Zbeam2 )/ Ek …
Range~ ∫dx/dE .dE ~ Ek2/ (Ztarget. Zbeam2 )
NRIB ~ s .<Beam Intensity> x beam Energy 2 x Transmission
s Fission cross section at RIBF
s Cross section depend on the reaction :
Projectile fragmentation populates the chart close to the primary beam
In flight fission @ E>300MeV/u populate all the nuclear chart on the neutron rich side

## Slide 16
Heavy Ion Accelerators : What is the best for R.I.B.
Exemple of production with in flight method : 80Ga*
RIBF-RIKEN : today 238U @ 340 MeV/u production of 80Ga* ?
s= 5 10-2mb target Dx=1000mg/cm2 I=7 1011pps Transmission in separator (~ 5-10% )
(GANIL_LISE x 10000)
FRIB : today 86Kr @ 230 MeV/u
s= 4 10-4mb Dx=400mg/cm2 I=3 1012pps RIBF/25
  tomorow 238U @ 400 MeV/u 2. 1011pps
s= 5 10-2mb Dx=1200mg/cm2 I= 3. 1012pps ??? RIBFx 5
FAIR : after tomorow 238U @ 1500 MeV/u
s= 5 10-2mb Dx=4000mg/cm2 <I>=2 1011pps RIBF /5

## Slide 17
Accelerator for medical applications : Heavy Ion versus e/p
R&D C400 : cyclotron 400MeV/A 12C6+
Hadron therapy with a very compact machine
Radio Isotopes production (>700 in the world ):
Mainly Proton /D cyclotrons
Cancer Treatment (>10 000 electron linac // 60 protons facilities // 10 heavy ions )
X ray therapy with 5-25MeV electrons-linac ( 600 in France)
  Proton Isochronous proton cyclotron (PSI,…,), proton synchrotron
  250 MeV proton Synchro-cyclotron (IBA) : … Orsay, Nice,Caen,…
C,Ne,.. 400 MeV/A HI Synchrotrons ( 4 in EU, 0 in Fr )
CNAO Pavie (It)

## Slide 18
New H.I. Accelerator for medical applications
C400_IBA : 400MeV/A 12C6+ / 250 MeV Proton
Hadron therapy with a very compact machine
Isochronous cyclotron K=1600 MeV; 660 tons
Diameter total 6.9 m; Rextraction: 1.8m
Bfield 4,5 T (Hill) // 2.5 T (Valleys)
RF =75 MHz; Harmonic H=FRF/Frevol.=4
Transmission ~ 0.5%
2024 :
First model C400 being installed in France (Caen , Normandy)

## Slide 19
Heavy Ion Accelerators in Europe
CERN : HI LINAC3 +LEIR … for ALICE // Isolde Linac
GSI-Fair (Germany)
Dubna (Russia)
Ganil (Fr), Alto(Fr),…
LNL Legnaro (it),LNS Catania (it)
Warsaw cyclotron facility (Po)
UCL Louvain (Bel.)
RADEEF Jyvaskyla (Fin.)
…etc…

## Slide 20
Heavy Ion Accelerators in France
Iba C400

## Slide 21
Heavy Ion Accelerator in France
Low energy plateforms :
(2-4MV electrostatics ) ANDROMEDE, ARTEMIS, ASTER, New AGLAE,…
7MVtandem&4MV DAM-Bruyere
ALTO (Tandem-14.5MV)
Ganil_Cyclotrons (C-U up to 95 MeV/A, RIB-ISOL up 20 MeV/u)
Ganil_Spiral2 ( Cw Linac proton 33 MeV, Heavy Ions : 10MeV/A )

## Slide 22
France HI Accelerators : Low energy platforms
Small, Multidisciplinary : ANDROMEDE et ARAMIS @IJCLAB
Beam : from hydrogen to nano-particles (Au400+4) : 4MVolts
Surface analysis, Material science, Secondary Ion Mass Spectrometry (SIMS), Ion Beam Analysis,…
Beams : 2MVolts HI ARAMIS+ IRMA 190kV
Analysis with ion Beam (RBS, RBS/C, PIXE, PIGE, ERDA,TEM)
solid state physics, Ion implantation, Material science

## Slide 23
Heavy Ion Accelerator in France: Low energy plateforms
Accelerator Mass Spectrometry (environnement, Datation 14C,…26Al,36Cl)
ARTEMIS LMC_14@Saclay , ASTER @Aix en provence, ECHoMICADAS MHSN@Paris
ASTERisques 5MV (Accélérateur pour les Sciences de la Terre et les Risques)@ Aix en Provence
ARTEMIS@Saclay : 3MV

## Slide 24
Heavy Ion Accelerator in France: GANIL_Spiral2 (Linac)
LINAC proton 33 MeV, H.I. 14 MeV/A
1 RFQ, 26 RF Accelerating cavities
Achievements
1-2 kWatt D beam on NFS for neutron TOF
5mA + bunch selector F~1 MHz
16 kWatt Deutons
Heavy ions tested for S3

## Slide 25
Heavy Ion Accelerator in France: GANIL_Spiral2 (Linac)
Operation : D/H beam for NFS (Neutron TOF facility)
Project New gain: ( New RFQ + New SC ECRIS@28Ghz )
existing Linac A/Q<3: good for light Ions, New RFQ+SC ECRIS good for heavier Ions
Asterics SC ECRIS
New RFQ

## Slide 26
S3 project : CEA+ IN2P3 +….
International collaboration :
7 SC Multipole Triplets

## Slide 27
Cold box
27
PSS connected to SMT
2 SMT’s on the central line
SMT's, PSS and Cryogenics
Cold box in operation
since 2018
Central cryoline
  In use since 2019
West & East cryolines
  Cold tested April 2023

## Slide 28
S3 project status 2024
7 SC Multipole Triplets
Construction ~ done
Installation ~ done
Still many tests to be realised
Cryogenics + SC. Magnets + Deflector (+/-250 kV)
Serious problems detected :
Cryogenic, LTC, Magnets : HTS, Alignement, quenches
1 magnet to be repaired in US
Expert committee working on the different topics
…Operation very difficult
Quad+Hexa+Octupole+Steerer

## Slide 29
Heavy Ion Accelerator in France: GANIL_Cyclotrons
Operation: experiments 4000h/year
up to 3 experiments in parallele , operating since 1983
(Nuclear Physics, Atomic Physics, Radiobiology, Material physics, Industrial Applications
A New opportinity : The SAGA project try to increase the beam time for SPACE APPLICATION
Projects
with strong support of French community
Project CYREN (renovation)
Project DESIR (Low energy Radioctive Ion Beams)
X2
X2

## Slide 30
GdR SCiPAC: What to do ?
Transverse topics for R&D laboratories, Facilities, Universities
Maintain critical skillls :
create/ maintain training program (Master Gd Instrument, option acc., Training period )
Communication
  Help to attract new talents, to get new R&D bugdet, to get new positions
Improve sustainability of our activities
less energy // societal applications (pollution, climate, space industry)
Improve ratio beam time/ Budget (BEAM SHARING)
Develop societal applications (Space applications, Medical,….)
The large accelerators make efforts : MEDICIS@CERN (isotopes), COMET@PSI (treatment), ? SAGA@Ganil?
Nasa Space Radiation Lab(NSRL@BNL) …
Accelerator Science are already structured : Facility/University/Lab CEA+IN2P3
Existing Collaborative projects (New Gain ,Perle , Asterics, S3,Desir…), SFP Roscoff meeting,…
GdR may contribute to transverse topics - Improve collaborations
- Make emerging new ideas ?

## Slide 31
An important topic for GANIL: BEAM SHARING
  Strong demand on Space applications at Ganil , what about ALTO ?
  Need : increase the beam time for industry. New economic model ?? New method ?
Generates many charge states with a stripper
Many Br separated in
a magnet
? Want to join the R&D about beam sharing?
B. Jacquot, M. Lalande,
J.M. Lagniel, M.H. Moscatello
SAGA project (E. Dessay) at GANIL : More Beam time for Space Applications at GANIL(€!?)
Project of 3 HI beams at the same time : with beam sharing ( 1 week=3 weeks)

## Slide 32
GdR SciPAC
Heavy Ion Accelerators
Additive slides

## Slide 33
  2 familles, cavités ¼ d’onde. T = 4.5K. E = 6.5 MV/m max (~8 à présent) :
12 Beta = 0.07 (1 cavité / cryomodule)
14 Beta = 0.12 (2 cavités / cryomodule)
40 Quadrupôles
Diamètre : 56mm, Champ : 29 T/m
1 BPM par section chaude
1 BEM dans les 5 premières mailles
L~35 m
Section Beta 0.07
Section Beta 0.12
maille
1190 mm
maille
1940 mm
GANIL Linac : rappel de ses constituants
BEM très précis pour la longueur de paquet mais lent, peu utilisé hors commissioning

## Slide 34
Innovative set-up : HITRAP Deccelerator @GSI
HITRAP is a ion trap facility which is designed for capturing and cooling of highly charged ions produced at the GSI. up to uranium U92+ , hydrogen-like ions or few-electron systems at low temperatures
Heavy Ion deccelerator :
Experiments
At rest

## Slide 35
GdR Scipac : What to do ?
Status of Ions Accelerators
Accelerators are an enabling technology for basic nuclear physics*/particle physics
but
Accelerator has significant impact on medicine (Radio-isotope & cancer treatment ) *
on industry (space application )*
on environnement, climate study
GdR SCiPAC Heavy Ions/protons Find & develop activities in coherence with the
« french Accelerator strategy » (IN2P3 strategy + CEA)
IN2P3 strategy : 4 axes - support to basic sciences (particle/nuclear) and Applied (medical,ADS)
- support to IN2P3 platforms
- support to project, National/Regional (Equipex,Labex…)
- Increase the R&D > 30% of the activities
CEA strategy : …

## Slide 36
Accelerator in France : Accelerator Strategy
*A. lucotte 2022
RH IN2P3: 2022
Accelerator Road map
RH DACM-CEA :
Département des Accélérateurs, de Cryogénie et de Magnétisme ~ ~150 agents