## Slide 1: ELECTRON CYCLOTRON RESONANCE CHARGE BREEDERS FOR ISOL FACILITIES
J. Angot - LPSC Grenoble
GDR SCIPAC (Axe 1), Production d’ions lourds
Strasbourg – May 27, 2024

## Slide 2
Outline
Introduction
ECRIS and EBIS CB technics
R&D on ECRIS CB – European context
Future prospects
Conclusion

## Slide 3
Introduction
Principle of the Isotope Separation On Line method

## Slide 4: Introduction
ANL - CARIBU
USA
CERN – ISOLDE
Switzeland
IBS – RAON
Korea
TEXAS A&M
USA
TRIUMF
Canada
LNL – SPES
Italy
GANIL – SPIRAL1
France
MSU - ReA
USA
VECC
India
KEK - TRIAC
Japan
Under operation, project, stopped
Great diversity of 1+ ion sources, RI flux, post accelerators, RI species
Constraints on CB device (1+ beam emittance, energy spread….)
ISOL facilities with post acceleration

## Slide 5
Introduction
Performances
Efficiency :
Process Time
Beam purity
Beam quality
Instrument characteristics
Operation mode (CW, pulsed)
Robustness
Cost
Additional instrument necessary ?
CB
Σ Xn+
X+
A/q
I (A)
time
I X+(A)
time
I X7+ (A)
CB time
A/q
I (A)
X+
X1+
X7+

## Slide 6: ECRIS CB
14.5 GHz 500W
Injection optics
Extraction optics
1+ beam, CW
Σ N+ beam, CW
Plasma
Injection
Capture
multi ionisation
extraction
3 coils + yoke
Axial B field
Hexapole
Radial B field
Modified min-B ECR ion source
Room temperature coils
Permanent magnet hexapole
B: 0.4 – 1.7T
14.5GHz – 600W
HV: 50kV
ne- ~ 5x1011 cm-3
CW or pulse mode
0.6 m

## Slide 7: Electron Beam Ion Sources CB
Characteristics
A cooler buncher is necessary to prepare the beam (accumulation, bunching, cooling)
Total efficiency of the cooler-buncher + EBIS : 5 to 20% (EBIS alone up to 35%)
CB time of cooler-buncher + EBIS : 10 to 100 ms
A/q : 2 - 3 for light ions, 5 -7 for heavy ions, tunable with breeding time
The charged particules have low interactions with the walls, base vacuum ≈ 10-11 mbar  high beam purity
Main limitation
Limited 1+ beam flux (<1011 pps) due to the max. number of charges stored into the cooler buncher or into the EBIS
Superconducting solenoid
B: 2-8T
Electrodes for longitudinal trapping
e- beam: 0.2 - 3A , 5 - 30 keV
e- beam radius : < 0.6mm
Pulse mode
0.7 m
Lapierre, Snowmass2021 Ion Source Working Group
Wenander, JINST 5 C10004

## Slide 8: R&D on ECRIS CB
ECR CB technics developed at LPSC (ISN) in late 1990s for the « PIAFE » project
Different laboratories conceived CB from modified ion sources or new design
PHOENIX CB developed at LPSC since early 2000s
Installed at GANIL – TRIUMF – LNL + 1 R&D model at LPSC on the 1+N+ test bench
LPSC – GANIL collaboration on ECR CB performances in the frame of the« ions radioactifs » IN2P3 master - project
GANIL - LPSC – LNL collaboration for the contaminants reduction (in particular LPSC – LNL research collaboration agreement)
Extended collaboration for ECR plasma and Charge Breeding process studies (GANIL – JYFL – LNL – LPSC – RAL)

## Slide 9: R&D on ECRIS CB
LPSC
5 coils configuration :
ease the tuning and stabilize the plasma
Improve the axial magnetic field profile
Decrease the cross talk between the coils
Reinforced injection Binj 1.2  1.6T:
enhance efficiency
Inprove the plasma confinement
Large diameter configuration 72  100mm :
increase high charge state production
decrease the density of contaminants
Increase the plasma volume
sealing exclusively with metal gaskets
18GHz operation, two frequency heating
2018-2022
Under test
Assembly phase

## Slide 10: R&D on ECRIS CB
GANIL
Double frequency heating, frequency tuning :
vary the charge state distribution
  Optimize efficiency at a given charge state
  To reach lower and higher beam energies
  To avoid contamination att q/A =1/4, 1/3…
stabilize the plasma
Maunoury, ECRIS2022 talk

## Slide 11: R&D on ECRIS CB
Problem for ISOL facilities if :
Production yield is low
Too low downstream resolving power
Double task :
Measure / identify the species
  Development of diagnostics
  Improvement of command - control
  Development of identification code
Reduction :
  Experiments with liners
  Support gas decontamination
  Effect of plasma stability
a
b
c
d
a
b
c
d
Solid : with
Dashed : with +
a
b
c
b
c
d
a
x0.1
Contaminants reduction

## Slide 12: R&D on ECRIS CB
Extended collaboration on charge breeding research : GANIL – JYFL – LNL – LPSC - RAL
Different studies on plasma stability, charge breeding time in pulse mode … at LPSC and GANIL
Recently : the capture of injected ions
Historically : Capture process theory based on small angle deviations by ion-ion collisions with the buffer gas plasma ions leading to their thermalisation
New model : slowing down of injected ions essentially electrostatically
Wenander, Charge Breeding of Radioactive Ions
- K8+

## Slide 13: R&D on ECRIS CB
Technology | EBIS CB | ECRIS CB
Max 1+ RIB intensity (pps) | <1011 | >1013
CB time (ms) | 10 - 100 | 100 - 300
Operation mode | Pulsed | CW or pulsed
Robustness | Medium | High
1+N+ conversion efficiency (%) | 5 -20 % | 10 – 20%
RIB total contamination rate extracted (pps) |  105 | 109 - 1010
Upstream requirement | Ion cooling | None
Maximum A/q : A  60 Maximum A/q : A  150 | 2 - 3 6 - 7 | 2 - 3 5 - 6
ECR CB offers high 1+ beam acceptance > 1013 pps with a constant contamination yield but higher than EBIS CB
High RIB fluxes are expected in future ISOL facilities like FRIB (1012pps in some cases, under commissioning) or EURISOL (1012 pps)
TRIUMF facility recently equipped with both technologies

## Slide 14: R&D on ECRIS CB
Flat Field ECR CB @ 14-18 GHz, NbTi@4 K
plasma chamber
Pure metal or light alloy
Thermal screen
and Water cooled 300°Surface
Heater wire to bake
The plasma chamber
Online up to 400°C
HV insulator
Plasma chamber:
Ø200 mm
L~1000 mm
ECR Zone ~500 mm
CRYO PUMP
CRYO PUMP
Thuillier, ECRIS 2018 workshop
New concept of superconducting Charge Breeder
+20% efficiency, -40% CB Time, drastic reduction of contaminants

## Slide 15
Conclusion
ECR Charge Breeders are efficient instruments that accept a very high 1+ beam flux which could be of high interest for future ISOL facilities with high production yield
The beam purity issue can be addressed with high downstream separation and additional R&D must be carried out to reduce the contaminants
ECR Charge Breeding technics can be improved and solutions are identified to enhance the performances through a new generation of source

## Slide 16
Thank you for your attention

## Slide 17
LPSC 1+N+ test bench

## Slide 18: Beam purity issue
  2.7% of RIB content in the beam with
  60% RIB would need
68Zn13+
47Ti9+
94Mo18+
94Zr18+
120Sn23+
136Xe26+
146Ba28+
193Ir37+
198Hg38+
~3% of total beam current
Ionization chamber signals
146Ba
case
Thuillier, ECRIS 2018 workshop

## Slide 19: Beam purity issue
Signal (pps) | 103 | 104 | 105 | 106 | 107
Signal/Noise | 0.01 | 0.1 | 1 | 10 | 100
N+ RIB fraction | 0.9% | 9% | 50% | 91% | 99%
Signal/Noise | 1 | 10 | 100 | 1000 | 10000
N+ RIB fraction | 50% | 91% | 99% | 99.9% | 99.99%
Signal to noise ratio is a key parameter for ECRIS CB at low RIB intensity:
14 GHz ECR
Itotal~1 mA
(~
Buffer gas
~
1+ signal
N+ signal
Wall sputtering
~ whole ion spectrum
~ within
~ within
contaminants
Gases contaminants
~ within within
For
For
Thuillier, ECRIS 2018 workshop
ANL

## Slide 20: ECR Charge Breeder performances
Different CB configurations
Different facility configurations
Efficiency : 5 to 20%
Total efficiency : 35 to 90%
CB time : 10 – 28 ms/q
ECR CB offer high 1+ beam acceptance > 1013 pps with a constant contamination yield
High RIB fluxes are expected in future ISOL facilies like FRIB (>1010pps in some cases, under commissionning)
or EURISOL (1012 pps)
At FRIB a High Capacity EBIS is under development, should accept 1011 pps for low mass A≈20 (H.J. Son, NACB 2021)

## Slide 21: ECRIS CB
14.5 GHz 500W
Injection optics
Extraction optics
1+ beam, CW
Σ N+ beam, CW
Plasma
Injection, capture, multi ionisation, extraction
3 coils + yoke
Axial B field
Hexapole
Radial B field
Modified min-B ECR ion source
Room temperature coils
Permanent magnet hexapole
B: 0.4 – 1.7T
14.5GHz – 600W
HV: 50kV
CW or pulse mode
0.6 m
V
ΔV