## Slide 1: Status of SEASON
Damien THISSE
May, 28th 2024
SEASON development team
Project Managers
O. Cloué (technic) M. Vandebrouck (scientific)
Mechanical conception
S. Cazaux, P. Daniel-Thomas
Detection/Acquisition
F. Bouyjou, T. Chaminade
Control & Command
A. Gaget, J. Relland, A. Roger
Electrical engineering
J. Noury, Y. Reinert
Simulations
E. Rey-herme

## Slide 2: Summary
Quick reminders on SEASON
Current status of the development
Schedule for upcoming months
Main objectives
Description of the detector
Technical specifications
Focus on detector/acquisition test bench
Towards the full assembly of SEASON
Implementation of SEASON at Jyväskylä
1

## Slide 3
SEASON’s objectives
It has been designed to be set at the end of S3 low energy branch (LEB).
The two main purposes of SEASON@S3-LEB :
Act as a counter for laser spectroscopy.
Perform a detailed α-e─-γ decay spectroscopy.
Coupling of both nuclear and atomic approaches to get a more complete description of the nucleus.
Diff. pumping mRFQ
QMF
(m/Dm ~ 100)
RFQ
buncher
MR ToF MS
(m/Dm ~ 105)
Bender
l1,2
l2
l1
ERs
Neutralized ERs
Photoions
Gas cell
S-shaped RFQ
ERs from S3 (E~0.1 MeV/u)
Pulse up (~ 3 kV)
Gas jet
SEASON
2

## Slide 4
SEASON decay station
View of SEASON in GEANT4
Wheel
2 mm thickness 35 cm ⊘
5 DSSD
Main station
2 DSSD
Deported station
Long T1/2
2 HPGe detectors
EXOGAM
Carbon foil
~90 nm thickness
Beam
3 - 30 keV
3
a
e-
e-
Variable
Min. 2 mm

## Slide 5
SEASON decay station
View of SEASON in GEANT4
Wheel
2 mm thickness 35 cm ⊘
5 DSSD
Main station
2 DSSD
Deported station
Long T1/2
2 HPGe detectors
EXOGAM
Beam
3 - 30 keV
Carbon foil
~90 nm thickness
3
Clipped
Wings must be easy to place

## Slide 6
SEASON decay station
View of SEASON in GEANT4
Wheel
2 mm thickness 35 cm ⊘
5 DSSD
Main station
2 DSSD
Deported station
Long T1/2
2 HPGe detectors
EXOGAM
Beam
3 - 30 keV
Carbon foil
~90 nm thickness
3
Clipped
Wings must be easy to place

## Slide 7
SEASON decay station
View of SEASON in GEANT4
Wheel
2 mm thickness 35 cm ⊘
5 DSSD
Main station
2 DSSD
Deported station
Long T1/2
2 HPGe detectors
EXOGAM
Beam
3 - 30 keV
Carbon foil
~90 nm thickness
3

## Slide 8
SEASON decay station
View of SEASON in GEANT4
Wheel
2 mm thickness 35 cm ⊘
5 DSSD
Main station
2 DSSD
Deported station
Long T1/2
2 HPGe detectors
EXOGAM
CAD of SEASON
Carbon foil
~90 nm thickness
Beam
3 - 30 keV
S. Cazaux, P. Daniel-Thomas
3

## Slide 9
SEASON decay station
Calibration arms
2 pairs (one for each station) holding 3-α and 133Ba sources
Translation/Rotation movement in order to place a calibration source at the position of the implantation foil
S. Cazaux, P. Daniel-Thomas
4

## Slide 10
SEASON decay station
S. Cazaux, P. Daniel-Thomas
4

## Slide 11
SEASON decay station
S. Cazaux, P. Daniel-Thomas
4

## Slide 12
SEASON’s technical specifications
High efficiency for both electron and α-particle
E. Rey-herme simulation/analysis
Most compact configuration :
Alpha efficiency = 84 %
5

## Slide 13
SEASON’s technical specifications
High efficiency for both electron and α-particle
Most compact configuration :
Alpha efficiency = 84 %
Electron efficiency = 56 %
… but impact of the summing effect to be taken into consideration
6
E. Rey-herme simulation/analysis

## Slide 14
SEASON’s technical specifications
Good energy resolution for both electron and α-particle
Some important characteristics :
32 strips on each face
Active area : 6.4 x 6.4 cm²
Dead layer : 50 nm
Thickness: 1037 µm
Ultra high resistivity
Nominal depletion voltage : ~75 V
BB7 detector from Micron
7

## Slide 15
SEASON’s technical specifications
Good energy resolution for both electron and α-particle
Development of a front-end electronics for DSSD signal processing
Front-End Adaptive gaiN Integrated CircuitS
Shaping
Double gain preamplifier with automatic gain switch
Work of F. Bouyjou and T. Chaminade
8
CSA floor noise (no detector) : ~2.3 keV

## Slide 16
SEASON’s technical specifications
Good energy resolution for both electron and α-particle
Development of a front-end electronics for DSSD signal processing
Front-End Adaptive gaiN Integrated CircuitS
Double gain preamplifier with automatic gain switch
Work of F. Bouyjou and T. Chaminade
8
CSA floor noise (no detector) : ~2.3 keV
New version of the cards :
QFN packaging
New voltage regulator
→ Less noise from alimentation
Duplication of capacitors between the detector and FEANICS
→ Less leakage current

## Slide 17
Current status of SEASON’s development
Focus on our DSSD test bench
We’re characterising the full electronic acquisition chain : DSSD → FEANICS → Numexo2
9
Work of M. Ragot

## Slide 18
Current status of SEASON’s development
Focus on our DSSD test bench
Pole-zero cancellation
Trapezoid filter
9
Work of M. Ragot
We’re characterising the full electronic acquisition chain : DSSD → FEANICS → Numexo2

## Slide 19
Current status of SEASON’s development
Focus on our DSSD test bench
Pole-zero cancellation
Trapezoid filter
9
Work of M. Ragot
We’re characterising the full electronic acquisition chain : DSSD → FEANICS → Numexo2
L
L
G

## Slide 20
Current status of SEASON’s development
Focus on our DSSD test bench
3-α calibration source (239Pu, 241Am, 244Cm)
FWHM @ 5804.77keV : 11.8 keV (was 17 keV!)
Obtained with fixed Gain
Measured on central strips (normal incidence)
Electron source (133Ba)
FWHM @ 320.3 keV : ~6 keV (was 10.2 keV!)
Obtained with fixed Gain
Measured on central strips (normal incidence)
10
Work of M. Ragot
FWHM
FWHM
FWHM
FWHM
We’re characterising the full electronic acquisition chain : DSSD → FEANICS → Numexo2

## Slide 21
Current status of SEASON’s development
Focus on our DSSD test bench
High Gain regime
Low Gain regime
Baseline
Gain Switch Threshold
Development of methods to accurately tackle with the gain switched traces
11
Time (ns)
Amplitude (A. U)
We’re characterising the full electronic acquisition chain : DSSD → FEANICS → Numexo2

## Slide 22
Current schedule for SEASON commissioning
2024
2025
T1
T2
T3
T4
Mechanical mounting at CEA-Saclay
12
T1
T2
T3
General test of all the electronics
Test of control and commands (wheel, det. position, calibration arms…)
Mounting and alignment of SEASON with and without vacuum
Write/adjust a set-up protocol

## Slide 23
2024
2025
T1
T2
T3
T4
Source commissioning at GANIL
Complete test of SEASON without beam using GANIL acquisition system
First real-case measurement of SEASON’s characteristics (efficiency, timing properties, ...)
12
T1
T2
T3
Mechanical mounting at CEA-Saclay
Current schedule for SEASON commissioning

## Slide 24
2024
2025
T1
T2
T3
T4
Source commissioning at GANIL
* without deported station
12
Online commissioning at Jyväskylä
T1
T2
T3
Transport and installation at IGISOL
Complete* test of SEASON with beam using Jyväskylä acquisition system
Commissioning experiment :
232Th(p, xn)233-xPa (accepted)
Considered experiments :
232Th(α, xn)236-xU
233U(p, xn)234-xNp
233U(α, xn)237-xPu
Coupling with mass measurement (trap)
Mechanical mounting at CEA-Saclay
...
Experimental campaign
Current schedule for SEASON commissioning

## Slide 25
Conclusion on SEASON’s development
Assembly of SEASON at Saclay + Reception and test of the 6 remaining detectors should start in June
The interface and network for the control of SEASON’s elements (wheel, detector positions, …) is under development.
The carbon implantation foils have been tested several times on different real case experiments (VADER@JYFL in Oct. 2022, Musett@ISOLDE in June 2023)
The first DSSD of SEASON is being tested with the new FEANICS card.
Very promising results regarding the energy resolution.
Current schedule :
Assembly and test at Saclay : June – October 2024
Moving to GANIL for offline commissioning : November 2024
Moving to Jyväskylä for online commissioning : Spring 2025
13

## Slide 26
Conclusion on SEASON’s development
Assembly of SEASON at Saclay + Reception and test of the 6 remaining detectors should start in June
The interface and network for the control of SEASON’s elements (wheel, detector positions, …) is under development.
The carbon implantation foils have been tested several times on different real case experiments (VADER@JYFL in Oct. 2022, Musett@ISOLDE in June 2023)
The first DSSD of SEASON is being tested with the new FEANICS card.
Very promising results regarding the energy resolution.
Current schedule :
Assembly and test at Saclay : June – October 2024
Moving to GANIL for offline commissioning : November 2024
Moving to Jyväskylä for online commissioning : Spring 2025
13
Thank you for your attention

## Slide 27
Leakage current comparison
4 times smaller compared to the previous FEANICS card
BU1

## Slide 28
BU2