## Slide 1
Status and Operational experience of the SuperKEKB positron source
F. Miyahara (KEK, Acc. Lab.) for Injector Linac Group

## Slide 2
Overview of KEK e+e-Linac and Positron Production

## Slide 3: Google Street View@KEK
Zoom and click around here

## Slide 4: Linac Tunnel
You can see the inside of the tunnel and Klystron Gallery

## Slide 5: KEK Linac
1 2 3 4 5
1.1 GeV e+
Damping Ring
ECS
BCS
Photocathode
RF gun
e+
target
HER
LER
ECS
1.5 GeV
PF
PF-AR
chicane
Energy Knob
Energy Knob
Thermionic gun
e+ target
5
4
3
2
1
C
e-
e+
1.1 GeV
4.2 GeV
1.5 GeV
LER 4 GeV e+
PF-AR 6.5 GeV
PF 2.5 GeV
HER 7GeV
Deceleration
Acceleration
Stand-by
Acceleration
e+ capture section
Beam energy for each beam mode along the beam line after the J-Arc.
J-Arc
A
B
C
HER | 2
LER | 11 e- for e+ @gun exit
 | 3.5 nC @end
PF/ PF-AR | 0.3
Bunch charge [nC]
Linac has some beam modes matched beam injection to 4 circular accelerators
Beam modes can be switched at 50 Hz
E =2.9 GeV@targ.

## Slide 6: Positron Capture Section

## Slide 7: Capture Section Layout
Kl_15 (Klystron)
Kl_16
6 accelerating structures
Long DC Solenoids Section
Chicane for e+/e- separation
Flux Concentrator
4 Steering Coils
Bridge Coil
Target
Klystron Gallery
Tunnel

## Slide 8: Head of e+ Capture Section
Bridge Coil (DC)
Cross-section view of the capture section
DC Solenoids
Flux Concentrator
Large Aperture S-band
Accelerating structure

## Slide 9: Target
Target
3.5
f2.0 target hole
for e- beam
f2.0x14 Tungsten Targe
hole
Flux Concentrator
Y. Enomoto
Photo looking at FC from beam exit
Copper Holder

## Slide 10: DC Solenoid
A. Enomoto
Two-layer structure of hollow-conductor
To the back
side
7 Layers
Axial symmetry of the magnetic field is broken due to this part

## Slide 11: Steering Coils
Steering Coil (1 of 2)
Beam Position Monitor
Steering coils were installed in 2020.
4 Steering coils to compensate for kicks caused by non-axisymmetric magnetic fields
Ratio of coil current to optimum value
e+ yield at capture section exit
operation
point
K. Kakihara, K. Yokoyama
Steering coils are very important
for positron capture section
The electron beam through the hole shifts by up to 3.8 mm compared to the solenoid OFF
[%]

## Slide 12: Capture Section Particle Motion
FC
Deceleration @1st Acc. Capture
e+ are captured in a deceleration phase of first accelerating structure
Decelerated e+ move to the acceleration phase

## Slide 13: Longitudinal Phase Space
Deceleration
Capture
Acceleration
Capture
Acceleration capture has a large energy spread
Difficult to transport beam up to DR with small beam loss.
Beam transport line to the DR has only a 10% energy aperture
exit of last acc.
~1 m from 1st acc.
entrance

## Slide 14: Beam line after the Cap. Sec.
Many quadrupoles are installed at short intervals up to the Damping Ring
Chicane for e+/e- separation (e- beam is stopped by beam stopper)

## Slide 15
Positron Beam Tuning

## Slide 16: Beam tuning procedure
RF phase and beam orbit rough tuning  Beam reaches up to DR and Linac End (Beam loss is OK)
RF Phasing Change the RF phase to find the crest phase from the position change at a Beam Position Monitor where the dispersion is large
Manual beam tuning Operator loads previously best parameters.  Energy and beam orbit tuning
Fine tuning with a machine learning (ML tuning)
Beam tuning procedures after long-term shutdown

## Slide 17: RF Phasing after the cap. section
The RF crest phase is found by varying the RF phase and measuring the beam position at location with a large dispersion function.
1 2 3
e+
target
chicane
e+ capture section
A
B
C
Klystron phase and e- beam position in the center of the chicane
Hole
Measured with e- beams passing through the hole
e+ beam in/after capture section has a large energy spread and it’s difficult to transport
 Using low charge primary electron beams passing through the target hole (e+ crest phase = e- crest phase + 180 deg.)

## Slide 18: Fine tuning with ML

## Slide 19: Why use machine learning?
After the capture section, energy spread, beam size and emittance are very large
(Design optics are no longer relevant for fine tuning)
ML tuning can be worked all the time
ML tuning does not depend on the skill of the operator
Too many parameters ( depends on the goal)
Quadrupole
Dipole (streering)
Target
Linac layout from the target to switch yard to Damping Ring
~160 parameters
Manual tuning is almost impossible

## Slide 20: Optimization Program
T. Natsui
f = -(Q(BPM1)+Q(BPM2)+Q(BPM3))/Q(BPM0)
Minimizing this function is equivalent to maximizing beam transmission
Objective Function
Files with list of magnets
Parameters
Alias used in objective
function
Using Bayesian optimization, or Downhill simplex
The process of the objective function decreasing during an optimization.
Example of an
optimization

## Slide 21: Tuning of Quadrupole, Steering Magnets
Beam orbit and charge before ML tuning
Beam loss
Capture
Section
Bunch
Charge
X
Y
Goal: Minimize beam loss up to the DR beam transport line

## Slide 22: Improvement of transmission
Before
This tuning process (~160 parameters) takes a few days, so we have only done it once so far.
T. Natsui
After
Progression of tuning process

## Slide 23: Optimization to keep the condition
Downhill simplex
Bayesian optimization moves parameters significantly
 The downhill simplex method is used when condition deviates slightly from best ones

## Slide 24: Current Status
1 2 3 4 5
ECS
BCS
HER
LER
ECS
1.5 GeV
PF
PF-AR
chicane
Energy Knob
J-Arc
A
B
C
Q1st = 9.5 nC (100%)
Q2nd = 8.6 nC (100%)
Q1st = 5.9 nC (62%)
Q2nd = 5.3 nC (62%)
Q1st = 3.7 nC (39%)
Q2nd = 3.2 nC (37%)
Target
Linac End
Cap.Sec. Exit
Q1st = 11 nC (116%)
Q2nd = 10.5 nC (122%)
Gun
Exit
Q1st = 3.9 nC (39%)
Q2nd = 3.7 nC (37%)
DR Entrance
[mm]
Bunch charge and normalized emittance
[mm]
DR Entrance
DR Exit (Position back in the Linac)
Primary electron beam has large energy spread and emittance, so it loses about ~20% up to the target
Conversion efficiency of primary electron beam to positron beam is ~60%
30% of the beam is lost in the Beam transport line (SY2 to DR)  Bunch charge decreases to ~40% at the end
1.1 GeV

## Slide 25: Comparison of simulated and measured data
Simulation (EGS5 and GPT) roughly reproduce experimental values for the phase dependence of yield
Slightly different phase-dependent structure  Simulation studies are needed (Fahad will reports on this topic on Friday)
Klystron phase of 1st accelerating structure and positron yield
Measured data
Simulation
Dec. Capture
Acc. Capture

## Slide 26: Summary
KEK e+e- Linac and Positron Capture Section Overview
Positron beam tuning : Manual and machine learning are used together
Bayesian optimization is very useful in improving position yield and beam transmission
If the parameters deviate slightly from the optimum, Downhill Simplex is effective
Current Status of the positron beam
Bunch charge : 11 (Gun Exit)  9.5 (Target)  3.9 (DR)  3.7 (Linac end) [nC]
Normalized Emittance (x,y) : (~4000, ~3600) @DR, (~140, ~10) @Linac end [mm]
Measurements and Simulation
Simulation roughly reproduces experiment
However, differences also exist, and further investigation is needed

## Slide 27
Backup

## Slide 28: Electron Guns
Photocathode RF gun
Low emittance e- beam for SuperKEKB HER
Thermionic gun on the other side of this wall
High bunch charge for e+ production
0.3 nC e- beam for PF/PF-AR

## Slide 29: Increase in bunch charge through ML tuning
ML Tuning

## Slide 30: Rough beam tuning
Once RF crest phases are found, load the previous beam parameters
Check for anomalies, etc.
Adjust manually so that the bam passes downstream of the Linac

## Slide 31
Tuning performed at accelerator start-up or on a daily basis

## Slide 32: Tuning to increase e+ yield
Maximization of the primary electron beam charge and positron yield at the capture section exit.
Beam loss reduction in J-Arc
RF phase in the capture section
ML tuning
Manual
J-Arc Entrance
J-Arc Exit
Target
e- to e+ conversion efficiency
+0.3%
Parameter: Quadrupoles, Strength of steering magnets, RF phases of klystrons
Change in incident position and yield due to tuning
ML tuning
x
y

## Slide 33: Tuning to increase transmission to DR
Parameter: Strength of steering magnets, RF phases of klystrons
SY2 exit
Cap. Sec. Exit
Klystron Phase
Quad. and Steering Mags of SY2
Energy Knob for 2-sector

## Slide 34
FC Current

## Slide 35
LTR
RTL
1.1GeV
DR
Sect.2
Sect.3 to Sect.5
ECS
BCS
ECS
Injection point
for LER
Injection point
for HER
Arc1
Arc2
Arc3
Linac
BT
Arc0
Arc4
BT1
BT2
Figure 1

## Slide 36: Switch Yard (SY2)
電子ビームは通過
Electron go straight ahead
Back from DR
Go to Damping Ring

## Slide 37: Beam Loss along cap. sec.

## Slide 38: electron positron separation
electron
positrion
High-frequency components are attenuated at the cables and connectors, resulting in a distorted wave form.
（Butterwoth filter: -3 dB @6GHz ）
The original waveform can be restored using the de-embedding method.
Simulation of signal distortion
A structure similar to the Button-type BPM with a protruding central conductor
(Actual protrusion amount is very shot (1 mm))

## Slide 39: Beam signal observed with a board band oscilloscope
Raw signal
Corrected wavefrom
Oscilloscope:
KEYSIGHT UXR00334A
(Bandwidth: 33 GHz)
e-
e+
Signal with de-embedding applied
Even at 33 GHz bandwidth, the e- e+ separation is impossible due to the attenuation of high-frequency components of the signa.
Measurements taken using the demo unit
(33 GHz Osc. is too expensive)
De-embedding method
The method to reconstruct the original waveform using the S-parameters(amplitude, phase) of the transmission line.

## Slide 40
electron
positron

## Slide 41: Switch Yard (SY3) at Linac End
e- beam: HER
e+ beam: HER
PF
PF-AR

## Slide 42: Evolution of luminosity（2019～）
successfully squeezed to 0.9 mm
>1500 mA
>1200 mA
Current Record
4.65 x1034 cm-2s-1
(4.71 x1034 cm-2s-1)
HER(e-)
beam current
LER(e-)
beam current
Luminosity
Integrated
Luminosity
531 fb-1