## Slide 1: Bilan commissioning linac (à compléter)
H. Guler, S. Chance
21/10/24

## Slide 2: Démarrage linac
Faisceau de 50 MeV, 100 pC, 10 Hz
  Photocathode Laser alignement :
    Alignment method (DC Current or BPMs or YAG) : done (BPM/YAG alignement chosen)
  Solenoid alignment :
    Matlab script : done (/data/shared/commissioning_scripts/MatLab/pilotagesoleno_TLSST1_thomx_Dark_dim_bary_v2.m)
    Xopt : still to be done to have more precise alignement (beam centroid precision measurement ?)
  Section alignement : done
    Difficulties during alignement :
      Bad charge transport
      Jumps who appear (ICT ?)
  Quadrupoles alignement : (Align_Quad.py) : done (depends on how we want to align)
    Two different alignments done, need to choose one
    Need to steer the beam for the ring

## Slide 3: Beam measurements
Photocathode laser :
  Iris size measurement :
    At each size : save laser image, scan size vs soleno, scan charge vs phase
Solenoid :
  Main solenoid current at different gun gradient : measure image on YAG screen, check dependance with gun phase
  Scan Beam Size vs Solenoid with LI/YAG for gun caracterization  Simulations comparison /data/shared/commissioning_scripts/MatLab/pilotage/LISST1_vs_Isoleno.m
  Scan Beam Size vs Solenoid with TL1/YAG for section caracterization  Simulations comparison
Losses along the linac
Charge transport measurement :
  Vs RI section phase
  Vs solenoid strength
  Vs steerers (to check alignment)
Energy measurement :
  gun : /data/shared/commissioning_scripts/MatLab/pilotage/LISST1_Steerer_Energy.m
  section :
Emittance measurements (LI, TL)
  @different soleno B
  @ different laser iris opening
  Extract twiss parameters
  Comparison with simulations
Matching
Beam length measurement
Energy dispersion measurement : (/data/shared/commissioning_scripts/MatLab/pilotage/dipole_energie.m)
  Optimisation
  Vs phase section
  Vs Soleno
Extraction line

## Slide 4: Tools for measurements
Tools
  Image analysis : fit of the projection with offset, need to be fixed if we want it to be common. Now rms and fit. Two methods can be tested. Better the fit.
  Beam charge measurement : method has been chosen
  BPMs : calibration
  Save data (Archiving) : for linac , TL and Ring change a bit steerers values and have a data model of the machine and compare with simulations.