## Slide 1: WP2: Low level RF controls Padova meeting, March 13, 2025
All information contained in this presentation and any accompanying documents is for iSAS project only, and must be treated as strictly confidential.
Any dissemination, distribution or other use of this information without the consent of its owner is prohibited.
Funded by the European Union. Views and opinions expressed are however those of the authors only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the granting authority can be held responsible for them.

## Slide 2
WP2: Low Level RF controls 10.01.2025
DESY, HZB, CNRS
Convener & deputy: Holger Schlarb (DESY) & Julien Branlard (DESY)
Main contacts with other partners: Axel Neumann (HZB), Christophe Joly (CNRS)
Task 2.1: Coordination of R&D on LLRF – M1-M48
Task 2.2: Efficient field control for high loaded-quality factor cavities – M1-M48
Task 2.3: Vibration analysis and detuning control of cavities – M1-M36
Task 2.4: Integrated LLRF control using Ferro-Electric Fast Reactive Tuners– M13-M48
Task 2.5: Energy efficient supervisory control and fault diagnosis– M1-M48

## Slide 3
WP2 – LLRF: status/evolution of Task 2.1
Task 2.1: Coordination of R&D on LLRF – M1-M48
Past developments
  WP2 coordination meetings in place
    Status update of the different labs
    Reporting about iSAS project activities (website, industrial board, next in-person meeting)
  Communication structure established
    Email distribution list
    Shared repository (meeting minutes, status reports, presentations)
  Identified test possibilities in each lab
    Test stands, facilities, type of cavities, tuning systems, power sources, etc.
Current developments
  New position
    HZB: postdoc for iSAS
    DESY : new position opening to support with tests (100% iSAS)
    DESY : new senior LLRF to support R&D, start in May 25 (not directly iSAS but will help)
  Change in WP2 management
    Lead Holger Schlarb  Julien Branlard
    Deputy Julien Branlard  Christian Schmidt

## Slide 4
WP2 – LLRF: status/evolution of Task 2.1
Task 2.1: Coordination of R&D on LLRF – M1-M48
Past developments
  WP2 coordination meetings in place
    Status update of the different labs
    Reporting about iSAS project activities (website, industrial board, next in-person meeting)
  Communication structure established
    Email distribution list
    Shared repository (meeting minutes, status reports, presentations)
  Identified test possibilities in each lab
    Test stands, facilities, type of cavities, tuning systems, power sources, etc.
Current developments
  New position
    HZB: postdoc for iSAS
    DESY : new position opening to support with tests (100% iSAS)
    DESY : new senior LLRF to support R&D, start in May 25 (not directly iSAS but will help)
  Change in WP2 management
    Lead Holger Schlarb  Julien Branlard
    Deputy Julien Branlard  Christian Schmidt

## Slide 5
WP2 – LLRF: status/evolution of Task 2.2
Task 2.2: Efficient field control for high loaded-quality factor cavities – M1-M48
Past developments
  Evaluate methods for changing QL (at the cavity coupler and waveguide level)
    (HZB) Tests done at HoBiCat with 3-stub tuner
    (DESY) Modify test stand for operation with SSA : done and approved by German authority (TUEV)
Current developments
  Test with Q-tuner last month
    Developed new devices to extend Qext range
    First result with high power look promising, but need to investigate heating of couplers

## Slide 6: Why is bandwidth and resonance control crucial for efficiency
Operating at higher Qext (narrower bandwidth)
  reduces the power needs IF resonance control can be guaranteed
  makes resonance control extremely challenging
Bandwidth (Qext) and Resonance (f) control
Parameters for SRF gun
r/Q = 208 Ohm Vacc = 5 MV (energy gain from the gun at 50 MV/m -> 5 MeV) Ib = 100 uA (100 pC at 1 MHz)
b = 0 deg.
4 kW
Qext = 1e7
Qext = 4e7
1 kW
1.3 kW
2 kW
3.3 kW
The challenge is to find the highest Qext one can operate the cavity at while still meeting the resonance control goals and without compromising operability and reliability of the system.

## Slide 7: Extending the Qext range
First test with 3-stub tuner at HobiCat
CST simulation
Courtesy A. Neumann
(HZB) re-measured Qext change with 3-stub tuner at HobiCat (had already been done a long time ago…)
Cross checked results with CST simulations.
3-stub tuner

## Slide 8
WP2 – LLRF: status/evolution of Task 2.2
Task 2.2: Efficient field control for high loaded-quality factor cavities – M1-M48
Past developments
  Evaluate methods for changing QL (at the cavity coupler and waveguide level)
    (HZB) Tests done at HoBiCat with 3-stub tuner
    (DESY) Modify test stand for operation with SSA : done and approved by German authority (TUEV)
Current developments
  Test with Q-tuner last month
    Developed new devices to extend Qext range
    First result with high power look promising, but need to investigate heating of couplers

## Slide 9: Developed 2 prototypes to extend the Qext range
Waveguide components to increase Qext range
Courtesy V. Katalev
Iris-tuner (variable)
I-tuner motor
coupler motor
Q-corrector (fixed)
coupler motor
fixed stud
Several devices are being developed to increase or shift the Qext tuning range
High-power test started
Currently investigating induced heating of coupler
T300K heating
T70K heating
coupler motor

## Slide 10
WP2 – LLRF: status/evolution of Task 2.3
Task 2.3: Vibration analysis and detuning control of cavities – M1-M36
Past developments
  Characterize environmental disturbances and transfer to the cavity perturbation.
    First estimation of EuXFEL microphonics indicate +/- 3Hz
    First RF tests at SeaLab (BerLinPro SRF gun), repeat with beam before summer 2025
Current developments
  Investigate and develop detuning counter measures based on advanced feedforward, feedback and active noise cancellation including AI methods.
    (DESY) Implementation of Luenberger Observer to estimate bandwidth and detuning
    (HZB) Estimating cavity detuning using Neural Network
    (DESY) Demonstrated RF phase modulation to achieve stable cavity ramp up in pulsed mode
    (DESY) Demonstrated a more efficient Lorentz Force Detuning compensation at EuXFEL

## Slide 11
WP2 – LLRF: status/evolution of Task 2.3
Task 2.3: Vibration analysis and detuning control of cavities – M1-M36
Past developments
  Characterize environmental disturbances and transfer to the cavity perturbation.
    First estimation of EuXFEL microphonics indicate +/- 3Hz
    First RF tests at SeaLab (BerLinPro SRF gun), repeat with beam before summer 2025
Current developments
  Investigate and develop detuning counter measures based on advanced feedforward, feedback and active noise cancellation including AI methods.
    (DESY) Implementation of Luenberger Observer to estimate bandwidth and detuning
    (HZB) Estimating cavity detuning using Neural Network
    (DESY) Demonstrated RF phase modulation to achieve stable cavity ramp up in pulsed mode
    (DESY) Demonstrated a more efficient Lorentz Force Detuning compensation at EuXFEL

## Slide 12: Detuning estimation using ML
Deep learning of cavity detuning (HZB)
  Primary goal is to see if one can use machine learning, specifically auto-encoders, to predict detuning in CW
  Use deep learning to adapt the cavity model to real-time variations
  Use Koopman filter to make dynamics of the system appear linear
  Simulated detuning data, then used to train and test model
  Next, get experimental data (at Hobicat) to re-train model
Courtesy Andrei Maalberg

## Slide 13: Resonance control
Operating high-Qext cavities in pulsed mode
Ramp-up
  Iterative learning to match the drive signal (amplitude and phase) to the cavity resonance
  i.e. like Self-Excited-Loop (SEL) but with Generator Driven (GDR) approach
  Better suited for pulsed and vector-sum operation
Demonstrated RF phase modulation to achieve stable cavity ramp up in pulsed mode
Courtesy Bozo Richter
1
2
3
4
Qext = 4e7
BW = 32 Hz

## Slide 14: Optimizing Lorentz force detuning at EuXFEL
Parameter optimizer
Courtesy Jannis Luebsen
1. Bayesian optimization of piezo stimulus parameters:
      delay
      amplitude
      offset

## Slide 15: Optimizing Lorentz force detuning at EuXFEL
Use double instead of single sine
2. Using a double sine excitation
  doubles the stimulus time  2 energy
  requires half of the amplitude   4 energy
= net energy saving factor of 2
Courtesy Mariusz Grecki

## Slide 16: Optimizing Lorentz force detuning at EuXFEL
Minimizing the in-rush current reduction
Smoothing the leading edge of a double sine piezo pulse to reduce the in-rush current
  reduces energy
  Increase piezo life time
Courtesy Max Herrmann

## Slide 17
WP2 – LLRF: status/evolution of Task 2.4
Task 2.4: Integrated LLRF control using Ferro-Electric Fast Reactive Tuners– M13-M48
Past developments
  FE-FRT development at HZB  see WP01
  Seminar last week at DESY (Nick Shipman) to present latest FE-FRT results at HZB
Current developments
  Goal is to integrate a ferro-electric fast reactive tuner (FE-FRT) with a digital LLRF system
    Hardware development 2026/27 within WP1
    Simulation on effect and operation range can be carried out
    When type and actuation is defined, digital interface can be defined
  Demonstrate microphonics compensation using a FE-FRT at a horizontal test stand
    Demonstration at HoBicat
  Development of Matlab/Simulink model of RF control loop to simulate resonance control for PERL (ICJLab)
    FE-FRT can be included in model

## Slide 18
WP2 – LLRF: status/evolution of Task 2.4
Task 2.4: Integrated LLRF control using Ferro-Electric Fast Reactive Tuners– M13-M48
Past developments
  FE-FRT development at HZB  see WP01
  Seminar last week at DESY (Nick Shipman) to present latest FE-FRT results at HZB
Current developments
  Goal is to integrate a ferro-electric fast reactive tuner (FE-FRT) with a digital LLRF system
    Hardware development 2026/27 within WP1
    Measure FE-FRT voltage response and temperature dependence
    Evaluation of existing MTCA hardware as potential FE-FRT driver
  Development of Matlab/Simulink model of RF control loop to simulate resonance control
    Using FE-FRT voltage response, include it in LLRF control simulation environment
  Demonstrate microphonics compensation using a FE-FRT at a horizontal test stand
    First demonstration at HoBicat
Roadmap toward milestone

## Slide 19
WP2 – LLRF: status/evolution of Task 2.5
Task 2.5: Energy efficient supervisory control and fault diagnosis– M1-M48
Past developments
  1st milestone delivered and approved : (D35) ML implementation plan
Current developments
  Develop fault diagnosis and anomaly detection of LLRF systems using ML approaches
    Demonstration of quench detection in CW using Luenberger Observer
    Development of a machine learning-based anomaly detection
                Software implementation deployed in 1 RF station at XFEL (fast development)
    Firmware (FPGA) implementation deployed on ALL stations at XFEL (observation phase)

## Slide 20
WP2 – LLRF: status/evolution of Task 2.5
Task 2.5: Energy efficient supervisory control and fault diagnosis– M1-M48
Past developments
  1st milestone delivered and approved : (D35) ML implementation plan
Current developments
  Develop fault diagnosis and anomaly detection of LLRF systems using ML approaches
    Demonstration of quench detection in CW using Luenberger Observer
    Development of a machine learning-based anomaly detection
                Software implementation deployed in 1 RF station at XFEL (fast development)
    Firmware (FPGA) implementation deployed on ALL stations at XFEL (observation phase)

## Slide 21: Anomaly detection
Machine-learning assisted anomaly detection
References:
Anomaly detection at the European X-ray Free Electron Laser using a parity-space-based method
A. Eichler, et al, Phys. Rev. Accel. Beams 26, 012801 – Published 4 January, 2023
A Two-Stage Machine Learning-Aided Approach for Quench Identification at the European XFEL
L. Boukela, et al. arXiv:2407.08408
1. Benchmarking of FW implementation using off-line quench data
FW
SW
2. Testing FW implementation at EuXFEL by triggering anomaly (incorrect trace scaling)
Will be presented at IPAC 2025
Courtesy B. Dursun & Ch. Schmidt

## Slide 22
WP2 – LLRF: status/evolution of Task 2.5
Task 2.5: Energy efficient supervisory control and fault diagnosis– M1-M48
Past developments
  1st milestone delivered and approved : (D35) ML implementation plan
Current developments
  Develop fault diagnosis and anomaly detection of LLRF systems using ML approaches
    Demonstration of quench detection in CW using Luenberger Observer
    Development of a machine learning-based anomaly detection
  Investigate energy saving options, based on RF solutions
    Applying techniques modulator shaping techniques to support longer RF pulses
    Development of an SSA test stand
                Software implementation deployed in 1 RF station at XFEL (fast development)
    Firmware (FPGA) implementation deployed on ALL stations at XFEL (observation phase)

## Slide 23: Saving energy with RF
Now implemented on all RF stations at EuXFEL
Shaping modulator pulses (and compensate with LLRF) to keep AC consumption to its bare minimum
Ref. “RF-based energy savings at the FLASH and European XFEL LINACs”
J.Branlard et al. in proc. of LINAC 2024
Example:
How shaping the modulator pulse can save power
 LLRF development to compensate introduced non-linearities
Power savings > 1 MW (i.e. Mio €)

## Slide 24: Applying the same technique to offer longer beam time
Studied at several stations at EuXFEL
Configuration | Tfill (usec) | Tflat (usec) | Ttotal (usec) | AC power (kW) | Max energy (MV)
Short flat top with energy saving | 750 | 650 | 1400 | 182 | 845
Long flat top (no energy saving) | 650 | 850 | 1400 | 283 | 845
Long flat top with energy saving and Qext optimization | 630 | 850 | 1480 | 200 | 845
Lower Qext also increase the power during beam time
Further optimization possible by starting modulator slope earlier (“final tweaking”)
No energy saving, no Qext adjustment
Energy saving measures, Qext adjustment
650 usec beam time
850 usec beam time
disaster
only 10%
+200 usec = 30% more beam

## Slide 25: SSA R&D at DESY
SSA test stand (1 kW amplifier)
Cooling plate
1 kW dummy load
Preparation of a SSA test stand
GaN 1 kW prototype
Cooling / load / power supply
Experiment with pulsed/CW operation
Understand efficiency optimization with drain voltage adjustments
Reference: “High-efficiency industrial 130 KW CW solid-state RF amplifier for 1.3 GHz”, M. Nedos, N. Pupeter et al. in proc. IPAC 2023
Example
GaN technology
1.3 GHz
130 kW SSA
drain voltage (Vdd) adjustments

## Slide 26
WP2 – LLRF: points of attention
Points of attention
  Personnel setback
    key person for R&D left DESY in Fall 2024
    mitigation: opened replacement position but challenging to find qualified personnel
  Dependence of iSAS R&D on laboratory schedule
    availability of test stands is not always predictable (delay, warm up, etc..)
    mitigation: compiled a list of tests capabilities in partner labs
  Future hardware development – on going
    “Evolution” step : Development of next generation digitizers (heterodyne detection mode)
    “Revolution” step : First successful test of CSI (carrier suppression interferometer) integration with LLRF system at test stand with cavity

## Slide 27: Carrier Suppression Interferometer
Concept
Overcome noise limits of the post-IQ system
CSI performance scales with RF input power
Source  very low amplitude noise !
Replace the DUT with the LLRF system
CSI signal contains no carrier
  no absolute information of amplitude and phase
CSI signal as amplified error signal
  Combination of CSI and standard measurement as controller input
Courtesy: M. Hoffmann

## Slide 28: Measurement Results from CMTB
Lab MO as Reference (best results)
Cavity at QL ~ 107 (f12 = ~ 65 Hz)
Open loop vs. PI controller vs. CSI with PI
Reached noise floor of FSWP
Requires stable condition of the cavity (steady state CW)
Cavity tuning (PZT) to maintain operation at resonance
Courtesy: M. Hoffmann

## Slide 29
WP2 – LLRF: plans to achieve milestones & deliverables
Milestones & deliverables on track?  yes
Plans to achieve milestones & deliverables
  Delay risks to be anticipated?  some unknowns but nothing critical. Plan B as back up
  Cooperation with other WP(s) to be reactivated?  clearly potential to increase collaboration, not always easy in practice due to daily “emergency” in home institute + budget / travel restrictions
  Risk mitigation measures to be implemented?  develop official impact risk analysis Feb. next year

## Slide 30
WP2 – LLRF: financial status
Financial status
  Funds engaged in the WP by institute to date, differentiating EU-budget from matching funds
  With highlight of staff dedicating time on the iSAS project, to date & projections if possible
Deviations?  I think still on track
WP 2 | EU-Budget | Matching funds
2024 | 7,050.55 | 111,687.13
2025 | 2,147.25 | 5,862.23
Total | 9,197.80 | 117,549.36
Most of the budget is foreseen to hire personnel.
iSAS position to be released this month + advertised on iSAS
Money already spent was to pay personnel to bridge the gap

## Slide 31
THANK YOU
FOR YOUR ATTENTION !
WP2: Low Level RF controls 10.01.2025
DESY, HZB, CNRS
Convener & deputy: Holger Schlarb (DESY) & Julien Branlard (DESY)
Main contacts with other partners: Axel Neumann (HZB), Christophe Joly (CNRS)

## Slide 32: BACKUP

## Slide 33: Example 3a
What is the wall plug AC-to-RF power efficiency?
Metric: AC-to-RF efficiency
Example 1 LDMOS technology
1.3 GHz
4 kW SSA
Pout (dBm)
Efficiency (%)
Example data from LCLS-II SSAs
Example: How the choice of amplifier class can affect efficiency  LLRF development to compensate non-linearities
Reference: “Tutorial: RF amplifiers Overview and Impact on LLRF control loops”, E. Montesinos, LLRF workshop 2017

## Slide 34: Example 3b
Can we optimize the efficiency by keeping the amplifier in saturation ?
Metric: DC-to-RF efficiency
Example : How adjusting the drain voltage (Vdd) can improve the DC-to-RF efficiency
 LLRF development to control Vdd & optimize efficiency
Example2
GaN technology
1.3 GHz
130 kW SSA
Reference: “High-efficiency industrial 130 KW CW solid-state RF amplifier for 1.3 GHz”, M. Nedos, N. Pupeter et al. in proc. IPAC 2023
drain voltage (Vdd) adjustments
Note that efficiency alone doesn’t tell the whole story
efficiency
operability
stability
design
choice