## Slide 1: Perle Buncher AG du Pôle Ingénierie Orateur : S. Marchal
+ Contributions through iSAS of

## Slide 2
Parameters | Values
Injection Energy | 7 MeV
Electron beam energy PHASE 1 (single turn) | 89 MeV
Electron beam energy PHASE 2 (three turns) | 250 MeV
Normalised Emittance γεx,y | 6 mm.mrad
Average beam current | 20 mA
Bunch charge | 500 pC
Bunch length | 3 mm
Bunch spacing in injector | 25 ns
RF frequency | 802 MHz
Duty factor | CW
Two phases :
1-turn ; 3-turns
PERLE @250 MeV 3-turns
PERLE @89 MeV 1-turn

## Slide 3: DC Gun installation status LASER room
Photocathode Production Facility (PPF) assembly
Gun chamber HPR cleaning in clean room
Mobile clean room
Progress
In the installation of
The DC-gun complex
05/02/2025

## Slide 4: Project Phasage - Macro view with milestones
DC Gun @350 keV
2024
2025
2026
2027
2028
2029
2030
2031
Injector @ 7MeV
ERL 1-LOOPS
DC gun
operation
Cryogenic
installed
Injector installed
Cryomodule
tested
Cryomodule
Installed
First ERL
demonstration
3-loop ERL
demonstration
ERL 3-LOOPS
Design
Procuirement / Construction / Installation
Commissioning
20 mA
2MW
5MW
TDR
PERLE 1-LOOP 89MeV
PERLE 3-LOOPS 250MeV
IGLOO ready
20 mA

## Slide 5
Buncher localisation
Buncher

## Slide 6
Buncher specifications
Specifications :
Frequency = 801 MHz
Maximum length = 200 mm
Targeted temperature = 30°C
Power dissipated = 1,6kW or 5kW
Material : OFHC
Beam axes flange : CF50
2 ports : CF 16
Vacuum port : CF40
RF power coupler port : ?

## Slide 7
Buncher design review
Cerl Type buncher :
Manufacturing with 3D printed copper
Nose Cone type buncher with cooling system brazed :
Classic machining
Cooling system brazed
Nose Cone type buncher with cooling system machined :
Classic machining
Cooling system machined
Buncher
Cerl type
Nose Cone type

## Slide 8
Cerl Type buncher
3D printed

## Slide 9
Buncher RF characteristics
Jean Louis Munoz from ESS Bilbao Simulation’s

## Slide 10: Buncher equipment
CF50
Plunger
Grid
Vacuum pump
Antenna

## Slide 11: Buncher design

## Slide 12: Cooling system pressure losses
Inputs :
Inlet velocity of 3,5 m/s (0,1L/s)
Outlet pressure of 0,2 MPa
Ra of 25 μm
Results :
Pressure losses = 0,5 MPa (5 bar) for three circuit in series
0,17 MPa per circuit
Characteristics :
3 circuits in //
Pipe of Ø6 mm (internal)
min radius of 5mm

## Slide 13: Thermal simulations
Results :
T max < 30°C
Inputs :
Inlet water temperature at 20°C and a flow of 0,1 L/s
Absorbed power of 5kW distributed according to the heat flow field (simulated by Patricia Duchesne)

## Slide 14: Mechanical simulations
Results :
Y Deformation (Beam axes) : 0,008 mm
X Deformation : 0,006 mm
Inputs :
Intern pressure : -0,10132 MPa
Thermal dilatation based on thermal simulation
Pipes pressure : 1MPa
Pump weight : 50 N
Gravity

## Slide 15: Mechanical simulations
Results :
Constraint < 33 MPa

## Slide 16
Nose Cone type buncher
Cooling system brased

## Slide 17
Jean Louis Munoz from ESS Bilbao Simulation’s
Buncher RF characteristics

## Slide 18: Buncher design

## Slide 19
Nose Cone type buncher
Cooling system machined

## Slide 20
Buncher design review

## Slide 21
Frequency shift
R out at ± 1mm
W/2 at ± 1mm
G/2 at ± 1mm
θ at ± 1 degre

## Slide 22
*Frequency shift due to the mechanical constraint and thermal dilatation only
5kW
1,6kW
Results

## Slide 23
Next steps
2025
2026
Research on the feasibility
Finalisation of the design
Finalisation of the design
Simulations
Estimation of the cost
Estimation of the cost
Estimation of the cost
FINAL DESIGN
Technical drawings
Tests
RF tests
Mechanical tests
Cooling system tests
Vacuum tests
Fabrication
Adjustment
RF Power coupler
design
Technical drawings
Estimation of the cost
Fabrication
INSTALATION
Call for tenders
Call for tenders
Simulations

## Slide 24: MERCI
Contributions :
D. Reynet, R. Roux, J.L. Muñoz (ESS Bilbao), P. Duchesne, C. Joly, A. Blot, T. Proslier (CEA), W Kaabi, F. Bouly (LPSC)…

## Slide 26: Thermal results
Results :
T max < 35°C
Input :
Inlet water temperature at 20°C and a flow of 0,1 L/s
Absorbed power of 5kW evenly distributed

## Slide 27: Mechanical result
Results :
Y Deformation (Beam axes) : 0,032 mm
X Deformation : 0,005 mm
Input :
Intern pressure : -0,10132 MPa
Thermal dilatation based on thermal simulation
Pipes pressure : 0,5 MPa
Gravity

## Slide 28: Mechanical result
Results :
Constraint < Elastic Limit*
* The copper elastic limit is 33MPa, in some point of this simulations, the constraint is > 33 MPa. It’s due to the mesh, not the real constraint

## Slide 29: Thermal results
Results :
T max < 42,5°C
Input :
Inlet water temperature at 20°C and a flow of 0,1 L/s
Absorbed power of 5kW evenly distributed

## Slide 30: Mechanical result
Results :
Y Deformation (Beam axes) : 0,047 mm
X Deformation : 0,040 mm
Input :
Intern pressure : -0,10132 MPa
Thermal dilatation based on thermal simulation
Pipes pressure : 0,5 MPa
Gravity

## Slide 31: Mechanical result
Results :
Constraint < Elastic Limit

## Slide 32: Buncher in stainless with copper coating
Stainless VS copper
Can be bolted instead of brazed
Similar efficiency of the mechanical strength
CF flanges can be integrated in the 3D model
Lower efficiency of the cooling system

## Slide 33
Buncher with or without reinforcement
Results :
without reinforcement Deformation = 3,75 x with reinforcement Deformation

## Slide 34
Buncher with full or inclined reinforcement
Results :
Deformation : Full = 0,87 x inclined
Weight : Full = 1,33 x inclined

## Slide 35
Buncher with vertical or inclined reinforcement
Results :
Deformation : Vertical = 1,28 x inclined
Constraint : Vertical = 1,04 x inclined

## Slide 36
Simulations with 1,6kW

## Slide 37
Simulations with 1,6kW

## Slide 38
Simulations with 1,6kW