## Slide 1: SiW-ECAL Status
DRD6 3rd collaboration meeting
01/04/25 @ IJCLab
Vincent Boudry Institut Polytechnique de Paris for the SiW-ECAL groups
/ DRD6

## Slide 2: Design Constraints
PP ↔ Cont
+ timing
Physical
Instrumental
Electronics
Mechanical Thermal
Production / Integration
Cooling
DAQ
Structure
B = 2 – 3.5 T
Mininal Margins

## Slide 3
Timeline of SiW-ECAL Prototypes
Physical (2005-11)
  1×1 cm² on 500μm 6×6 cm² Pad glued on PCB Floating GR
  × 30 layers (10k chan).
  External readout
  Proof of principe
Technological (now)
  Embedded electronics
    Power-Pulsed, Auto-Trig, delayed RO
    S/N = (MPV/σNoise) ≥ ~12 (trig)
  Compatible w/ 8+ modules-slab
  5×5 mm² on 320–650m 9×9 cm² × 26–30 layers
    8k (slab) ~ 30k (calo) channels
Pilote ➡︎ Full Detector
  1M ➡ ︎ 70M channels
  on 725μm 12×12 cm² 8’’ Wafers ?
  Pre-industrial building
  Full integration (⊃ cooling)
  Final ASIC
‘dead space free’ Carbon Fibre-W Structure
We are here
× 45
× (40+24)
× 4
× 8 × 2
‘Almost ready’ for LC To be revisited for CC

## Slide 4: Technological Prototype Beam test at DESY & CERN
2022 DESY & CERN BT
Masking Beam profiling
Yuichi Okugawa (PhD in Feb. 2024)

## Slide 5: New FE boards (2023)
Improvements:
  Power distributions
    Local LV power regulation: LDO’s
    Local HV filtering & Supply
  Signal distribution (buffering), data paths
  Monitoring (single ID, temp, probe analogue line)
  ASIC shielding/routing
Status:
  Noise uniformity dramatically improved (ex: outliers in thr. / 20)
  version 2.1 produced
    4 cabled, 2nd metrology, 2 equipped with sensors (Fev’25)
Pedestal measurements vs. Ch# + Mem#×100)
FEV11
FEV2.0
SIngle channel ➞ the fault on the ASIC/packaging

## Slide 6: Hybridization studies (2024): How to assemble silicon sensors & PCB ?
Flatness of PCB
Measurements by C. Orero, IFIC
Revisiting gluing (IFIC, IJClab, DMLAB)
  PCB metrology
    Bef. & After curing & soldering
  Glue formula & preparation
  Gluing methods
    Robot
    Stencil
  Reenforcement
    Filling glue
    Adhesive films
Conductive glue + filling (~invisible) on a glass plate
Puncturated adhesive film (DMLab)
+ conductive glue dots
Same PCB before / after 10-day dry storage
IJClab (méca)
IFIC (optical)
See Adrián’s presention in side SiW-ECAL meeting
for a complete overview

## Slide 7: ASU2025_001 + 002 (2025)

## Slide 8: Commissioning: Analogue Probes
Analogue Probes
1 value (LV, Channel, …) ➞ common line
See Roman’s presention in side SiW-ECAL meeting
for a complete overview

## Slide 9: Commissioning: 90Sr
Tests made one week
before BT at DESY
Beam test reports:
  See (next) Yukun’s presentation

## Slide 10: Fluxes in Calorimeters
Take Home:
  Even at Z peak power dominated by pre-amp (⬌ conversion power in negligible)
  Tool is there, missing:
    Digitization (easier way in Key4HEP ?)
    Mapping needs to be adapted for each calorimeter readout topology

## Slide 11: ECAL adaptation : flat cold plate, preliminary thermal studies
Uniform solutions:
“Standart Slab”:
  8 ASU (1440mm)z, 8192 ch / 128 ASICs
  100 W
Passive cooling: Cu of 2mm (W, C ignored)
Adiabatic, but for heat bridge at the end
∆T = 500°C on Wafer surface at 𝑡 = ∞
“Standart Slab”:
  8 ASU (1440mm), 8192 ch / 128 ASICs
  128 W (1W/ASIC ~16 mW /ch)
Active cooling:
  Hollowed Cu of 4mm, with 1ℓ/min of water @ 15°C
Adiabatic, but for heat bridge at the end
∆T = 12°C on Wafer surface at 𝑡 = ∞
© Oscar Ferreira, François Joubert @ LLR
Connections ?
Status:
  Limited flow of water seems enough…
  Now looking into pipe in 4-mm Cu layer
    Replaces W in 1st half of SiW-ECAL
    Replaces ½ the W in the second part
  To be validated on simulations

## Slide 12
Centimetric Timing

## Slide 13: Timing in Calorimeters: 0.1–1 ns range
Cleaning of Events
Particle ID by Time-of-Flight
  Complementary to d𝐸/d𝑥
    Here with 100 ps on 10 ECAL hits
Ease Particle Flow with 𝒪(30) ps ?
  Cleaning of late neutrons & back scattering (ns)
  𝒪(30) ps for mips… HGCAL / 100!
  Identify primers in showers
  Help against confusion better separation of showers
    Requires ‘4D clustering’
time cut
(1 ns)
[CLIC CDR: 1202.5940] adapted from L. Emberger
S. Dharani, U. Einhaus, J. List
Ch. Graf
1 cm/c = 30 ps
Started in KIT, JGU, IJClab, LLR and IP2I (Lyon): Calo5D & T-Calo

## Slide 14: Time measurement methods
0
t
Thr.
ToA : TDC + ADC
0
Shaping : ADC × n
Thr.
0
CFD
Valid
Valid
CFD : TDC + Gating
t’
Slew time (vs amplitude)
Time fit (vs shaping)
Time ~ cst (vs pedestal, noise)
In SKIROC2. Validation of digi on beam tests…

## Slide 15: Conclusions
SiW-ECAL technological prototypes
  2022: Heterogeneous 15 layers
    1st full calorimeter working [DESY22, CERN22]
      Shower seen, Detailled simulation ready
      Analysis on-going ➞ resolutions, ...
    Numerous emerging issues
      gluing, HV filtering at high energy
  2024 2025–26: Uniform 15 layers
    ➞ New VFE boards
      Cleaner PS & Clock distributions; more uniform
    Gluing being revisited
    Material available.
    To be tested in 2025
      ➞ Provide reference sample for GEANT4
      ➞ With funding ➞ “full” LUXE, EBES, Lohengrin ?, SHiP ?
    Start FE board on HKROC ?
SiW-ECAL design for HET factories
  2023–25: Power budget & performances to be re visited
    Occupancy, power, data fluxes (on-going)
      ➞ Granularity; Passive or Active cooling
      ➞ new ASIC attributes (← CALOROC Pres Dulucq)
    2025–27: PFA & Timing & Physics performances
  2025–27 : Blue-print for a SiW-ECAL detector for the next ee collider
    ➞ planning for a pilote module @ T0 collider-8y -5y (1 Mch, 1/60th of real detector)
      semi-industrial, quality, ASICs, …
+1
+1
+1

## Slide 16: Planning towards a pilot module… just in case
T0-8 : production start
?