## Slide 1: ECAL-P status
Yan Benhammou on behalf of the ecal-p collaboration

## Slide 2: Outlook
General design
Mechanics
Absorber
Sensors
Readout
Test beam/assembly

## Slide 3: From COMPACT luminosity calorimeter …
For more than 15 years, FCAL collaboration is working to design a compact calorimeter for luminosity measurement (and also on other forward calorimeters)
LumiCal
BeamCal
4 sectors:
L2
L1
R1
R2
channels: 1 - 64
Outer active radius R = 195.2 mm
3 x 100 μm guard rings
8.1 ± 0.1 (stat) ± 0.3 (syst) mm
Effective Moliere radius :
transverse shower development

## Slide 4: … To LUXE @ DESY
For strong fields, QED perturbation theory breaks down and becomes non perturbative
At the Schwinger critical field, ecrit = me2c3/eh ∼ 1018 V/m, the vacuum becomes unstable to pair production
In the last five years, the FCAL collaboration used its knowledge to built a calorimeter to detect the positron : the ECAL-P

## Slide 5
General design
Highly compact calorimeter
Silicon – tungsten planes
Six sensors per plane (~55cm)
20 planes
Distance between tungsten : 1mm
Front End Boards above the sensors : readout and HV
Possibility to remove one layer

## Slide 6: Mechanics: mainframe and combs
Aluminium : bottom (30mm), bakcplane (20mm), combs (20mm and 10 mm)
Overall precision assembly ~10 mm
Connection to the electronic board frame
Combs pitch : 4.5 mm (tungsten: 3.5 mm + detector: 1 mm)
Comb gaps : 3.5 + 0.08 mm (bottom combs), 3.5 + 0.08 (side combs)
Technical holes for future lowering mechanism
WARSAW University

## Slide 7: Mechanics : sensor and readout electronics FRAME
It defines the position of all the sensors and the Front End Boards (FEB)
Need to be really precise ~10 mm
Possibility to remove/install a full layer (sensor+FEB)
Precision pins

## Slide 8
Mechanics : sensor and readout electronics
Precision pins

## Slide 9: Absorber: Tungsten
~55 cm x ~10 cm x 3.5 mm (1X0)
Tungsten with purity > 99.9 %
Weight ~3.6 kg
Purchased : 3 + 3 (from two different chinese companies).
four new are now being ordered and should arrive before April

## Slide 10
Absorber: CMM measurement
New tolerance : 3.5 +0 -0.1 mm

## Slide 11: Sensors : silicon with calice design
16x16 pads of 5.52 x 5.52 mm2
320 mm thickness
90 sensors purchased
Tel Aviv University

## Slide 12
Sensors : silicon with calice design
DONOR DENSITY
DEPLETION VOLTAGE

## Slide 13: Sensor plane: production of the PCB
Fan out PCB : produced
HV PCB: will be sent to production next week

## Slide 14: Sensor plane: conductive gluE THICKNESS STUDY
Need to glue the sensor to :
  Readout flexible PCB
  HV flexible PCB
IFIC - Valencia

## Slide 15
Sensor plane: conductive glue THICKNESS STUDY

## Slide 16: Sensor plane: non conductive glue study
Need to glue the sensor to the fiber carbon envelop : tests conducted
with conductive glue (H20) ~ 45 microns

## Slide 17: Sensor plane: GLUING JIGS
Study and creation of jigs to glue the different detector layers
Precision pins

## Slide 18: Gluing jigs

## Slide 19: Sensor plane: carbon fiber envelop
Carbon fiber needs to be machined with precise holes
High precision holes and low precision holes CF were produced

## Slide 21: Readout: FLAXE
FLAME ASIC: developed for the luminosity detector at future e+e- accelerators.
  32 channels
  Analog front end in each channel. CR-RC shaper of 50 ns
  10 bit ADC at 20 MHz
  High speed serializer
FLAXE is similar without the high speed serializer (not needed at LUXE)
FLAXE
https://iopscience.iop.org/article/10.1088/1748-0221/20/01/C01026/pdf
AGH - Krakow

## Slide 22: Readout: Flaxe production and test
Production in April 2024
100 bare dies and packaged ASIC where received in june-july
Almost all the production failed because of manufacturing problems !!!
Flame will be used until new production

## Slide 23: 2022 test beam @ DESY : setup
5 GeV electron beam
Telescope based on the Alpide sensor (6 planes)
Two silicon sensors
Two GaAs sensors
Trigger with TLU
Electron beam

## Slide 24: 2022 test beam @ DESY : detectors
Silicon (CALICE)
Array of 5.5x5.5 mm2
Thickness 500mm
10mm between pads
p+ on n substrate
Produced by Hamamatsu
Gallium Arsenide
Array of 4.7x4.7 mm2
Thickness 500mm
300mm between pads
Produced by Tomsk State University

## Slide 25: 2022 test beam @ DESY : connection
Silicon (CALICE)
Kapton fan out with copper traces (to the connector) glued (conductive glue) to the sensor
Gallium Arsenide
Aluminum traces in between the pads
Bonding to PCB

## Slide 26: Edge effects: signal
GaAs
Silicon
2x2 pads
2x2 pads
50% drop
2% drop
Pad is subdivided into 100 strips
10mm between pads
300mm between pads

## Slide 27
Edge effects: sum of adjacent pad signal in X
Silicon
GaAs
Drop of 40% (traces)
No drop
10mm between pads
300mm between pads
Paper submitted to The European Physical Journal C, https://arxiv.org/abs/2501.07431

## Slide 28: Test beam/assembly : JUNE 2025 @ DESY
Setup:
  10 tungsten plates
  10+1 sensors x 2 towers: 22 silicon sensors
  FLAME ASIC and dedicated FEBs (1 FEB per layer)
  Each FEB is connected to one FPGA board
Goal : electromagnetic shower study
  Electron beam entering in the middle of the sensor/ in between two sensors
  Electron beam perpendicular/with an angle respect to the calorimeter

## Slide 29
Test beam structure
Detector
Sensors and FEB
FPGA card
FPGA cards

## Slide 30: Test beam/assembly : JUNE 2025 @ DESY
Problem with tungsten plaTes : redesign of the combs from 1mm to 1.2mm : smoothly insertion of the sensors

## Slide 32: conclusion
Mechanics : the frame (sensors, tungsten and electronics) designed and produced.
Absorber : six plates arrived with deviation respect to our needs. Another four ordred with different specs
Detector plane: 90 silicon sensors purchased and tested. Different PCB designed and fan out produced. Jigs for the gluing have been designed. Carbon Fiber envelope needs special attention. Gluing protocol has been deeply investigated.
Readout: new ASIC (FLAXE) developped and produced with problems (due to the company). New run in Q2 2025. Using the FLAME in the meantime.
Test beam 2022 : characterization of silicon and GaAs sensors.
Test beam 2025 : ten layers with two towers : 20 sensors, ten tungsten planes, ten FEB boards
the FCAL collaboration is moving to a new structure : including a LUXE part and a future collider part