## Slide 1
simulations for ACTAR TPC decay experiments
Réseau R&D Détecteurs à Gaz
March 31th –April 1st 2025 – Saclay
J. Giovinazzo – LP2iB (former CENBG) – Bordeaux
 decay experiments with ACTAR TPC
 simulations for detection efficiency
 decay simulation principles
 application to tracks analysis

## Slide 2
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
decay experiments with ACTAR TPC
designed as “active target”…
high efficiency, thick target, vertex, tracking,
good energy resolution…
inverse kinematic reactions
unbound resonances, highly excited states
transfer & charge exchange reactions
…and implantation/decay TPC
high efficiency, transp. to beta, low threshold
multi-particle tracking…
charged particles / exotic decay modes
beta-delayed (multi-)proton
particle decay of excited states

## Slide 3
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
decay experiments with ACTAR TPC
time offset
track length
y
x
t/z
150 ns
ion  1 GeV
proton  1 MeV
E690 (GANIL, 2019): proton decay of 54mNi

## Slide 4
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
decay experiments with ACTAR TPC
time offset
track length
y
x
t/z
few ms
150 ns
ion  1 GeV
proton  1 MeV
E690 (GANIL, 2019): proton decay of 54mNi
E791 (GANIL, 2021): 2p radioactivity of 45Fe & 48Ni
different events
for implantation
and decay

## Slide 5
simulations for detection efficiency
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments

## Slide 6
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
need for simulations: escape probability
2 proton energies
 relative decay branches intensity ?
○ different track energy / length
↔ different escape probabilities
○ proton track hidden in ion track
○ missing regions in the pad plane
(+ analysis procedure and cuts)
track length ↔ proton energy
E690

## Slide 7
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
need for simulations: escape probability
2-proton radioactivity
single decay branch
event by event analysis (counting)
E791

## Slide 8
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
need for simulations: escape probability
2-proton radioactivity
single decay branch
event by event analysis (counting)
beta-delayed 1,2,3-proton(s)
 from several nuclei (cocktail beam)
 decay scheme
E791
45Fe
48Ni
IAS
2p?
QEC
β+ / EC
p
γ
F
GT
p
γ
S2p(Xb)

## Slide 9
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
need for simulations: escape probability
2-proton radioactivity
single decay branch
event by event analysis (counting)
beta-delayed 1,2,3-proton(s)
 from several nuclei (cocktail beam)
 decay scheme
absolute transitions intensities
 function of transition energy
E791
β-1p
β-2p
β-3p
β-1p
45Fe
48Ni

## Slide 10
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
detection efficiency
simulation run
simulation of decay events
 scan of simulation space
• emission point ( )
• decay energy ( )
simulation is only
the first step

## Slide 11
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
detection efficiency
analysis
• pads mult.
• X-Y escape
• Z escape
simulation run
result
stat. confidence
intervals
interpolation
graph
interpolated
histogram
(binomial
uncertainty)
intrinsic efficiency…
probability of full detection
of a proton emitted with
energy

## Slide 12
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
detection efficiency
intrinsic efficiency…
…convoluted with experimental implantation
…distribution for nucleus Y
beam parallel to X axis:
uncertainty:
• statistics
number of sim. events
• systematics
+ simul. param.: pressure, ampl., disp., noise, TZ profile…
+ analysis param.: threshold, escape cuts
(see further)

## Slide 13
ACTAR TPC simulations main lines
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments

## Slide 14
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation
purpose is not the full reproduction of the experiments
(unlike particle physics)
estimate the number of protons escaping full detection

## Slide 15
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation: event generator
event generator
simple ad hoc generator
implantation basically not needed
(but backward tracking for E690 – see further…)
generate primary particles at
any (implantation) point
 direction
 energy
incoming ion
proton
beta
recoil

## Slide 16
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation: tracking
tracking with Geant4
basically a simple gas volume
with particles travelling inside
• primary vertex
• tracking of primary particle
recording all steps / hits
proton
beta
recoil
event generator
tracking
tracking parameters
• gas pressure
• physics list (processes)
 energy loss along the
particles path
E690

## Slide 17
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation: signal collection
event generator
tracking
signal collection
proton
beta
recoil
drift of ionization signal
• from tracking steps energy loss
• parameter: drift velocity (from exp. data)
 Z to T conversion

## Slide 18
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation: signal collection
event generator
tracking
signal collection
proton
beta
recoil
drift of ionization signal
• from tracking steps energy loss
• parameter: drift velocity (from exp. data)
 Z to T conversion
signal dispersion
• 3D Gaussian dispersion (XY & Z/T)
• dependence with drift path:
size of the
entrance
window
preliminary

## Slide 19
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation: signal collection
event generator
tracking
signal collection
proton
beta
recoil
drift of ionization signal
• from tracking steps energy loss
• parameter: drift velocity (from exp. data)
 Z to T conversion
signal dispersion
• 3D Gaussian dispersion (XY & Z/T)
• dependence with drift path:
amplification
• collection gain from micromesh
• adjusted from known proton energies
(after processing…)
size of the
entrance
window
preliminary
preliminary

## Slide 20
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation: signal processing
electronics response function
charge preamp. + shaper from
GET electronics
• theoretical R.F. (P. Baron):
• effective analytical R.F.:
• comparison with empirical R.F.
2 parameters:
 amplification ()
 shaping time ()
event generator
tracking
signal collection
signal processing
CSA
shaper
memory

## Slide 21
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation: fluctuations and noise
more realistic signals ?
input & output (Gaussian) noise
amplitude for simulation
 input noise filtered by resp. function
 output noise not modified
pads noise
simulated noise
input
resp.
function
output
input
noise
output
noise
pads noise
simulated noise
input
noise
output noise
event generator
tracking
signal collection
signal processing
analysis of spectral power distribution
adjust noise on experimental S.P.D.
 from pads in “read always” pads
(if no signal)  from events with no signal
chip architecture
effects no reproduced
input noise constraints:
power vs filtering (shaper)

## Slide 22
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
analysis cuts
event generator
tracking
signal collection
signal processing
analysis cuts
simulation  tracks signal on each pad
include exp. data analysis parameters
 bad pads suppression
 pad validation from signal threshold
 global trigger multiplicity
 number of border pads for
for escape condition
for E690
 suppression of pads “hidden” by
implantation signal
ion track back-traced according to
experiment directions distribution
for ion pads suppression
number of fully reconstructed tracks:
detection efficiency

## Slide 23
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
efficiency uncertainties
event generator
tracking
signal collection
signal processing
analysis cuts
gas pressure
physics list
dispersion
collection gain
input noise
amplification
output noise
threshold
XY escape border
trigger multiplicity
all parameters need to be considered
in resulting efficiency error budget
some correlated parameters
heavy to take into account (not difficult)
( × computing time)
simulation
E690

## Slide 24
simulations for tracks analysis
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments

## Slide 25
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
tracks analysis
“standard” analysis
signal amplitude + CFD timing
2D (X,Y) A & T
 2 × 16k = 32k data

## Slide 26
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
tracks analysis
“standard” analysis
signal amplitude + CFD timing
2D (X,Y) A & T
 2 × 16k = 32k data
deconvolution analysis
 response functions for each channel
full 3D (X,Y,T) signal distribution (from FFT)
 512 × 16k = 8000k data
JG, NIM A 2020
analysis / computing cost
×200 !!

## Slide 27
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
tracks analysis
“standard” analysis
signal amplitude + CFD timing
2D (X,Y) A & T
 2 × 16k = 32k data
deconvolution analysis
 response functions for each channel
full 3D (X,Y,T) signal distribution (from FFT)
 512 × 16k = 8000k data
JG, NIM A 2020
problem at large
vertical angles
incorrect
track
length

## Slide 28
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
tracks analysis
“standard” analysis
signal amplitude + CFD timing
2D (X,Y) A & T
 2 × 16k = 32k data
deconvolution analysis
 response functions for each channel
full 3D (X,Y,T) signal distribution (from FFT)
 512 × 16k = 8000k data
JG, NIM A 2020
problem at large
vertical angles

## Slide 29
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
tracks fitting
  • trajectory (geometrical) definition
  start and stop 3D points
  (+ additional control points for segments
  or Bézier curves)
   3 param. per point
  ○ 2D ampl. + time  2×16k pads (A+T)
  ○ full 3D rec. charge  512×16k voxels
  (deconvolution from R.F.)

## Slide 30
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
tracks fitting
  • trajectory (geometrical) definition
  start and stop 3D points
  (+ additional control points for segments
  or Bézier curves)
   3 param. per point
  • Bragg peak model (energy loss)
  projected along the trajectory
  amplitude factor () & length fraction ()
  ○ 2D ampl. + time  2×16k pads (A+T)
  ○ full 3D rec. charge  512×16k voxels
  (deconvolution from R.F.)
Geant4
simulation

## Slide 31
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
tracks fitting
  • trajectory (geometrical) definition
  start and stop 3D points
  (+ additional control points for segments
  or Bézier curves)
   3 param. per point
  • Bragg peak model (energy loss)
  projected along the trajectory
  amplitude factor () & length fraction ()
  • dispersion along drift
  ○ 2D ampl. + time  2×16k pads (A+T)
  ○ full 3D rec. charge  512×16k voxels
  (deconvolution from R.F.)
Geant4
simulation

## Slide 32
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
tracks fitting
  • trajectory (geometrical) definition
  start and stop 3D points
  (+ additional control points for segments
  or Bézier curves)
   3 param. per point
  • Bragg peak model (energy loss)
  projected along the trajectory
  amplitude factor () & length fraction ()
  • dispersion along drift
   fit signal function ,
  or
   comparison to experimental distributions
  from fit: track length (≡ energy), angles (x-p), charge deposit
  ○ 2D ampl. + time  2×16k pads (A+T)
  ○ full 3D rec. charge  512×16k voxels
  (deconvolution from R.F.)
Geant4
simulation

## Slide 33
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation for tracks fit dispersion
  many parameters in fits
  dispersion depends on detector conditions, not from events
  test fit of “point-like” energy deposit
  with
   fixed , variation of position
   fixed position, variation of
(constant)
Gauss 2D fit
track fit
wrong fit output for dispersion parameter !

## Slide 34
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation for tracks fit dispersion
  many parameters in fits
  dispersion depends on detector conditions, not from events
  test fit of “point-like” energy deposit
  with
   fixed , variation of position
   fixed position, variation of
(constant)
Gauss 2D fit
track fit
intrinsic dispersion from pad size
 matches simple 2D Gauss fit !!!

## Slide 35
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation for tracks fit dispersion
  many parameters in fits
  dispersion depends on detector conditions, not from events
  test fit of “point-like” energy deposit
  with
   fixed , variation of position
   fixed position, variation of
  •
OK down to
low dispersion
(close to pad plane)

## Slide 36
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation for tracks fit dispersion
  many parameters in fits
  dispersion depends on detector conditions, not from events
  test fit of “point-like” energy deposit
  with
   fixed , variation of position
   fixed position, variation of
  •
  • reduced threshold
  (cannot be changed in real data !!!)
  • analytical integral over pad signal
  instead of mean/center value
  (4× erf function instead of 1× Gauss
   20× slower fit…)
OK down to
low dispersion
(close to pad plane)
improved but
useless for real data

## Slide 37
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation for effect of recoil nucleus
  energy calibration (track length ↔ energy conversion) based on known (β-)proton transitions
  calibration curve from SRIM at optimal pressure
  recoil nucleus (ion):
  2-3 % of transition energy (1/A)
  very short range
  most likely quenching
  neutralization
  neglected
  Ok for β-p decays
  (same conditions)

## Slide 38
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation for effect of recoil nucleus
  energy calibration (track length ↔ energy conversion) based on known (β-)proton transitions
  calibration curve from SRIM at optimal pressure
  recoil nucleus (ion):
  2-3 % of transition energy (1/A)
  very short range
  most likely quenching
  neutralization
  neglected
  Ok for β-p decays
  (same conditions)
  problem for 2p decays
  measured Q-value lower than previous measurements
  p
  p
  rec
  p
  p
  rec
  momentum conservation
  different contribution of recoil with p-p angle

## Slide 39
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation for effect of recoil nucleus
  energy calibration (track length ↔ energy conversion) based on known (β-)proton transitions
  calibration curve from SRIM at optimal pressure
  recoil nucleus (ion):
  2-3 % of transition energy (1/A)
  very short range
  most likely quenching
  neutralization
  included in fits (param. Lrec and fQ)
  of simulated events
  (recoil from β neglected)
  recoil
  proton
  Lrec
  Qp
  dE/dx
  Qrec  fQ·(1/A)·Qp

## Slide 40
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation for effect of recoil nucleus
  energy calibration (track length ↔ energy conversion) based on known (β-)proton transitions
  calibration curve from SRIM at optimal pressure
  recoil nucleus (ion):
  2-3 % of transition energy (1/A)
  very short range
  most likely quenching
  neutralization
  included in fits (param. Lrec and fQ)
  of simulated events
  (recoil from β neglected)
  recoil
  proton
  Lrec
  Qp
  dE/dx
  Qrec  fQ·(1/A)·Qp
intrinsic length
dispersion from
simulation
(for information)
  35 % length difference
  (fit vs simul. length)

## Slide 41
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
simulation for effect of recoil nucleus
  energy calibration (track length ↔ energy conversion) based on known (β-)proton transitions
  calibration curve from SRIM at optimal pressure
  recoil nucleus (ion):
  2-3 % of transition energy (1/A)
  very short range
  most likely quenching
  neutralization
  included in fits (param. Lrec and fQ)
  of simulated events
  (recoil from β neglected)
  p
  p
  rec
  p
  p
  rec
  2P decay:
  Q-value from fitted length
  increased by 2%

## Slide 42
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
concluding remarks
 simulations needed for ACTAR TPC decay detection efficiency
custom empirical simulation (no need for microscopic description)
parametrization based on experimental data
dominated by systematic uncertainties
slight differences in E690 & E791 procedures
 simulations help tracks analysis and fits
identification of events topology (not discussed here)
control and correction of fit procedure
 corrected dispersion
 included recoil signal
 still some work to be done…
sorting of decay events types (for now “artisanal” way…)
improve fits (3D fits extremely slow)
control G4 results (problems…)

## Slide 43
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
concluding remarks
 simulations needed for ACTAR TPC decay detection efficiency
custom empirical simulation (no need for microscopic description)
parametrization based on experimental data
dominated by systematic uncertainties
slight differences in E690 & E791 procedures
 simulations help tracks analysis and fits
identification of events topology (not discussed here)
control and correction of fit procedure
 corrected dispersion
 included recoil signal
 still some work to be done…
sorting of decay events types (for now “artisanal” way…)
improve fits (3D fits extremely slow)
control G4 results (problems…)
thank you for your attention !

## Slide 44
J. Giovinazzo (LP2iB – CNRS IN2P2 / Univ. Bordeaux)
2025/03 réseau R&D détecteurs à gaz – simulations for ACTAR TPC decay experiments
problems
updated SimRange program for GSimTPC 6.0 (for rocky linux 8)
recomputed Bragg peak histograms (fit pattern) for alpha and protons
in Ar-C4H10 (90%-10%): 50000 events
• 10 MeV protons, P = 5 bar (file proton_10MeV_5bar.root)
• 10 MeV alpha, P = 1 bar (file alpha_20MeV_2bar.root)
???
average of energy deposit along “normalized” track path
20 MeV alpha average energy loss
in Argon-Isobutane (90-10%) gas (P = 2 bar)
G4 10.03.p01
centos 7, g++ 4.8.5
(50000 events)
G4 11.1.2
rocky8, g++ 8.5.0
(5000 events)