## Slide 1
Positron production for FCC-ee
Iryna Chaikovska
Laboratoire de Physique des 2 Infinis Irène Joliot-Curie (IJCLab)
CNRS, Université Paris-Saclay
on behalf of the FCC-ee Injector Study collaboration

## Slide 2: Future Circular Collider- electron positron (FCC-ee)
FCC-ee (Z, W, H, ) as Higgs factory, electroweak & top factory at highest luminosities.
*Most demanding mode for the positron source due to the high beam current requirement.
~90.7 km
2045 - 2065
parameters | Z* | WW | H (ZH) | 
beam energy [GeV] | 45.6 | 80 | 120 | 182.5
synchrotron radiation/beam [MW] | 50 | 50 | 50 | 50
beam current [mA] | 1294 | 135 | 26.8 | 5.1
number bunches / beam | 11200 | 1852 | 300 | 64
total RF voltage 400/800 MHz [GV] | 0.08 / 0 | 1.0 / 0 | 2.09 / 0 | 2.1 / 9.2
luminosity / IP [1034 cm-2s-1] | 145 | 20 | 7.5 | 1.4
total integrated luminosity / IP / year [ab-1 / yr] | 17 | 2.4 | 0.9 | 0.17
beam lifetime [min] | 21 | 13 | 9 | 10
parameters | Z* | WW | H (ZH) | 
beam energy [GeV] | 45.6 | 80 | 120 | 182.5
synchrotron radiation/beam [MW] | 50 | 50 | 50 | 50
beam current [mA] | 1294 | 135 | 26.8 | 5.1
number bunches / beam | 11200 | 1852 | 300 | 64
total RF voltage 400/800 MHz [GV] | 0.08 / 0 | 1.0 / 0 | 2.09 / 0 | 2.1 / 9.2
luminosity / IP [1034 cm-2s-1] | 145 | 20 | 7.5 | 1.4
total integrated luminosity / IP / year [ab-1 / yr] | 17 | 2.4 | 0.9 | 0.17
beam lifetime [min] | 21 | 13 | 9 | 10
4 interaction points.

## Slide 3: FCC-ee Injector Layout: Optimized Concept
Collider and booster parameters used as specifications for the injector design
4 bunches (25 ns), 100 Hz
FCC-ee injector with HE Linac on CERN Prévessin site
High-Energy Linac next to North Area and Beam Dump Facility
Courtesy T. Watson, W. Bartmann (CERN)

## Slide 4: Positron Sources Performances
Modified from Y. Enomoto (KEK)
High production positron 6D emittance → appropriate capture, focusing and post acceleration sections need to be integrated immediately after the target
Accepted e+ yield is a function of primary beam characteristics + target + capture system + DR acceptance

## Slide 5: FCC-ee Positron Source: Current Requirements
Ne-/bunch ⨯ ηe+Accepted ≥ 5 nC/bunch ⨯ 2.6
The complete filling for Z running → Requirement ∼ 3 ⨯ 1010 e+/bunch (4.8 nC) at the linac end
*A safety margin of 2.6 is currently applied for the whole studies (losses for injection in the DR + losses along the e+ pre-injector)
➜ positron flux of ∼1.2⨯1013 e+/s (⨯2.6). Demonstrated at SLC (a world record for existing accelerators): ∼ 6 ⨯1012 e+/s
or 5 nC accepted in the DR
Beam energy | 2.86 GeV
Bunch charge | ∼5 nC (max)
Bunch length | 1 mm
Bunch transverse size | ≳ 0.5 mm
Nb of bunches per pulse | 4
Bunch separation | 25 ns
Repetition rate | 100 Hz
Beam power | ∼5.7 kW (max)
e- drive beam
~ 13 nC
with Ne-~5 nC (max) ➔ ηe+ ≳ 2.6 Ne+/Ne-

## Slide 6: Positron Production @FCC-ee: Design Choices
PL1
PL2
MS
TL + ESC to DR
2.86 GeV
CL
CH
DR
T
MD
Transfer Line + Energy Compression System + Damping Ring
Large acceptance/short damping time DR
Design studies in progress
15 mm-thick W target-converter
Matching Device (MD) → a fast phase space rotation to transform the small size/high divergence in big sizes/low divergence beam
2.86 GeV
MD: HTS solenoid
Capture Linac and Positron Linac
2 GHz RF structures
(2a = 60 mm)
L-band large-aperture acc. structures
NC solenoid channel
Bz = 0.5 T
FODO lattice

## Slide 7: Validation of the FCC-ee Positron Source Design Framework
F. Alharthi et. al.,"Modeling of the positron sources: an experiment-based benchmarking", Phys. Rev. Accel. Beams (Sept. 2025)
e- beam energy | 2.9 GeV
Rep. rate | 25 Hz
Number of bunches | 2
Bunch charge | ∼10 nC
Beam size | ~0.5 mm
e+ yield after chicane | 0.6 Ne+/Ne-
e- beam position scan on the target
Magnetic field scan in the capture system
Positron capture system
Start-to-end model: Geant4 + RF-Track
Benchmarked against other tools (EGS5+GPT, Geant4+ASTRA)
Validated with SuperKEKB experimental data. Excellent agreement: meas. yield (0.603 ± 0.003) vs. simulated 0.603.
→ Framework ready for FCC-ee design optimization
Positron source

## Slide 8: Positron Production: Capture System
Target & cryostat
Positron/Electron
Separation at 170 MeV
Energy collimator
and compressor
2.86 GeV electron beam
from e- linac
Injection section
Damping Ring
E = 2.86 GeV
Qb = 5 nC
E = 2.86 GeV
Q = 13 nC (considering 60% losses for transport, collimation and injection into DR)
E = 2.86 GeV
Q = ~3.8 nC
Capture linac 2 GHz, 13.3 MV/m
100 Hz, 6 RF structures
DC solenoid
DC solenoid
Electron/Photon dumps
346 mm
105 mm
72 mm
240 mm
509.5 mm
3000 mm
200 mm
Capture system (~ 20 meters)
Positron production : conventional scheme (e- beam size on target = 1 mm rms ). Target exit located at 40 mm w.r.t. HTS solenoid peak field.
Matching device is based on the SC solenoid (5 HTS coils, 72 mm bore,  60 mm including shielding)
Capture linac is based on the 6 L-band TW RF structures ( 2 GHz,  60 mm, 3-m long)
NC solenoid B = 0.5 T (realistic conventional design based on the short coils B = 0.31 T) + short “tuning” solenoid B = 0.25 T before the 1st RF structure
Positron linac 2 GHz, 13.3 (12.8) MV/m
100 Hz, 20+52 RF structures
Dedicated FLUKA model is developed for the target and e+ capture section
→ no showstoppers regarding thermal load or radiation damage

## Slide 9: Positron Production: Capture System
Capture section is based on the conventional NC solenoid technology.
The first RF structure operates in deacceleration phase improving bunching and longitudinal phase space.
~ 33% e+ losses occur between the AMD and the first RF structure and ~ 9% additional losses at the chicane.
PL1
PL2
MS
TL + ECS to DR
2.86 GeV
CL
CH
DR
T
MD

## Slide 10: Positron Production: Positron Linac
Target & cryostat
Positron linac 2 GHz, 13.3 (12.8) MV/m
100 Hz, 20+52 RF structures
Positron/Electron
Separation at 170 MeV
Energy collimator
and compressor
2.86 GeV electron beam
from e- linac
Injection section
E = 2.86 GeV
Q = 13 nC (considering 60% losses for transport, collimation and injection into DR)
E = 2.86 GeV
Q = ~3.8 nC
DC solenoid
DC solenoid
Electron/Photon dumps
Separator chicane : Rectangular beampipe and hor./vert. collimators, Dipole peak field: ~0.2 T
Section 1 : up to ~ 930 MeV. Same RF structure as that of the Capture Linac (CL). 20 structures. G = 13.3 MV/m
Matching section : 5 quadrupoles (0.4 m long)
Section 2 : up to 2.86 GeV. Same RF structure as that of the CL. 52 structures. Quadrupole (0.4 m long), 2 structures per FODO cell. G = 12.8 MV/m
Positron linac (~ 280 meters)
Capture Chicane Positron linac - Section 1 Matching section Positron linac - Section 2
section
400 mm
400 mm
3000 mm
200 mm
Capture linac 2 GHz, 13.3 MV/m
100 Hz, 6 RF structures
Damping Ring
E = 2.86 GeV
Qb = 5 nC

## Slide 11: Positron Capture and Linac Overall Efficiency
*Simulations include collective effects
(space charge and short-range wakefield)
e+ yield ~ 3.4 (≳ 2.6)
Accepted yield @ DR ~ 3.0
(ΔE: 2%, Δt: 20 mm/c)
Start-to-end simulation (from target to the DR)
The impact of these imperfections is found to be negligible: e+ yield ↓1.3%, emittance x/y ↓0.4/0.8 %
Design ensures reliable e+ production and meets the requirements set by FCC-ee (Z-pole) with the safety margins
PL1
PL2
MS
TL + ECS to DR
2.86 GeV
CL
CH
DR
T
MD

## Slide 12: Summary of the Simulation Results
Thickness [mm] | 15
Production rate [Ne+/Ne-] | 7.07
Deposited power [kW] | 1
PEDD [J/g] | 5.8
Beam energy [GeV] | 2.86
Repetition rate [Hz] | 100
Number of bunches | 4
Bunch charge [nC] | 3.8
Bunch length [mm] | 1
Beam size @Target [mm] | 1
Beam power [kW] | 4.3
AMD peak field [T] | 15 (12)
Solenoid strength [T] | 0.5
AMD/CS aperture [mm] | 60
Average energy [MeV] | 173
Positron yield [Ne+/Ne-] | 4.2
Average energy [GeV] | 2.87
Positron yield [Ne+/Ne-] | 3.4
Accepted positron yield @DR [Ne+/Ne-] | 3
Bunch length [mm] | 16 (2.8)
Energy spread [%] | 5 (0.9)
Spots size [mm] | 5.3/2.8
Normalized emittance [mm∙rad] | ~13
e- Drive beam
Target-converter
e+ Capture system
e+ Linac

## Slide 13: Crystal-Based Positron Source for FCC-ee
→ typical angular range ∼a few mrad at 6 GeV for <111> axis in W
oriented crystalline target
Use of lattice coherent effects in oriented crystals: channeling and over barrier motion
Novel production scheme for positron sources
Enhancement of photon generation in oriented crystals → enhancement of pair production / positron charge
Lower energy deposit and PEDD in target → lower heating and thermo-mechanical stress (target reliability)
Originally proposed by R. Chehab, A. Variola, V. Strakhovenko and X. Artru
R. Chehab et al., in Proc. of the 1989 IEEE Particle Accelerator Conf., 1989, pp. 283–285
Several options were considered for FCC-ee
Several experiments: Orsay, WA103@CERN and KEK (in the 1 – 10 GeV region)
2.86 GeV e- beam on
1 mm-thick W target

## Slide 14: Crystal-Based Positron Source for FCC-ee (towards conceptual design)
Simulation studies converge to a total W thickness of about 10 - 12 mm
→ need D∼0 (2 targets) or 1 thick single-crystal
The whole setup was simulated through Geant4 toolkit taking advantage of GeantG4ChannelingFastSimModel, which is based on CRYSTALRAD code
The simulation environment was benchmarked/validated with experiments at energies of interest for positron sources of future colliders → optimization studies for the FCC-ee
L. Bandiera et al., Eur. Phys. J. C (2022) 82:699
A. Sytov et al. JKPS 83 (2023)

## Slide 15: Integration and Operation of the Crystal Target
Crystal heating The photon yield remains stable up to ∼500 ⁰K
Crystal alignment No goniometer. The typical precision of the pre-alignment procedure ∼1 mrad Margins for improvement.
Crystal quality The crystalline quality of 10 – 12 mm thick W sample is lower than for a thin sample → lower yield, but larger acceptance angles
At local level: mosaicity is contained within 0.2 – 0.4 mrad
At larger scale: separate crystal domains (on 10x10x10 mm3, total angular distribution of all the crystals domains is within 8.7 mrad)
Experimental studies and validation are needed !
(tests @MAMI, DESY, CERN, potential target design validation at P3)
Misalignment w.r.t. desired axis <111> of 12 mm-thick W crystal @500 ⁰K
Imaging of the sample mosaicity measured at BM05 beamline
of ESRF for 10 mm thick W
Beam test at the DESY TB 21 with 5.6 GeV
Spectra of Eloss at various angular configurations
Courtesy of Thu Nhi Tran Caliste (INFN)
2.25 mm thick W crystal

## Slide 16: PSI Positron Production experiment: P3 or P-cubed
N. Vallis et al., Phys. Rev. Accel. Beams 27, 013401 – 2024
Key Technology: High-Temperature Superconducting (HTS) solenoid to deliver high field near the target exit.
P3 Layout
HTS solenoid integrated in the cryostat (M. Duda et al.)
Peak magnetic field: 12 T (tested up to 18 T)
Demonstrator for positron production and capture using the 6 GeV linac of the SwissFEL facility at PSI will be realized to validate the proposed concept for the FCC-ee positron source
The installation works at SwissFEL are progressing smoothly
Based on the current progress, the major part of the installation work is expected to conclude by the end of 2025, making it possible to start the operation in 2026

## Slide 17: Towards the TDR
The current design assumes L-band 2 GHz RF frequency → limited availability of the power sources
Strong recommendation: investigate the feasibility of adopting “commercial” S-band frequency for the positron capture and linac.
Choice of RF frequency 3.006 GHz (e+ linac) and 2 GHz and 1.504 GHz (capture linac). Further investigations on NC vs. SC solenoid focusing, solenoid vs. quadrupole focusing for positron linac, e- driver parameters ☞ impact on overall performance, layout, cost and power consumption.
Start-to-end simulations and optimizations including the TL, Energy Compressor and tracking in the Damping Ring
Detailed misalignment/error studies and tolerances. Hardware specs. Diagnostics.
Longitudinal phase-space after the ECS and TL
(preliminary, work in progress)

## Slide 18: Summary and outlook
FS baseline design relies on the HTS solenoid. The e+ yield is ~3.4 Ne+/Ne- in the end of linac. Simulations with ECS+TL+DR in progress. Proof-of-principle with P3 experiment @PSI starting from 2026. Next: TDR phase.
The very first studies to investigate the feasibility of 3 GHz RF frequency in the e+ capture and 2.86 GeV linac started. Final choice of RF frequency: simulated performance, injector integration and overall cost.
Conceptual design studies of the crystal-based positron source for the FCC-ee are well advanced and ongoing. Next steps: integration studies and beam tests with potential proof-of-principle at P3 experiment 2nd phase.
Feasibility Study Report published on 31 March 2025
Vol. 2: Accelerators, Technical Infrastructures, Safety Concepts
submitted for publication to EPJ (Springer-Nature)

## Slide 19: Credits
PSI | B. Auchmann, I. M. Besana, S. Bettoni, P. Craievich, M. Duda, R. Fortunati, H. Garcia-Rodrigues, D. Hauenstein, R. Ischebeck, P. Juranic, J. Kosse, F. Marcellini, U. Michlmayr, G. L. Orlandi, M. Pedrozzi, J.-Y. Raguin, S. Reiche, R. Rotundo, S. Sanfilippo, M. Schär, N. Strohmaier, N. Vallis, M. Zykova, R. Zennaro, H.H. Braun, M. Seidel all the technical groups involved in the P3 experiment
IJCLab | F. Alharthi, I. Chaikovska, R. Chehab, V. Mytrochenko, Y. Wang
CERN | W. Bartmann, H. Bartosik, M. Calviani, S. Doebert, Y. Duthell, J. L. Grenard, A. Grudiev, B. Humann, A. Kurtulus, A. Latina, A. Lechner, R. Mena Andrade, A. Perillo Marcone, K. Oide, Y. Zhao, F. Zimmermann, Z. Vostrel, M. Benedikt
SLAC | T. Raubenheimer
KEK | Y. Enomoto, K. Furukawa, F. Miyahara
INFN-LNF | C. Milardi, A. De Santis, O. Etisken, S. Spampinati
and L. Bandiera, N. Canale, A. Mazzolari, G. Paternò, M. Romagnoni, A. Sytov (INFN/Ferrara), A. Bacci, M. Rossetti Conti (INFN/Milano) | A. Bacci, M. Rossetti Conti, L. Bandiera, D. Boccanfuso (INFN Naple) , N. Canale, O. Lorio (INFN Naple), A. Mazzolari, R. Negrello, G. Paternò, M. Romagnoni, M. Soldani, A. Sytov
FCCIS: 'This project has received funding from the European Union's Horizon 2020 research and innovation programme under the European Union's Horizon 2020 research and innovation programme under grant agreement No 951754.'
This work was done under the auspices of CHART (Swiss Accelerator Research and Technology) Collaboration, https://chart.ch - CHART Scientific Report 2022: https://chart.ch/reports/