## Slide 1: Longitudinal beam dynamics considerations of the FCC-ee high energy booster
Lina Valle*, Ivan Karpov, Rama Calaga, Heiko Damerau and Wolfgang Hofle
Acknowledgements: Birk Karlsen-Bæck, Antoine Chance, Karin Canderan, Elleanor Lamb,, Mariangela Marchi and all FCC-ee colleagues
Journées Accélérateurs, 7-10 octobre 2025, Roscoff, France
*lina.valle@cern.ch

## Slide 2: Outline
Introduction
Summary and next steps
Booster cycles: energy ramps for all physics modes
Power transients at injection: mode

## Slide 3: Future Circular Collider project overview
90,7km tunnel to host FCC-ee
then FCC-hh
Stage 1: FCC-ee as a Higgs factory
  Four operation energies (per beam):
  at 45.6 GeV,
  at 80 GeV,
  at 115 GeV,
  at 180 GeV
Stage 2: FCC-hh (~100 TeV)
Physics of FCC: https://cds.cern.ch/record/2928193/files/2505.00272.pdf
Michael Benedikt, FCC week 2025, Vienna, Austria

## Slide 4: RF requirements for the FCC-ee booster
The RF section of the booster, located in Point L, will be installed in two stages, with additional cavities installed for operation.
Therefore, the first 112 cavities need to provide a wide range of voltage (from 50 MV to 2 GV), while minimizing RF power requirements and a minimal voltage per cavity of 2 MV.*
Booster 800 MHz cavities
, , : 112 at 2K in 28 cryomodules (CM)* (4 cavities per CM)
,
: 448 at 2K in 112 cryo-modules (4 cavities per CM)
*S. Gorgi Zadeh, 800MHz cavity design update, FCC WP1, January 2025
Reverse Phase Operation** (or counter-phase***)
Increased voltage per cavity,
Optimal static beam loading compensation,
Homogenized voltage range through all ramps
** Y. Morita et al., SRF, 2009
Experimentally verified in Y. Morita, IPAC, 2010
*** Similar concept used at CERN SPS since the 70s.
I. Karpov, FCC_Week_2025_IK.pdf

## Slide 5: Booster cycles
Energy ramps for all physics modes

## Slide 6: Booster cycles selected parameters
Continuous operation of the booster in parallel to the collider, following three different modes:
Filling mode: to fill the collider from scratch, with maximum bunch intensity.
Top-up mode: top-up the collider bunches with a personalized charge.
Polarized bunches (Z): for precise energy measurement and pilot bunches.
Extraction energy will be varied in the coming weeks, depending on the collider optics and injection scheme.
 | Z | WW | ZH | ttbar
Characteristics of the ramp |  |  |  | 
Injection energy [GeV] | 20 |  |  | 
Collider energy [GeV] | 45.2 | 80 | 120 | 182.5
Energy deviation at injection | (TBD) |  |  | 
Accumulation time [s] | 2.8 | 2.32 | 3.0 | 0.64
Total ramping time [s] | 1.0 (1.14) | 1.6 | 2.6 | 4.3
Cycle length [s] | 3.8 | 5.5 | 10 | 10
Bunches per cycle | 1120 | 928 | 300 | 64
Particles per bunch | 2.725e10 | 1.268e10 | 1.268e10 | 1.268e10
 | Z | WW | ZH | ttbar
Characteristics of the ramp |  |  |  | 
Injection energy [GeV] | 20 |  |  | 
Collider energy [GeV] | 45.2 | 80 | 120 | 182.5
Energy deviation at injection |  |  |  | 
Accumulation time [s] | 2.8 | 2.32 | 3.0 | 0.64
Total ramping time [s] | 1.0 (1.14) | 1.6 | 2.6 | 4.3
Cycle length [s] | 3.8 | 5.5 | 10 | 10
Bunches per cycle | 1120 | 928 | 300 | 64
Particles per bunch | 2.725e10 | 1.268e10 | 1.268e10 | 1.268e10
Booster physics mode selected parameters
Changes from FCC week 2025
→ Increased cycle duration for , and in filling mode
→ The voltage program will be adjusted to match a variable extraction energy () and the extraction bunch length

## Slide 7: Booster energy ramp analytical computation
Example of 𝑡𝑡 ̅
Motivation: Optimization the energy and voltage ramps for all four physics modes, all operation modes, including RPO program, homogenize dynamic losses and reduce RF power requirements.
Analytical tools to compute the energy and voltage ramps of the high-energy booster (code on GitLab)
Faster optimization including dynamic effects (power transients, beam loading)
For now, energy ramps for a single bunch, no intensity effects.

## Slide 8: Booster ramping strategies for Z mode
Transverse emittances requirements at extraction energy (45.6 GeV)*:
nm.rad × pm.rad and
Acceleration during 0.7 s (total cycle 1/1.14 s) for large damping times.
A boost of synchrotron radiation is required to reach the target beam sizes at extraction.
* Specified by Y. Dutheil, FCCee injectors parameters - Google Sheets and presented in 3rd Meeting of the FCC-ee Layout and Optics Design (30 avril 2025) · Indico
** L.Valle, FCC_WP1_25_03_2025.pdf
Damping times | 20 GeV | 45.6 GeV
 | 9.05 | 0.74
 | 4.52 | 0.37
Damping times | 20 GeV | 45.6 GeV
 | 9.05 | 0.74
 | 4.52 | 0.37
Horizontal emittance remains above requirements.
Maximum energy gain: 100 GeV/s
Optimized overshoot energy ramp with Particle Swarm Optimization (PSO)**
for lower transverse emittances at extraction

## Slide 9: Booster ramping strategies for Z mode
Adding damping wigglers…
Already considered for stability considerations at injection*.
First approach: wigglers of constant magnetic field (1 T), 4.925 m long, 43 95 mm-long poles, gap of 20mm (collider specifications)
Natural energy spread at 45.6 GeV blows up from to () or ()
* S. Gorgi Zadeh, FM passband **L.Valle, FCC_WP1_25_03_2025.pdf
Maximum energy gain: 100 GeV/s
Optimized overshoot energy ramp with Particle Swarm Optimization (PSO)**
including two damping wigglers

## Slide 10: Booster ramping strategies for Z mode
Adding damping wigglers…
Already considered for stability considerations at injection*.
First approach: wigglers of constant magnetic field (1 T), 4.925 m long, 43 95 mm-long poles, gap of 20mm (collider specifications)
Natural energy spread at 45.6 GeV blows up from to () or ()
Maximum energy gain: 100 GeV/s
Idea: Switch the wigglers off during the ramp to restore the expected natural energy spread or move the beam away from the wiggler.
Acceleration and deceleration in 1.14 s
Optimized overshoot energy ramp with Particle Swarm Optimization (PSO)**
including two damping wigglers disabled during the ramp
Getting closer to the target parameters. Wiggler parameters to be optimized.
* S. Gorgi Zadeh, FM passband **L.Valle, FCC_WP1_25_03_2025.pdf

## Slide 11: Voltage per cavity program including Reverse Phase Operation
Optimized overshoot, no damping wigglers
Reverse Phase Operation voltage per cavity (identical for all cavities) and phase verify:
Conservation of the energy gain
Conservation of the synchrotron tune
A. Blednykh et al, https://www.osti.gov/servlets/purl/1888292
Phase reset
Reverse Phase Operation
Accumulation and acceleration
ramp
Number of focusing cavities
Synchronous phase
Total voltage
Voltage per cavity
Defocusing cavity phase

## Slide 12: Dynamic power losses in the high-energy booster
Dynamic power loss is the power dissipated in the RF cavity from its own resistivity. For a superconducting RF cavity, the dynamic power loss is expressed as:
With the voltage per cavity, the unloaded Q-factor and a geometry-dependent factor.
Arbitrary start of the accelerating ramp for , and
Dynamic power loss during different booster cycles
→ Lower than the static heat loads in all modes
(#350 – 500W) *
* K. Canderan, FCCweek2025_SRF_CM_Design_Evolution.pdf
Duty factor for all physics modes | Z | WW | ZH | ttbar
Peak [W] | 2.21 | 9.30 | 16.2 | 25.7
Average [W] | 0.676 | 1.29 | 1.42 | 2.02
Integrated power [W.s] | 2.66 | 10.1 | 14.2 | 20.2
Duty factor (average/peak) | 0.31 | 0.14 | 0.088 | 0.079

## Slide 13: Power transients at injection z mode
Overshoot energy ramp, no damping wigglers.
Results are subjected to large variations depending on the energy ramp strategy and use of damping wigglers throughout the booster cycle.

## Slide 14: RF power requirements in the booster with optimal detuning
The power required by the RF cavities can be minimized with the choice of the loaded Q factor and a detuning program Δ𝜔.
In the case of FCC-ee, the cavities are fixed, and identical for 𝑍, 𝑊𝑊 and 𝑍𝐻 modes.
Minimization can therefore only be conducted with detuning of the cavities.
Clamp at 50kW per cavity
(overshot to be verified dynamically)
Overshoot energy ramp, no wigglers
DC beam current
Form factor

## Slide 15: RF power transients at injection using BLonD
To complete previous calculations* with tracking tools, RF power requirements are simulated using the code BLonD**.
Adapted LHC Cavity Loop class in BLonD**
Sampling time: 25 ns (every 20 booster buckets)
Fixed beam in the longitudinal phase space
First four equal bunches injected at , equally spaced by 25 ns
Two RF cavities: focusing and defocusing, located at the same place, with their own feedback loop.
LHC Cavity Feedback loop diagram as implemented in BLonD**
*I. Karpov, FCC_optics_meeting_27022025_IK.pdf
** BLonD, Beam Longitudinal Dynamics simulator, https://blond.web.cern.ch/
*** B.E. Karlsen-Bæck, H. Timko, 2024 JINST 19 T04005

## Slide 16: Injecting the four first bunches – Z mode
Injection of the first four bunches from the linac:
2.725e10 particles per bunch,
25 ns bunch spacing,
No intensity nor injection errors,
Fixed beam in the longitudinal phase space in a first approach,
Consistent with expected stabilised value (total 48kW for the first injection)
Averaged at 70kW including transients
RF power transients per cavity at injection in the booster (Z mode, 20 GeV)
Accelerating ramps and voltage programs from FCC_week_2025_valle.pdf

## Slide 17: Summary and next steps
Summary
Codes available on GitLab (develop branch)
Energy ramp designing and optimizing functions for all target physics modes
LHC Cavity feedback loop being adapted to the FCC-ee booster for RF power transient calculation
Power transients studied during the first turns after injection in the booster, for Z mode bunches
Next steps
Ongoing optimization of the energy ramps (esp. Z):
  Damping wigglers requirements to meet the extraction targets to be determined,
  Bunch rotation at flat top to transfer energy spread into bunch length,
Study of booster availability
  Trips of RF cavity, redundancy, recovery procedures, …
Full injection scheme (multi-turn injection) in BLonD(3?) in filling and top-up mode:
  Booster filling scheme,
  Injection mismatches, inhomogeneous bunches,
  Coupled-bunch instabilities to be assessed (P. Hickersberger)
BLonD 3 source code at: https://gitlab.cern.ch/blond/BLonD/-/tree/blonder?ref_type=heads

## Slide 18: Accelerator Early Career Researchers (AccelECRs)
An accelerator science and technology ECR community is in the pipelines. Our goals:
Build a Europe-wide network of early-career researchers (ECRs) in accelerator science and technology,
Support ECRs with their professional and personal development, career and research opportunities,
Organize topical workshops locally and globally to maximize knowledge sharing and interactions of the community
Get involved in building this community!
How to join:
Simply subscribe to the ‘accelerator-ecr’ e-group mailing list here:
https://e-groups.cern.ch/e-groups/EgroupsSubscription.do?egroupName=accelerator-ecr
For now: CERN-based, we are looking to build antennas in different European labs 

## Slide 19: Thank you for your attention

## Slide 20: Introduction - appendices

## Slide 21: RF operation requirements for FCC-ee and its high-energy booster
Compensation of SR losses require many RF cavities
Booster
Collider
800MHz cavities
, , : 112 at 2K in 28 cryomodules* (4 cavities per CM)
,
: 448 at 2K in 112 cryo-modules (4 cavities per CM)
800MHz cavities
: + 408 at 2K in 102 cryo-modules
400MHz cavities
, , : 132 at 2K in 66 cryomodules
* K. Canderan, FCCweek2025_SRF_CM_Design_Evolution.pdf
** See Ivan’s talks (e.g. FCC_Week_2025_IK.pdf)
400 MHz 2-cell cavity
800 MHz 6-cell cavity
S. Gorgi Zadeh, Accelerating cavities with HOM damping for FCC-ee.pdf
Main challenge: SYNCHROTRON RADIATION LOSSES up to 10 GeV energy loss per turn.
400MHz CM
800MHz CM

## Slide 22: RF operation requirements for FCC-ee and its high-energy booster
Compensation of SR losses require many RF cavities
Booster
Collider
800MHz cavities
, , : 112 at 2K in 28 cryomodules* (4 cavities per CM)
,
: 448 at 2K in 112 cryo-modules (4 cavities per CM)
800MHz cavities
: + 408 at 2K in 102 cryo-modules
400MHz cavities
, , : 112 at 2K in 66 cryomodules
* K. Canderan, FCCweek2025_SRF_CM_Design_Evolution.pdf
** See Ivan’s talks (e.g. FCC_Week_2025_IK.pdf)
Main challenge: SYNCHROTRON RADIATION LOSSES up to 10 GeV energy loss per turn.
I. Syratchev, FCC_Week_2025_Syratchev.pdf

## Slide 23: Injection chain into the FCC-ee

## Slide 24: Synchrotron radiation in Beam LONgitudinal Dynamics (BLonD)
BLonD* is a CERN simulation suite for longitudinal particle tracking in synchrotrons.
Its latest version includes:
Synchrotron radiation damping and quantum excitation (using synchrotron radiation integrals),
FCCee booster feedback loops adapted from the LHC cavity loops
*BLonD website: https://blond.web.cern.ch/
BLonD 3 source code at: https://gitlab.cern.ch/blond/BLonD/-/tree/blonder?ref_type=heads
BLonD3 is a restructuration of BLonD and is under development, and will be adapted to future accelerators (FCCee, muon colliders especially.)
Developer and beginner friendly,
High test coverage and numerous examples (training in preparation),
XSuite wrappers for lattice import,
No backward compatibility with BLonD.

## Slide 25: Energy ramps - appendices

## Slide 26: Injection error in the booster: Z ramp
Acceleration of an early-injected bunch
Maximum jitter implemented in the BLonD simulation of the acceleration:
  50ps time jitter
  relative energy error
Slight oscillations remaining at extraction, almost fully damped with the wigglers.
disabled at t = 0.4s

## Slide 27: Z mode overshoot
Overshoot energy ramp could meet the requirements on the extraction transverse emittance…
with at least 850 GeV/s energy gain in less than 0.05s!

## Slide 28: Z voltage per cavity for RPO and RF power
Optimized overshoot, no wigglers
Clamp at 50kW per cavity
(overshot to be verified dynamically)

## Slide 29: Z voltage per cavity for RPO and RF power
Optimized overshoot, two wigglers

## Slide 30: WW voltage per cavity for RPO and RF power
4.5% RF power overshoot at flat top
RPO
Phase reset

## Slide 31: ZH voltage per cavity for RPO and RF power
5% RF power overshoot at flat top
Constant voltage
RPO
Phase reset

## Slide 32: voltage per cavity for RPO and RF power
43% RF power overshoot at flat top
Constant voltage
RPO
Phase reset

## Slide 33: Power transients- appendices

## Slide 34: RF power transients at injection using BLonD
Adapted LHC Cavity Loop class in BLonD
Sampling time: 25ns
Fixed beam in the longitudinal phase space
Parameters of the FCCee feedback system | 
Time delays | 
Loop delay | 700 ns
Analog feedback delay | 28,3 us
Digital feedback delay | 66,7 us
Gains | 
Maximum stable analog gain | 
Fraction of maximum gain | 5
Analog gain | = 90e-9
Digital gain (eff. ) | 10
Other parameters | 
Pre-detuning | 0 Hz
Sampling time | 25 ns
Pretracking turn number | 50
Phase offset between analog and digital | - 6,7 degrees (foc.)
 | + 6,7 degrees (defoc.)
Parameters of the FCCee feedback system | 
Time delays | 
 | 700 ns
 | 28,3 us
 | 66,7 us
Gains | 
 | 5
 | 10
Other parameters | 
 | 0 Hz
Sampling time | 25 ns
Pretracking turn number | 50
Phase offset between analog and digital | - 6,7 degrees (foc.)
 | + 6,7 degrees (defoc.)