## Slide 1: Polarimetrie compton
TAMAZIRT juba (IJCLab Orsay)

## Slide 2: Polarimétrie pour FCC-ee
Energie du centre de mass au pole du Z0
soit 45.6 Gev par faisceau
Première phase : sonder le secteur électrofaible
avec des processus couplant les bosons
de jauge au Higgs avec une précision sur les
paramètres électrofaibles <1ppm
Calibration de l'énergie au centre de masse en
temps réel en utilisant la dépolarisation
résonnante: incertitude < Mev sur l'énergie
Dépolarisation résonnante :
B
n
S
tune of closed orbit:
k = aɣ + Qymy +Qxmx + QLmL
spin tune transverse Longitudinal
planes plane
(synchrotron)
La polarisation des électrons précesse
Grace au champ magnétique oscillant de
l’anneau de stockage.
Quand la fréquence de précession des
électron et des spins sont en résonnance
induit une Dépolarisation du faisceau

## Slide 3: polarimètre Compton
Blondel et al., arXiv:1909.12245; Muchnoi, INST 17 P10014 (2022)
photons diffusés
Faisceau d’éléctrons
electrons diffuses avec la plus
basse énérgie
Dipole (field B)
Laser ()
Région d’interaction
Nouveau concept (N. Yu Muchnoi) pour mesurer tous les parametres de polarisation  polarimetre 3D
environ 100m
x
X0
X1
X2
Calibration de l’énergie au centre de masse à l’aide de la dépolarisation résonante Monitoring de
l’énergie du faisceau à partir de la géométrie dans le plan de mesure → utile lorsque les paquets pilotes ne peuvent pas être polarisés ?

## Slide 4: Section efficace differentielle
Muchnoi, INST 17 P10014 (2022)
Outre la conception et la validation réalistes du détecteur et du système, une extraction précise des paramètres est nécessaire
, et sont des fonctions de ()
est negligeable
: parametres de polarisation du faisceau d’e-
parametres de stokes
NB: polarisation circulaire gauche/droite
Les électrons sont situés sur une surface ellipsoïdale dont la paramétrisation peut être transformée en un disque unité, sur lequel l’expression de la section efficace différentielle est plus commode
Example electron distribution
NB: devient >> aux limites du cercle

## Slide 5: Resultat– fit des Distributions
Obtenu en 30s pour un seul bunch
Blondel et al., arXiv:1909.12245; Muchnoi, INST 17 P10014 (2022)
En plus de la DPR l’energie est aussi extraite de ce fit
Tous les parametres sont extrait avec une precision de ~0.001 en quelques seconds

## Slide 6: Conclusion
Dépolarisation résonnante permet la calibration en temps réel de l’énergie du faisceau
Le polarimètre sera basé sur l’interaction Compton qui dépend de tous les paramètres
de polarisation
Il sera possible d’aussi bien de mesurer directement l'énergie, que de l’extraire grâce
à la dépolarisation résonnante par les mesures d’asymérie (Voir Poster)

## Slide 7: Merci pour votre attention

## Slide 8: backup

## Slide 9: Intégration du détecteur
[GeV]
La position des électrons de haute énergie est
Superposé avec celle du faisceau
Limite sur l’intégration du détecteur
Etude de l’impacte sur l’extraction
15mm
60mm
40mm
beam pipe
x2
x
30mm
50mm
X0
Y
Etude au pole Z0
Toy: 100 expériences de 1min de
prise de donnés
[mm]
[mm]
Moyenne et deviation standard de la valeur fitée
Uncertitde statistique sur la valeur fitée
Moyenne sur les incertitudes
L’extraction des paramètres de polarisation ne sont pas affecté
Augmentation de l’incertitude sur la mesure de l'énergie du faisceau (x2.5 de 15 to 60mm)
On choisie 40mm comme référence
See Poster at FCC Physics Week, Jan. 2025
Updated

## Slide 10: Simulations avec une géométrie réaliste
pixellisation:
nX=21020 pixels en l’horizontale
nY=320 pixels en verticale
18µm
18µm
pixel
Dead zones
Conception déjà disponible pouvant répondre aux besoins → ALICE MOSS prototype sensor NB : il ne s’agit que d’une des possibilités, à titre d’illustration
arXiv:2502.13591
Simulation prend en compte les « dead columns », et un rebinnig en X et en Y
Taille faisceau effective de 500 um sur le détecteur dans la direction horizontale
Fusionner les pixels en largeur afin d’économiser du temps de calcul sans perte significative
de précision

## Slide 11: Table des paramètres
Input parameter | Value
Dx (dispersion horisontale) | 28.6572 mm
Dy (dispersion verticale) | 0.0000 mm
Dpx (dispersion horizontale angulair ) | -0.0021
Dpy (dispersion horizontale angulair ) | 0.0000
εx (emmitance en x) | 0.0007 mm*rad
εy (emmitance en y) | 19*10-7 mm*rad
βx (fonction beta en x) | 392.6665 m
βy (onction beta en y) | 62.06445 m
Αx (fonction alpha en x) | 2.3819
Αy (fonction alpha en y) | -3.1232
𝛥 ( Energie spread) | 10- 3
θo (angle de courbure) | 0.0021 rad

## Slide 12: Further simplification
sign correspond to two energy solutions possible to reach a given position on detector
Observation is averaged over this un-observed quantity
Detailed analysis shows that further simplification is possible exploiting the structure of the , and functions and averaging over the two solutions
Improved
B=
A=
= is the maximum bend
With
The terms in green are neglected in the simmulation !!
Small terms but kept in the simulation

## Slide 13: Simulation implementation
320 pixels (16)
dead zone 34 pixels (2)
Rebinning on x axis by 16
Rebinning on y axis by 3
1320 nXpix with
60 dead zones
warning! 5 rows of dead pixels instead of 2 for better visualisation
dead zone 34 pixels (2)
320 pixels (16)
80 nYpix (3)
Typical simulation output
Rebinning applied at fit level to save simulation time
Configurable as option before fit
Example for 16, : pixels of 288x18 µm2
NB: initial simulations were 250x38 µm2
New baseline scenario

## Slide 14: Phase space correlations
Beam phase space correlation not implemented initially in Nickolai’s software
Improved
Electron sampling according to the electron beam size
Example result
, and are random numbers
and are Courant-Snyder parameters
and are dispersion functions
See Charlet et al. JINST 18 (2023) P10014 for instance

## Slide 15: Luminosity and crossing-angle
Simulation was using a fixed number of events instead a computation of expected number of scatters from luminosity and total cross-section
Simulation now also includes accounting of crossing angle  significantly modifies some approximations used in initial software, as photon energy in e- rest frame
Extraction of beam energy from horizontal photon and electron spots position gets modified too:
Now also update saving of fit results to analyse fit correlation
initial electron energy; intial photon energy; orentz factor
Laser-electron beam crossing angle
bending angle
Correction to account for scattered electrons at high energy
Improved

## Slide 16: Some results
Efit-Ebeam [Gev]
Θ=0.13
Θ=0
3
Θ=0.13
Θ=0
Unexpected behavior but pixel size
Much better behavior
Impact of crossing angle
not understood at this stage
Prefer 18um vertical pixel size (Ry=1) otherwise too large
wrt effective vertical beam size on detector.
Residual effect of crossing angle on ellipse position
and polarization still to understand
σyfit
PZ1fit-PZ1exp

## Slide 17: Fit correlation matrix (photons)
Correlations of ξ₁ and beam sizes σₓ,y and longitudinal polarization as they all affect scattered photon spatial distribution
Longitudinal polarization affects total cross-section and thus normalization
Rx=16
Ry= 1
Crossing angle
5x107 events (60 seconds of data aqcuisition)
Average of correlation coefficients over 100 exps.
Standard deviation
??? Investigations
on going

## Slide 18: Fit correlation matrix (electrons)
Ellipse parameters correlated with beam sizes
Correlations of ξ₁ and longitudinal polarization
Longitudinal polarization affects total cross-section and thus normalization
Rx=16
Ry= 1
Crossing angle
5x107 events (60 seconds of data aqcuisition)
Average of correlation coefficients over 100 exps.
Standard deviation
Next step: simultaneous fit of electrons and photons

## Slide 19: Asymmetry
for
Asymmetry induced by laser helicity flip improves robustness
against systematic uncertainties in transverse polarization extraction.
Reproductible and well known laser helicity flip is required

## Slide 20: Asymmetry
The position and spatial resolution parameters are fixed, as the fit is found to be largely insensitive to their variation.
No bias at the 10^-4 level except for 𝛇_y (7x10^-4) to be investigated.
Next step evaluate how uncertainties in these fixed parameters might affect the systematic errors
NB: systematics related to fixed parameters to be looked at.

## Slide 21: Asymmetry scan
epy
epz
pPX
pPz
pPY

## Slide 22: Simulation on Monolithic pixel sensor
Beam energy extraction (ellipse coordinates)
is significantly affected by the pixel size (few per-mil level)
    Interesting correlation with vertical pixel size ! (why ?)
Significant effect on longitudinal polarization too (why situation improves when pixel area increases ?)
Much smaller impact on vertical polarization (small fraction of per-mille)
Efit-Egen.[Gev]
𝛏3𝝵y fit- 𝛏3𝝵y gen
𝛏3𝝵z fit- 𝛏3𝝵z gen
Ry=2
Ry=3
Rx
Rx
Rx

## Slide 23: Compton polarimeter initial layout
Blondel et al., arXiv:1909.12245; Muchnoi, INST 17 P10014 (2022)
Scattered photons
Electron beam
Lowest energy scattered electrons
Dipole (field B)
Laser ()
Green wavelength
Interaction region
New concept (N. Yu Muchnoi) to measure all polarization parameters  3D polarimeter
about 100m
x
X0
X1
X2

## Slide 24: Asymmetry fit (preliminary)
Narvaez, EPOL meeting
Preliminary
More investigations
ongoing

## Slide 25: Typical result – fit of Asymetry
Based on measurement of scattered particles transverse distributions (pixelized detectors)
Typically obtained in 30s for a single bunch
Blondel et al., arXiv:1909.12245; Muchnoi, INST 17 P10014 (2022)
Beam energy may be extracted too!  redundancy with RDP
All components extracted with ~0.001 precision in few seconds

## Slide 26: Fit refinements
Narvaez, EPOL meeting
Extend calculation over extended range beyond sensitive area

## Slide 27: Updated toy study
see also J. Tamazirt poster
Beam energy [GeV]
(electron detector)
(electron detector)
(photon detector)
Residual biases (1-5 10-4) under investigation
Electron detector
Photon detector
4mm
400 mm
10 mm
X: 1200 1400 1600 1800
Y: 40 60 80 100
X: 1200 1400 1600 1800
Y: 40 60 80 100
Npixels for electrons
X: 1200 1400 1600 1800
Y: 40 60 80 100
Npixels for electron detector
X: 40 60 80 100
Y: 40 60 80 100
Npixels for photon detector
Combined fit to be investigated
A toy MonteCarlo procedure is applied (100 experiments, 108 events each

## Slide 28: Impact on integration
Laser does not travel through dipole  easier integration
(Q-switch would)
Vacuum chamber concept adapted from SuperKEKB concept
Validated for impedance budget

## Slide 29: Physics requirements
Blondel et al., arXiv:1909.12245
Beam-based measurements in real time, including beams energy with resonant depolarization
High reproductibility of measurements for various sqrt(s) is critically needed
Extract as much information as possible from physics experiments themselves
(crossing angle, luminosity, sqrt(s) spread)
24/7 operable measurement of (de-)polarization
Required accuracy of <1ppm

## Slide 30: Integration
Polarimeter integrated close to experiments IP
1/beam (baseline)
Oide, https://indico.cern.ch/event/1237189
Demanding operational constraints
laser room in the parallel technical gallery
24/7 access to the laser system and related electronics
Oide
e-beam size at Compton IP :
~500µm (horizontal)
Robust laser technology is available nowadays

## Slide 31: Laser helicity asymmetries
Reproductible and well known laser helicity flip is required
Blondel et al., arXiv:1909.12245

## Slide 32: QED corrections
Studied in details at SLD
Denner & Dittmaier Nucl. Phys. B 540 (1999) 58, Swartz Phys. Rev. D 58 014010 (1998), Veltman Phys. Rev. D 40 2810 (1989), Veltman Phys. Rev D 42 1856E (1990);
A. Martens et al 2023 JINST 18 P10001
at 45 (80) GeV
at 45 (80) GeV
Measurement of transverse polarization at FCCee :
photons
electrons
at 45 GeV
Measurement of longitudinal polarization at FCCee :
If and only if laser helicity asymmetries are measured

## Slide 33: Magnetic field tolerancing
Nominal vertical field for reference:
Many potential sources of ‘bending angle’ uncertainties (for instance genuine inhomogeneities of B-field, short-/long-term fluctuations of currents, temperatures, alignments)
Over the useful aperture of the magnet:
Fringe fields also may affect performance of polarimeter
By product: angular alignment
NB: Requirements not met  not a show-stopper but detailed studies required

## Slide 34: Physics requirements cont’d
Wilkinson at EPOL workshop https://indico.cern.ch/event/1181966
High accuracy longitudinal polarization measurement is needed
Naturally small at IPs but with what accuracy ?
Measure it !

## Slide 35: Compton cross-section
Berestskii & Lfshitz QED textbook
The Compton cross-section averaged over scattered particles spins:
Differential cross-section
Electron beam polarization independent
Electron beam polarization dependent
Transverse laser polarisation: nuisance parameter to minimize and keep under control
Transverse electron beam polarisation: intervenes as an asymmetry in the transverse plane
⚠️ But small opening angle of scattered particles:
  Electrons  spectrometer
  Photons  difficult to measure asymmetric distribution of a narrow spot  long lever arm needed

## Slide 36: Laser integration
Some constraints
  Small crossing angles are preferred (cross-section, beam jitters) few mrad typically
  Beams crossing plane neither horizontal nor vertical
  beam impedance
  beam induced currents in metallic parts  avoid
  mechanical stability
  ease of maintenance works
SuperKEKB upgrade concept
Box with rough temperature control
Box with rough temperature control
laser
Polarisation &
beam shaping
Position, pointing control and monitoring
Polarisation independent intensity monitoring
Optical spectrum monitoring possible
Polarisation monitoring
Duplicated at injection
Add Position and pointing monitoring
R&D needed to reach required perf.
24/7 operable laser system, with full monitoring, remote control

## Slide 37: Some laser systems
Laser param. | 1 pilot | 1 pilot v2 | All colliding bunches (at Z)
Repetition rate | 3 kHz | 3 kHz | 30 kHz
Pulse energy | 1 mJ | 1 mJ | 10x0.05mJ
Pulse duration | 3 ns | 30 ps (**) | 30 ps
Average power | 3 W | 3 W | 15 W (***)
Scattering rate | 3x105/s (*) | 3x105/s (****) | 4x107/s (****)
Scattering rate per bunch | 3x105/s (*) | 3x105/s | 4x105/s
Nikolai’s baseline (Q-switch Nd-YAG)
(*) crossing angle ~ 2mrad
(**) related to optical bandwidth  constrains resolution of ‘direct’ energy measurement from polarimeter
(***) Can be increased to typically ~100W (nowadays) but requires operational validation
(****) not limited by Piwinski contribution  can be several degrees without affecting rate
Same oscillator may be used but two different amplification schemes
adaptable
Versatile Yb system

## Slide 38: Scattering rates
Laser-beam single pulse energy
Photon rate
Compton cross-section
Electron bunch charge
(25nC for colliding bunches,
1.5nC for pilots)
Geometrical factor
Laser photon energy
(2.4eV for 0.5µm wavelengths)
Transverse beam sizes:
  =1000µm
  500µm, =10µm, mm

## Slide 39: QED corrections
QED corrections<0.001 @ 45 GeV
Denner & Dittmaier Nucl. Phys. B 540 (1999) 58, Swartz Phys. Rev. D 58 014010 (1998), Veltman Ophys. Rev. D 40 2810 (1989), Veltman Phys. Rev D 42 1856E (1990)
Involved processes e𝛾 e𝛾, e𝛾eee, e𝛾 e𝛾𝛾
Scattered electron energy
Need to be eventually included in simulations…

## Slide 40: The Compton process
Klein O. and Nishina Y., Z. Phys. 52(1929) 853; Ginzburg I. et al., Nucl. Instr. Methods in Phys. Research 219 (1984) 5, V. B. Berestetskii, E. M. Lifshitz, L. P. Pitaevskii (1982). Quantum Electrodynamics. Vol. 4 (2nd ed.)
Compton x-section
~0.3b (Ee~45GeV)
Kinematic edge