## Slide 1: ND for Reactors: “What we need for GEN-III, GEN-IV, for SMR, for all solutions”
D. BERNARD, on behalf of all the « Nuclear Physics & Nuclear Data + applied neutronics & photonics for reactors » group at CEA

## Slide 2: Nuclear (+Atomic) data needs for reactor applications
Application-driven activity :
  For reactor physics under operating and accidental conditions, including instrumentation…(static+dynamic physics of neutrons)
  For, back-end cycle, radiation exposure…
General goals/objectives: Ensure safety and competitiveness !
Methodology : Industrials have to propose operating realistic margins (safety vs $) to TSOs. In other words, they have to demonstrate the validation of reactor physics codes associated to a given nuclear data library.
Ways to achieve :
  compare code&ND calculations to integral measurements or propagate ND prior uncertainty (ND assimilation is according to the desire…)
  Select (specific) ND to be measure to reduce the C/E values or uncertainties via, for instance, Target Accuracy Requirement exercices
Short term actions (5-10 years) GEN-II & III
Long term actions (>10 years) GEN-IV, Fusion

## Slide 3: Reactor physics: neutron act as a gas without mutual interactions  Fokker-Planck Boltzmann non-relativistic mesoscopic equation
+ Bateman ODE equations
+ a derivation of both: the in-hour equation.

## Slide 4: Nuclear Data for GEN-II+III current and actual reactors
12 main parameters:
AND
g-heating in structural materials (prompts by capture/fission and delayed by activation/fission)
Vessel fluence and DPA (Prompt Neutron Fission Spectra, 56Fe(n,n’)SAED)
Power over Activation (P/A) for in-core instrumentation, Self Power Neutron Detectors…
Neutronic emmisivity and spectrum of start-up sources (a,n) XS
Cladding rupture (Fission Gas Released  niFY), some devices are radiosensitives…
Neutron noise to prevent accident and to measure neutron dynamicP(n)
Target accuracy on LWR neutronics parameters is about 2 to 5 times lower than the a priori uncertainty (1σ) due to nuclear data.
@Santamarina, ND2007

## Slide 5: Nuclear Data for GEN-II+III fuel cycle
Gas inducing cladding pressure (fission yields), Tritium production (fuel via ternary fission and primary circuit via 10B(nFAST,t))
Primary circuit corrosion products: (n,lcp) reactions
Spent fuel caracterisation ([232U], [244Cm]…) for
radioprotection, Dose, Decay Heat (241Am(nth-epi,g)242g+mAm, 242Pu(n,g)243Pu(b-)243Am(n,g)244g+mAm(b-)244Cm)
Neutron rate emission (spontaneous fission and (g,n)+(a,n))
Non destructive identification of nuclear waste packages/Safeguards and Nuclear Material Management :  (g,f) Fission Yields

## Slide 6: Example #1 of ND needs for GEN-III reactors
Prior uncertainties covariance propagation is about ±5% on radial assembly power maps on large and heterogeneous cores. This is leading to about ±10% on control rod worth !
Usual suspects (for different reactor configurations):
238U(n[2-5]MeV,n’cont) plateau XS.
p(n[0.1-5]MeV,p)n : a IAEA standard, but still work to to !
p(nth,g)d, very usefull for Big Bang Nuclear Synthesis, but for LWR aswell 
Eigen Value Separation

## Slide 7: Example #1: 238U(n [2-5]MeV,n’) for almost all reactors
Lower XS value @1MeV because of Ramsauer-Townsend effect:
This gives large migration area to 1 MeV neutrons
This constrains the radial map in large LWR !
These 1 MeV neutrons are coming from 238U(n[2-5]MeV,ncont’) !
Why inelastic from continuum ? Because of secondary K-M angle+energy distributions (MF6/MT91) !
The regime change between discrete and continuum has to be smooth:
TALYS, EMPIRE… :
Zone of interest

## Slide 8: Example #1: 238U(n[2-5]MeV,n’) for almost all reactors
Lot of integral and ToF new experiments:
238U(n,n’g) for which nuclear structure data are needed, even for 238U !!
At the end of the day, JEFF-4.0/238U+n solves partially the issue…but we still need some associated realistic covariances there…

## Slide 9: Example #2: 1H(nth,g) for GEN-III reactors
(n+p) system is evaluated mainly at US/LANL through phenomenological R-Matrix formalism including almost 6000 experiments (direct and inverse d+g)…More experiments will not help…
Improvements are still needed for LWR temperature coefficients, radial power and reactivity.
My point: nuclear theory is always useful and will become essential ! Choose your dof:
Very encouraging results coming from basic nuclear cEFT theory and LQCD !
ENDF/B-VIII.1 :
(C = 317.7 mb)

## Slide 10: Example #3: 238U(n36eV,g) for GEN-III reactors
Doppler reactivity coefficient
T=900K
Resonant Up-scattering
Need to reduce the uncertainty of the 36eV resonance parameters and phonon spectra of many molecules

## Slide 11: Example #4: neutron induced fission yields for GEN-III reactors
Fuel depletion (Post Irradiation Experiments = radiochemical analyses) and its reactivity, a long standing problem partly solved in JEFF-4.0
239Pu(nth,f)153Sm cumulated yield measurement @ILL/Lohengrin to restore the JEFF-3.1.1/LWR reactivity versus burn-up.
+ New JEFF/4.0/147Pm(nth+epi,g)148g+mPm…+70pcm…

## Slide 12: Example #4: neutron induced fission yields for GEN-III reactors
Decay Heat:
N-FY “experimental” covariance : JEFF-4.0 matrices
Decay heat
Cooling time [s]
Experimental correlations and charge invariance lead to decrease prior ND uncertainty

## Slide 13: Example #5: neutron start-up sources for almost all reactors
New JEFF-4.0/9Be(a,n0)/SAD during core loading to prevent low reactivity accidents
During fuel loading (keff<1), i.e. subcritical approach, low (<1 MeV) and high (>3 MeV) energy neutrons are crucial for:
their amplification through 235U(n,f) and 238U(n,f),
their monitoring by ex-core detectors.

## Slide 14: Examples #6 of ND needs for nuclear cycle
Photofission XS+yields for g-inspection
237Np(n,2n) and 241Am(n,g) branching ratios resp. for radiotoxicity [232U] and decay heat [242Cm]
FIFRELIN/EM cascade calculations for the 2 Jp resonances with different LDM and PSF.

## Slide 15: Longer term : GEN-IV reactors
Molten Salt Fast Reactor dedicated to transmute transuranians as an example.
241Am(nFAST,f)PFNS is mandatory !
keff uncertainty [pcm]
Leff (effective neutron generation time) uncertainty [pcm]

## Slide 16: EU/SANDA project (2019-2023), http://www.sanda-nd.eu/
+ 27Al(n,n&n’), 27Al(n,g), 135Xe(n,g) for JHR studies
+ Chlorine, Calcium, silicium isotopes, for High Level Waste disposal studies
+ Tungstene & Osmium for fusion applications

## Slide 17: Conclusion
Thanks to HPC, Nuclear Data is now the main source of uncertainty in reactor calculations !
Structure data is mandatory to reduce data from independent FY or (n,n’g) measurements
Reaction data: Big5 n-XS (235,238U, 239Pu, 1H, 16O)+ structural/absorbing materials, PFNS, SAD, SAED, P(n), r(w), n+g induced FY, g production…
Short lived nuclei XS (IAEA initiative few years ago?): 135mXe…
Delayed neutron emission (experiments are on going), spectra have to be re-measured or calculated (summation calculations will need to improve Pxn in Decay Data files)
SPND (51V(n,g), 59Co(n,g), 103Rh(n,g)), dosimetric files…
Decay Data: full covariance is needed (b±/e,a, g/ICC, eA, X-rays…)…
Almost all you want to know : see HPRL website https://www.oecd-nea.org/download/wpec/hprl/

## Slide 18: Merci ! Questions ?
CEA CADARACHE
13115 Saint Paul Lez Durance Cedex
France
david.bernard@cea.fr
iresne@cea.fr
Site internet CEA IRESNE
LinkedIn CEA IRESNE