## Slide 1: Linear Collider Facility @ CERN: Accelerator aspects
Angeles Faus-Golfe
Notes: After the physics intro I will review the accelerator aspects.

## Slide 2: Outline
Context:
      LCs basics
      LCs projects: ILC, CLIC, C3
      LCs related R&D programs
LCF@CERN Baseline
250-550 GeV
2 IPs
Energy Upgrades
Boosting the performances: HG RF, ERLs
                Advanced Upgrade Paths
                photons, LPA
Notes: To understand better this project, we need to review the LCs basics, the projects as: ILC, CLIC and in the last times C3, and the R&D related programs.
I will describe after the LCF facility at CERN and the possible upgrades.

## Slide 3
Luminosity & Energy Frontiers
Luminosity
Energy
Notes: The two most important parameters for a collider are: Energy and Luminosity. In a simple way we could say, the physics case fix the energy and the precision of the measurement is mainly given by the luminosity.
This plot is showing the collider projects in function of the energy and luminosity. We will see the conventional Higgs factories in red / blue, the ERLs in green, LPA in yellow, muons in pink and the hadrons in grey around the 100 TeV.

## Slide 4
Luminosity & Energy Frontiers
Higgs
Luminosity
Energy
Notes: If we will focus in the Higg sector, left plot:
Luminosity at low-energies for CC surpass (reduction at high energy due to SR), at high-energies LC excel (Luminosity per beam power roughly constant)
For LCs luminosity increases with energy, e.g. 1-3 x 1034 cm-2s-1 for Higgs factories at 250 GeV, 6 x 1034 at 3 TeV
For LCs higher energies “easy” – 3 TeV studied (CLIC), but many TeVs challenging:
  Power proportional to luminosity
  Consider up to 50km
  Higher-energy means smaller beams and increasingly important beam-beam effects
LCs have polarized beams (80% e-, ILC also 30% e+), the spin of the e+e- beam can be maintained during the acceleration and collision. This can help significantly improve measurement precision.
A new factor have to be considered in the new colliders we are designing that is the: sustainability. For the first time in the design of a collider we have to take into account:
Energy consumption, efficiency, sustainability, carbon footprint
And we have to develop the technical devices that are needed for this, as:
High-Efficiency RF power sources: Klystrons, Solid State Amplifiers, IOTs...

## Slide 5
Luminosity & Energy Frontiers
Sustainability Frontier
Higgs
Luminosity
Energy
Notes: If we will focus in the Higg sector, left plot:
Luminosity at low-energies for CC surpass (reduction at high energy due to SR), at high-energies LC excel (Luminosity per beam power roughly constant)
For LCs luminosity increases with energy, e.g. 1-3 x 1034 cm-2s-1 for Higgs factories at 250 GeV, 6 x 1034 at 3 TeV
For LCs higher energies “easy” – 3 TeV studied (CLIC), but many TeVs challenging:
  Power proportional to luminosity
  Consider up to 50km
  Higher-energy means smaller beams and increasingly important beam-beam effects
LCs have polarized beams (80% e-, ILC also 30% e+), the spin of the e+e- beam can be maintained during the acceleration and collision. This can help significantly improve measurement precision.
Since ESPPU 2020, a new factor has to be considered in the new colliders we are designing that is the: sustainability. For the first time in the design of a collider we have to take into account:
Energy consumption, efficiency, sustainability, carbon footprint
And we have to develop the technical devices that are needed for this, as:
High-Efficiency RF power sources: Klystrons, Solid State Amplifiers, IOTs..., permanent magnets...

## Slide 6: LCs Accelerator Challenges and Key Technologies
Energy
Luminosity
Construction cost $ ~ l
High Gradient g
Operation cost $ ~ PAC
High Efficiency η
Nanobeam Technology
Damping ring (ε)
Final focus (β*)
Main Linac Technology
Small Beamspot σ*xσ*y
Losses in cavity walls
Small duty cycle:
Pulsed operation
Low resistivity
High frequency &
Ultra-short pulses
CLIC NCRF
2 beam acceleration
ILC SCRF
Linac Technology
Key Technologies
Nanobeam Technology
ECM = l g
L
l
Notes: If we analyze Energy & Lumi in the case of LCs we have:
Energy is given by the Length and the gradient
Luminosity is proportional to beam power ( AC (wall-plug) power x efficiency ) and inversely proportional to the beam sizes at the IP
Energy column -> the “gradient” and the “efficiency” are given by the “main linac technology” if you choose Superconducting RF as in ILC we have low resistivity in the case of NCRF as in CLIC we have higher frequencies and ultra short bunches. In the two cases we use pulse operation.
Luminosity column -> a very small beam sizes are needed of the order of nanometers, this is given by the emittance means the DRs and the small beta function this means the Final Focus section.
In summary the key technologies are the linac and the nanobeams.

## Slide 7: ILC accelerator: Technology updates
http://www.linearcollider.org/

## Slide 8
ILC parameters and beam accelerator sequence
  e- blue
  e+ red
SC helical undulators (baseline): rotating target, polarized (e- at 125 GeV)
Electron driven source: dedicated 3 GeV NC S-band TW e- (pair production).
Energy upgrades: 500 GeV (31.5 MV/m Q0=1 x 1010) , 1TeV (45 MV/m Q0=2 x 1010, 300 MW) more SCRF, tunnel extension
- Kitakami site: 50km long, sufficient for 1TeV
Luminosity upgrades:
- 2 x bunches, 2 x RF (1.35 -> 2.7x1034)
    - Run = 500GeV machine at 250GeV,
    10Hz: factor 2 (2.7x1034 -> 5.4x1034)
  - Improve power efficiency
ILC 250 GeV
Notes: The beam sequence for electrons and positrons for the baseline at 250 GeV is sketched in the upper left part of the slide, starting with electrons in blue and positrons in red. In the case of the positron production a baseline solution with SC helical undulators is adopted but an option with a classical production with an electron driven linac source is being studied as backup.
The main parameters for the initial baseline at 250 GeV and the subsequent luminosity and energy upgrades are summarized in the table in the down right part.

## Slide 9: Progress in SRF
Yield evaluation of cavities based on TDR
Eng. design
Euro-XFEL Operation (Europe)
~800 cavities/
~100 Modules
LCLS-II Construction (USA)
~280 cavities/
~35 Modules
High performance and cost reduction
Cavity manufacturing, performance demonstration (Yield demonstration in three areas)
Demonstration of cryomodule assembly, transfer, and performance
Cavity
Cryomodule
～2017
2018～2021
Pre-lab
Module assembly
The mass production of European XFEL has reached ≥ 83% of the ILC specification yield (90%).
US-Japan: high performance with new surface treatment, etc.
France-Japan: Automation of cavity cleaning
Realized through international cooperation and procurement
Accelerator performance verification at KEK-STF2
Final design is underway to comply with "High Pressure Gas Safety".
Germany-Japan: Improving Efficiency in Cavity Manufacturing.
ILC
European XFEL: 29 ± 5.1 MV/m
LCLS-II: 18-21 MV/m
Q>2.7 1010
Notes: The Main linac is made of around 8000 SC 9 cell cavities at 1.3 GHZ, 1 m long and with a gradient of 31.5 MV/m, the total length of the cryomodule with all the services is 12 m. The cavities are powered by 10 MW pulsed klystrons for 4 and half modules. The cavities are operated at 2K and between 4 and 6 cryoplants at 19 kW at 4.5 k are needed. They operate in pulse regime an the we have around 1300 bunches per pulse.
A SC linac of these characteristics is working in the EU XFEL in Hamburg with 800 cavities (10% of ILC) and others two LCLS-II at SLAC and SHINE in Shanghai are under construction.
--------------------------------------
In the last years an important R&D effort has been made in order to reduce the cost fabrication and to push the performance limits.
Two aspects have been considered: the Nb preparation and the SCRF cavity fabrication process.
A new approach to realize the thin film coating is the High Power Impulse Magnetron Sputtering (HiPIMS) instead of DC Magnetron Sputtering, giving high-Q with a flatter slope.
From the performance point of view the baseline specifications of a gradient of 31.5 MV/m, Q0 of 1x1010 and 90% yield with new surface treatments we could achieved gradient of 35 MV/m, Q0 of 1.6x1010
Concerning the cryomodules there is also an International effort to automatize the assembly, the integration and the compatibility.
Mass production challenge including transfer to Japan, planned R&D will be made in the framework of the ILC-IDT.
------------------------------------------------------------------------------------------------
High-Q means power saving ( ratio between the stored energy (W) and power dissipated by RF cycle (P) multiplied by the angular frequency (w) -->=Q= w W/P)
European XFEL completed and in operation with cavities after retreatment having a Gradient of around 30 MV/m and more than 10% exceeding 40MV/m.
LCLSII SCRF linac is under construction by (SLAC/Fermilab/Jlab collaboration) to be completed in 2020, CW operation, cavities having 18-21 MV/m with a quality factor 2.7 1010 average.
Ingot – bar or block of metal
High Power Impulse Magnetron Sputtering (HiPIMS)
Sheeting – chapa, tole, feuilles metaliques
Piping – collections of pipes, canalisations

## Slide 10: SRF R&D items
International Cooperation R&D Items:
Establishment of international standards of the SRF cavity satisfying the Japanese High-Pressure-Gas-Safety regulation (requires common drawings)
Advancement of SRF cavity and surface treatment technology, performance evaluation
Optimization of cryomodule (CM) design and overall performance evaluation of cavity packages
Efforts to apply advanced SRF cavity technology such as crab cavity
SRF cavity
Cryomodule
ILC crab cavity system
Nb Fine Grain (FG) Disc
Grain Size: 50 - 100 um
A New Approach:
Nb Medium Grain (MG) Disc
Grain Size < 1 mm
Type-B CM has one unit of “SCQ + cold BPM” at the center position.
CM design for ITN comprehensively includes the design for E-XFEL, LCLS-II and ILC/TDR
IJCLab
Notes: SRF technology has matured through the construction and stable operation of the European XFEL.
Superior power efficiency of SRF technology has been demonstrated, and its application is expected to expand.
  Global efforts to improve cavity performance and reduce costs have progressed.
  Demonstration of the production of high-performance cavities, leading to various accelerator applications.
Prospects for the advancement of SRF technology applications.
  ex. Semiconductor lithography, medical application, environmental remediation, etc.
SRF part is separated into cavity production as WPP-1, globally common design of CM as WPP-2, and crab cavity as WPP-3:
- In WPP-1, cavity production and surface treatment method will be established
- In WPP-2, design of cryomodule will be done globally
- License agreement is significant and urgent issue for globally common design of CM
- In WPP-3, crab cavity teams will produce and test prototype cavities
- KEK already started the technical discussion with Europe, USA and Korea
- The CM design for ITN is based on E-XFEL, LCLS-II and ILC/TDR. Then, the license agreement with DESY and SLAC should be done significantly and urgently.
- Unify cryomodule (CM) design with ancillaries, based on globally common engineering design, drawings & data-base. Establish globally compatible safety design base to be approved/authorized by HPGS regulations individually in each region, most likely referring ASME guidelines to be compatible with Japanese regulations.
- The crab cavity system is the must item for ILC. Peter McIntosh (STFC) has organized this activities leading the globally collaborative team since 2021. Two of five designs were selected at the international review hosted by KEK in Apr/2023.

## Slide 11: Progress in positron source
～2017 technical design
2018～2021 technical verification
Alternative: Conventional e-Driven
Undulator prototype
Photon dump design
Mag. focusing
Paricle simulation
Target thermal simulation
Target Prototyping
Vacuum characteristics Testing
Practical Operation of Superconducting Helical Undulator (Alternate Periodic Structure)
Ti target beam test
Long undulator operation at European XFEL
Plan A:Undulator scheme
Plan B:e-driven scheme (same tunnel)
Plan C:e-driven scheme (extra tunnel)
Optics design
Optics design
Next Steps: evaluate both schemes by international cooperation
Thermal analysis
Loading compensation
Pulse solenoid design
APS cavity
Target maintenance
RF stability test
Technology selection
High-speed rotating positron target, Technology Design
Pre-lab
Baseline Undulator scheme to obtain polarization
Notes: One of the others areas where there have been an important R&D effort is on the positron sources.
The baseline positron source of ILC is based on an undulator scheme producing polarized e- and e+. To mitigate the risk of such a scheme a conventional e-beam driven has been also studied in detail.
In the recent years various modifications and improvements are undergone. The new undulator based design supposes: reduced target heat load, the Radiative cooling (heat transferred from rotating target to sitting copper by radiation, no vacuum leak), the Magnetic bearing in vacuum and the Focusing by pulsed solenoid.
These studies. have demonstrated the required performances, and in particular the e+ / e− yield is technically feasible. The level of maturity of the positron source for the ILC is fairly advanced and the RD is ongoing to optimize further this option. As an alternative a conventional e−-driven source (3 GeV e−) has been developed. This alternative low-risk option offers some advantages from the flexibility operation point of view, but no polarization is provided.
All of these studies are going on in the framework of an International collaboration in the framework of the ILC-IDT.
---------------
The design of the undulator system has been changed since then:
  What did not change : Ti-alloy, 1m diameter wheel, rotation speed 100 m/s
OLD design
Water cooling (water flows inside the wheel, must be taken out through the axis of the rotating shaft, keeping vacuum)
Vacuum seal by ferro-fluid
Focusing by flux concentrator
NEW design
Radiative cooling (heat transferred from rotating target to sitting copper by radiation, no vacuum leak)
Magnetic bearing in vacuum
Focusing by pulsed solenoid

## Slide 12: Sources R&D items
International Cooperation R&D Items:
Electron source including the recent developments
Undulator positron scheme: rotating target, magnetic focusing
Electron driven positron scheme: rotating target, magnetic focusing, capture cavity
Target replacement
Target
Magnetic focusing
Photoguns based on a compact insulator to reach high-voltage and free field emission
Rotating Target
Electron source
e-driven scheme
undulator scheme
Capture cavity (L-band)
Girder structure on rail
Target replacement
3D RF simulation of APS cavity at KEK
Flux concentrator for e-driven scheme
Test bench in KEK
Automatic connection coupler
Pillow sea
IJCLab
Notes: Polarized electrons are also useful for observing of magnetism (Spin-Polarized Low Energy Electron Microscopy, SPLEEM).
Positrons have been used in colliders such as SLC, SuperKEKB, DAFNE, and CESR.
In the future, more intense positron sources will be needed for circular colliders such as FCCee and CEPC, linear colliders such as ILC and CLIC, and muon colliders (LEMMA).
High-intensity slow positrons are expected for surface structure analysis.
Positron targets and beam dumps are also closely related to targets for neutron and beam irradiation used in industrial medical applications.
The development of SRF accelerators has increased the beam intensity, and the development of target technology that can effectively utilize this intensity is of great interest worldwide.
There are many research topics in this field
- Photo cathode
- High power laser
- Ultra high vacuum and voltage
- High power target
- Pulsed magnet and power supply
- Undulator
- Accelerating structure
- Handling of activated materials

## Slide 13: Progress in Final Focus
Tech. design completed
Spec. almost achieved
Detailed design
Stable operation demonstration
～2017
2018～2021
Pre-lab
Wakefield effects
ATF: achieved 41nm (2016)
（37nm=ILC（7.7nm)）
High-speed beam position control technology was also demonstrated.
Wakefield effect was evaluated at ATF.
-confirm no serious problem at ILC
-demonstrate a technique to reduce the wakefield effect
ATF International Review (Committee)*
-The committee highly evaluated the achievements of ATF so far.
-The committee pointed out the importance of continuing research to contribute to the detailed design of the ILC final convergence.
* https://agenda.linearcollider.org/event/8626/
Distribution of bunch positions measured at IPB, with two-BPM FB oﬀ (green) and on (purple)
FONT feedback system
Ultra low-b* studies
ATF2 wakeﬁeld knobs system be-tween BPM QD10BFF and QD10AFF
Modify the beam monitor system, etc. at ATF to demonstrate stable operation.
Final doublet optimization
Notes: The Final Focus System is one of the most challenging of the LCs. ATF2 is a scale down version of the Final Focus to test local chromaticity correction and to demonstrate the nano-beam technologies for LCs: ILC and CLIC.
There has been a continuous work from many labs, in ATF first and ATF2 after to get nanobeam size and its stabilization, last times centered in ultra-low beams for CLIC and intensity dependence studies. “Outstanding” and “Unique” results are obtained in ATF2.
I remind the two main goals of ATF2:
-Achievement of 37 nm spot size
-Control of beam position at nm level.
What we have obtained:
-Nano-beams: 41 nm (10 % target)
-FB latency of 133 ns and a direct stabilization of position IP jitter of 41 nm (limited by IPBPMs resolution)
Left figures:
Distribution of bunch positions measured at IPB, with two-BPM feedback oﬀ (green) and feedback on (purple).
The Position Jitters of the Bunches with Feedback Oﬀ and On, for Two-BPM Feedback:
------------------------------------------------------------------------------------------------------------------------
Feedback Position jitter (nm) Correlation (%)
Bunch1 Bunch 2
Off 106 +- 11 96 +- 10 91.6
On 106 +- 11 41 +- 4 41.3
------------------------------------------------------------------------------------------------------------------
Predicted vertical position jitter (calculated from the position at P2 and P3) in the region of the focal point with feedback off (solid) and feedback on (dashed).
In ILC and CLIC we profit from the level arms for the BPM location that are at a certain distance.
But the small beam sizes where obtained with reduced bunch intensity and aberration optics.
Since November 2016, hardware improvements have been accomplished to mitigate the wakefield effect. Wakefields studies to mitigate its impact are going on with very promising results.
In the next future the main studies will be centered in necessary R&D to maximize the luminosity potential of ILC. In particular, the ILC final focus system (FFS) design must be assessed from the point of view of beam dynamics, choice of technology and hardware, and long-term stability operation issues.
---------------------------
Complete the QD0 R&D prototype vibration measurement testing at 2K
Update IR baseline magnet designs to take into account the detector specific requirements (MDI) and advances in magnet coil winding technology since the TDR was written

## Slide 14: Nanobeams R&D items
International Cooperation R&D Items:
Optimization of damping ring design.
Advancement of high-speed beam injection/extraction technology (nanosecond beam control).
Upgrade of beam diagnostics at ATF through in-kind contribution.
Establishment of nano-beam tuning technology utilizing ATF (including machine learning, etc.).
Vibration evaluation of final SC magnets.
Establishment of megawatt-class beam dump technology (application to neutron target and beam dump).
KEK-ATF
Fast kicker (injection/extraction)
Swap-out injection system planned at LBNL
Beam injection/extraction system for CLIC DR
Maximum search algorithms to be applied to beam tuning (Machine Learning)
Wakefield test station
Intensity dependence studies
Prototype of ILC service cryostat
( 2K cooling system ; BNL )
Final doublet optimization
Vortex water flow
17 MW at 500 GeV beam
1 MPa to prevent boiling
Beam window Ti-alloy
1m-long x 2m(diameter) water
Beam Dump
IJCLab
Notes: Pioneering achievements in nanobeam technology at KEK's ATF through international collaboration.
  Realization of the world's smallest beam through improvement of beam quality and beam focusing technology.
  Demonstration of nanosecond scale fast beam injection/extraction technology.
Expectations for the advancement of nanobeam technology.
  Nanobeam in new-generation synchrotron light source, application of microbeams to industrial medical applications.
  Advancement of beam diagnostics, beam tuning by machine learning, beam control technology on the nanosecond scale can be applied to a wide range of accelerators.
WPP 12: System design of ILC DR
Objectives:
Improved design by incorporating the latest light source design and technologies.
Evaluation and optimization of the DA with a more realistic modelling of the quadrupoles including the fringe field effects.
WPP 14: System design of ILC DR injection/extraction kickers
Objective:
The technical evaluation of the fast kicker power supply using the recent semiconductor technologies
WPP 15: System design of ILC FFS
Objectives:
wakefield mitigation strategies
correction of higher-order aberrations
training for ILC beam tuning
WPP 16: Final doublet design optimization
Objectives:
Complete the QD0 R&D prototype vibration measurement testing at 2K
Update IR baseline magnet designs to take into account the detector specific requirements (MDI) and advances in magnet coil winding technology since the TDR was written
WPP 17: Beam Dump
Objective:
Finalize the engineering design of the main beam dump system, in particular:
  Vortex water flow in the dump vessel
  Cooling water circulation and heat exchange
  Remote exchange of the beam window
  Countermeasure for failures / safety system

## Slide 15: CLIC accelerator: Technology update
http://clic-study.web.cern.ch/

## Slide 16: CLIC parameters and beam accelerator sequence
  e- red
  e+ yellow
Luminosity performance studies (Z-pole and gamma-gamma)
Notes: The beam sequence for electrons and positrons for the baseline at 380 GeV is sketched in the upper left part of the slide, starting with electrons in red and positrons in yellow. In this case the main linac is powered but decelerating a high intensity drive beam (two beam scheme).
The main parameters for the initial baseline at 380 GeV and the subsequent luminosity and energy upgrades are summarized in the table in the down right part.

## Slide 17
CLIC baseline – a drive-beam based machine with an initial stage at 380 GeV. The main challenges:
  High-current drive beam bunched at 12 GHz
  Power transfer and main-beam acceleration, efficient RF power
  Towards 100 MV/m gradient in main-beam X-band cavities
  Alignment and stability (“nano-beams”)
CLIC 380 GeV with X-band klystrons (larger tunnel, klystron design not optimized…)
The CLIC Test Facility at CERN (CTF3) programme addressed all drive-beam production issues
Other critical technical systems (alignment, damping rings, beam delivery, etc.) addressed via design and/or test-facility demonstrations
X-band technology developed and verified with prototyping, test-stands, and use in smaller systems and linacs
Target and achieved emittance in existing and planned machines
CLIC accelerator challenges/technologies
CTF3 facility
XBox facility
IJCLab
Notes: A version for a 380 GeV Stage 1 with Klystrons is has been studied:
- Design made, many parts prototyped and available (and used in the smaller linacs)
- Need larger tunnel for klystron gallery (CE study also made for this option)
- Also in this case the upgrades would require a drivebeam
- Challenges: number of klystrons a factor 10 higher than in drive-beam version (~5500), lifetime a concern, costs (RF costs per 2m module approaching 1 MCHF)
Redesign to reduce the klystron challenge – fewer, current design not optimized since 2018 ?
CDR 2012
PIP 2018

## Slide 18: Examples of technical developments
CLIC Technical developments of key elements
Extensive prototyping over the last ~5-10 years
Notes: Some examples of prototypes of the key elements are illustrated in this slide: X-band cavities and related ancillary, components, permanent magnets, inductive adders as power sources...

## Slide 19
Drivebeam klystron: The klystron efficiency (circles) and the peak RF power (squares) simulated for the CLIC TS MBK (solid lines) and measured for the Canon MBK E37503 (dashed lines) vs total beam power. https://ieeexplore.ieee.org/document/9115885
Industrial questionnaire:
Based on the companies feedback, the preparation phase to the mass production could take about five years. Capacity clearly available.
Fundamental process for high-fields and material dynamics
Structures and components production program to study designs, operation, conditioning, manufacturing, industry qualification/experience. Understanding the limits by: Field emission, Vacuum arcing (breakdown) and Fatigue due to pulsed surface heating
X band RF structures fabrication:
Processes, Developments (rectangular disks, brazing, halves), Fabrication capacity
and Components for system.
High Efficiency Klystrons:
for LHC, CLIC, FCC-ee and ILC. For CLIC, this includes the L-band and X-band sources
Progress in X-band Technical Systems
EU projects: ARIES, I-FAST, new TNA
Notes: In the last years an important R&D effort has been made in order to reduce the cost fabrication and to push the performance limits.
Three aspects have been considered:
Study of the fundamental limits of the high-fields and the material dynamics as: field emission, breakdowns and material fatigues.
Xband fabrication flow and cost optimization as well as industrialization (a questionnaire addressed to companies worldwide)
Finally, the High-efficiency klystrons for the L and X band, that have extended to other projects and frequencies, in collaboration with industry.
--------------------------------
Normal conducting accelerating structures are limited in gradient by three main effects (setting aside input power):
Field emission
Vacuum arcing (breakdown)
Fatigue due to pulsed surface heating
Understanding these processes gives important input into:
RF design – Optimizing structures also coupled with beam dynamics
Technology – Material choice, process optimization
Operation – Conditioning and recovery from breakdown
X band RF structures fabrication
Processes
Developments; rectangular disks, brazing, halves
Fabrication capacity
Components for system

## Slide 20
Cool Copper Collider: Technology updates

## Slide 21: C3 RF technology
Exceeding Gradients and Pulse Lengths Required for C3
Quarter cryomodule
C3 is based on a new RF technology
Dramatically improving efficiency and breakdown rate
Distributed power to each cavity from a common RF manifold
Operation at cryogenic temperatures (LN2 ~80-K)
Potential for High gradient: 155 MeV/m
Scalable to multi-TeV operation
C3 Prototype One Meter Structure
High power Test at Radiabeam

## Slide 22
C3 Accelerator complex and performances
8 km footprint for 250/550 GeV CoM ⟹ 70/120 MeV/m
7 km footprint at 155 MeV/m for 550 GeV CoM – present Fermilab site
Large portions of accelerator complex are compatible between LC technologies
Beam delivery and IP modified from ILC (1.5 km for 550 GeV CoM)
Damping rings and injectors to be optimized with CLIC as baseline
Costing studies use LC estimates as inputs
C3 Beam Delivery System (Adapted from ILC/NLC)
C3 - 8 km Footprint for 250/550 GeV
Cryomodule Unit - 9 m
(630 MeV/1 GeV )

## Slide 23
The Complete C3 Demonstrator
Demonstrate fully engineered cryomodule
~50 m scale facility
3 GeV energy reach
Answer technical questions needed for CDR

## Slide 24: C3 R&D programme
Notes: R&D programme is carried out by the C3 Collaboration

## Slide 25
The LCF@CERN
Much more than shipping ILC @ CERN

## Slide 26
The LCF @ CERN roadmap
Basic assumption is to provide a scenario that can start “now” and that can be progressively upgraded to cover the physics needs and/or to be able to react on “surprises”. The guiding line should be to avoid as much as possible major civil construction for the upgrades. Upgrades should benefit from technology updates with the aim that the LC project benefits but also drives the innovation.
The first step is construction of 250 GeV ILC at CERN. This requires a 33.5 Km tunnel in the CERN area, a first implementation already studied by CLIC project, with 2 IRs sharing Luminosity.
After 10 years construction and 10 years data taking at at 250 GeV, the accelerator will be upgraded in stages with more advanced technologies to achieve higher-energies ( 500 GeV – 1 TeV) or higher-luminosities as:
    Higher-gradient SRF, NCRF CLIC or Cool Copper C3
    ERLs
    Plasma wakefield
    gg collider (optical or XFEL lasers)
    .....
Upgrades have to be understanded like: we have a tunnel with an ILC machine available and we need R&D to see how the new technologies can fit in such a facility, where DRs exists, tunnel diameter is fixed and a cryo-system is available.
In later stages the 2IRs can be used by sharing luminosity by running parallel programs at higher and lower energy as a testbed for technology development.
The LCF@CERN roadmap
Notes: In view of the ESPPU a project for having a LC at CERN has been submitted.

## Slide 27
The LCF@CERN baseline
ILC spec
LCF spec
Notes: Key parameters for LCF compared to ILC

## Slide 28
The current baseline ILC BDS at 250 GeV (BDS-250) has been designed to be scaled until 1 TeV (BDS-1000), keeping the same geometry. The total length is around 2400 m with a crossing angle of 14 mrad.
The optics has been designed taking as starting point the BDS-250 magnet configuration. The BDS-500 optics has been matched with the same magnet configuration. The field strength of the Final Doublet (FD) quadrupoles (QD0, QF1) for the BDS-250 is half of the BDS-500.
The BDS-1000 needs some additional magnets, in dedicated locations that are free magnet areas for the lower energy operation modes.
The performance and tolerances optimization, including different bending magnets strengths compatible for all the energies, collimation depths and different possible beamline geometries between others, are ongoing.
BDS for 250 GeV with half-lenght FD (bx,y* = 13 / 0.41 mm)
BDS for 500 GeV (bx,y* = 11 / 0.48 mm)
BDS baseline and the energy upgrades

## Slide 29
LCF@CERN with 2 IPs
Layout of the two IRs with 20 and 2 mrad crossing angle
Layout of the BDS section after the Main Linac and the FF section
In the ILC Baseline Conceptual Design, the ILC was designed with 2 BDS sections and two independent IRs with 20 and 2 mrad. At that time others schemes were under study, including one of 14 mrad and a head-on scheme.
A detailed study of dual BDS serving 2 IPs has been realized in the framework of the CLIC project, this work could be taken as reference for future studies (PhD V. Cilento UPSay)
Layout of the two IRs at 380 GeV with 16.5 and 20 mrad crossing angle
Layout of the two IRs at 3 TeV with 20 and 25.5 mrad crossing angle
IJCLab
Notes: The design of the dual CLIC BDS system is optimized to minimize the luminosity loss due to emittance increase and related widening of the beam sizes caused by the emission of SR generated in the bending magnet section in the first added part of the BDS, to separate the 2 IRs. This effect is much more significant for the CLIC at high-energies as the 3 TeV case, since the contribution to the IP beam size scales with the fifth power of energy. To mitigate luminosity loss from this contribution the bending angle, needs to be as large as possible, which determines the length of the BDS.
Crossing angle choice and other issues has to be studied in detail.

## Slide 30: Energy Upgrades beyond 550 GeV
1 TeV and beyond
Philosophy: prioritize
  advanced technologies over more civil construction
  flexibility over a fixed future: choices should be made later depending on scientific and technological developments - or even revolutions
replacing the linacs, re-using as much as possible from initial machine (DRs, BDS, …)
Example options:
  CLIC technology: 72-100 MV/m warm copper cavities, klystron-driven => 1.5 - 2 TeV
  C3 technology: up to 150 MV/m cool copper cavities => 1.5…3 TeV
  Others HG SCRF

## Slide 31
Boosting the Energy: HG SCRF
IJCLab

## Slide 32
Boosting the Luminosity: ERLs
LCs with energy recovery potential reach luminosities 2 orders of magnitude higher than ILC. Two different concepts of LC with energy recovery:
After the IP, the beams are decelerated and stored in damping rings until the beam properties (emittance, energy spread, etc) are restored. Then, accelerated again (ReLiC, CLERC...)
polarized e+e- Recycling Linear Collider with high-energy, high luminosity reach (ReLiC)
1.5 GHz SRF, Q > 1011 , 1.5 K
After IP, the beams are decelerated and weakly damped by wigglers (single pass). Then, accelerated again (ERLC, Ghost Collider)
IJCLab
Notes: DEFINITION
Using linear collider approach for IRs: flat, low emittance beams with reasonable vertical disruption
Recycling of the beam energy
Recycle and re-use collided electrons and positrons
Use damping rings to repair and polarize recycled beams for next collisions
Keep under control the beamstrahlung – collide mono-energetic beams
SUMMARY
• Proposal is at conceptual development stage
• Only major processes (beam-beam collisions, beamstrahlung, effect of beam separators were either simulated or scaled from other projects such as CERC etc.). No realistic cost estimate is generated.
• Power estimations may miss significant components – cooling of the tunnel, heat losses for LiHe transfer lines, etc.
• Main Accelerator challenges:
• 1.5 GHz SRF cavities with quality factor Q > 1011 at 1.5 K
• High-efficiency 1.5K LiHe refrigerators
• Reactive tuners to reduce power to suppressing microphonics
• Damping rings with very flat beams (εh/εv ~2,000-4,000)
• Damping rings with 10% energy acceptance
• 10-fold bunch compressor/decompressor at 10 GeV
• MHz rate injection/ejection kickers
• Vertical beam stabilization at the IPs
• High efficiency LiHe refrigeration systems
• Very high-Q SRF cavities
• Reactive tuners in SRF systems
• Damping rings
• MHz rated kickers

## Slide 33: Additional Upgrade Paths
Photon Collider
  complementary physics case, e.g. self-coupling in 𝛾𝛾 -> HH with different BSM behavior than e+e- / pp
  install in one of the IPs
  either classic way with optical lasers or XCC-like with X-ray lasers
Layout of the XCC photon collider

## Slide 34
The basic idea is – there are enough problems with a PWFA e- accelerator; e+ is even more difficult. Bypass this for e+e- collider by using conventional linac for e+.
For this to be attractive financially, conventional linac must be low energy => asymmetric energy machine.
This requirement led to (at least for us) unexpected directions – the more asymmetric the machine became, the better!
Additional Upgrade Paths
HALHF Status
Hybrid Asymmetric Linear Higgs Factory (HALHF)
Notes: Principal problems for old design:
“Turn-around” too small to retain required beam quality & scales badly with energy;
“Dual-Purpose” linac difficult to design and inflexible.

## Slide 35
Thanks for your attention
Notes: On behalf of ILC and CLIC collaborations

## Slide 36
Timeline for European Strategy Update 2026
We are here !!!
June 2024: appointment of Strategy Secretary, Strategy Secretariat and European Strategy Group (ESG) by CERN Council

## Slide 37
The crossing angle choice
The long ILC inter-bunch spacing of 554 ns (366 ns for upgrade luminosity), gives the possibility of having a large range of crossing angle configurations from large (20 mrad) to quasi head-on (2 mrad).
Larger crossing angle separate the incoming beam from spent beam, with no shared FF magnets. This separation facilitate the beam optics for the spent beam extraction line at the expense of some detector hermeticity in the forward region and the more complex tracking calibration procedures. In addition, larger crossing angles are more reliant on a Crab Cavity (CC) system, which rotates the bunches, in order to maximize their overlap and hence the luminosity.
Small crossing angles are generally favoured from the point of view of detector hermeticity and are less reliant on the CC system. However, the fact that the incoming and outgoing beams must to share the inner most magnets reduces significantly the design flexibility that has to deal with the reduction of the backgrounds and the minimisation of energy losses in the critical elements.

## Slide 38: ILC@CERN with 2 IPs (I)
  In the case of 2 IPs only baseline operation will be used (baseline 554 ns bunch separation / high-lumi 366 ns).
  Concerning the crossing angle, options including a “quasi-head on” (2 mrad) are very difficult to implement from the outgoing beams.
  Options for different longitudinal positions for the 2 IPs, indeed they the advantage of allowing less separation between the 2 detectors will have timing issues due to the different lengths for the BDSs, implementation will be complex (for instance, the length has to be half-integer of the DR length).
  In the same longitudinal position for the 2 IPs, an optimization of the 2 IPs cavern have to be performed to provide a minimum distance of 30 m between two detectors.
  The beam dumps have to be reconfigured and special attention has to be paid to the photon dump location. In particular, the photon dump location at the center (between two tilted beams) becomes a critical issue in the case of the undulator positron source.
The angle choice has not been determined, but in principle the 2 angles will be different to have physics complementarity between he two detectors. Preliminary design studies and CFS cost with 20 mrad between the MLs, and with 2 IPs with 14 / 26 mrad crossing angle with the two detectors in the same longitudinal position, are being performed but not detailed design of the optics is being planned. Discussions are ongoing to found an optimal solution; some issues have been identified:

## Slide 39: ILC@CERN with 2 IPs (II)
  The angle between the MLs has to be optimized to minimize the SR generated by the bending magnets of the BDS separation region, taking into account the 2 IPs crossing angle choice.
  The idea of having parallel MLs is also being considered and this option could be better for the future implementation of an upgrade by means of ERLs, nevertheless the impact of the increase of total length and the SR losses in the splitting section should be considered.
  The split location of the BDSs has to studied in detail, as well as the split magnet technology for the high-energy upgrades.
  Compatibility with a possible future gg collision mode have to be evaluated, with both optical lasers or FEL options. Options with XFEL lasers are optimal when the crossing angle is "quasi-head on" contrary to the optical ones.
  ....

## Slide 40
Cryomodule Unit - 9 m
(630 MeV/1 GeV )
ILC
Usable Tunnel Width - 11 m
C3 Usable Tunnel Width - 9.5 m
CLIC modules operate at 100 MeV/m and fit easily in ILC main linac tunnel, but additional drive beam turnaround one possible complication.
ILC provides a large tunnel suitable for multiple technologies
LCF @ CERN CFS: tunnels

## Slide 41: The LCF @ CERN and beyond
General considerations
Robust planning:
  costs (construction and operation), CFS design, environmental impact etc assessed in a consistent way between all projects proposed for CERN
  accelerator cost well known thanks to the 2024 update of the ILC costing, to a large extent based on new quotes from industry
Timing is important:
  current young researchers are key to both the HL-LHC program and the future Higgs factory
  prolonged uncertainly or delays in decision making discourage ECRs => loss of talent
  clear and timely transition from HL-LHC to next collider will provide long-term research opportunities
Higgs factory and intensified R&D:
  eventually, we need to explore the 10-TeV pCoM energy scale
  we don’t have an affordable technology today
  all routes (pp = HFM; 𝜇𝜇 = cooling; ee/𝛾𝛾 = PWA) need expensive R&D and demonstrators
  costs need to be shared globally, a staged and flexible Higgs factory aligns best with R&D needs

## Slide 42: Next Steps towards a LCF @ CERN
Short-term investment needed
project implementation: 6-year preparatory period
  ideally starting after conclusion of EPPSU in mid-2026
  split in two 3-year phases
  prior to construction start in 2032
Phase 1 (~35 MCHF + 180FTEy)
  in parallel to ILC Technology Network
  placement study at CERN, review with stakeholders (local region / host states / ..)
  design and technical studies to determine and confirm the LCF parameters
  moderate investment from CERN, could be pursued in even parallel to FCC
Phase 2 (~120 MCHF + 420 FTEy)
  only after decision to go ahead with LCF
  pre-series production
  engineering design
  more substancial investment by CERN
world-wide expertise in SCRF-based XFELs and ILC R&D => significant contributions from outside CERN?
in parallel: set-up detector collaborations, build on exiting concepts, but embrace new ideas
=> ready for construction start in 2032

## Slide 43: Strategic Considerations
Resources & competition
with ~8 BCHF, the LCF is affordable for CERN without major external contributions
  CERN council could decide for this project without a (potentially lengthy) period of international negociations
  fast & robust way forward
nevertheless excellent opportunities for additional contributions
  e.g. lumi-upgrade (2x for ~0.8 BCHF)
  contributions of more SCRF cryomodules to reach higher energies faster can be incorporated anytime - either “cash” - or in-kind (more attractive for local industry etc)
  but start of project independent of these under CERN council’s control
scientific flexibility
  should scientifc developments point to going to higher ECM faster - e.g. LHC discovery or competition at low energies - this can be done any time, depending on resources

## Slide 44: Conclusions
As submitted on March 31
we need a new e+e- collider to study the Higgs - now
a Linear Collider has decisive physics advantages: polarisation & high-energy reach
  required to do the full Higgs and Top program
  with sufficient redundancies and complementarities to truely enable discovery via precision measurements
  supports flexible upgrades with advanced accelerator technologies
a well-understood technology and a staged approach allows a fast start
a Higgs factory must not saturate our field - but stay affordable, in parallel to HL-LHC, SuperKEKB, smaller experiments - and R&D towards the 10-TeV pCoM scale
the EPPSU shall determine the next flagship collider project for CERN
LCVision team
  contributed the physics and technology case for Linear Colliders in general
  and proposed a Linear Collider Facility @ CERN as the next flagship project

## Slide 45: LCVision EPPSU documents
LC Physics Case & long-term vision
LCF @ CERN
C3
HALHF
10 TeV Wakefield
Technologies and upgrades
CLIC at CERN
Beyond Collider
ILC in Japan (IDT)
arxiv paper & EPPSU submission
EPPSU submission & back-up document
arxiv:2504.01434
arxiv:2503.24049
arxiv:2503.24168
arxiv:2503.23489
arxiv:2503.21857
arxiv:2503.20214
arxiv:2503.19880
arxiv:2503.19983
arxiv:2503.20829
arxiv:2504.XXX
https://cds.cern.ch/record/2927631
… and relation to other inputs