## Slide 1: Bringing Metrological Precision to Scientific Networks: Digital Solutions for Ultra-Stable Time and Frequency Transfer
Idrogen : Antoine Back*, Cédric Esnault*, Monique Taurigna*, Chafik Cheikali*, Christelle Soulet*, Cédric Viou**, Michel Lours, Paul-Eric Pottie, Daniel Charlet*
REFIMEVE : Etienne Cantin***, Christian Chardonnet***, Anne Amy-Klein***, Benjamin Pointard, Rodolphe Le Targat, Neelam, Philip Tuckey, Paul-Eric Pottie
*: IJCLAB (Paris-Saclay, Paris-Cité and CNRS)
**: ORN (OP-PSL, Uni. Orléans, and CNRS)
***: LPL (USPN and CNRS)

## Slide 2
Context - Motivations
  Basics on Fiber Links
The REFIMEVE network
Advancing the Electronics: The Idrogen Board
  Recent results at Observatoire de Radioastronomie de Nançay
Emerging Scientific and Technological Applications
  EU perspective for the European fiber network
Outlook
Contents

## Slide 3
Motivations for time and frequency dissemination
Tests of Special &
General Relativity
Definition & Variations in fundamental constants
Fundamental Scientific Applications
Sensing/Defense:
Positioning, Navigation and Timing
synthetic aperture
global imaging
Large instruments, array of detectors
astronomy, astro particle, geoscience
multi-messenger astronomy, seismology
Illustrations: courtesy N. Newbury, NIST
VLBI…
Earth Science and climate change
geodesy, chronometric leveling
10-18/cm
Dissemination of Time and Frequency from standards (atomic clocks, timescales)
for industry / society : Telecom and network synchronisation, smart grids, finance, manufacturing…
Timing+syntonisation:
ms-ns, 1e-11-1e-15
Traceability
Timing+syntonisation:
ns, 1e-13-1e-16
Resiliency
Timing+syntonisation:
  ns-ps, 1e-16
Comparisons
Timing+syntonistion:
  ps, 1e-18 and better!
Comparisons

## Slide 4
KM3Net
SKA
CTA
VLBI
Astronomy
Particle detectors
Super-K
see also :
T. E. Mehlstäubler et al., Atomic clocks for geodesy. Rep. Progress in Physics 81, 064401 (2018).
Y He et al., Optica, 5, 138–146 (2018).
see also :
C. Clivati et al., IEEE Trans. on UFFC 62, 1907–1912 (2015).
Scientific cases in astronomy and geodesy
PAON IV / Idrogen
Geodesy
Clocks comparisons

## Slide 5
  Phase fluctuations induce frequency fluctuations:
Doppler shift and Doppler canceller
Variable delays induce a Doppler shift.
Mainly white phase noise + white frequency noise (< 10 Hz).
Modulation index is defined as the peak-to-peak amplitude of phase variation. It can be >> 1 for long haul links.
Compensation system acts to make
In loop, the two waves are in phase, with an unknown phase offset.
Doppler shift:

## Slide 6
Optical frequency transfer : key elements
Unbalanced Michelson interferometer
Heterodyne detection: eliminates mutli-path
Fully bi-directional. A 2nd link transfers back the signal
Guided propagation: ensure paths reciprocity
Assumption : Forward noise = ½ Round-trip noise
→ corrects only reciprocal noise
Coherent regime if coherence length > 2L (need ultra-stable laser !)
Fundamental limits set at short term by the finite velocity of light in media
Local End
Noise correction
mirror
Optical fiber
(delay line)
laser
Photodiode
< propagation noise >
User
w
photonic device
splitter
𝜑round trip = 2𝜑Fiber
-𝜑fiber
splitter
Remote End
𝜑correction + 𝜑fiber = 0
Michelson
opto-electronic compensation
Shorter delay, larger bandwidth
Signal regeneration with a narrow laser (a few kHz at 1 Hz bandwidth, free running)
Local
end
Remote
end
Repeater
Station
N
Repeater
Station
N+1
Repeater
Station
N-1
Link
N-1
Link
N
Multi-segment approach
Repeater laser station (RLS) functionalities :
sends back signal to station N-1,
corrects the noise of next link N,
provides a user output
Multi-branches Laser Station (Hub station)
can correct the noise of several (~5) links
A second set-up on a second fiber transfers back the signal: « End-to-end » measurement, out of loop.
O. Lopez, et al.. OE 18, 16849–16857 (2010).
E.Cantin et al. New J. Phys. 23, 053027 (2021).

## Slide 7
Radio-frequency and time transfer by White Rabbit: key elements
Based on 1Gb/s ethernet communication
Layer-1 syntonization (SyncE)
  Local RF oscillators are phased locked with ~20-70 Hz bandwidth to a common RF frequency reference
  All nodes of the network are locked to the frequency of the System timing master
Precise Time Protocol is used to retrieve precise time stamps
FPGA technology to implement a precise phase/time measurement with 20 ps resolution single shot (~ every 50 ms).
Static link asymmetry can be compensated for.
N. Kaur doi: 10.1109/TUFFC.2021.3134163. (2022)
N. Kaur, phdthesis https://hal.archives-ouvertes.fr/tel-01909292
White Rabbit on 500-km uni-dir on spools
See D. Charlet’s talk Thursday, 11:40

## Slide 8
Coherent optical fiber links and white rabbit links
TW-CP : Two-Way Carrier Phase; IPPP : Precise Point Positioning with integer ambiguity resolution
see review: O. Lopez et al., CRAS, 16 (5), pp. 459-586 (2015) (2015)
CCTF task force at BIPM for the redefinition of the SI-s:
https://www.bipm.org/documents/20126/52354676/CCTF_2020_Task_force_Introduction_Finale.pdf/62bb4dc1-a662-a07e-dd9c-d9ed17829d70
optical clocks
μw clocks
GPS
GPS IPPP
TW-CP
Coherent Optical Links
Coherent optical links are the only technique to date to enable optical clocks comparisons at continental scale
Guided propagation:
  Low noise
  No interferences
  Low optical losses
  Excellent reciprocity
Major drawback
  Point to point
Fiber links: pro and contra
Goal for SI-s re-definition
White Rabbit

## Slide 9
Refimeve network map (2025)
4 international connections (DE, UK, IT; CERN)
  + Belgium-France cross-connection planned
Clocks @INRIM, PTB, NPL, and LTE connected.
REFIMEVE connects ~30 labs by 11/2025.
REFIMEVE connects 6 research infrastructures:
    LSM, CERN,SOLEIL (done)
    ESRF, IRAM, LOFAR (planned)
  Link with EPOS-FR, …
FIRST-TF (Research federation) acts for the scientific animation of the French users connected by the fiber network.
EURAMET: 5 EU projects to develop technology, + run optical clock comparisons,…
ORB
VSL

## Slide 10
4 links: {340,650,900,440} km x2 = 2x2330 km
>70% / 1/2 year (2022)
>90% uptime for several months
next objective: 90 % / year
Towards a highly available signal
Relative frequency fluctuations vs time (days)
1000 s / point

## Slide 11
10 optical clocks
6 countries
Fiber and Satellite links (GPS IPPP)
38 optical frequency ratios
Evaluation of the correlations
Clock comparisons: towards redefinition of the SI second
Coordinated international comparisons between optical clocks connected via fiber and satellite links
Robust optical clocks for international timescales (ROCIT)
https://empir.npl.co.uk/rocit/
T. Lindvall et al., Optica, 12 (6), p. 843‑852, juin 2025, doi: 10.1364/OPTICA.561754.

## Slide 12
Frequency Transfer and Time Transfer
Frequency transfer: delay fluctuation stabilisation
Time transfer : delays determination (both instrumental delays and propagation delay)
Precise sub-picosecond time transfer need a specific electronic development for exquisite instrumental delays stability and reproducibility
Illustration credits :
B. Liu, et al. doi: 10.3390/photonics9080522.
D. Chen, et al. doi: 10.3390/photonics9050293.

## Slide 13
Advancing the Electronics: The Idrogen Board
Design & development: IJCLab
  WR schematic from CERN improved
  PCB design compliant with EMC rules
  Micro Telecommunication Computing Architecture
  Crate or Stand-alone mode available
Firmware development: ORN + IJCLab
Clock expertise and measurements: LTE
Simplified and improved clock design
Components upgrade: FPGA, VCXO, PLLs, …
SFP+
QSFP+
AMC
RTM
FMC
USB
15 cm
~15 cm
Additional functions on daughter boards
FPGA Mezzanine Card (FMC) carrier board:
  ADC, DAC, Clock synthesis, ...
Front panel connectivity:
  Small Form-factor Pluggable (SFP+) 1/2.5 Gb/s
  Quad SFP+ (QSFP+) 40Gb/s
  Universal Serial Bus (USB)
Backplane connectivity:
  Advanced Mezzanine Cards (AMC)
    l Gb/s ethernet IPbus, PCIe 4x Gen3 and Gen4
    Intelligent Platform Management Bus, Clock & trigger lane
  Rear Transition Modules (RTM)
FPGA
VCXO.
See D. Charlet’s talk Thursday, 11:40

## Slide 14
High performance WR low jitter node :
  Accuracy < 20 ps
  rms time jitter < 1ps
High performance data acquisition system:
  PCI express > 25 Gb/s Ethernet > 20-40 Gb/s
Configurable output clock
Crate (µTCA) or stand alone use
Idrogen: best in class WR end-node
Integration bandwidth : 100 Hz- 1 MHz
Main limitations :
PLL bandwidth
oscillator frequency ~125 MHz
Noise floor of some components

## Slide 15
Measurement set-up at LTE

## Slide 16
Idrogen : longterm performances
+30 days continuous acquisition
Time stability :
Modified Allan deviation < 1e-17 @ 3 days measurement time

## Slide 17
Acquisition and signal generation with extension boards
Acquisition main features:
  2 channels, 14b, 500MSPS, JESD204B, 2GHz analog bandwidth
Signal generation main features:
  clocked by idrogen3. > accuracy of the WR
  4 outputs 10KHz to 2.75GHz
FMC board

## Slide 18
Nançay, 15/10/2025
Crédits image : Olivier Perdereau (IJCLAB).
idrogen
First synchronized acquisition at two radio antenna
Première expérience d’observation radio connectée en temps réel à la référence nationale UTC(OP).
PAON IV is a 4-antenna demonstrator at Observatoire de Radioastronomie de Nançay.
+300 km optical link connect ORN to OP through a multiplexed fiber pair of RENATER network (REFIMEVE).
Idrogen system is disciplined via WR on UTC(OP).
An extension board of Idrogen (one per antenna) acquire syntonously and synchronously @ 1 Gb/s.
The picture shows the stable interference pattern around 1.4 GHz versus time.
Next step: additional daughter board for an ultra-precise time transfer (<50 fs) on stabilized optical carrier.

## Slide 19
Next technological development: White FOX
Goal : ultra-stable and accurate time transfer for multi-messenger astronomy (« time-domain astronomy »)
Target : < 30 fs resolution at 1 second measurement time
How:
  combine Idrogen as an ultra-precise time modem and the coherent optical frequency transfer technology
  No ethernet protocol, no share with data traffic
  Link bandwidth at the fundamental limits
  Optical phase modulation
  Optical demodulation
Technical choices
  Frequency carrier: 125 MHz —> ~1.25 GHz (cf. phase noise curves)
  Encoding time as a Barker code (the simplest)
Time delayed
TX Barker code
RX1 Barker code
RX2 Barker code
Prior demonstration on 50-km spools
F. Frank et al. , « A sub-ps stability time transfer method based on optical modems », (2018)
doi: 10.1109/TUFFC.2018.2833389.

## Slide 20
Next steps at Nançay: nenuFAR, LOFAR, PTA
1824 antennas :
  96 mini-arrays (MA) of 19 antennas each
  spread over ~ radius 1000 m.
ORN, participating to European Pulsar Timing Array (EPTA), is among the stringest end-user of the REFIMEVE network, as for frequency accuracy (~1e-16) and as for time accuracy (ns)

## Slide 21
EU fiber network
KM3Net
Virgo
The prospect of the fiber interconnection between major research infrastructures / observatories with time frequency references « in common view »
VLBI / LOFAR infrastructures
CERN is connected to REFIMEVE
KM3Net, EGO, Gran Sasso, subterranean laboratories
Efforts in EU to interconnect the national networks (cf. FOREST candidacy to ESFRI)
Connection Belgium and The Netherlands to be completed within next 2 years
WR deployment all over REFIMEVE happening now !
CERN
Gran Sasso
IRAM
Network size ~12,000 km

## Slide 22
Summary - take away message
Outlook
Fiber links can effectively disseminate time and frequency signals without degradation.
REFIMEVE is an optical fiber networks that connects major infrastructure, with very high up-time and show available signal over nationwide area.
Regular clock comparisons are operated with the European fiber network
Advanced electronic development enable precise timing with synchronous signal generation and signal acquisition
A first demonstration was recently made at ORN with PAON IV
Very precise timing can be bring within the next 5 - 10 years in Europe to major infrastructures: VLBI stations, LOFAR, KM3net and EGO.
Another hot topic: quantum sensor networks and multi-messenger astronomy
Not addressed here : projects are going on to investigate fiber network sensing.
Outlook

## Slide 23
Fundings
LOFIC
  JRP:
NEAT FT, OFTEN, WRiTE, TIFOON
ITOC, ROCIT (clock comparisons)
CLONETS
CLONETS-DS
EU Research infrastructure
LIOM, REMIF, REFIMEVE+, T-REFIMEVE, FIRST-FT
INSU
GRAM
  H2020, Horizon Europe:
ICOF, SENSEI

## Slide 24
Thank you for your attention !