## Slide 1
Caterina Bloise / INFN Frascati, Maxim Titov / CEA Saclay
on behalf of the LDG WG
10th French-Ukrainian Workshop,
Orsay, France June 10-12, 2025
Sustainability Assessment of Future Accelerators:
LDG WG Report
ESPPU Input #162 & arXiv: 2504.01235
Full report will be available in June 2025:
https://ldg.web.cern.ch/working-groups/sustainability-assessment-of-accelerators

## Slide 2
Sustainability Working Group (added to 5 LDG Expert Panels) since January 2024
CERN Council has mandated the Laboratory Directors Group (LDG) to define and maintain a prioritized accelerator R&D roadmap towards future large-scale facilities for particle physics.
https://cds.cern.ch/record/2800190/files/146-138-PB.pdf

## Slide 3
Walib Kaabi - PERLE, EU-iSAS
Mats Lindroos - ESS (deceased May 2, 2024)
Roberto Losito - CERN Sust. Panel
Ben Shepherd - STFC Sust. Task Force
Andrea Klumpp - DESY Sust. Panel, EU-iFAST
Hannah Wakeling - ISIS-II Neutron & Muon Source
Patrick Koppenburg - NIKHEF Sust. Panel
Johannes Gutleber - FCC
Yuhui Li - CePC
Benno List - ILC
Emilio Nanni - ICFA Sust. Panel & C3
Vladimir Shiltsev - LHeC
Steinar Stapnes - CLIC & Muon collider
Caterina Bloise - Co-Chair
Maxim Titov - Co-Chair, EU-EAJADE
in the Editorial Board also
Enrico Cennini (CERN), Luisa Ulrice (CERN).
Beatrice Mandelli (CERN), Niko Neufeld (CERN)
Thomas Schoerner (DESY)
Panel consisting of 15 members with technical expertize in evaluation of accelerator sustainability and future collider project representatives
Ensuring broad
community representation:
Sustainability Lab. Panels established at CERN, DESY, ESS, NIKHEF, STFC
ICFA Sustainability Panel
EU- Horizon Programs
Future accelerator projects: FCC, ILC, CePC, CLIC/Muon, LHeC, C3
Invited experts on specific topics
LDG Sustainability WG Mandate and Composition
Development of guidelines and a minimum set of key Indicators for the sustainability assessment of future accelerators

## Slide 4
LDG Sustainability Working Group Report
Framework for Sustainability Assessment of Future Accelerators (100 pages):
Landscape of comprehensive sustainability analysis (best practices to be adopted by Ri)
Basis of LCA - Status & recommendations for developing analysis of accelerator components and systems
Environmental impact of Large RIs during construction, operation, and decommission phases
Mitigation and Compensation Measures
- Targets particle physics projects, relevant for
other research infrastructures
- Promotes transparent, open discussions within research communities
- To adequately inform management, authorities, society - Establishing “Guidelines” is the responsibility of each RI, to long-detailed national and local legislations
Not all of sustainability topics can be addressed in details in 2025 report
A homogeneous evaluations of all issues deserves a future strategy to be pursued

## Slide 5
IV. Building Strategic Accountability: Sustainability Assessment
Report provides a reference framework to enable coherent flux of information
- Focused on future colliders - much of the work is relevant for current and future RIs
- Summary of current best practices, obligations, and standards
Sustainability assessment is complex
- Criteria to be tuned to the maturity of the project
- Separately developed for scientists, policy- makers, and society
Economists and environmental scientists contributed a range of work
- Used in setting guidelines, standards and legislation
EU Policies
- Global Reporting Initiative
- European Sustainability Reporting Standards
- European Union Eco-Management and Audit Scheme (EMAS)
- EC Economic Appraisal Vademecum
National Guidelines (France, Germany, Swiss, …)
Carbon Footprint Accounting and Reporting
- Shadow Carbon Cost
ESFRI Roadmap 2026 will put significant focus on the financial sustainability of the RI ecosystem, while introducing the new dimension of ‘environmental considerations’ to foster environmental sustainability”.

## Slide 6
Setting Sustainability Basis (Society, Economy, Environment)
Comprehensive sustainability assessment of particle accelerator-based research infrastructures – as recommended by OECD – is based on quantitative Cost-Benefit Analysis (CBA)
List of elements evaluated in a comprehensive cost-benefit analysis of research infrastructures.
The EU-funded project RI-PATHS has developed a toolkit federating research infrastructures across various domains, including particle accelerator facilities, such as ALBA, CERN and DESY
Future projects are encouraged to carry out a comprehensive charting of the impact pathway potentials to develop sustainability-enabling plans:
Fundamental Physics Knowledge
Sustainability through education and training
Sustainability through engagement of international research communities and collaborations
Sustainability through industrial spillovers.
Sustainability through open information and computing technologies
Sustainability through cultural goods
Sustainability through positive environmental externalities
Innovation and R&D

## Slide 7
Social - Economic Benefits of HEP accelerator-based Research Infrastructures: in relation to the UN Sustainability Development Goals (environment, economy, society)
  SDG Reference Matrix from UN (2024)
    Fundamental Physics Knoweledge, Accelerator and Detector R&D
    Economic Growth (regional, international, developing countries)
    Education, Innovation, International Cooperation, Cultural Exchange
Social – Economic Benefit Analysis
Comprehensive sustainability assessment based on quantitative Cost-Benefit Analysis: state-of-the-art economics knowledge that integrates total costs, negative environmental externalities, industrial, social and environmental benefits
Benefits and positive externalities not fully captured: RIs should “Develop internal expertise for impact assessment” and “define relevant impact dimensions in a proactive way”
Reference for the integrated model FCC

## Slide 8
:
  LCA Goal and Scopes Definition
  - project stages: design, construction, operation, decommissioning
  - functional units: accelerator, supporting infrastructures, cryogenic systems, detector, computing
  - boundaries: Cradle-to-gate, Cradle-to-grave
  LCA Methodology
    - Impact Categories (Midpoint vs Endpoint)
    - Impact of Emission on Climate Change: GWP100
    - Beyond GWP : ReCiPe2016, ILCD2011, CML-IA2012
  LCA Inventory Analysis
  - infrastructure, materials, energy, production process
    Construction Phase
    Operation Phase
    Decommissioning
  LCA Assessment and
  Interpretation
  - environmental impact,
  - methodology, specific software, databases,
  - evaluation of uncertainties
IV. Life-Cycle Assessment (LCA) Methodology
LCA Targets:
Understand in each area what are the largest sources
What to focus on and not focus on
Start to look at mitigation strategies
Develop tools to do this type of analysis for the future
Quantifies environmental impact (ISO14040 standard)

## Slide 10
V. Environmental Impacts of Large RI’s Facilities (I)
The construction phase (stages A1 to A5 of the LCIA process), covers the environmental impact up to the start of accelerator operation, considering all processes necessary to build CE infrastructure and components, from raw material supply (stage A1), transport (A2) to manufacturing (A3), as well as the assembly, from transport (A4) to installation at the site (A5).
Civil engineering works: LCA for accelerator infrastructure (e.g. tunnels, caverns) & Civil engineering (LCA A1-A5), excavated material and transport away from construction site
 civil engineerings works give a large contribution. but market is the most advanced in producing new materials with net- zero cement (at an extra cost), we might see a fast change in the next 5-10 years
Accelerator construction: early assessment of areas with the largest emission, beam line shielding, steel girders and supporting structures, magnets, RF cavities, power supplies, …
 material manufacturing (e.g. high-purity Ni, permanent magnet alloys) - construction of accelerators will always rely on mining and mineral processing that is a hard-to-abate activity (independently of the energy used…)

## Slide 11
Reporting in the common format proposed by the LDG sustainability working group
Accelerator operation: electricity consumption, power for operation (air conditioning, waster cooling, cryogenic plants, RF and klystrons, magnets)
Particle detectors/computing: impact of gas emissions in detectors, optimization of power consumption/ environmental impact of computing
V. Environmental Impacts of Large RI’s Facilities (II)
The operation phase (stages B1 to B7) covers the environmental impact of the operational lifetime of an accelerator project: necessary to operate (B1) and maintain (B2) the accelerator and experiments, including repairs (B3), replacement of components (B4) and refurbishments (B5). of particular interest are the impact of energy (B6) and water (B7) required for operation
Assessment of future accelerator projects concentrate frequently on electricity consumption, assuming that it will constitute the dominant impact, at least in terms of GHG emissions:  valid assuming that future Ris overcome the current situation, where direct emissions from particle detectors & cooling plants are the most abundant
 Environmental impacts from maintenance (B2), repair (B3), and replacement (B4) have been rarely considered inaccelerator LCAs.
Decommissioning: (stages C1 to C4 of the LCIA process) radioactive waste, land reuse

## Slide 12
V. Data on Future Accelerator Projects
Preliminary – numbers are not final and not for distribution (sort of confidential)
Key parameters relevant for GHG emissions in construction and operation phases of future collider projects, as discussed and agreed by the Sustainability WG.
Concurrent reporting of methods, assumptions and simplifications adopted to evaluate carbon footprint is needed to clarify the boundaries of the assessment.
Available for ILC in Japan  scaled / adapted for an LCF at CERN
Tunnels: emission factors for tunnels in Japan and CLIC tunnel in Geneva almost identical – keep • Scale up main linac and damping ring componentry for longer main linac and 3rd damping ring

## Slide 13
V. Data on Future Accelerator Projects
Preliminary – numbers are not final and not for distribution (sort of confidential)
Key parameters relevant for GHG emissions in construction and operation phases of future collider projects, as discussed and agreed by the Sustainability WG.
Concurrent reporting of methods, assumptions and simplifications adopted to evaluate carbon footprint is needed to clarify the boundaries of the assessment.

## Slide 14
LC Example: Towards Carbon Accounting with LCA
S. Stapnes
CLIC example,

## Slide 15
Open Questions: Regional versus Globally Averaged Impacts
Carbon intensity of electricity production varies enormously across regions &countries
 reference values for assumed CO2 intensity of electricity for relevant regions/labs
Carbon intensity of materials also varies
  Different local standards
  Different geology, primary minerals, concentrations
  Different carbon intensity for local energy, esp. electricity (-> copper, niobium)
Civil construction: steel and cement mostly from local sources, adhere to local codes
Result of LCA depends heavily on
  Source of used materials
  Construction and operation site
  LCA Method: use local values or global averages
Should we evaluate impacts using site-specific or globally averaged impact values?  or use general LCA database and move to more local information as the project matures (for materials CO2 content) ?
IEA (2022), World Energy Outlook 2022, IEA, Paris https://www.iea.org/reports/world-energy-outlook-2022,
License: CC BY 4.0 (report); CC BY NC SA 4.0 (Annex A)
https://ourworldindata.org/grapher/carbon-intensity-electricity

## Slide 16
V. Mitigation and Compensation Strategies (I)
RI Design with Sustainability as a Goal  optimization of large civil engineerings works & better/greener materials:
- establishing performance oriented requirements (architecture and design optimized from construction, operation and maintainace perspectives)
- optimizing tunnel shape and evacuation methods
- detailed geological assessment
- use of precast concrete segments, fiber reinforced concrete
Responsible Procurement Policy  based on the international standard ISO 20400:2017
- balancing of the initial, purchasing cost with total lifecycle cost (maintenance, operation, disposal) - environmental impact against a given set of environmental objectives (reduction of CO2 emissions, minimization of radiological impact) - social responsibility (e.g. extraction of raw materials)
Sustainable operational concepts  power purchase agreements (PPA) & dynamic operation
- portfolio of supply contracts or PPA constitutes a strategic choice to foster transition to renewables and reduce the GWP impact of accelerator-based RiI’s  pooling suppliers in a sufficiently large procurement action / establishing a dedicated energy supply contract
Heat Recovery and Supply
- comprehensive cost-benefit assessment is needed to understand if heat recovery is viable for a specific project and to develop the most suited heat recovery and supply scenario. The LCA approach can be integrated in this analysis to better quantify negative externalities

## Slide 17
Energy Recovery Concepts
- demonstrate the full potentiality of ERL’s (PERLE, LHeC, …)
Investment in R&D in Green Technologies:
- improve the efficiency of the RF systems (vacuum electron devices & solid state amplifiers)
- design advanced permanent magnets
- use high-temperature superconductors (HTS - !) in high-field magnets
- development of of innovative solutions to contain the energy demand of future accelerators
(iFAST, iSAS, EAJADE, RF2.0, …)
Nature-Based Interventions for Carbon Removal  also termed ‘Nature-based climate
solutions’ (NbCS) - “conservation, restoration and improved management strategies (pathways) in natural and working ecosystems with the primary motivation to mitigate GHG emissions
- decreasing GHG emissions related to deforestation and land use - capturing and storing CO2 from the atmosphere - enhancing the resilience of ecosystems
V. Mitigation and Compensation Strategies (II)
J. Gutleber, FCC Renewable Energy Supply Feasibility Study,
https://zenodo.org/records/10023947
“Green ILC Concept”
SOME
EXAMPLES:

## Slide 18
Fluctuating Energy Sources: PPA & Running on Renewables
Switch to carbon-neutral energy sources &enabling framework for renewables: power purchase agreement (PPA) - long-term contract for the electricity supply (~ 20 years)
A. Sunesson
Study by Fraunhofer institute (2018) considered running CLIC (380 GeV) for a total power of 200 MW (in reality only 110 MW needed) on renewables and participating in demand side flexibility:
CLIC’s total energy consumption could be generated from renewables (using local solar plant of 330 MWp a local wind farm of 220 MWp), but still needs public grid for continuity
Operating modes with power modulation were investigated
https://edms.cern.ch/document/2065162/1
Power
purchase
agreement
full collider operation at times of high grid production
reduced operation or standby modes with fast L recovery otherwise
Linear
Colliders
R. Losito

## Slide 19
Decarbonisation of Large Research Infrastructures
Funding and financing landscapes are changing rapidly in Europe and beyond, which will require addressing carbon explicitly in the business case for large research infrastructure
Mitigation of the transition risks for RI’s:
this can lead to increase of costs, reduced funding – maybe one of the future discussion topics within the WG – start developing thinking …
H. Pantelidou / ARUP
Construction of accelerator large-scale RI’s has to face decarbonisation path, with the associated increase of the shadow Carbon cost over the years

## Slide 20
Identifying relevant initiatives to complement decarbonisation: - prioritising nature-based interventions for NEW RI’s: integration in local environment as part of the asset management (e.g. CERN. Green ILC concept)
- potential to contribute towards carbon removal through environmental enhancement
Prioritising Nature-Based Interventions (ILC Example)
Asurnipal CC-BY-SA-4.0
For ILC: renewable energy available (Tohoku Electric Power) in local grid at ~23% level, need 0.5-1 % for ILC. Additionally considers increased CO2 absorption to be fully neutral

## Slide 21
LDG WG Report: (Some) Strategic Recommendations
Perform a cost-benefit analysis (becomes more & more important these days):
i) guidelines and evaluation models exist + are being developed; ii) the format depends on the size, expected impact and location of the RI (national framework), requirement from funding agencies etc…; iii) sustainability enablers: fundamental physics, education, technological innovation, industrial spillover, cultural activities
Environmental sustainability assessment is complex, especially as the criteria must be tuned to the maturity of the project and differently developed for researchers, for management, and for society:
 Perform LCAs at each project stage (proposal, CDR, TDR) to understand the most critical elements in the design & to provide input for technological choices reducing the environmental impact  Coordinated approach to develop a common database for accelerator materials and components is strategic to establish a framework for project accountability
Adoption of Responsible Procurement Policy (ISO20400) is a key to reduce an impact
Implementation of Energy management plans (ISO 50001 standards):
i) development of a policy for the efficient use of energy, ii) identification of targets & objectives, Iii) implementation of procedures and systems to gather data on energy consumption, iv) planning of review processes to enable further improvement in the energy management
Investment in R&D for "green" accelerator technologies:
i) greener materials and procedures for construction: superconductivity , permanent magnets
efficient cryoplants …

## Slide 22
Summary and Outlook
Funding landscape are changing rapidly in Europe and beyond, which will require addressing sustainability and GWP potential for the future large-scale research infrastructures
Sustainability assessment for future large-scale accelerator infrastructures is quite complex:  assessment criteria needs to be properly tuned to the maturity of the project (stage)  differently developed for Researchers, Management and Society
The LDG Sustainability WG report is close to final, the bulk of issues elaborated pertain to:
- socio-economic benefits of accelerators-based reaserch infrastructures
- basis of sustainability assessment
- methodology and reporting of LCA for future HEP accelerators
- evaluation of Greenhouse gas (GHG) emissions in construction, operation, decommissioning
- mitigation and compensation strategies
Input to the European Strategy process submitted [arXiv:2504.01235]
Complete WG report will be published in June 2025

## Slide 23
BACK-UP SLIDES

## Slide 24
Mandate / Charge of Sustainability LDG Working Group
Definition of key indicators to be reported
Possible examples: - Peak / instantaneous lifetime- & specific (per luminosity) energy consumption
- Lifetime and specific Global Warming Potential (GWP), including construction
- Include margins of uncertainty and possibly an assessment of the potential for improvement
Definition of methodology & assumptions to be applied for transparent determination of key figures across proposals.
- The maturity of a proposal should be determined, for example, at early concept phase, CDR, TDR levels
Identification of additional high level environmental impacts that may be relevant for all or specific collider proposals
Also, VERY IMPORTANT - impact on society and public appreciation of the WG report:
HEP benefits and decarbonization path for the future large – scale accelerator RI’s

## Slide 25
Some Other (More Technical) Objectives
• Treatment of future carbon intensity of electricity and materials:
- what scenarios should be assumed?
• Assessing the potential for dynamic operation of the various facilities:
- i.e. the ability to adapt to a fluctuating energy supply in a grid fed by renewables. This may include standby mode power consumption, recovery time to full luminosity and fraction of integrated luminosity per year preserved in a dynamic operation scenario.
• Treatment of regional vs global parameters: - how to treat differences e.g. in carbon intensity between different host countries?
• Carbon intensity / lifecycle inventory (LCI) studies of materials specific to the
accelerator projects: high-purity niobium, permanent magnet alloys etc.
• How to interface with open-source LCI databases and LCA tools to potentially
ease/automate the assessment for future research infrastructures
• How the recommendations for colliders can be extended to other scientific /endeavours related to HEP
• How HEP labs represented in the LDG can share/build up expertise jointly
LDG WG may comment on other aspects if deemed appropriate, for example:

## Slide 26
Example: ILC & CLIC LCA Studies
Reduction potential: 40% reduction through use of low-CO2 materials (steel, concrete) and reduction of tunnel wall thickness)
CO2-eq from underground civil engineering and electricity for operation
CERN commissioned a study with ARUP to perform a Lifecycle Assessment for the CLIC and ILC civil infrastructure (tunnels, shafts, caverns)
ARUP report:
https://edms.cern.ch/document/2917948/1
Study provided results on greenhouse gas emissions from civil engineering construction:
  - ILC/CLIC Reduction potential (40%) from optimized design & use of lower carbon material
  - FCC LCA shows similar reduction potential (~50%)
  for civil engineering footprint
New LCA study on ILC/CLIC accelerator construction is being finalized:
- Quantify LCA impact of the full project (data inventory for ILC CLIC accelerator & detector)

## Slide 27
ZEPTO: Electromagnet Operation vs. Manufacturing Footprint
Novel (Efficient) Accelerator Technologies
Efficient RF Power Sources (klystrons)
Improving the key technology
for energy efficiency:
High gradient and Q0 cavities, operation at higher T
High efficiency RF sources (klystrons)
Permanent magnets
State-of-the-art surface treatment of bulk Nb: baking/annealing/doping, plasma processing (possibly reducing aggressive chemicals, required for electropolishing)
R&D into replacement of bulk niobium cavities with Nb or Nb3Sn coated copper (beyond bulk Nb – thin-film SRF): reduce Nb consumption, increase performance, higher T operation
https://indico.cern.ch/event/1138197/contributions/4821294/attachments/2474897/4246880/HE_WS_2022_Syratchev.pdf
Technology R&D for SRF cavities:
Major progress during past 10 years:
B. Shepherd

## Slide 28
R. Losito
Future Colliders: Running on Renewables
Two factors provide uncertainty today in a scenario fully based on renewables:
  Lack of one or more efficient technology to store energy in order to provide a sufficiently stable baseload  adapt to fluctuating power supply will remain a concern
  Lack of capacity and of the possibility to reserve capacity to move energy across borders
FCC-ee: has warm magnets but a large SRF system with stable power required for cryogenics:
- Large oscillations among operational modes makes it difficult to manage the excess energy with the legal framework of today.
- Energy required in stand-by ~25% of energy during beam operation.
There will be no future large-scale collider project without an energy management component:
fluctuating sustainable energy - energy management / dynamic operation  use surplus energy for RIs
CERN
Energy
Use in
2017
Modulate power according to availability (price)