## Slide 1: Quenching factor measurements for NEWS-G
By
Neha Panchal
Queen’s University, Canada

## Slide 2: NEWS-G
NEWS-G experiment searches for Light Dark Matter
Uses SPCs as detector: Metallic vessel filled with a noble gas mixture, with a single high voltage anode at center
Low mass target atoms increases sensitivity to low-mass dark matter
Low electronic noise and Townsend avalanche provides large gain
Single ionization detection threshold!

## Slide 3: Quenching factor
Dark matter sensitivity: Very important to know actual nuclear energy spectra
As nuclear recoil and an electronic recoil of same energy do not produce same amount of primary ionization
Definition
Notes: The quenching factor is the ratio of energy deposited in the electronic channel and nuclear channel

## Slide 4: Quenching factor measurements so far
Quenching factor measurements at TUNL (Duke tandem facility)
10 MV tandem accelerator
Neutron energy En = 545 20 keV
Gas mixture: Neon + CH4 (97:3) @ 2 bar
The nuclear recoil energies covered were 0.34 to 10 keVnr
Marie et al.
Phys. Rev. D. Vol. 105, No. 5, 052004 (2022)

## Slide 5: Quenching factor measurements so far
Quenching factor measurements at TUNL (Duke tandem facility)
10 MV tandem accelerator
Neutron energy En = 545 20 keV
Gas mixture: Neon + CH4 (97:3) @ 2 bar
The nuclear recoil energies covered were 0.34 to 10 keVnr
Marie et al.
Phys. Rev. D. Vol. 105, No. 5, 052004 (2022)
Backing detectors sensitivity low <200keV

## Slide 6: University of Montreal (UdM) facility
Wonderful facility just next door!
It is facility which can be used for any institution in Canada
Convenient for us to just drive to Montreal.

## Slide 7: UdM Facility: Accelerator Hall
Pelletron accelerator
Bending magnets
Bending magnets

## Slide 8: Facility: Target Room
Huge facility
7 beam lines

## Slide 9: UdM plans: TUNL vs Montreal
51V(p,n) has a large number of near threshold resonances
Minimum measurable recoil momentum ~6 times lower at Montreal
Better gamma background rejection is obtained by B-10 capture at Montreal

## Slide 10: UdM facility
The only problem was the lack of backing detector
Group at UdM is working on a B-loaded scintillator as backing detector

## Slide 11: New Backing Detector
The Backing Detector is an annulus structure
Provides better angular coverage
Based on n-capture on Li
Detection efficiency 27% at 2keV
Mean neutron capture time 17usec

## Slide 12: New backing detector (at Queen’s Uni)
  It is a layered detector with scintillator sandwiched between HDPE and Acrylic
  The neutrons are slowed in the HDPE and then captured in Li
  n-capture produces alpha and triton; scintillation light with ZnS
  The scintillation light is totally internally reflected in the WLS fibers (got it for free)
  Read out by PMTs (leftovers from other experiment)

## Slide 13: Fully assembled detector

## Slide 14: Amplitude Spectra for gammas

## Slide 15: Amplitude Spectra for neutrons

## Slide 16: Tests at UdM (1st Campaign)

## Slide 17: Beam characteristics (1st Campaign)
Lower energy neutrons
  aiming for En = 147 keV
  Ne (n,total) cross section has a resonance at 147 keV
Target LiF
Expecting 200 neutrons per second
Size of the beam 1 inch

## Slide 18: UdM control room

## Slide 19: Results (1st Campaign)

## Slide 20: Tests at UdM (2nd Campaign)
30cm
40 cm
52.5 cm
57.5 cm
280
380
740

## Slide 21: Gamma background from LiF target
19F (p,𝛂𝛄) 16O
ddoi:10.1016/j.nimb.2006.03.089oi:10.1016/j.nimb.2006.03.

## Slide 22: Thank you
Saint Joseph’s Oratory of Mount Royal