## Slide 1: Transverse Beam Dynamics
Julien Michaud
Accelerator physicist at IJCLab, Orsay (Paris)
jmichaud@ijclab.in2p3.fr

## Slide 2: Particles dynamics specificity
Particles dynamics in an accelerator is usually treated in 2 specific formalisms :
  Transverse beam dynamics
    Associated velocities are relatively small
    Beam visible « shape »
    Beam guidance
    Necessary to avoid losses in the walls
  Longitudinal beam dynamics
    Very high velocities
    Acceleration
First course
Second course

## Slide 3: First course : content
  Charged particle in electromagnetic field
    Around Lorentz equation :
  Guided and focalization magnets : dipoles, quadrupoles, multi-poles
  General development of magnetic field around the reference trajectory:
  The magnetic field equation :
  Particles motion around the reference trajectory :
  Beam envelop and emittance

## Slide 4: References
  CERN accelerator School: http://cas.web.cern.ch/cas
  CERN Joint Universities Accelerator School (JUAS) : https://indico.cern.ch/event/356897/contributions, https://indico.cern.ch/event/286275/contributions
  K.L. Brown, D.C. Carey, Ch. Iselin and F. Rothacker, Transport, a computer program for designing charged beam transport systems, CERN 80-04
  F. Dupont, Cours élémentaire sur les transports de faisceau et les accélérateurs de particules, janvier 1988
  Bernhard Holzer, CERN-LHC, Introduction to accelerator Physics
  Marc Muñoz, CELLS-ALBA, Introduction to charged particle optics, Jan 2010
  Stanley Humphries, Principles of Charged Particle Acceleration, Wiley-Interscience, 1986
  A.P. Banford, The Transport of Charged Particle Beams, Spon, 1966
  http://bc1.lbl.gov/CBP_pages/educational/WoB/home.htm
  P.J. Bryant, A Brief History and review of accelerators, CERN, Geneva, Switzerland
  E. Baron, Panorama des accélérateurs et de leurs utilisations, HAL Id: cel-0012288
  A. R. Steere, A Timeline of Major Particle Accelerators, Michigan State University, Department of Physics and Astronomy, 2005
  M. Sands, The Physics of Electron Storage Rings, an Introduction, SLAC-121, UC-28 (ACC), 1970

## Slide 5: I – Charged particles in electromagnetic fields
First let us define some important values :
Einstein's mass-energy
  With: particle mass
  speed of light
  Typical masses : 511keV for e-
  938.3MeV for protons
Total energy
  With:
Kinetic energy
  For a rest particle :
  For a non relativist particle :
  For a ultra-relativist particle (close to speed light) :
  Momentum :
  For , , we have :
  Therefore :

## Slide 6: I – Charged particles in electromagnetic fields
  Lorentz force
  The motion of a charged particle in a electro-magnetic field is given by:
                F : lorentz force in Newton
                p : momentum in kg.m/s
                q : particle charge (±Ze) in Coulomb
                E, B : electric and magnetic induction (resp. V/m and T)
                Remark : B is the magnetic induction,
                is the magnetic field (A/m)
                is the permeability of the medium (the degree of magnetization of a material in response to a magnetic field) in henries per meter (). More explanation in the chapter 2.
B
v
z
x
y
q<0
E

## Slide 7: I – Charged particles in electromagnetic fields
  No acceleration with magnetic fields !!
  To accelerate or increase the particle energy:
  Only electric field is useful
  If , there is no acceleration
  There is acceleration only if //
v
z
x
q<0
E
  Energy gain in a static electric field is :
  with the applied potential in MV
Important remark : variation of energy in EM fields :
An eV is the energy gained by an electron under 1V of potential difference

## Slide 8: I – Charged particles in electromagnetic fields
  Example :
  Considering an Electron () and a Proton () at
  We apply a accelerating potential of 10MV
  For both particles, energy gain is 10MeV
  The speed gain will be:
  For Electron : and
  For Protons : 07 and
  Accelerator and structures must be design according to particle characteristics

## Slide 9: I – Charged particles in electromagnetic fields
x
y
z
a
0
q>0
  Particle motion in a transverse electric field :
, with : , , at :
We have : , therefore : , then
With : and , then
Particle trajectory is parabolic :

## Slide 10: I – Charged particles in electromagnetic fields
x
y
z
a
0
q>0
  Particle motion in a transverse magnetic field :
  , with : ,
With : , then
Solution is :
At :
We can verify that velocity is constant :
Finally :
  with

## Slide 11: I – Charged particles in electromagnetic fields
  Particle motion in a transverse magnetic field is a circle
  With radius centered in :
  The cyclotron frequency is
  The revolution period is then
  The magnetic rigidity is :
  Numerically :
  In the same way, we speak also about the electric rigidity of the beam with :
  Example : at 95MeV/u :
  at 60keV :
  Protons at LHC : 7TeV

## Slide 12: Parenthesis : mass separation, spectrometers
(Non-relativistic approx.)
No mass dependance on electric fields !
Particle mass separators (or spectrometers) need a magnetic field !

## Slide 13: I – Charged particles in electromagnetic fields
Maxwell Equations :
Divergence of the electric field equals charge density divided by :
Divergence of the magnetic field is zero :
Curl () of the electric field is minus the rate of change of the magnetic field :
Curl of the magnetic field equals times current density , plus the rate of change of electric field divided by :
In a more general approach, electric and magnetic fields are described by the Maxwell equations

## Slide 14: I – Guiding and focalizing magnets : dipoles, quadrupoles and multipoles
  Generalities
  In beam optic, we apply a analogy with the geometrical optic where light beams are deflected by prisms and focus by using focusing or defocusing lenses.
  Same approach is applied in corpuscular optic.
  Optic structures are designed in order to induce bending and focalization of the charged particles.
  Bending and focalization can be separated or combined.
  Systems with electric and/or magnetic fields around a central trajectory are realized.
  Systems ensure the transverse dimensions of the beam (transverse = orthogonal plane of the beam direction)

## Slide 15
  From Lorentz equation, we can deduce :
Use of magnetic and electric fields :
  Acceleration is only possible with electric fields
  Bending/manipulations can be done with both electric or magnetic fields
Q : In which case do we use electric or magnetic fields for bending ?
  Answer :
  Magnetic fields at high energy (high )
  Electric fields at low energy (low )
  In any case, feasibility and cost have to be taken into account
Ex : A Tin beam 122Sn50, 1+ of energy 60keV has a magnetic rigidity of 0.3894Tm, electrostatic is more interesting. For 1GeV protons, Brho=5.65838Tm, magnetic is more interesting.
  In most circular accelerators, conventional electro-magnets (with iron) inducing magnetic fields to at room temperature are used.
  In protons or heavy ions machines at very high energy () like at LHC, we use superconducting magnets inducing fields up to 10T.
I – Guiding and focalizing magnets : dipoles, quadrupoles and multipoles

## Slide 16: I – Guiding and focalizing magnets : dipoles
Magnetic optical element n°1 : the bending magnet, or dipole
Dipole, means a north and a south pole : 2 poles
It results a constant magnetic field ()
Used to guide the central trajectory of a beam
  Magnet dipole
  Bend with flat and parallel poles create a field uniform at the center in the gap
  Bend can be small (for e- beam at few 100 keV) or huge (15m at LHC for protons at 7TeV)
Iron yoke
Coil (I)
LHC Bending magnet
r=2804m, L=15m
N=1232
Br=23352.6Tm
B=8.33T
C-shape
H-shape
Window shape
  Structure of the yoke
  give the name of bends

## Slide 17: I – Guiding and focalizing magnets : dipoles
  Determination of the magnetic field is obtained by the application of the Ampère theorem at circuit surrounded the two excitation coils designed by conductors in which circulate a current .
  In the gap, induction is
  In the Iron, where is the vacuum permeability () and is the relative permeability of Iron
  Ampère theorem :
  With (continuity of the orthogonal part of ) and (outside saturation) :
  Ampère-turns is , for , , cost
  The gap of high .
  Length in Iron .
  Ex: LISE spectrometer at GANIL: for with ,

## Slide 18: I – Guiding and focalizing magnets : dipoles
At room temperature, is not linear due to circulation of in Iron.
Relative permeability of Iron is a function to ( when ).
Hysteresis curve
level depend to
Permeability dependence to induction for various steel types
Yoke which channeling the magnetic flux can be realized in massive Iron or by stack of bonded plates in order to reduce the Foucault currents produce by the B dependence to time (useful in synchrotron)
Ampere-turn are realized by the appropriated number of spires surrounded upper and lower pole of the bend. In the precedent case, we have conductors (Copper) are carrying by the maximum current to 850A (equivalent maximum magnetic rigidity of the beam with dipole radius to ).

## Slide 19: I – Guiding and focalizing magnets : dipoles
Building a bending magnet :
Specifications are fixed by beam dynamics : which beams ? Which deviation ? Which beam size ? …
ex.: , deviation angle , curvature radius , therefore , , extension of the good field zone
Magnetic study using calculation codes 2D (POISSON, OPERA2D), 3D (OPERA3D, ANSYS)
Optimization (shimming of the return yoke, coils)
Mechanical conception (CATIA…), detailed drawings
Call for tender; building in company of the system
Magnetic measurements (conformity)
On-site installation and alignments (by surveyors)
Yokes : 560kG of Iron
2 coils : 105kG of Copper
Spires

## Slide 20: I – Guiding and focalizing magnets : quadrupoles
Magnetic optical element n°2 : the focaization magnet, or quadrupole
Quadrupole, means a north, south, north and south poles : 4 poles
Magnetic field evolves linearly with distance to the center ()
Used to focus or defocus the beam envelop
  Equipotential :
  Field line :
  z
  Hyperbolic pole
  y
  x
Q : What is the effect of this quad on the beam ?

## Slide 21: I – Guiding and focalizing magnets : quadrupoles
Magnetic optical element n°2 : the focaization magnet, or quadrupole
Quadrupole, means a north, south, north and south poles : 4 poles
Magnetic field evolves linearly with distance to the center ()
Used to focus or defocus the beam envelop
  Equipotential :
  Field line :
  z
  Hyperbolic pole
  y
  x
  Using with in the .
  Horizontal component of the Lorentz force bring back particles in the
  Vertical component eject particles of the plan Oxz
  on
  on
  on
  on

## Slide 22: I – Guiding and focalizing magnets : quadrupoles
Electrostatic quadrupole :
  Q1 : where are the poles ?
  Q2 : what voltage sign on the poles ?
  z
  Hyperbolic pole
  y
  x

## Slide 23: I – Guiding and focalizing magnets : quadrupoles
  z
  Hyperbolic pole
  y
  x
  Quad is focusing in the horizontal plane and de-focusing in the vertical plane.
  If the quadrupole is rotated by 90° or if the polarities are inverted, the opposite effect is obtained.
  For mechanical and electromagnetic symmetry reasons :
  By( x, -y) = By(x,y)
  By( -x, y) = -By(x,y)
  Bx( x, -y) = -Bx(x,y)
  Bx( -x, y) = Bx(x,y)
  Or By even in y, odd in x
  Or Bx odd in y, even in x
  We can develop the transverse and magnetic field (see Taylor expansions) :
  Therefore at . A centered beam on the axis is not deflected.
Field increase linearly with distance to the center

## Slide 24: I – Guiding and focalizing magnets : quadrupoles
  Field gradient G as a function of Ampere-turns (the current) in the quadrupole coils is determined by using the Ampère theorem to .
  From 0 to 1 :
  From 1 to 2 : because
  From 2 to 0 : , therefore
  and the gradient with R the quadrupole radius.
  Particle travelling into a magnetic quadrupole of length at a distance from the central axis is deflected by :
  The quadrupole focal length is : with

## Slide 25: I – Guiding and focalizing magnets : dipoles, quadrupoles and multipoles
  Few examples :
  Calculation using Poisson code of the magnetic field in a warm quadrupole.
  Field lines
  Pole / Yoke
  Vacuum pile for the beam
  Summarize : HEBT quadrupoles at SPIRAL2 Caen :
  , , aperture radius
  4 coils to 25160A.turn.
  Yoke Iron weight : 750kg, 4 Coils Copper weight : 132kg.
  , (need water cooling)
  68 turns (Copper length 1.1m for One turn), water cooled along 75m circuit.
  690mm

## Slide 26: I – Guiding and focalizing magnets : multipoles
  Ex.: PS at CERN
  Bend with combined function
  Used in synchrotron with strong focusing
  Combination of deflection and focalization using hyperbolic poles
  Such bend can be considered like a quadrupole at a distance from the center.
  We can deduce and component of the field :
  Using the new reference to : and
  with

## Slide 27: I – Guiding and focalizing magnets : multipoles
Magnetic optical element n°3 : the sextupole
Sexupole, means 6 poles (alternate south and north)
Magnetic field evolves quadratically with distance to the center ()
Used to correct higher order effects (chromatic aberrations)
  N
  N
  N
  S
  S
  S
  Using Ampère-theorem, the turn-numbers are function to the force by :
  with R the sextuple aperture radius

## Slide 28: I – Guiding and focalizing magnets : multipoles
  According amplitudes of non linearity (effects on the beam), the compensation of these defects can justify the use of multipolar lenses. These lens create non linear fields at a given order.
  These elements correct induce aberrations.
  The much common lens use is the sextuple (or hexapoles).
  Multipolar lenses
  Strictly, expressions of the magnetic field components already seen are valid only close to the center of the gap in a bend. Higher order of the Taylor expansion of the field have been neglected and transverses position of particles were small.
  Therefore, it exist high order (non linear terms) terms due to finite dimensions of the pole surface :
  Extension of the poles in the transverse plane (section of hyperbole in quadrupole)
Plateau
Leakage field
  Finite length of bend which induce a leakage field

## Slide 29: I – Guiding and focalizing magnets : multipoles
A magnetic dipole, is meant to apply a… dipolar field on the beam
A perfect dipole would, but reality hits sometimes :
dipole
quadrupole
sextupole
(or hexapole)
Hecatonicosapentacontapole
octupole
Harmonic content of a magnetic dipole (for illustration)
Higher-order fields will affect the shape of the beam : this is called optical aberrations
Can be corrected with higher order multipole :
Example of a 48 poles electric multipole

## Slide 30: I – Guiding and focalizing magnets : dipoles, quadrupoles and multipoles
Hexapolar aberration ( order)
is dominant
Octupolar aberration ( order)
Hexapolar corrected
Higher order aberration ( order)
Octupolar corrected
Typically « C-shaped »
Typically « S-shaped »
Optical aberrations tend to increase the beam size and need to be corrected

## Slide 31: II – Guiding and focalizing magnets : dipoles, quadrupoles and multipoles
  LHC at CERN

## Slide 32: II – Guiding and focalizing magnets : dipoles, quadrupoles and multipoles
  LHC at CERN

## Slide 33: III – Magnetic field around the reference trajectory
  III.1 Coordinate systems
  Accelerators are structured by a succession of bending magnets and multipolar lenses (quadrupoles, sextupoles …).
  In practice, we try to put these elements in the same horizontal plane which is call mid-plane.
  For the calculation of the beam (a set of particles) motion, we describe the system in the single referential.
  By convention, we use the system (x, y, z) with a reference trajectory (C) associated to a particle (impulsion p0)
  We use also (x,y,s) system instead of (x, y, z).
Beam vector is described in 3D by :
Transverse
horizontal
Transverse
vertical
Longitudinal
It can be extended to mass and charge:
but not often used

## Slide 34: II – Guiding and focalizing magnets : dipoles, quadrupoles and multipoles
  III.2 Field Development
  From this taylor expansion we can deduce dipole, quadrupole, sextupole… terms
The (magnetic) fields can be developed with a taylor expansion :

## Slide 35: IV – Particles motion around the reference trajectory
Particle dynamics is calculated using the « Newton-Lorentz » equation :
B field expression injected here
Finally we have a simple equation for
Where x : position, x’ : angle, : energy

## Slide 36: IV – Particles motion around the reference trajectory
Particle dynamics is calculated using the « Newton-Lorentz » equation :
General transport matrix :
B field expression injected here
It is usually sufficient to describe beam dynamics at 1st order.
Development of equations along reference path at 1st order, as a function of the 3D(+) phase space.
This can be expressed under the form of matrix transport :

## Slide 37: IV – Particles motion around the reference trajectory
Particle dynamics is calculated using the « Newton-Lorentz » equation :
It is usually sufficient to describe beam dynamics at 1st order.
Development of equations along reference path at 1st order, as a function of the 3D(+) phase space.
This can be expressed under the form of matrix transport :
General transport matrix :
But at first order, horizontal and vertical motions are generally independant
horizontal
vertical
B field expression injected here

## Slide 38: IV – Particles motion around the reference trajectory
The motion equations are also called Hill’s equations
K is also part of the general expression of the Hamiltonian function in accelerator physics

## Slide 39: IV – Particles motion around the reference trajectory
  IV.2 General solution of the linear equation – Transfer matrixes
Finally we have a simple equation for
Where x : position, x’ : angle, : energy

## Slide 40: IV – Particles motion around the reference trajectory
  In practice, beam lines are structured by various optical elements (dipoles, quadruples, drift, …).
  We calculate the transfer matrix Tx, Tz of each single elements.
  Total matrix transfer Mx, Mz is the product of each single matrix Tx,z.
Matrix formalism :

## Slide 41: IV – Particles motion around the reference trajectory

## Slide 42: IV – Particles motion around the reference trajectory
Particle dynamics is calculated using the « Newton-Lorentz » equation :
It is usually sufficient to describe beam dynamics at 1st order.
Development of equations along reference path at 1st order, as a function of the 3D phase space.
This can be expressed under the form of matrix transport :
General transport matrix :

## Slide 43: IV – Particles motion around the reference trajectory
For spectrometers :
No energy change
Time of fligth (bunched beams)
Magnification (minimize if possible)
Dispersion (sometimes expressed in cm/%)
Point-to-point focusing
The final position of a particle depends on the magnification and the dispersion

## Slide 44: IV – Particles motion around the reference trajectory
Iron length
Magnetic length
  a - Magnetic length
  b- Sector dipole magnet

## Slide 45: IV – Particles motion around the reference trajectory
  c- Bend with combined functions

## Slide 46: IV – Particles motion around the reference trajectory
  d- Contribution of the dipole with entrance and exit face angle
2nd order effects can be added by using parabolic faces

## Slide 47: IV – Particles motion around the reference trajectory
  e- Transfer matrix of the quadruple
For quadruple is beam focusing on horizontal plane and defocusing in vertical plane.
For quadruple is beam defocusing on horizontal plane and focusing in vertical plane.

## Slide 48: IV – Particles motion around the reference trajectory
  f- Thin lens
  Thin lenses are use at the very beginning of a project.
  A quadruple (length L) is a thin lens with 2 drift space to length.
  focusing
  defocusing

## Slide 49: IV – Particles motion around the reference trajectory
  g- Matrix of the drift space to length L
Q : transfer matrix of a drift ?

## Slide 50: IV – Particles motion around the reference trajectory
  g- Matrix of the drift space to length L

## Slide 51: IV – Particles motion around the reference trajectory
  h- Some keys words
  Achromatic system :
  System resolution :
  Dispersion :

## Slide 52: V – Beam envelop and emittance
  V.0 Introduction
  A beam is a set of particles with different initials conditions values (x0, x’0, y0, y’0 ,z and d). What happened to this set of particles along a line in terms of trajectories. We take about beam envelope.
  At first order, horizontal and vertical motion are decoupled.

## Slide 53: V – Beam envelop and emittance
  V.1 Phase space and emittance ellipse
  For each particle of the beam, we give a point in the phase space (x,x’) et (y,y’).
  In each plane, the surface occupied by all particles define the phase extension or beam emittance.
  In the general case, complete phase space is 6 dimensions x, x’, y, y’, z, d where l is the trajectory length difference of the beam particles.
x or y
Gx or Gy
x’ or y’
The ellipse area, called the (RMS) beam emittance, is a quantity which is constant along the beam trajectory

## Slide 54: V – Beam envelop and emittance

## Slide 55: V – Beam envelop and emittance
  1 – Ellipse transformation in a drift space to length L :
  2 – Ellipse transformation in a focusing lens (same for quadrupole) :
  3 – Ellipse transformation in a defocusing lens (same for quadrupole) :

## Slide 56: V – Beam envelop and emittance
18/06/2025
Front view: tantal mask
Side view:
MCP + Phosphore screen
Front view:
CCD camera
Pepperpot
Emittance-meter

## Slide 57: V – Beam envelop and emittance
  V.3 Effect of the dispersion energy
  For 2 individual particles

## Slide 58: V – Beam envelop and emittance
  V.3 Effect of the dispersion energy

## Slide 59: V – Beam envelop and emittance
  Resolving power

## Slide 60: V – Beam envelop and emittance
  Example with the dispersion section of the LISE (Ligne d’Ions Super Epluchés) spectrometer at GANIL in Caen.
  Primary Beam
  Target (object)
  2 quads
  45° bend
  2 quads
  Dispersive plane (image)
  Section length : 7.46m
  Full spectrometer length : 43m
  1st Transfer matrix of the section (units : cm, mrad, %):
  -0.73928 0.00017 0.00000 0.00000 0.00000 -1.65347
  8.65925 -1.35471 0.00000 0.00000 0.00000 -3.59935
  0.00000 0.00000 -3.73131 -0.00203 0.00000 0.00000
  0.00000 0.00000 -6.96975 -0.27180 0.00000 0.00000
  -1.69788 0.22406 0.00000 0.00000 1.00000 -0.20355
  0.00000 0.00000 0.00000 0.00000 0.00000 1.00000
  D en cm/%

## Slide 61: V – Beam envelop and emittance
  Example with the dispersion section of the LISE (Ligne d’Ions Super Epluchés) spectrometer at GANIL in Caen.
  Primary beam on Be target
  2 quads
  45° bend
  2 quads
  Dispersive plan (image)
  d=-1%
  d=1%
  d=-2%
  d=2%
  D=-16.5mm/%
  Each spot can be secondary beam produce in target with
  All secondary beam summed

## Slide 62: Thank you for listening !