## Slide 1: WP5: Integration into a new LINAC Cryomodule Annual meeting, Apr 23, 2025 WP Leader: Nuno Elias (ESS) WP Deputy: Vittorio Parma (CERN)
All information contained in this presentation and any accompanying documents is for iSAS project only, and must be treated as strictly confidential.
Any dissemination, distribution or other use of this information without the consent of its owner is prohibited.
Funded by the European Union. Views and opinions expressed are however those of the authors only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the granting authority can be held responsible for them.
With contributions of colleagues from ESS, CERN, CNRS, EPFL

## Slide 2
WP5: Integration into a new LINAC Cryomodule
ESS | CNRS | CERN | EPFL
Convener: Nuno Elias (ESS)
Main contacts with other partners: G. Olry (CNRS), V. Parma. CERN); M. Siedel (EPFL)
The design of any LINAC cryomodule is optimised to meet the specific research objectives of the accelerator facility, while addressing common challenges such as high-power electric fields, ultra-low temperatures, ultra-high vacuum, precise alignment, etc.
WP5's main goal is to tackle the common engineering challenges of integrating iSAS technologies into a parametric design of a new cryomodule, building on developments made with ESS cryomodules whilst benchmarking against other facilities.
In addition, to unlock the full energy-saving capability of this cryomodule, the objective of WP5 is to also address the challenging beam dynamics requirements when operating the new cryomodule in Energy Recovery Linacs with recirculating beams.

## Slide 3
WP5: Integration into a new LINAC Cryomodule
ESS | CNRS | CERN | EPFL
Convener: Nuno Elias (ESS)
Main contacts with other partners: G. Olry (CNRS), V. Parma. CERN); M. Siedel (EPFL)
Task 5.1: Coordination on cryomodule design activities– M1-M48
• General coordination by ESS as described above.
Task 5.2: ESS cryomodules experience and benchmarking with other recent facilities– M1-M36
• Compile the lesson learned from the ESS CM testing activities, technical commissioning, and initial operation.
• Benchmarking with projects in the implementation phase (worldwide).
• Develop a roadmap to develop a new, sustainable CM design.
Task 5.3: Sustainable criteria for LINAC cryomodule design– M24-M48
• Integrate findings from the other iSAS WPs into a generic CM design.
• Explore the sustainability criteria for the design.
Task 5.4: Beam Dynamics for ERL-based accelerators with energy-efficient cryomodules – M1-M48
• Simulate the beam dynamics of ERL-based accelerators when the energy efficient CM is included.
• Study the lattice design to optimize the beam and energy saving performances.

## Slide 4
WP5: Integration into a new LINAC Cryomodule
ESS | CNRS | CERN | EPFL
Work Plan
COMPLETED
COMPLETED
COMPLETED
In-Progress
Recently Started
Recently Started
In-Progress

## Slide 5
WP5 – Coordination: status/evolution of Task 5.1
Activities
  Regular WP5 Coord.: meetings + dedicated meetings task specific (ongoing)
  Milestone 21: Completed “In-person WP kick-off meeting at ESS” :
  Milestone 42: Completed “WP5 impact Risk Analysis” :
  Deliverable 16: Completed Report “Compilation of ESS CM lessons learned & benchmarks from facilities in implementation phase”
    Annex I : Detailed Report on ”Compilation of Lessons Learned from ESS”
    Annex II: Detailed Report on “Benchmarking Cryomodule Designs for iSAS WP5”
  Recruitment PhD student (EPFL): Started: (Apr-2024) ; Completed (Oct-2024)
  Recruitment Junior Engineer (ESS): Started: (Mar-2025) ; Completed (Oct-2025)
  In-Person meeting at IJCLab: Workshop Prepare start of Task 5.3
Report Period 1
  Report on WP5 activities conducted up to RP1
Task 5.1: Coordination on cryomodule design activities– M1-M48
• General coordination by ESS as described above.

## Slide 6
WP5 – Coordination: status/evolution of Task 5.1
Task 5.1: Coordination on cryomodule design activities– M1-M48
• General coordination by ESS as described above.
Milestone : M21 In-person WP kick-off meeting at ESS (Due date: M3 or Jun-2024)
Milestone : M42 Impact Risk analysis (Due date: M24 or Feb-2026)
Deliverable: D16 Compilation of ESS CM lessons learned & benchmarks (Due date: M24 or Feb-2026)
Deliverable: D17 Roadmap for the CM design (Due date: M36 or Feb-2027)
Deliverable: D18 Parametric design for a sustainable CM with iSAS tech. (Due date: M46 or Dec-2027)
Deliverable: D19 Report on beam dynamics study for ERL with iSAS CM (Due date: M43 or Sep-2027)

## Slide 7
WP5 – Experience/Benchmark CMs: status of Task 5.2
Activities: Delivered
Task 5.2: ESS cryomodules experience and benchmarking with other recent facilities – M1-M36
• Compile lesson learned from the ESS CM testing activities, technical commissioning, initial operation.
• Benchmarking with projects in the implementation phase (worldwide).
• Develop a roadmap to develop a new, sustainable CM design.
• Compile lesson learned from the ESS CM testing activities, technical commissioning, initial operation.

## Slide 8
WP5 – Experience/Benchmark CMs: status of Task 5.2
Scope
System Overview
CM Design Phase Lessons
Manufacturing and Assembly phase Lessons
Testing and Commissioning
Sustainability aspects
Conclusions
Task 5.2: ESS cryomodules experience and benchmarking with other recent facilities – M1-M36
• Compile lesson learned from the ESS CM testing activities, technical commissioning, initial operation.
• Benchmarking with projects in the implementation phase (worldwide).
• Develop a roadmap to develop a new, sustainable CM design.
• Compile lesson learned from the ESS CM testing activities, technical commissioning, initial operation.

## Slide 9
WP5 – Experience/Benchmark CMs: status of Task 5.2
Scope
System Overview
CM Design Phase Lessons
Manufacturing and Assembly phase Lessons
Testing and Commissioning
Sustainability aspects
Conclusions
Task 5.2: ESS cryomodules experience and benchmarking with other recent facilities – M1-M36
• Compile lesson learned from the ESS CM testing activities, technical commissioning, initial operation.
• Benchmarking with projects in the implementation phase (worldwide).
• Develop a roadmap to develop a new, sustainable CM design.
• Compile lesson learned from the ESS CM testing activities, technical commissioning, initial operation.

## Slide 10
WP5 – Experience/Benchmark CMs: status of Task 5.2
Scope
System Overview
CM Design Phase Lessons
Manufacturing and Assembly phase Lessons
Testing and Commissioning
Sustainability aspects
Conclusions
Task 5.2: ESS cryomodules experience and benchmarking with other recent facilities – M1-M36
• Compile lesson learned from the ESS CM testing activities, technical commissioning, initial operation.
• Benchmarking with projects in the implementation phase (worldwide).
• Develop a roadmap to develop a new, sustainable CM design.
• Compile lesson learned from the ESS CM testing activities, technical commissioning, initial operation.

## Slide 11
WP5 – Experience/Benchmark CMs: status of Task 5.2
Scope
System Overview
CM Design Phase Lessons
Manufacturing and Assembly phase Lessons
Testing and Commissioning
Sustainability aspects
Conclusions
Task 5.2: ESS cryomodules experience and benchmarking with other recent facilities – M1-M36
• Compile lesson learned from the ESS CM testing activities, technical commissioning, initial operation.
• Benchmarking with projects in the implementation phase (worldwide).
• Develop a roadmap to develop a new, sustainable CM design.
• Compile lesson learned from the ESS CM testing activities, technical commissioning, initial operation.

## Slide 12
WP5 – Experience/Benchmark CMs: status of Task 5.2
Scope
System Overview
CM Design Phase Lessons
Manufacturing and Assembly phase Lessons
Testing and Commissioning
Sustainability aspects
Conclusions
Task 5.2: ESS cryomodules experience and benchmarking with other recent facilities – M1-M36
• Compile lesson learned from the ESS CM testing activities, technical commissioning, initial operation.
• Benchmarking with projects in the implementation phase (worldwide).
• Develop a roadmap to develop a new, sustainable CM design.
• Compile lesson learned from the ESS CM testing activities, technical commissioning, initial operation.
Paper at ICEC30-ICMC2026, Daejeon, South Korea: “Lessons Learned from the ESS Elliptical Cryomodule Design and Operation : Paving the way for Sustainable Accelerating Systems (iSAS)”

## Slide 13
The scope of the benchmarking study is to establish a robust baseline for the definition of the sustainability criteria to consider for the design of a new cryomodule.
The study has been conducted through a questionnaire across five key domains.
This comparative approach highlights how differing requirements, constraints, and strategic priorities shape design choices and lead to distinct technical configurations. Link
Study conducted for high-beta elliptical cryomodules with frequencies between 400MHz and 1.3GHz, across six facilities SNS, LHC, PIP-II, XFEL, LCLS-II, and ESS, to ensure a relevant comparison
Task 5.2: ESS cryomodule experience and benchmarking with other recent facilities
Karin Canderan (CERN, SY-RF) on behalf of WP5

## Slide 14: Facilities
European Spallation Source (ESS)
Spallation Neutron Source (SNS)
Proton Improvement Plan II (PIP-II)
Large Hadron Collider (LHC)
European X-ray Free-Electron Laser (XFEL)
Linac Coherent Light Source II (LCLS-II)
Notes: The chosen facilities represent a broad spectrum of machine parameters - particles, current, beam power, frequency, duty cycle, etc. - and design philosophies – segmented / continuous layout, cavity supporting systems, cryogenic schemes, etc. In this way, a diverse range of high-beta designs was represented.
The facilities represent a wide spectrum of maturity and lifecycle stages.
This diversity allows for a comprehensive analysis of the transition from "as-designed" specifications to "as-operated" realities.
By including facilities that range from those starting installation soon to those with years of proven performance, the benchmarking exercise can capture lessons learned across the full engineering lifecycle. This ensures that the proposed roadmap for a sustainable "Cryomodule of the Future" is informed by both cutting-edge design and the practical challenges of long-term maintainability and hardware degradation.

## Slide 15: CM design concepts
ESS
LHC
SNS
LCLS-II
XFEL
PIP-II

## Slide 16
  1
Beam and RF parameters
  2
Cryogenic Systems and thermal management
  3
Cryomodule design
  4
Commissioning insights
  5
Operational experience and reliability
Main steps of the benchmarking methodology:
Definition of key technical areas of interest to be included in the benchmarking study
Proposal of cryomodule design concepts, facilities and experts
Definition of specific points of interest for each area and drafting of the questionnaire
Literature research and pre-filling of the answers
Initial contact and questionnaire distribution
Follow-up face-to-face interviews
Compilation of answers and final report.

## Slide 17: Summary of the benchmarking analysis
  1
Beam and RF parameters
•Focus: particles, accelerating gradients, operating frequencies, duty cycle.
•Goal: Understand how beam physics requirements drive the complexity and energy demands of the CM.
CW machines prioritize high Q0 to minimize dynamic losses, while pulsed machines tend to push higher peak gradients
The type of machine (circular multi-pass, linear single-pass) and particles to be accelerated also dictate different requirement (alignment, losses, beam stability thresholds, etc.)
Wide range in delivered FPC power. Moreover, within the limit of the six facilities considered, two main families were identified, when it comes to orientation within the cryomodule, either vertical or horizontal.
In proton linear accelerators, the beam exhibits lower sensitivity to trapped HOM perturbations
 |  |  | LCLS-II and PIP-II use nitrogen-doped cavities to achieve a high Q0: 2.7x1010 at 16 MV/m for LCLS-II and 3.3x1010 at 21 MV/m for PIP-II.
 |  |  | Peak value gradient above 16MV/m for all the facilities operating in pulsed mode. ESS and XFEL cavities are equipped with fast-piezo tuners, while SNS cavities do not need fast compensation with piezo actuators.
 |  |  | XFEL, LCLS-II, and PIP-II operates with average RF power of 2.15kW, 7kW and 35kW respectively, with FPCs designed for a peak power of 156 kW, 7 kW and 43kW respectively, at the nominal duty cycle. The FPCs have horizontal orientation and bellows in the transmission line ensure sufficient flexibility to compensate for the cold mass thermal contraction.
 |  |  | ESS, SNS and LHC operates with average RF power of 43 kW, 44kW and 300 kW respectively, with FPCs designed for a peak power of 1.1 MW, 550kW and 350 kW respectively, at the nominal duty cycle. The FPCs have a vertical - bottom or top for the LHC- orientation, these designs do not have bellows in the transmission line.
 |  |  | ESS and PIP-II cavities do not have HOM couplers. SNS originally included HOM couplers, however operational experience indicated they were not required to achieve goal performances, and given occasional leaks and failures, they have been progressively removed during cryomodule repairs.
 |  |  | Circular colliders like the LHC, and electron machines like XFEL and LCLS-II require the integration of HOM couplers in the cavity design.
The beam structure requirements and RF parameters, including choice of frequency, fundamentally dictate the SRF and cryomodule architecture:
ESS | SNS | LHC | XFEL | LCLS-II | PIP-II

## Slide 18: Summary of the benchmarking analysis
  2
Cryogenic Systems and thermal management
•Focus: Machine architecture, Cooling circuit layouts, temperature and pressure levels, static and dynamic heat loads, and cooling capacity cryogenic plant. Management of helium inventory and ODH risk
•Goal: Characterizing design choices for cryogenic systems.
Significant diversity exists in cooling circuit segmentation, temperature levels, and thermal shield configurations
A multi-level temperature architecture (2K, 4.5/ 5-10K, 35–80 K) is standard across all facilities.
For cavities operating at low duty cycles, static heat loads strongly impact the total cryogenic consumption. For cavities operating in CW instead, the cryogenic losses are driven by the dynamic heat loads (except for LHC).
For the FPC outer conductor, it was observed a preference for the active cooling with helium, for operation with high average RF power (>40/50 kW). Active cooling is considered more flexible / adjustable, than fixed thermal intercepts.
Cryogenic distribution strategy (continuous vs segmented) strongly affects maintainability and failure recovery capability.
 |  |  |  |  | A three-level architecture (typically 2 K, 4.5–10 K, and 35–80 K) is the standard for optimizing thermal efficiency across all facilities.
 | Due to assembly compromises, the LHC uses a single temperature level (4.5 K) and a floating thermal shield made of MLI blankets. |  |  |  | 
 |  |  |  | The percentage of static heat load, compared to the total heat load to the cavity bath, is indicated per facility: ESS 44.1%, SNS 73.7%, LHC 83.7%, XFEL 45.8%
 |  | The percentage of static heat load, compared to the total heat load to the cavity bath, is small for facilities operating in CW, LCLS-II 10%, PIP-II 12.5%. |  | 
 |  |  | Active helium cooling is considered more flexible for high average RF power operations or for designs qualified for higher values of peak power, ESS, SNS and LHC use ~5 K helium to cool the FPC outer conductors.
 |  |  | Facilities with lower average power, such as XFEL, LCLS-II, and PIP-II, the outer conductor is cooled with fixed temperature thermal intercepts (copper braids) connected to the cryogenic lines.
 |  | Accelerating modules are integrated into a single vacuum vessel string. In case of maintenance the entire linac must be warmed up.
 |  | Cryomodules are stand-alone units, with access hatches, connected to the external distribution line via bayonets. The maintenance work may be performed through the access hatches, otherwise the cryomodule can be removed with the rest of the machine cold.
 |  | Cryomodules are stand-alone units, with access hatches, connected to the external distribution line via jumper with welded connections. The maintenance work may be performed through the access hatches, otherwise the cryomodule can be removed, warming up the linac
ESS | SNS | LHC | XFEL | LCLS-II | PIP-II

## Slide 19: Summary of the benchmarking analysis
  3
Cryomodule design
•Focus: characterize internal components, cavity string assemblies, power couplers, tuners, and magnetic shielding.
•Goal: Map the constraints, design choices and integration aspects regarding the cryomodule design and its assembly sequence
While cavity technology is broadly similar (elliptical SRF cavities), integration philosophies differ:
Variations in cavity supporting schemes, vacuum forces compensation, longitudinal references and alignment strategies have been identified.
Helium tank design influences mechanical stiffness and microphonics sensitivity.
Variations in Magnetic shielding implementation (cold vs warm, single vs multi-layer) with impact on achievable Q₀
Some facilities reported design compromises made to facilitate assembly, reduce cost, or drivers related to schedule
The integration of a second thermal shield, when in presence of the 8-10K heat intercept, was evaluated but not always considered convenient
It appears now a standard to include access hatches in the cryomodule design.
 |  | Cavities are supported by the Helium Gas Return Pipe (GRP), which acts as the main structural backbone and an Ivar rod that provides longitudinal anchoring.
 |  | Cavities are supported and aligned with spaceframe at ambient temperature connected to the vacuum vessel. For the SNS cryomodule, a Nitronic rod is added for longitudinal anchoring.
 | Cavities are supported by a frame anchored to the vacuum vessel through six tie rods. | 
 | Cavities are supported by two support posts (one fixed, one sliding) mounted on a strongback support at ambient temperature. | 
 |  |  |  |  | The introduction of a cold magnetic shield outside the helium tank is a common practice for all the facilities using Niobium cavities. LCLS-II cavities have two layers of cold magnetic shielding.
 |  | SNS and PIP-II cryomodules have also a warm global magnetic shield. |  |  | 
 |  | LCLS-II and PIP-II cavities rely as well on fast cooldown across the Nb transition temperature to sweep out the trapped magnetic flux and reach the required Q0. |  |  | 
 | LHC cavities in copper with Nb coating are not sensitive to magnetic field. |  |  |  | 
 |  | For LCLS-II and PIP-II, given the availability of a low temperature heat intercept, it was evaluated the possibility of having a second thermal shield. Although, the effective reduction of the heat load to the 2K was not considered sufficient to justify the cost, complexity and space occupation of a second shield.
 | In the XFEL cryomodule instead, there are two thermal shields, resulting in very minimal heat loads to the cavity bath. | 
ESS | SNS | LHC | XFEL | LCLS-II | PIP-II

## Slide 20: Summary of the benchmarking analysis
  4
Commissioning insights
•Focus: Knowledge gained during the assembly, testing, and initial installation phases.
•Goal: Document technical difficulties in the commissioning phase, providing useful feedback for future sustainable designs.
A primary goal across facilities is to minimize discrepancies between "as-designed" and "as-tested/operated" performance, specifically addressing issues like cryoplant limitations and unexpected heat load differences
Success depends on maximizing preparation before tunnel installation, maintaining strong in-house expertise, accurate planning that allows smooth sequence and sufficient flexibility
It is strongly recommended to develop the design of cryomodules and their associated services together, to ensure system compatibility and avoid late-stage conflicts
Focusing on continuous quality controls and accurate interface matching is essential to reduce rework
Several key elements emerged during the discussion on commissioning experience and lessons learned:

## Slide 21: Summary of the benchmarking analysis
  5
Operational experience and reliability
•Focus: Factors limiting cryomodule performance, mitigation strategies, machine availability, capability for maintenance, repair and replacement.
•Goal: Use real-world operational data to ensure that energy-saving innovations do not compromise the facility's scientific output.
Long-term availability emerged as a critical sustainability metric. Facilities emphasized:
Redundancy of internal equipment is critical in operation (ex: facilities now design for extra RF capacity, when possible, to compensate for individual cavity failures without beam degradation).
Different experiences have been described regarding cavity performance degradation and strategies for compensation with the remaining cavities.
Modular cryogenic systems and replacement strategies. The ability or not to isolate a single cryomodule for maintenance without affecting adjacent units strongly impacts overall machine uptime.
Importance of accessibility was emphasized, more specifically for couplers and tuners.
Failure modes reported include FPC degradation, tuner actuator failure, and vacuum-related incidents.
Cryoplant trips remain a major bottleneck for availability.
The cryoplant design includes safety margins to compensate for uncertainty in the estimation of cryomodule static and dynamic heat loads.

## Slide 22
  1
Beam and RF parameters
•Focus: particles, accelerating gradients, operating frequencies, duty cycle.
•Goal: Understand how beam physics requirements drive the complexity and energy demands of the CM.
  2
Cryogenic Systems and thermal management
•Focus: Machine architecture, Cooling circuit layouts, temperature and pressure levels, static and dynamic heat loads, and cooling capacity cryogenic plant. Management of helium inventory and ODH risk
•Goal: Characterizing design choices for cryogenic systems.
  3
Cryomodule design
•Focus: characterize internal components, cavity string assemblies, power couplers, tuners, and magnetic shielding.
•Goal: Map the constraints, design choices and integration aspects regarding the cryomodule design and its assembly sequence
  4
Commissioning insights
•Focus: Knowledge gained during the assembly, testing, and initial installation phases.
•Goal: Document technical difficulties in the commissioning phase, providing useful feedback for future sustainable designs.
  5
Operational experience and reliability
•Focus: Factors limiting cryomodule performance, mitigation strategies, machine availability, capability for maintenance, repair and replacement.
•Goal: Use real-world operational data to ensure that energy-saving innovations do not compromise the facility's scientific output.
Conclusions and next steps
Beam and RF parameters are the design drivers, while cryogenic efficiency impacts the overall sustainability.
Common trends, (multi-level temperature architectures, modular cryogenic segmentation, accessibility) have emerged as industry standards.
High availability and long-term reliability are primary metrics for sustainability.
The collected data will be translated into practical engineering strategies, to build a Roadmap for the development of sustainable cryomodules (D17).
The resulting guidelines will directly contribute to the development of a parametric tool for cryomodule design (Task 5.3 - D18).

## Slide 23
Acknowledgments
PIP-II (Fermi National Laboratory, Batavia, Illinois, USA)
Donato Passarelli
Vincent Roger
LCLS-II (Linac Coherent Light Source II, SLAC, California, USA)
Thomas Petersen
Sebastian Aderhold
XFEL (European X-ray Free Electron Laser, Hamburg, Germany)
Serena Barbanotti
Kay Jensch
Julien Branlard
Joshua Einstein-Curtis
SNS (Spallation Neutron Source, Oak Ridge, USA)
John Mammoser
Paolo Pizzol
ESS (European Spallation Source, Lund, Sweden)
Paolo Pierini
Nuno Elias
Emma Simpson
Henry Przibliski
Marek Skiba
CERN (LHC, Geneva, Switzerland)
Vittorio Parma
Karin Canderan
Katarzyna Turaj
Krzysztof Brodzinski
David Smekens
We wish to extend their sincere gratitude to the experts who participated in the benchmarking process, the amount of information shared have exceeded our expectations.

## Slide 24
WP5 – Design new CM: status/evolution of Task 5.3
Task 5.3: Sustainable criteria for LINAC cryomodule design – M24-M48
• Integrate findings from the other iSAS WPs into a generic CM design.
• Explore the sustainability criteria for the design.
Activities: Task planned start: M24 (Mar26)
  In-person workshop at IJCLAB in 28-Jan-2026, brainstorming towards parametric design (create a team)
Deliverable 5.3 : Parametric design for a sustainable CM with iSAS tech. (Due date: M48 or Feb-2028)
PARAMETRIC
DESIGN for a
SUSTAINABLE
CRYOMODULE with
ISAS TECHNOLOGIES
- Which Parameters are relevant?
- Desired / Achievable degree of complexity?
- Design Drivers?
- Requirements?
- Constraints ?
- Uncertainty ?
- Best Practices
- Systems Engineering approach
- Energy Savings
- Lifecycle
- Availability
- Maintainability
- Repairability
- Industrial Solutions?
- Main Functions
- Main Components
- Systems Integration
- Design Dilemmas
- State-of-the art
- Looking into the future at proposed acc. syst.
- Quantification of gains
Engineering Toolbox for CM design: Decision making tool

## Slide 25
WP5 – Design new CM: status/evolution of Task 5.4
Task 5.4: Beam Dynamics for ERL-based accelerators with energy-efficient cryomodules – M1-M48
Beam Dynamics for ERL-based accelerators with energy-efficient cryomodules
Single- and multi-bunch instability studies in the iSAS/PERLE cryomodules
  Development of simulation tools
    Multi-pass recirculation model
    Wake field model
  Single- and multi-bunch beam breakup and beam loading studies
Energy-recovery efficiency studies

## Slide 26
WP5 – Design new CM: status/evolution of Task 5.4
Task 5.4: Beam Dynamics for ERL-based accelerators with energy-efficient cryomodules – M1-M48
Figure 1: Benchmark of the evolution of the transverse beta functions and beam size of a bunch through the PERLE cryomodule between Bmad/Tao, BDSIM, RF-Track, and the PERLE RF field map simulated in RF-Track; the grey rectangles on top indicate the location of the 5-cell standing-wave cavities.

## Slide 27
WP5 – Design new CM: status/evolution of Task 5.4
Task 5.4: Beam Dynamics for ERL-based accelerators with energy-efficient cryomodules – M1-M48
Developed recirculation model in Python package (PyERL) interfaced with RF-Track
  Simulate end-to-end arbitrary ERL’s
250 MeV PERLE MAD-X lattice (v2.4.250) [A. Fomin] :
  Very good agreement (2% error)
Figure 2: Comparison of the horizontal beta function through the PERLE 250 MeV lattice.

## Slide 28
WP5 – Design new CM: status/evolution of Task 5.4
Task 5.4: Beam Dynamics for ERL-based accelerators with energy-efficient cryomodules – M1-M48
Developed new wake field model
  Recirculation
  (A)symmetric structures up to the n-th order (monopole, dipole, quadrupole, etc.)
  Cavities dressed with HOM/FP couplers
Kick and wake function benchmark:
  New model vs Xwakes (PyHEADTAIL):
Figure 3: Transverse wake function comparison with , , and .

## Slide 29
WP5 – Design new CM: status/evolution of Task 5.4
Task 5.4: Beam Dynamics for ERL-based accelerators with energy-efficient cryomodules – M1-M48
Single- and multi-bunch instability studies in ERL-based accelerators (PERLE/general ERL):
  Current/HOM threshold: maximum beam current/quality factor/shunt impedance before an instability appears
  Effect of dipole modes (and monopole)
  (Regenerative) multi-pass beam breakup
  Beam loading effects
    Model LLRF system in beam dynamics framework to mitigate transient beam loading effects
Energy recovery efficiency studies:
  PERLE
  General ERL collider study
  Specific ERL-based collider project: LHeC, ERLC, erc@CERN, FCC-ee ERL, and more….

## Slide 30
WP5 – Design new CM: status/evolution of Task 5.4
Figure 4: The average evolution of individual horizontal and vertical dipole HOM voltages experienced by a test particle at a 1 mm offset inside the 4th PERLE dressed 5-cell half-wave cavity excited by 25k bunches passing through the PERLE 250 MeV lattice at 435 mA.
No instability
Instability appears

## Slide 31
WP5 – Design new CM: status/evolution of Task 5.4
Figure 5: Average horizontal position of 25k bunches at the exit of the 250 MeV PERLE linac after the last decelerating pass at 435 mA.
No instability

## Slide 32
WP5 – Design new CM: status/evolution of Task 5.4
Figure 6: Average vertical position of 25k bunches at the exit of the 250 MeV PERLE linac after the last decelerating pass at 435 mA.
Instability appears

## Slide 33
WP5 – Design new CM: status/evolution of Task 5.4
Task 5.4: Beam Dynamics for ERL-based accelerators with energy-efficient cryomodules – M1-M48
Preliminary threshold current found at injection current of 430 mA
Operating Beam current of 2.50 A in the linac
21.5 times the nominal current of 20 mA / 120 mA
Instability seems to appear first on the vertical axis before appearing on the horizontal axis
Dominant dipole HOM in -plane has a shunt impedance larger than the shunt impedance of the dominant dipole HOM in -plane
Further investigate and search for thresholds

## Slide 34
Past developments:
  Meetings/communication with PERLE collaboration, discussing details on the lattice, RF structure and HOM parameters
  Evaluated and tested beam various dynamics codes to enable ERL simulations
  Developed recirculation tracking model that allows to track any arbitrary recirculating lattice in RF-Track
  Developed wake field model that allows for symmetric and asymmetric mode excitation in recirculating lattices
  Gathered preliminary results on the threshold current in the 250 MeV PERLE lattice (v2.4.250)
Current developments:
  Model optimisations
  Single- and multi-bunch instability studies for PERLE
  Beam loading studies for PERLE
    Modelling of LLRF system
  Evaluation of ERL collider/light source applications for iSAS technology
WP5 – Design new CM: status/evolution of Task 5.4
Task 5.4: Beam Dynamics for ERL-based accelerators with energy-efficient cryomodules – M1-M48

## Slide 35
WP5 – Title: points of attention
Points of Attention:
  1st June 2026, 9:00-12:30 : “iSAS 1st reporting period project review meeting”
    Online interview with the PO and the external expert of the EU (WP leader , + all?)
Submitted:

## Slide 36
WP5 – Coordination: status/evolution of Task 5.1
Impact Risk Analysis
Task 5.1: Coordination on cryomodule design activities– M1-M48
• General coordination by ESS as described above.
Critical risks & risk management strategy |  |  |  |  | 
Risk No | Description | Prob | Sev | Critic. (PxS) | Mitigation measures
5.1 | Beneficiary leaves the project | 1 | 2 | 2 | Pro-actively: document, collaborate, strong coordination; Post-facto: redistribute tasks
5.2 | Lack of candidates for temporary positions | 1 | 2 | 2 | Maximize job advertisements as early as possible and as wide as possible (professional networks), leverage on the iSAS consortium
5.3 | Absence of WP leader | 1 | 2 | 2 | Assign a deputy WP leader
5.4 | CERN junior engineer leaves | 1 | 3 | 3 | Tasks sharing in progress with ESS junior engineer.
5.5 | ESS Junior Engineer only covers half of the project might enter project too late or leave project too early | 1 | 2 | 2 | The assignment of Junior Engineer position at ESS is valid for 2 years shared with WP6. Optimise the hiring process start to match project
5.6 | EPFL Ph.D candidate leaves | 1 | 3 | 3 | Maintain Candidate stimulated
5.7 | Benchmarking facilities low availability from external partners | 1 | 2 | 2 | Gather as much data from bibliographic references, create a spirit of collaboration with benchmarking facilities, share the results
5.8 | Task 5.3, parametric design of sustainable cryomodule resulting to be over-optimistic and complex to parameterise (multiple choices). | 2 | 2 | 4 | Re-define goals towards list of best practises, and decision-making guidelines supporting design choices.

## Slide 37
Benchmarking (Detailed Slides)
Beam Dynamics ( Detailed Slides)
Report WP5 RP1 (Link)
Deliverable 16 Report (Link)
Annex I (Link) : ESS Lessons
Annex II (Link ) : Benchmarking CM Designs
Impact Risk Analysis (Link)
WP5 – Indico ShareSpace, links to reports

## Slide 38
Thank you
Big Thanks to WP5 colleagues:
Vittorio Parma, Karin Canderan, Lode Vanhecke, Emma Simpson, Guillaume Olry, Gilles Olivier, Tatiana Pieloni, Mike Seidel, Paolo Pierini, Henry Przybilski, Marek Skiba, Nuno Elias