## Slide 1
Simulation of quadrupoles on opera
Jana Souyani
Supervision:Hadil ABUALROB

## Slide 2: Outline
Collaboration in PERLE
PERLE Lattice
What is PERLE
My work
Future work

## Slide 3
My lovely university

## Slide 4: PERLE Lattice 250 MeV version

## Slide 5: What is PERLE ?
PERLE (Powerful Energy Recovery LINAC for Experiments): is an accelerator with 3 turns ,after 3 turns the maximum beam energy will be 250 MeV
Quadrupoles focus the beam in one plane and defocus it in the other plane
To achieve focusing in both planes need series of quadrupoles
Dipoles used to bend the beam (control the direction )

## Slide 6: My work where is it ?
Length of quads =5 cm
Number (24)

## Slide 7
3 Quadrupoles (cross talk study)
APERTURE =76 mm

## Slide 8: First design
Parameter | value | unit
Gradient (G) | 4.81 | T/m
NI for quadrupole | 11171.65 | A.turn
N (for quadrupole) | 48 | turns
N (for one coil) | 12 | turns
I (for quadrupole) | 60.48 | A
A (for coil) | 480 | mm2
current density (J) | 1,512 | A/mm2
A (for conducter) | 40 | mm2
Resistance ® | 0.952 | mΩ
power | 3.4822 | watt
Required to be achieved is Gradiant =4.5 T/m
z
X

## Slide 9: Second Design of quadrupole
It’s great !!!
Parameter | value | unit
Gradient (G) | 3.27 | T/m
NI for quadrupole | 7896.8 | A.turn
N (for quadrupole) | 48 | turns
N (for one coil) | 12 | turns
I (for quadrupole) | 41.129 | A
A (for coil) | 480 | mm2
current density (J) | 1.028 | A/mm2
A (for conducter) | 40 | mm2
Required to be achieved is Gradiant =3 T/m
Z
X

## Slide 10: Third design
Parameter | value | unit
Gradient (G) | -2.86 | T/m
NI for quadrupole | 7896.8 | A.turn
N (for quadrupole) | 48 | turns
N (for one coil) | 12 | turns
I (for quadrupole) | 41.129 | A
A (for coil) | 480 | mm2
current density (J) | -0.9 | A/mm2
A (for conducter) | 40 | mm2
Required to be achieved is Gradiant =-2.5 T/m
Z
X

## Slide 11: Model of 3 quadrupoles (cross talk) first study
Bx(T)
Physical dimension of com.In.Quad.10
Physical dimension of com.In.Quad.20
Physical dimension of com.In.Quad.30
com.In.Quad.10 is off
com.In.Quad.20 is off
com.In.Quad.30 is on
z
Y
X
Z(mm)

## Slide 12: Magnetic flux density in the yoke & center of quad
Gradient for com.In.Quad.30 =4.81 T as alone !!!

## Slide 13: Second study
Physical dimension of com.In.Quad.10
Physical dimension of com.In.Quad.20
Physical dimension of com.In.Quad.30
com.In.Quad.10 is off
com.In.Quad.20 is on
com.In.Quad.30 is on
Z(mm)
Bx(T)

## Slide 14: Magnetic flux density in the yoke & Gradient
Gradient for com.In.Quad.30 =4.81 T as alone !!!
Gradient for com.In.Quad.20 =-2.86 T as alone !!!
Good job Jana!!!

## Slide 15: Third study
Physical dimension of com.In.Quad.10
Physical dimension of com.In.Quad.20
Physical dimension of com.In.Quad.30
com.In.Quad.10 is on
com.In.Quad.20 is on
com.In.Quad.30 is on
Bx(T)
Z(mm)

## Slide 16: Magnetic flux density in the yoke & Gradient
Gradient for com.In.Quad.30 =4.81 T as alone !!!
Gradient for com.In.Quad.20 =-2.87 T, alone is 2.86 !!!
Gradient for com.In.Quad.10 =3.27 T as alone !!!
Y
Excellent work !!!

## Slide 17: Future work
According to the 3 Studes the quadrupoles design approximately acceptable
finish model of 3 quads
Design dipole