## Slide 1
The IDROGEN System
A high data rate acquisition system synchronized by an enhanced White Rabbit node
IJCLab : Scientific themes : Astroparticles, Astrophysics & Cosmology, Nuclear physics, High Energy Physics, Accelerator Physics, Theory, Heath, Energy
  Daniel Charlet, Antoine Back, Nawal Belouchrani, Cédric Esnault, Christophe Joly, Christelle Soulet, Monique Taurigna, Chafik Cheikali, *Gaetan Seuillot, *Mathias Vecchio, *Sid Ali Cherrati
Paris Observatory : Scientific themes : Time and frequency metrology, time and frequency transfer, inertial sensors, space-time reference frames, theory, epistemology
  LTE : Paul-Eric Pottie, Michel lours
  Obs Nancay : Cédric Viou
LPSC: Olivier Bourrion
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau
17/12/2025

## Slide 2: Agenda
Introduce the White Rabbit technology and how it works
Role of the IDROGEN board
Some projects examples
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau

## Slide 3
White Rabbit and its areas
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau
White Rabbit is a sub-nanosecond timing and frequency distribution technology developed by CERN & GSI, with a range of applications in distributed systems where timing precision is critical
Particle accelerators
& high-energy physics
Astronomy
Advanced Radar
Quantum networks
Financial sector
Telecomunications
Metrology
& National timing
Synchronizing thousands of nodes in accelerators chains
(eg CERN, FAIR …)
Timing for widely distributed detector arrays
Precise coordination
of antenna and sensor networks
Tests for synchronized quantum nodes & secure communications
Time synchronization in critical transaction networks
Precision time for critical communication infrastructure
Infrasturctures like REFIMEVE for distributing
Time & frequency references

## Slide 4: Technical Principles
White Rabbit Operation (Key concepts)
    SyncE (Synchronous Ethernet):
    shares a common frequency clock
    PTP (Precision Time Protocol IEEE1588)
    Message exchange to measure/deduce delays
    Ultra-fine phase measurement:
    Extremely precise phase alignment between clocks via DDMTD Phase tracking (Digital Dual Mixer Domain)
Tomasz Włostowski : Precise time and frequency transfer in a White Rabbit network
White Rabbit is a high precision synchronization technology based on Ethernet.
It synchronizes multiple devices on a network with sub-nanosecond precision.
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau
    Delivering synchronous clock and 1PPS via optical link
    Delivering synchronous clock 10 MHz, 1PPS and timestamping via optical link

## Slide 5: TECHNOLOGY OVERVIEW : Precision Time Protocol
Precision Time Protocol (IEEE 1588):
Protocol that allows devices to align their local clocks to a master clock by exchanging timing information.
Devices send timestamps (send and receive times), which allows calculation of propagation delays and clock offset
Key points:
Measures and corrects clock offset
Uses timestamps in exchanged messages
Enables deduction of propagation delay
Better precision than standard networks, but insufficient alone for sub-ns accuracy targeted by White Rabbit
White Rabbit: Sub-Nanaosecond Timing over Ethernet P.P.M. Jansweijera , H.Z. Peeka , E. de Wolfb,a,
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau

## Slide 6: TECHNOLOGY OVERVIEW : Synchronous Ethernet (Sync-E)
SyncE:
A method that allows all devices on a network to share the same clock frequency over Ethernet.
The receiver recovers the clock from the incoming signal, so all nodes “tick” at the same rate.
SyncE does not provide absolute time (like UTC), but ensures local clocks do not drift from each other
Key points:
- Frequency synchronization, at the physical network layer
Provide a stable base for DDMTD
SYNTONIZATION => SAME FREQUENCY
Tomasz Włostowski : Precise time and frequency transfer in a White Rabbit network
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau

## Slide 7: TECHNOLOGY OVERVIEW : Digital Dual Mixer Time Domain
DDMTD (Digital Dual Mixer Time Difference):
A technique for measuring the phase difference between two clock signals with extremely fine resolution.
In WR, DDMTD allows very precise alignment to a master clock’s phase.
Key points:
Very high-precision phase measurement
Resolution better than timestamp alone
Complements PTP to reach sub-nanosecond
Essential for demanding applications like LLRF
SYNCHRONISATION=> SAME PHASE
Tomasz Włostowski : Precise time and frequency transfer in a White Rabbit network
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau

## Slide 8: On the shelf White Rabbit solution
https://safran-navigation-timing.com/solution/white-rabbit-solutions/
http://www.synctechnology.cn/en_detaile.aspx?ClassID=1
Courtesy : Daniel Charlet
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau

## Slide 9: Accuracy system comparison
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau
Courtesy : Daniel Charlet

## Slide 10: THE IDROGEN BOARD
The IDROGEN board:
Full White Rabbit node designed for precision synchronization (based on CERN schematic) and high performance data acquisition by IJCLAB.
It integrates WR mechanism (PTP, SyncE, DDMTD) in FPGA hardware, allowing it to act as a synchronized endpoint in a WR network
Key points:
Integrate WR core
Can operate as slave node or a local grand master
Integrate with high-speed data acquisiton using standard procole
Fully re-configurable
Courtesy : Antoine Back
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau

## Slide 11: C&C Frequency Tuning system
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau
Timing disciplined by WR distribution µRTM
IDROGEN Eco-system
Ongoing:
500 MSps 4 channels
3GSps 2 channels
REFGEN FMC
ADC FMC
Acquisition board 16 channels

## Slide 12: IDROGEN: softwares
Configuration GUI tools over USB and Ethernet
  Power, PLL, FMC, ADC configuration
  Monitoring GUI for power supplies and temperature monitoring
Slow control library and tools (I2C, SPI, WR diagnostic, …)
Frame viewer
Acquisition software
Courtesy : Daniel Charlet
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau

## Slide 13
Bandwidth (single board): ~500Mhz (1GHz → 1.5GHz)
2 IDROGEN boards synchronized by WR
2 channels 1GSPS 14b ADC
Same RF signal (312.5MHz) split on boards
FFT 8k point
Cross correlation
1GSPS ADC board: Synchronization performance
Two IDROGEN boards
Time difference measurement : 2.2ps
2 channels on a single IDROGEN
Time difference measurement : 180fs
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau

## Slide 14: IDROGEN board performance
IDROGEN BOARD: 4x better than Switch Low Jitter from Safran/Seven Solution
Phase noise measurement
Integrated jitter according to integration range
Variation of lower bound of integration range.
Upper bound fixed at 1 MHz
Courtesy : Daniel Charlet
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau
Residual noise
Absolute measurement
Jitter: [1Hz- 1MHz] : 580fs in slave mode
Jitter: [1Hz- 1MHz] : 260 fs in master mode

## Slide 15: SuperKEKb : Master oscillator distribution
509MHz
Frequency offset: [10Hz → 10MHz] ; RMS jitter: 940fs at 508 MHz
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau
Courtesy : Daniel Charlet

## Slide 16: Laser synchronization
IDROGEN 1 : GM → IDROGEN 2 slave
Fiber length 5Km → 100Km
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau
Courtesy : Aurélien Martens
Preliminary results

## Slide 17
Objectives
In systems like Low Level RF (LLRF) for accelerators, separate modules must share a coherent time and frequency reference
Poor synchronization lead to phase errors and performances loss
Standard networks cannot reach sub-nanosecond precision.
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau

## Slide 18
Context & Synchronization need
Low Level RF:
Real-time control and regulation system for RF cavities:
Real-time measurement of the cavity (amplitude and phase)
Real-time correction (feedback loop)
Uses highly precise synchronization (White Rabbit)
Stabilizes beam performance (field/beam)
Controls the amplifiers for signal generation
Operator interface: global synchronization
LLRF Requirements to be confirmed by beam dynamics: based on 0.1° (phase) & 0.1% (amplitude)
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau

## Slide 19: Distributed Master Oscillator (DMO)
LTE
PARIS
Atomic Clock
Time and frequency
REFIMEVE: french network distributing time and frequency references over optical fiber.
SYRTE (LTE): Paris Observatory, provides highly precise references
WR carries these references to end users
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau

## Slide 20: Distributed Master Oscillator (DMO)
IDROGEN board
Grand Master Mode
Rubidium
10MHz + PPS
IDROGEN board
Crate
MTCA
Switch Mode
Frequency distribution Amplifier
Mode Slave
REFGEN FMC board
With a SI5362
10 MHz (synchronization of Scopes, …)
200.395 MHz (LLRF reference)
400.79 MHz (Laser reference)
801.58 MHz (Accelerator reference)
Or others frequencies in function of need
for diagnostics
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau
Courtesy : Daniel Charlet
Fractionnal PLL (FPLL) FMC (on test)
Replace very expensive system with recent, 30€ component
Generate arbitrary frequency disciplined by WR clock
  Frequency resolution 1 Hz
  Phase noise system: 1 ps (1 Hz, 10 MHz)
  ~0.3° RMS phase jitter at 375MHz below 1Hz
  4 outputs 10KHz to 1.3GHz (2.75GHz: SI5361H chip)

## Slide 21: New PLL : preliminary results
Rubidium
10MHz
SKY 63102
Jitter (rms) 400.79MHz@offset range [1Hzto 1MHz] =282fs
Jitter (rms) 176.1MHz@offset range [1Hzto 1MHz] =282fs
Jitter (rms) 125MHz@offset range [1Hzto 1MHz] =285fs
Jitter (rms) 88MHz@offset range [1Hzto 1MHz] =284fs
Jitter (rms) 10MHz
@offset range [1Hzto 1MHz]
=150fs
-10fs better than Si5362 used on FMC REFGEN board in offset range [12kHz to 1MHz]  validated
- Need characterization in the offset range [1Hz to 1MHz]
Jitter (rms) 10MHz@offset range [1Hzto 1MHz] =249fs (Rubidium)
Jitter (rms) 10MHz@offset range [1Hzto 1MHz] =150fs (Morion) from LTE
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau

## Slide 22: IDROGEN: roadmap and future directions
IDROGEN_V4
  Development for Q4 2025, mass production mid 2026
  Replacement of obsolete components
  Versatility Improvement
FMC-AD42JB69 (in development)
  4 channels 250MSPS 16bits
FMC-ADC 3GSPS
White Fox (Highly improved White Rabbit)
  Development with LTE
  Sub 100-fs performance (prototype in development)
Improve short term performance (ongoing development)
10Gb/s White Rabbit firmware
IDROGEN_v5
  New FPGA familly AGILEX
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau
Courtesy : Daniel Charlet
PERLE:
Improvements of slave IDROGEN jitter
Improvements by PTPrate & SoftPLL

## Slide 23: Conclusion
IDROGEN:
Very promising results with IDROGEN board (sub-picosecond RMS jitter)
New board version (v4) to be developed in Q1 of 2026
Focus on essential hardware development
PERLE:
Timegen board to be finalised
FTS board to be finalised
Installation of WR testbench
Bring WR switch
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau
Courtesy : Daniel Charlet

## Slide 24
17/12/2025
Journées annuelles 2025 GDR SCIPAC et Instrumentation Faisceau
Thank you for your attention