## Slide 1: ARRONAX: Accelerator for Research in Radiochemistry and Oncology at Nantes AtlantiX F. Haddad Prof. Nantes Université GIP Arronax / Subatech

## Slide 2
ARRONAX: Accelerator for Research in Radiochemistry and Oncology at Nantes AtlantiX
Professor ARONNAX
The name ARRONAX is a tribute to Jules Verne, born in Nantes in 1828.
Aronnax is the name of the main character of the novel «twenty thousands leagues under the sea » published in 1870
3 main fields of investigations :
  Radionuclides and radiopharmaceuticals production for nuclear medicine
  Research in related fields using our beams: Radiolysis, Radiobiology, nuclear physics, …
  Training of students

## Slide 3
Arronax un accélérateur dédiés à la recherche en santé
Production d’isotopes
Médecine nucléaire
Recherche en physique nucléaire
Recherche en chimie nucléaire
Utilisation des faisceaux
Radiobiologie
Radiolyse
Protonthérapie
Contrôle non destructif
Endommagements
Tests de détecteurs

## Slide 4: Cancer treatment
Cancer remains a leading cause of death globally, accounting for over 9.7 million deaths in 2022 and a Cancer incidence world wide of 19,98 million per year
Typical treatment strategy in cancerology is based on combination of treatment modalities and depends on the characteristics of the disease:
Targeted therapies including nuclear medicine
Chemotherapy
External radiotherapy
Surgery
Hormone therapy
SYSTEMIC
Local

## Slide 5
  Imaging and diagnosis (X-rays, γ-rays , β+ emitters)
    (e.g., PET, SPECT)
  Therapy (α particles, β- particles , Auger electrons)
    Targeted Radionuclide Therapy (TRT)
Nuclear Medicine
Nuclear medicine uses open sources (radionuclides)
Application
In some cases, the radionuclide can be used directly: I-131 for thyroid or Rb-82 for cardiology …
But, in most cases, a vector molecule (chemical molecules, peptides, antibodies … ) is needed to target the cells of interest.
Targeting Strategy

## Slide 6: We are all different
There is differences between patients:
Some are obvious : age, gender, height, weight, …
Some others are more subtle as biological constants, or genetic characteristics, …
There is a need to personalize treatment

## Slide 7: Theranostics
It is a treatment strategy that combines therapeutics with diagnostics as for example using matched pairs of radionuclides (68Ga/177Lu, 64Cu/67Cu,..).
The Right Drug To The Right Patient For The Right Disease
At The Right Time With The Right Dosage
Define the biodistribution of a therapeutic agent to anticipate its effect
Localized lesions
Calculate the optimal activity to be injected
Evaluate the response after treatment
Select patients which are expected to response to the therapeutic agent

## Slide 8
Activity injected to patient:
~few GBq
Targeted internal radiotherapy with β emitters

## Slide 9: Nuclear medicine at a glance
50 million nuclear medicine procedures performed annually
→ 90% for diagnostic purpose
Rapid evolution over the last 20 years:
  2000s: FDG becomes gold standard for PET imaging in oncology
  2005: FDA approval of Zevalin (⁹⁰Y-ibritumomab) for hematologic cancers
  2013: FDA approval of first alpha therapy using ²²³Ra
  2017: FDA approval of ¹⁷⁷Lu-DOTATATE for neuroendocrine tumours
  2022: FDA approval of ¹⁷⁷Lu-PSMA for metastatic prostate cancer
Targeted radiotherapies now available
→ Most pharmaceutical companies have launched nuclear medicine programs

## Slide 10
ARRONAX: Accelerator for Research in Radiochemistry and Oncology at Nantes AtlantiX
3 main fields of investigations :
Radionuclides and radiopharmaceuticals production for nuclear medicine
Research in related fields using our beams: Radiolysis, Radiobiology, nuclear physics, …
Training of students
Creation date 2008
First beams (Jan. 2011)
2 cyclotrons (C70XP and Kiube 180)
1 radiopharmacy (2018)
60 workers (including Phd students)
ISO 9001 certify since 2014
Key numbers :
Cyclone@Kiube 180 µA

## Slide 11
ARRONAX beam characteristics
With our cyclotrons with have access to a wide range of projectiles and beam energies at high intensity:
70 MeV proton beam: Sr-82
30 MeV proton beam: Ti-44
16 MeV deuteron beam : Cu-64, Hg197m
26 MeV deuteron beam : Cu-67
31 Mev deuteron beam: Pb-203
68 MeV alpha beam: At-211, Ru-97
18 MeV proton beam: F-18 (made by CPF - curium)
16 MeV proton beam: Cu-64
We are taking advantage of all beams available :
 | Projectiles | Particules accélérées | Energie (MeV) | Intensité (µA) | Modalités du faisceau | Nombre de casemate
C70XP | Proton | H- | 30-70 | 750 | dual | 5
 |  | HH+ | 35 | 50 | mono | 3
 | Deutons | D- | 15-35 | 50 | dual | 5
 | Alpha | He++ | 70 | 70 | mono | 3
IK18 | Protons | H- | 18 MeV | 180 | dual | 1

## Slide 12: ARRONAX Facility
A versatile facility:
  2000 m2 of restricted area
  2 cyclotrons
  4 vaults for isotope production
  1 vault with 3 beam line for research (2 horizontal and 1 vertical)
  3 lines of hot cells for radionuclides production
  A radiopharmacy with 3 lines of hot cells for sterile radiopharmaceuticals production
Several clinical trials performed using Ac-225, Lu-177 and Cu-64 and soon new ones with At-211 (IMPD approved by ANSM – bladder cancer).
The 200th clinical dose produced on October 10th

## Slide 13: ARRONAX beam characteristics
Main characteristics of the C70XP:
  Multi-particle
  High energy
  High intensity
  enlarge the scope of possible nuclear reactions for isotope production
low cross section phenomena usable
Neutron source with industrial capabilities possible
Large quantities to serve several users
Main characteristics of IK18:
  Cyclotron kiube 180
  1 beamline connected to a solid target station
  1 high power solid target station of the C70XP type connected to the existing rabbit system

## Slide 14: How to acces variable alpha energies?
Target handling after irradiation
Commissionning under way
Upgrade of the machine :
Development of an internal target to intercept the beam at the right energy (28-29 MeV)
  No more need to degrade the beam energy and better control of At-210 production
  Limitation will be now the target itself
Our Goals: improve both the quality and the quantities of the final product

## Slide 15
Sr-82
Cu-64
At-211
Cu-67
Hg-197m
Ti-44/Sc-44
Pb-203
Lu-177
Ru-97
Ac-225
Ge-71
Physics Chemistry pre Clinical Clinical
clinical trials Routine
Pipeline Arronax
New developments on Auger emitters

## Slide 16: The experimental vault AX @ Arronax
5 cm
Radiochromic film
33ns
Important work done by F. Poirier et al on a beam pulsing device
Important work done by C. Koumeir on beam shaping for experiment in AX
Casemate AX

## Slide 17
Nuclear data
Cross section measurements for radionuclide production
Detector testing
DORN detector that went on the moon
Archeometry
Determine the gilding thickness to understand the mediaeval manufacturing techniques
Bunch Counting : up to 100 particles par bunch (<1nA)
Train Counting : up to 1µA (FLASH)
Management of small animal irradiation in AX vault using our animal housing facility
Few examples of experiments at ARRONAX:
Irradiation
Notes: Utilisateurs : les laboratoires de santés (INSERM, CNRS, centre de lutte contre le cancer, CHU), la plupart des laboratoire de l'IN2P3 ont eu une équipe qui a travaillé chez nous (LPSC, LLR, IP2I, IJCLab, Subatech, LPC Caen, GANIL, LPC clermont, IPHC, Omega, CEA ...)

## Slide 18: Conclusions
Arronax possesses 2 cyclotrons:
  a versatile C70XP cyclotron allowing a wide range of radionuclide production as well as irradiation research.
  A kiube-180 cyclotron (named IK18) under final commissioning for F-18 and Cu-64 production mainly
GIP ARRONAX is producing radionuclides but also radiopharmaceuticals for research in nuclear medicine
GIP ARRONAX is conducting research with beams in diverse areas
After more than 15 years of operations, several upgrades are ongoing to increase services for users:
  Rejuvenation to compensate for component obsolescence (2M€)
  An internal target system to irradiate our alpha beam at 28 MeV directly (under commissioning)
These work can only be achieved through collective work at all scales (local, national and international)l and with all partners (academia and industry)

## Slide 19: The GIP Arronax evolution in time
2025:
commissioning of the new cyclotron
Commissionning of the internal target
1980
2019
Today
2007
2011
2012
2013
2014
2017
2018
2019
2020
Création du
GIP Arronax
Première
production
de Sr-82
ISO -9001
certification
Sr-82:
FDA and GMP agreement
Sr-82 approved in 8 european countries
Commissionning
Jannuary
Large projects funded at the national level
Equipex ArronaxPlus
Labex IRON
Ouverture de l’Annexe de la Pharmacie à usage intérieur
First clinical dose ever produced at our site
Projet initial : "un cyclotron à Nantes pour une recherche à dimension européenne en médecine nucléaire et radiochimie
Partners of European projects
PRISMAP and NOAR
More than 500 000 patients have benefited of our Sr-82 ain the USA since 2012
More than 20 000 euroepean patients have benefited of our Sr-82 since 2020
More than 200 clinical doses for clinical trials produced in our radiopharmacy
2018
2024
2023
New buldings
……..
First in Human Ac225-PSMA-R2

## Slide 20
The ARRONAX project is supported by:
  the Regional Council of Pays de la Loire
  the Université de Nantes
  the French government (CNRS, INSERM)
  the European Union.
This work has been, in part, supported by grants from the French National Agency for Research (ANR):
"Investissements d'Avenir", Equipex Arronax-Plus noANR-11-EQPX-0004, Labex IRON noANR-11-LABX-18-01.
"France 2030 investment plan" under the references I-SITE NExT (ANR-16-IDEX-0007) and Labex DHOLMEN.
Thank you for your attention