Detector optimisation for the ShiP Experiment

---
Prologue
SHiP is an approved CERN experiment
“Approved” means that CERN agreed to refurbish the Beam Dump Facility in the ECN3 experimental hall
Now formation of detector collaboration
Many components in very preliminary state in many aspects
This concerns in particular layout of Scattering and Neutrino Detector (SND, see later)
So far IJCLab gives technical help through IT staff (“historical” connection through LHCb)
Possible application of our SiW ECAL R&D in real experiment
Relevant physics case

---
Silicon Tungsten electromagnetic calorimeter
Optimized for Particle Flow:
Jet energy resolution 3-4%, Excellent photon-hadron separation
Basic Requirements:
Extreme high granularity
Compact and hermetic
(inside magnetic coil)
Basic Choices:
Tungsten as absorber material
X0=3.5mm, RM=9mm, lI=96mm
Narrow showers
Assures compact design
Silicon as active material
Support compact design
Allows for pixelisationRobust technology
Excellent signal/noise ratio: 10 as design value
The SiW ECAL in the ILD Detector
- O(108) cells
- “No space”
=> Large integration effort
All future e+e- collider projects feature at least one detector concept with this technology
Decision for CMS HGCAL based on CALICE/ILD prototypes

---
Silicon Tungsten electromagnetic calorimeter – Example ILD
Ecal alveolar structure
PCB+FEE
1.2 – 2.8mm
Sensor: ~500µm
Sandwich calorimeter
26 layers (+/- 4)
Thickness: ~20cm, 24 X0/1λI
Pixel size ~5x5 mm2
Expected elm. energy resolution 15-20%/√E
8.2- 13.5mm

---
SHiP Physics case
The SHiP experiment will search for a broad range of feebly interacting particles such as:
• Light Dark Matter
Heavy Neutral Leptons (HNLs)
• Dark photons
• Dark Scalar Higgs-like particles
• Axion-like particles (ALPs)
In addition SHiP will allow for a rich set of tests of Standard Model physics in with neutrinos
Relevsnt for today:
Neutrino Physics
LDM

---
SHiP Schematic Layout
Andrei Golutvin
ShiP Spokesperson

---
ShiP Calorimetry

---
ShiP Calorimetry

---
SHiP Schmatics

---
Scattering and Neutrino Detector (SND)?

---
A SHiP Layer?
Should be straightforward to arrange SiW ECAL ASUs
Modularity inherent to detector design
N.B.: 18x18 cm2 is not a canonical number but many tools are
or will be developed for this size
Cleary would need dedicated study on mechanical housing
“Long layer” tests will be part of the 2025/26 test programme
36cm
36cm

---
A SiW Ecal for SND?
Questions
How many SiW Ecal layers and where?
Rear part of target or MTC or both
Knowing that an SiW Ecal layer is not cheap
Require serious optimisation study

---
Optimisation How - Co-design?
What does it mean in practice?
It means creating a full parametric model of the detector, plugging in a surrogate model of the physics, and a differentiable model of the data reconstruction and inference extraction
Then you can iteratively modify the detector parameters following the gradient of the utility function – like in a NN
Detector parameters x
Utility evaluation and derivatives dU/dx
x x + λ dU/dx
Reconstruction and inference
Physics surrogate model
Dumbed down version of an optimization pipeline
Tommaso Dorigo, DRD Calo Meeting, April 2025
A fiirst proposal for P2I in April worked out with the help of Tommaso and Andrei was
not supported by IJCLab Direction (“too early”)

---
Summary
SHiP covers relevant questions of particle physics and is (among) most powerful experiment(s) for feebly interacting
particles for decades to come (at least in the low mas range < 10 GeV)
SHiP as potential application of SiW ECAL
Detector optimisation for SHiP would have to start soon, i.e. now!
In our case how many Ecal layers and where it’s best to place them
A nice use case to learn/apply the principle of Co-design?
We would however start exactly from zero!
Development for SHiP could/should leverage on R&D in DRD Calo
Building up on R&D for Linear Colliders, synergies with hardware development for FCCee
Synergies with other similar experiments (that may take data before SHiP)!?
IJCLab direction in favor of joining SHiP
Despite “rejection” of P2I proposal in April
CODEC in December 2025
Pre-discussions with direction before

---
Backup

---
SiW Ecal Technological prototype – Elements of (long) layer
Interconnection
(IJCLab)
HV Supply
(IJCLab, LLR)
ASIC SKIROC2(a)
(OMEGA)
Wire Bonded or
In BGA package
(IJCLab, U Tokya, LLR)
    ASIC+PCB+SiWafer
        =ASU
        Size 18x18 cm2
(IJCLab, U Tokyo, OMEGA, LLR, SKKU)
Connection between 2 A.S.U.
Digital readout
SL-Board (IJCLab)
 Si Sensors
  glued
onto PCB
Pixel size
5.5x5.5 mm2
(IFIC, CERN)
The beam test set ups comprised mainly short layers consisting of one ASU and a readout card each
7 A.S.U.
~1500mm
total
“end” PCB