## Slide 1: TTC 2026 meeting Paris-Saclay June 12 2026 Superconductivity in Space An active magnetic shield to protect astronauts for interstellar travels Bertrand Baudouy Université Paris-Saclay, CEA, Département des Accélérateurs, de la Cryogénie et du Magnétisme bertrand.baudouy@cea.fr

## Slide 2: Goal
Safe travelling into deep space for humans
Settlements on Mars
Retirement on the Moon
But…

## Slide 4: Radiation effects on biological tissues

## Slide 5: The interstellar travelling case
The evidence for cancer risks from humans who are exposed to low Linear Energy Transfer radiation is extensive for doses above 100 mSv
  Sievert represents the health risk of ionizing radiation (1 Sv = 5.5% prob. developping a fatal cancer)
The doses that are to be expected on space missions, as well as the nuclear type and energies are quite well understood but not really the effect…
The main contribution to the ionizing radiation encountered in deep space
  Solar Particle Events (SPE)
    Protons and helium from Sun
    High Flux – Low Energy
  Galactic Cosmic Rays (GCR)
    Protons, helium and ions
    Low Flux – High Energy
GCR are the dominant source of the dose for a long duration mission
Solar and Heliospheric Observatory, SoHO, 1995-2016…

## Slide 6: Radiation dose in different missions

## Slide 7: Doses in our Universe
Free space : above1200 mSv/year
Spacecraft (thin) shielding : 700-800 mSv/year
On the Moon surface : 223 ± 10 mSv/year as a function of the solar activity
ISS : 180 mSv/year so maximum 3 missions for 18 months total (only for men)
On the Mars surface : 100-200 mSv/year depending on the location
Maximum dose for professional workers : 20 mSv/year (1 Sv career)
Average dose on Earth : 1 mSv/year
Human body radiation : 0.25 mSv/year
Human body is not biological adapted to deep space

## Slide 8: % of death due to cancer for a Mars mission
A mission to Mars has up to 40% risk of cancer death and acute effects (with current protection)
High uncertainties for dose estimation and effects (up to 500%)
Of about 27000 man-days in space only 303 have been outside of the magnetosphere in the Apollo missions (1.1%)
Cucinotta, Durante, Nat. 2008

## Slide 9: Shielding strategies
Active
Based on the ionization losses
in materials of sufficiently depth to stop the incident particles
Current shielding for spaceship
Electrostatic
Plasma
Magneto-static
Large superconducting magnets surrounding the spacecraft human habitat
Passive

## Slide 10: Passive Shielding
Easiest solution
Stopping Power ∝ 𝒁𝟐
  very effective for heavy ions
  not for protons
Large thickness for shielding light ions
  Otherwise secondary emission
Effective for SPE but not for GCR
50 g/cm² for 500 days for mission
Thousands of tons for a Mars spacecraft
To Mars
200 mSv/year

## Slide 11: Magnetic active Shielding for spaceship
Physics requirements
  The magnetic field must be tangent to the shielding volume to bend the particles away
Biological requirements
  Low Magnetic Field inside the Human Habitat (less than 4 mT)
  Maximum Protection
  Uniform protection
Technical Requirements
  Launchability ⟶ (limits on dimensions and mass)
  Reliability
  Redundancy
  “Renewable” cryogenic cooling system

## Slide 12: It is a research topic for 50 years!
S.W. Kash and R.F. Tooper, ITT Research Institute, Chicago, 1967
5 T
NbTi
1961 - 2007 conceptual studies on magnetic shielding
Between 2010 and 2015, for the first time, technological investigations were carried out to verify the feasibility of superconducting magnets for cosmic radiation shielding.
ARSSEM 2010 partially funded by ESA
MAARS 2012-2014 funded by NIAC
SR2S 2013-2015 partially funded by the European Union

## Slide 13: Different types of magnetic shielding
Solenoids
Toroids
Large turns
Double helix

## Slide 14: The best classic solution: Toroids
Initial solution of the Space Radiation Superconducting Shield (EU-FP7-SR2S grant agreement n° 313224 2013-2015)
  develop, validate and increase the TRL of the most critical technologies related to a magnetic shielding system for protecting astronauts’ lives during long duration space missions
Low magnetic field inside de Human habitat
Maximum protection : B always perpendicular to the particles trajectories
Uniform protection
Launchability : depends on the mass
Redundancy
HTc superconductor and no cryogen reservoir
Reliability
  Quench protection
  High mechanical load towards the habitat
B = 40G isolines B over conductor = 4T
Analytic solution blue proton tracks

## Slide 15: SR2S Toroid design
Preliminary design of the magnet
Dimensions / weight / materials
No magnetic field inside the habitat
Reliability of the Active Shield
Mechanics
containing compressing forces/displacements
protect the habitat
Cryogenics and thermal interfaces
Decoupling the magnet from the habitat / heat sources (sun, planets)
Cool down the magnet
Dose reduction:
Optimize secondary particles production with materials
Reduce primary and secondary particle flux & dose with the magnetic field
Superconductive cable
Testing and Validating Ti clad MgB2 cable
How to protect the magnet from quenches

## Slide 16: Magnet parameters
MAGNET MAIN PARAMETERS | 
Current Density | 70
# of turns | 55
# of layers | 10
# of racetracks | 120
Bending Power | 7.51 Tm
Bmax over conductor | 3.7 T
Stored Energy | 953 MJ
Inductance | 3890 H
SC Mass | 36.7 tons
E/M ratio | 26 KJ/Kg
Inward force per racetrack | 4.2 MN
Mechanical Structure | 91.0 tons
MAGNET MAIN PARAMETERS | 
Current Density | 
# of turns | 55
# of layers | 10
# of racetracks | 120
Bending Power | 7.51 Tm
Bmax over conductor | 3.7 T
Stored Energy | 953 MJ
Inductance | 3890 H
SC Mass | 36.7 tons
E/M ratio | 26 KJ/Kg
Inward force per racetrack | 4.2 MN
Mechanical Structure | 91.0 tons
5.5 m long toroid
V. Calvelli (INFN)
Columbus lab Ø 4.5 m and 6.9 long

## Slide 17: Cable configuration
Ideal
Ti clad MgB2 with Al Strips
Ti/MgB2 ratio 2.7/1
Real (for now but known how to solve it)
Ti clad MgB2 with Cu Strips
The lighest superconductor ρ = 3000 kg/m3
380 m prototype

## Slide 18: Cable Magnet configurations
Configuration A
10 m
Main material: Titanium
Mass = 300 tons
BL = 7.9 Tm
Configuration B1
10 m
Main material: Kevlar
Mass = 100 tons
BL = 7.9 Tm
Configuration B2
10 m
Main material: Kevlar
Mass = 100 tons
BL = 11.9 Tm
A
B1
B2

## Slide 19: Dose reduction
Primary: Z=1-26
Off
On
Off
On
Off
On
B1
B2
A
HZE ions stopped (as forecast) by uniformity of materials
Secondary particle productions: neutrons are more present than protons (new result) ⟹ Toroids efficiency extremely reduced

## Slide 20: Thermal design
Human Habitat : 6,9 m long and 4,5 m diameter
MgB2 toroïdal magnet : 10 m long and 12 m diameter
Sun
1371 W/m²
Mars
~500 W/m²
Permanent heat loads
  Heat fluxes from the Sun and Mars/Earth
  Heat fluxes from the human habitat
Temperature sink 7 K

## Slide 21: Cooling design
Space
Earth
Cryogenic design of the SR2S Magnet
James Webb Space Telescope
ATLAS Magnet (CERN)

## Slide 22: Sunshield option
V-groove + MLI sunshield around the magnet to reduce the radiations heat loads coming from the sun or planets
3 V-groove layers (10 mm thickness)
3° between layers
MLI conduction modeled in every layer
Reduction of the sun heat load from 200 kW to 1 W

## Slide 23: Human Habitat heat load
80 K shield necessary to lower the heat fluxes from the human habitat
Human habitat
300 K
100 W to be extracted @ 80 K
10 mm Aluminum
80 K internal shield
10 W to be extracted @ 10 K
Magnet cold mass 10 K
MLI
MLI

## Slide 24: Thermal links
8 regular pulse tube cryocoolers (4 W @ 10 K) needed to cool down the entire magnet
Human habitat
300 K
110 W @ 80 K
11 W @ 10 K
Magnet cold mass 10 K
2nd Stage
1st Stage
2nd Stage : no need of any thermal link using pure titanium as the structural component
1st Stage : Long efficient thermal link
Development of extra long two-phase heat pipe working without gravity = Pulsating Heat Pipe (PHP)

## Slide 25: General thermal design

## Slide 26: Pulsating Heat Pipe
Two-phase capillary flow heat pipe → gravity independent
Passive heat exchanger with a capillary smooth tube
Tube arranged in U-shape in several turns thermally connected between an evaporator and an condenser separated by an adiabatic region
Tube partially filled by the working fluid in two-phase close to saturation
Tube diameter → dominating capillary force
Complex oscillating movement
  Vaporization at the evaporator and overpressure in the tube branches
  Vapor bubbles motion
  Liquefaction at the condenser
High heat transfer
  Combination of phase change and advection in the liquid parts

## Slide 27: The longuest cryo PHP
3.7 m long PHP
  1.5 mm inner diameter
  12, 24 and 36 tubes
  30 cm evaporator and condenser
  3.1 m adiabatic part
175 W cryocooler at 77 K

## Slide 28: The longuest cryo PHP
Condenser temperature controlled at 80 K Power 10 W Void fraction 33%
4 m PHP k≈ 200 kW/m.K to 300 kW/m.K
One hour stability!

## Slide 29: Will we go to Mars soon?
Will we go to Mars soon?
Better magnetic configuration
Improvement of the MgB2 cable properties
Improvement of the cryogenic system
Reduction of the mass
Construction of the magnet
Launch scenarios
And the cost…

## Slide 30: Spin-off : A new magnetic configuration
The pumpkin configuration
Valerio Calvelli (CEA Paris-Saclay)
Magnetic flux density contour lines of the new configuration
Calvelli, V et al. A Novel Configuration for Superconducting Space Radiation Shields, IEEE TRANSACTIONS ON APPLIED SUPERCONDUCTIVITY, 27, 4, 0500604, JUN, 2017, 10.1109/TASC.2016.2642638

## Slide 31: Spin-off : HTS magnet cooled by PHP
Most powerfull PHP in helium (more than 1 W à 4 -7 K)
First application of cooling a HTS magnet (5 T) by PHP neon and He temperature
Dixit et al., Cryogenics 132 (2023) 103670
Dixit et al., Applied Thermal Engineering 251 (2024) 123613
Dixit et al., Cryogenics 152 (2025) 104214

## Slide 32: Spin-off : SRF Cavity cooled two-phase He
Cryocooling for SFR cavity with two-phase flow or PHP
Fermilab
Helium circulation loop cooled by a cryocooler
Thomas Proslier at al.

## Slide 33
SR2S team
Maria “Asun” Barba (CEA Paris-Saclay)
Antoine Bonelli (CEA Paris-Saclay)
Romain Bruce (CEA Paris-Saclay)
Roberto Battiston (Italian Space Agency)
Valerio Calvelli (INFN)
Ricardo Musenich (INFN)
Giovanna Ober (CGS)
Martina Giraudo (Thales Alenia Space)
CREDITS
PHP team
Tisha Dixit (CEA Paris-Saclay)
Gilles Authelet (CEA Paris-Saclay)
Vadim Stepanov (CEA Paris-Saclay)