## Slide 1: Plasma Processing of elliptical cavities at INFN - LASA TTC 2026, WG2, Paris-Saclay Elisa Del Core LASA – INFN, Milan

## Slide 2
Outline
  Plasma Processing
    ESS MB 704.4 MHz – unity coupler
    ESS MB 704.4 MHz – custom antenna
    ESS MB 704.4 MHz – spectrometer analysis
  Summary & Next steps
    ESS MB 704.4 MHz – FPC
    PIPII LB650
INFN – Laboratori Nazionali di Legnaro
Quarta Giornata Acceleratori 3-4 Aprile 2025

## Slide 3
Outline
  Plasma Processing
    ESS MB 704.4 MHz – unity coupler
    ESS MB 704.4 MHz – custom antenna
    ESS MB 704.4 MHz – spectrometer analysis
  Summary & Next steps
    ESS MB 704.4 MHz – FPC
    PIPII LB650
INFN – Laboratori Nazionali di Legnaro
Quarta Giornata Acceleratori 3-4 Aprile 2025

## Slide 4: Plasma Processing @LASA
Initial Aim: develop a method to cure Field Emission both in situ and on the vertical test stand, for MB 704.4 MHz 6-cell ESS (β=0.67) and LB650 PIP-II 5-cell (β=0.61) cavities. We have started this activity in partnership with ESS, CEA and FNAL labs.
Our setup:
No HOM ports  we have to use unity coupler (for VT configuration) or FPC
In the VT configuration both input and output gas ports on PU side  Is hydrocarbons removal efficient?
Currently: experimental activity on ESS MB cavities
& simulations on PIP-II cavity
Mitigate Field emission to reduce RF power consumption
Prevent the need of disassembling cavities from cryomodules, leading to lower costs, reduced time and longer lifetime.

## Slide 5: First RF setup
RF rack

## Slide 6
Outline
  Plasma Processing
    ESS MB 704.4 MHz – unity coupler
    ESS MB 704.4 MHz – custom antenna
    ESS MB 704.4 MHz – spectrometer analysis
  Summary & Next steps
    ESS MB 704.4 MHz – FPC
    PIPII LB650
INFN – Laboratori Nazionali di Legnaro
Quarta Giornata Acceleratori 3-4 Aprile 2025

## Slide 7: First Setup
1.2 - 1.4 GHz 500 W / 0.5 – 2.5 GHz 200 W amplifier
Range covered with measurements: 1.1 – 1.7 GHz
Vacuum pressure: 0.25 – 0.35 mbar
Ignition gas: Nitrogen
Two viewports + 1 camera
Unity coupler
RF power levels constantly monitored
N2 IN
RF IN
ESS MB 704 MHz cavity MBLG002
𝑄0 ≈ 104 and a 𝑄𝑒𝑥𝑡 ≈ 6 ⋅ 109
Experimental apparatus
𝑁2 first ionization energy ≈ 14.5 eV
RGA not yet implemented
No active pumping

## Slide 8: VNA S21 & S11 1 – 2 GHz - ESS
Mode for ignition: 1.44897 GHz
Modes tried
S11 not calibrated
Several modes exhibit reasonable coupling at room temperature. Lower coupling requires more forward power to achieve plasma ignition.
Excited mode localized in the beam tube, on the main coupler side

## Slide 9: VT MC Antenna
L ~ 18 mm
 Tube inspection when FPC will be installed
Titanium nitride (?)
During these tests, we unintentionally ignited the main coupler antenna several times, using different frequencies.

## Slide 10
Outline
  Plasma Processing
    ESS MB 704.4 MHz – unity coupler
    ESS MB 704.4 MHz – custom antenna
    ESS MB 704.4 MHz – spectrometer analysis
  Summary & Next steps
    ESS MB 704.4 MHz – FPC
    PIPII LB650
INFN – Laboratori Nazionali di Legnaro
Quarta Giornata Acceleratori 3-4 Aprile 2025

## Slide 11: RF & vacuum setup

## Slide 12: S21, S11 new custom antenna
Chart: ESS MBLG002, Antenna 138 mm
L = 138 mm
Params | 
Q0 | 9600
QL | 8914
SWR | 12.014
Qext | 1.15E+05
βi | 0.083
Qext FPC ~ 7.5 E5

## Slide 13: Paschen Curve – N2
Chart: Pressure [mbar]
| 5.2999999999999999E-2 | 5.8000000000000003E-2 | 6.3899999999999998E-2 | 7.4499999999999997E-2 | 8.2100000000000006E-2 | 8.6499999999999994E-2 | 9.74E-2 | 0.105 | 0.14899999999999999 | 0.17699999999999999 | 0.21 | 0.24199999999999999 | 0.315 | 0.41399999999999998
P in cavity [W] | 27.0396 | 25.1189 | 23.8232 | 20.0909 | 18.7499 | 15.1356 | 12.6183 | 11.1944 | 8.2985 | 6.8077 | 6.223 | 4.7206 | 4.4566 | 3.4674
P amp [W] | 63.12 | 58.34 | 55.3 | 46.7 | 43.6 | 35.3 | 29.3 | 26 | 19.3 | 15.9 | 14.5 | 10.9 | 10.4 | 8.1
Theoretical Paschen curve
Experimental Paschen curve

## Slide 14: Propagation from cell to cell
Used modes
Successful ignition of several mode
Successful propagation from the 1st cell (PU side) to the last one (6th cell, MC side)

## Slide 15
Outline
  Plasma Processing
    ESS MB 704.4 MHz – unity coupler
    ESS MB 704.4 MHz – custom antenna
    ESS MB 704.4 MHz – spectrometer analysis
  Summary & Next steps
    ESS MB 704.4 MHz – FPC
    PIPII LB650
INFN – Laboratori Nazionali di Legnaro
Quarta Giornata Acceleratori 3-4 Aprile 2025

## Slide 16
Spectrometer analysis
~ 315 nm
~ 337 nm
~ 357 nm
~ 380 nm
N2 peaks
He gas injection
N2 gas injection

## Slide 17
Spectrometer analysis
He gas injection
N2 gas injection
Other N2 peaks
~ 388.9 nm
~ 501.6 nm

## Slide 18
Spectrometer analysis
N2 gas injection
He gas injection
~ 587.6 nm
~ 667.8 nm
~ 706.5 nm
~ 728.1 nm
He peaks
O2
Other N2 peaks

## Slide 19
Outline
  LASA introduction
  Plasma Processing
    ESS MB 704.4 MHz – unity coupler
    ESS MB 704.4 MHz – custom antenna
    ESS FPC
  Summary & Next steps
    ESS MB 704.4 MHz – FPC
    ESS HB 704.4 MHz
    PIPII LB650
INFN – Laboratori Nazionali di Legnaro
Quarta Giornata Acceleratori 3-4 Aprile 2025

## Slide 20: Summary ESS MB
Unity Coupler ESS MBLG002
This antenna configuration does not appear suitable for cavity processing  No additional modes are excited neither propagation observed
Antenna (L = 138 mm) – Test Results
Stronger coupling compared to the FPC
Ignition of several modes at relatively low power
Successful plasma bridging: propagation achieved from Cell I to Cell VI and vice versa, multiple times → Propagation strategy validated
Operating pressure: 1.13 × 10⁻¹ mbar
Repeat the procedure, using He instead of N2
𝑁2 first ionization energy ≈ 14.5 eV
He2 first ionization energy ≈ 24.6 eV

## Slide 21: ESS MB: Next Steps
Plasma processing with FPC (from CEA/ESS FPC + coax-to-N type adapter)
Transition from static to dynamic pumping configuration → Vacuum + gas injection chart to be developed with ESS, taking as reference the FRIB model

## Slide 22
PIPII LB650
Simulations done  suitable modes identified
Unity coupler weakly coupled  FPC
Proto cavity B61-EZ-001 from CEA and FPC from FNAL already at LASA  next week assembly of FPC and first experimental activities with
Bianca Giaccone
Activities developed in partnership with FNAL (B. Giaccone, T. Posos) and CEA
FPC
RF adapter

## Slide 23
ACKNOWLEDGEMENT
“This work was partially supported by the European Union’s Horizon Europe Marie Sklodowska-Curie Staff Exchanges programme under grant agreement no. 101086276.”

## Slide 24
THANKS FOR YOUR ATTENTION

## Slide 25
BACKUP SLIDES

## Slide 26
P. Tutt et al., "Plasma Processing of FRIB-Low Beta Cryomodules using Higher-Order-Modes", https://doi.org/10.48550/arXiv.2511.02151

## Slide 27: 1295.16 MHz
8

## Slide 28: 1238.97 MHz
9

## Slide 29: 1188.26 MHz
10

## Slide 30: 1135.598 MHz
11

## Slide 31: 1238.64 MHz
12

## Slide 32: 1507.2 MHz
13

## Slide 33: 1238.71 MHz
14

## Slide 34: 1295.6 MHz
15

## Slide 35: 1144.6 MHz
16

## Slide 36: FPC ESS

## Slide 37: FPC ESS