## Slide 1: SRF Robotic Assembly Development at Fermilab
Colin Narug
FERMILAB-SLIDES-26-0085-TD
June 10th, 2026

## Slide 2: Robotic Assemblies in Cleanroom
Multiple successful robotic assemblies have been performed on SRF cavities at Fermilab
Vacuum end couplers assembled on SSR2 cavities
Beamline bellows assembled on SSR2 cavities
Beam Flanges assembled after HPR
The robotic assembly of couplers and beamline bellows on SSR2 cavities has been validated and is now part of the cleanroom assembly procedure for the PIP-II SSR2 cavity string assembly.
Beamline bellows assembly on SSR2 cavity
Assembly of flanges on 650 Cavity
Vacuum-end Coupler assembly on SSR2 cavity

## Slide 3: Assembled Cavities
SSR2 cavities used to validate initial assembly
4/5 cavities met project requirements
2 pre-production SSR2 Field Emission Free cavities have been produced
String assembly validation in process
SSR1 Cavities
First cavity assembled in March has been qualified
Post-HPR Assembly
5 assemblies performed with 1 unqualified cavity
  Improvement from manual installation
Validation of processes done by cavities

## Slide 4: String Assembly
Two assembly tasks performed: Bellows Alignment and Coupler Assembly
Removed from cleanroom in November
Results from Cryomodule will be known Fall 2026
In September 2025, first string assembled with robotic assistance

## Slide 5: String Assembly – Lessons Learned
Assembly was able to be completed with minimal issues, but there is room for improvement.
Assembly takes 2x-4x longer than “manual” assembly
Small inefficient steps create delays
  Switching tooling, bolts in tooling, unclear program structures
Many things learned through doing assembly process

## Slide 6: Vision System
To allow for continual development, code and tutorials documented on Github
Fermilab's SRF Robotics group's automated alignment program.
  FERMILAB-CODE-2026-03-TD
Possible to swap out nodes for different robots, cameras, and detection algorithms.
Two methods setup:
  April Tag
  Markerless
Robotic Operating System (ROS 2) used to start creating a versatile environment for development

## Slide 7: April Tag Framework
To avoid focus on code framework, April tags chosen as initial alignment method.
Part of Visual Servoing Platform (VISP):
  Visual Servoing Platform: Tutorial: AprilTag/ArUco marker detection
Automatically detect 3D pose of marker
By placing 4 around desired position, center can be found while minimizing error
  Less reliant on precision of detected parts and geometric design
Developed by A. Ciaramella and N. Giffen
Image Source: Visual Servoing Platform: Tutorial: AprilTag/ArUco marker detection

## Slide 8: Markerless Framework
Optimal configuration allows for open cavity to be aligned.
6D point estimation performed using Perspective-n-Point pose computation
  Detects and extracts holes, fits ellipse, then tracks points.
Edge segmentation used to improve tracking
  Neural network trained detection algorithm to fit ellipse
0.11mm of precision achieved
Developed by A. Vivai and N. Giffen

## Slide 9: Vision Implementation in Cleanroom
Both assemblies showed mixed results for implementation of vision system due to setup errors.
Algorithm able to detect flanges however…
For first installation, manual creation of “Goal” position, lead to errors in desired position
  Both algorithms moved arm to a position, however final position was not correct.
Second installation fixed goal position, however networking issues prevented marker-less alignment from being performed.
Additional setup time planned for next installation
Planned July 2026
Two installations have been performed using an automated alignment process

## Slide 10: Path Forward
While process have improved, to ensure long-term stability, work focus will shift from specifically R&D to process improvements
Work focusing on improving efficiency, cleanliness, and Work Planning Controls
Adapting work to “similar” assemblies.
Future R&D tasks should be pursued in parallel when opportunities are available.
Some outstanding risk:
  Maintaining and expanding existing codebases consistency
  Maintaining design coherency
Next Milestone: SSR1 String Assembly planned for Fall 2026
Robotics have consistently been shown to enhance assembly capabilities over multiple projects.

## Slide 11: Special Thanks
Engineers/Scientists
D. Passarelli, G. Wu, M. Parise, T. Aiazzi, J. Bernardini, J. Helsper, M. Quinlan, Y. Xie
Cleanroom Team and Machinists
D. Bice, R. Kirschbaum, T. Fermanich, M. Battistoni, M. Chlebek, T. Ring, D. Santucci, P. Alexander, T. Kelly, and the village machine shop
University Partners
A. Ciaramella, A. Vivai [UniPi]
N. Giffen, J. Imburgia, C. Denton, I. Salehina, J. Ryu [NIU]
Work supported, in part, by the U.S. Department of Energy, Office of Science, Office of High Energy Physics, under U.S. DOE Contract No. DE-AC02-07CH11359.
Work presented was a result of a large collaboration between many groups