## Slide 1: COBOT operations and development at CEA
WG-4: R&D challenges for future advanced projects
J. Drant on behalf of DACM cobotization team
TTC 2026 Meeting – Gif Sur Yvette
June 10th, 2026

## Slide 2: Outline
TTC 2025 reminder
Coupler on cavity assembly
Bellows on cavity assembly
Extended blow cleaning capabilities
Use of programs
Actual and future developments
Conclusion

## Slide 3: TTC 2025 reminder
To continue and extend cobotization steps at CEA :
Use of a Fanuc CRX25 Cobot :
  25kg payload,
  Tool changer,
  Dedicated tooling for coupler and bellows
  3D vision system
  Suction gripper
  Path programming with digital mockup
A lot of work on particles contamination associated with assemblies using the new cobot
  Studies and mitigation of particles sources of cobot (venturi, power supply rack, …)
    Particles free
  Studies of contamination caused by a assembly/disassembly of a flange and assembly sequence of a PIP-II mockup coupler on cavity
    No particles >0,1µm inside the cavities during the whole sequences

## Slide 4: PIP-II coupler on cavity assembly
Validation and demonstration of the cobot’s effectiveness in PIP-II project by assembling a production coupler onto a PIP-II cavity.
Removal of fasteners
Validation of critical steps
Final installation and torque tightening of fasteners
Blow cleaning and particle counting of components
Removal of the cavity flange
Alignment and installation of the coupler
  Validation of coupler assembly with cold RF test in horizontal cryostat without field emission at Fermilab administrative limit 19,4MV/m

## Slide 5: PIP-II bellows assembly
Use of the cobot to assemble the bellows on PIP-II cavities
Removal of fasteners
Validation of critical steps
Final connection on the other cavity
Final installation and torque tightening of fasteners
Blow cleaning and particle counting of components
Removal of the cavity flange
Alignment and installation of the bellows on one cavity
  The cobotization of these steps helps to reduce the whole bellows assembly duration

## Slide 6: Extended blow cleaning capabilities
Building on the developments initiated during the ESS project, the blow cleaning and particle counting of components has been expanded by using versatile tooling :
  All the components flanges involved in the assembly (cavity, coupler, beam pipe ends )
  All the fasteners (studs, washers, nuts)
  The components (couplers, bellows, gate valves)
For the first assemblies, we keep a final particle control by operator before assembly to validate cobot particle counting
Significant time savings from working during hidden time (lunch time/night)

## Slide 7: Use of the programs
The wide range of possibilities offered by cobotization translates into a broad array of programs with 2 goals :
  Make it easier for cleanroom operators who are not cobot experts to use the cobot,
    Significant effort on the human-cobot interface
  Adaptation to different cavity strings configurations (ex: coupler assembled or not)
    Customized combination of core programs
Example of a program selection diagram for the operator
Example : Assembly a bellows between two cavities
AAN_24 + AAS_24
Cleaning of cavity blank flange
Cleaning of the bellows
Cleaning of cavity valve flange
Can be done in hidden time
Handling of cavity blank flange
Assembly of bellows
Must be done with an operator present in cleanroom

## Slide 8: Actual and future developments
With the recent integration of FANUC robots into the ROS2 infrastructure and the accelerated development of robotization/cobotization in laboratories, joint development projects can be simplified
Using the two robotic arms at the CEA (CRx10 and CRx25) to work in parallel or collaboratively
  Blow cleaning of different component at the same time
  One cobot is equipped with the blowing tool and the other with the particle counter to enhance the adaptability of the particle counting process
  Enhance the range of assemblies in collaboration with operators (ex: subassembly with a simplify accessibility for the operator to install the fasteners)
Continue to develop the two development axis of cobotization at CEA
  Cleaning a larger range of components (valves, small cavity string components, …)
  Assembling a extended range of component (gate valves, pumping crosses, …)

## Slide 9: Conclusion
At CEA, several tests and studies have demonstrated the value and effectiveness of cobot in assembling components in cleanroom
The objectives are to continue expanding the range of operations performed through cobotization by utilizing a second cobot and through collaborations (ex: program FJPPN with KEK colleagues: robotization of clean room assembly)
The cobot has been successfully integrated into the production of cavity strings assemblies for the PIP-II project (involving multiple cleaning operations on components and the assembly of couplers and bellows)
  The time savings in cleaning operations observed in the ESS project are also evident in the initial assemblies of the PIP-II project
  Time savings also translate to higher-quality assemblies due to the faster assembly processes (reduced alignment time and reduced exposure of RF surfaces to air)
  The time saved allows operators to focus more on high-value-added activities, such as detecting anomalies in components.

## Slide 10: Robotic Team at CEA / Irfu
Christophe SERVOUIN
Senior technician
CRX25 integration
Roboguide (visualization/simulation)
Cobot programs
Stephane BERRY
PhD
- Development of robotic assisted assembly
Julien DRANT
Mechanical Engineer
- End of arm tooling designer

## Slide 11: Thank you
CEA SACLAY
91191 Gif-sur-Yvette Cedex
France
julien.drant@cea.fr