## Slide 1: High-power operation of the FPC for HEPS 166.6 MHz SRF cavities
Tongming Huang
IHEP

## Slide 2
Outline
Introduction
High-power tests (on-stand, on-cavity)
On-line operation
Summary

## Slide 3
Introduction
Fundamental RF
RF frequency: 166.6 MHz
Total RF voltage: 5.14 MV
RF power per cavity: CW, 190 kW
Max. FPC power: CW, 250 kW (SSA limit)

## Slide 4
Challenges (compromise)
Challenges: CW 250 kW + Cavity-wall location
Compromise and balance have been essential throughout the entire design process.
High RF loss  High dynamic heat load
Minimum FE damage risk
Low cryogenic heat load
Cleanroom assembly
Coupler location: close to cavity’s
H-end
Large magnetic field leakage  High dynamic heat load
Coupler location:
far away from cavity’s H-end
Long outer conductor
Short outer conductor and limited by cryostat size
High power level

## Slide 5
Main features (series design-B)
RF window
- Single window (Tristan-type)
- Ceramic size: 27.4*120*10 mm
- Ceramic material: 97.6% Al2O3 (Morgan AL-300)
Coaxial section
- OC: Double-wall structure
  Φ: 100mm, length: 402 mm, Zc: 50 Ω
  Thickness: 1mm SS + 20μm RRR30 copper plating
- IC: Made of copper (OFHC)
Transition component
- T-box structure
- Outer T-box dimension: 340*340*340 mm
- DC bias: ±2000V
Cooling
- Inner conductor (vacuum part): water
- Outer conductor (vacuum part): cold helium gas
- Inner conductor (air part): forced air
- Inner T-box (air part): forced air
Detector
- Vacuum, electron current, arc
Vacuum part
Vacuum part assembled with cavity in clean room

## Slide 6
2 prototypes and 10 series FPCs were fabricated at Beijing HE-Racing Technology from 2017 to 2025.
Fabrication
Window frame
Window after 1st brazing
Window
Window-IC
T-box
Outer conductor
Coupler during assembly
Whole coupler

## Slide 7
On- stand test: Timeline
SW: standing wave, TW: travelling wave
Coupler | Time | Power source (SSA) | Mode | Max. power reached
PoP （HEPS-TF） | 2017.09 | 166.6MHz 50kW | TW & SW | CW, 50 kW
 | 2018.04 | 650MHz 150kW | TW | CW, 150 kW (Window)
Series design-A （1#, 2#） | 2022.02 | 166.6MHz 260kW | TW & SW | TW: CW 250 kW SW: CW 100 kW
Series design-B （6#, 7#） | 2024.9 | 166.6MHz 260kW | TW & SW | TW: CW 250 kW SW: CW 150 kW
Series design-B （8#, 9#） | 2024.11 | 166.6MHz 260kW | TW & SW | TW: CW 250 kW SW: CW 150 kW
Series design-B （4#, 5#） | 2025.4 | 166.6MHz 260kW | TW & SW | TW: CW 250 kW SW: CW 150 kW
Series design-B （3#, 10#） | 2025.5 | 166.6MHz 260kW | TW & SW | TW: CW 250 kW SW: CW 150 kW
Test Stand Validation: CW 250 kW (TW) ; CW 150 kW (SW)
On-stand high-power test

## Slide 8
The entire sequence of the on-stand tests was performed in cleanroom.
Reception
Ultrasonic clean
Ultra-pure water rinsing
Pure N2 gas drying
Assembly
(Vacuum part)
Baking
(120°C, ≥48h)
Assembly
(Air part)
High-power test
Disassembly
(Vacuum part)
Storage
(N2 cabinet)
Class 10000 (ISO 7)
Class 100 (ISO 5)
Class 10 (ISO 4)
Ultrasonic clean
Ultra-pure water rinsing
Custom-made baking oven (Located in ISO 5 cleanroom)
Air part assembly
(DC bias insulation test)
Test bench setup
(Located in ISO 5 clean room)
On-stand test: Procedure

## Slide 9
Vacuum and temperatures during power keeping
at CW 250 kW in TW mode for 120 hours
Duration of initial conditioning and power holding.
Temperature sensor location
TW mode
- Conditioned time: 96 h (design-A), 48 h (design-B)
- Power keeping: 120 h (design-A), 2.5~9 h (design-B)
- Max.T measured at outer window: 29 °C (Ambient T: 22 °C)
SW mode
- Phase shift: 1/16λ (step) * 8 positions (over 1/2λ range)
- Conditioned up to CW 100 kW (design-A), 150 kW (design-B)
- Power keeping for 1 hour at each phase
- Max.T measured at outer window: 35 °C (Ambient T: 17 °C)
On-stand test: Results

## Slide 10
Simulated MP with DC bias
Observed hard MP band : 10 kW~25 kW
Observed MP with DC bias
On-stand test: Multipacting validation
MP bands
- Simulation: 10-50 kW
- On-stand test: 10-25 kW
DC bias suppression
Simulation：
DC bias ±0.2kV  Exciting new MP
- On-stand test:
  +0.2kV  Fresh MP at 8kW,11kW
  -0.2 kV  New MP at 5.5 kW
Simu. & test: Agree well
DC bias of +0.8kV is suggested for on-line operation.
Simulated hard MP band: 10 kW ~ 50 kW

## Slide 11
On- cavity test: Timeline
SW: standing wave
Coupler | Time | Power source (SSA) | Mode | Max. power reached | Description
PoP | 2018.12 | 166.6 MHz 50 kW | SW | CW 50 kW | PoP HT
Series_2# | 2023.11 | 166.6 MHz 260 kW | SW | CW 120 kW | CM1 HT
Series_6# | 2025.2 | 166 MHz 260 kW | SW | CW 120 kW | CM2 HT
Series_9# | 2025.3 | 166.6 MHz 260 kW | SW | CW 120 kW | CM3 HT
Series_7# | 2025.5 | 166.6MHz 260 kW | SW | CW 120 kW | CM5 HT
Series_8# | 2025.6 | 166.6 MHz 260 kW | SW | CW 120 kW | CM4 HT

## Slide 12
Large performance degradation
Quench at 1.5 MV
On-cavity test: Overheating issue (PoP: Prototype)
Anomalous heat loss (11.1 W) → Likely mainly from FPC
（PoP, HT, Vc=1.0MV）
Observation: Detune  Tuned
- Temp at ‘CryoTempB’: 6.5 K  35.0 K
- Total module heat load: 12 W  28 W
H-field > 1000 A/m in the cavity-coupler
interface region (at 1.5MV）
Reason1: Field change (Detuned  Tuned)
Reason2: Field leakage (Cavity  FPC)
Cavity–coupler interface overheating  Thermal runaway  Cavity quench
11.4 K>9.3 K
Simulation: T_max on the Nb extension tube 11.4 K (Vc=1.5MV, He flow:14.4 slm)

## Slide 13
On-cavity test: Overheating solution (PoPCM1)
Solution1: Increasing Helium gas flow rate yielded little improvement
10.9 K>9.3 K
Simulated T_max on the Nb extension tube 10.9 K (Vc=1.5MV, He flow: 50 slm)
H-field along the FPC’s outer conductor
Simulated 4.2K heat loss from FPC
80 mm
120 mm
40mm extension of Nb tube
After 120 mm elongation:
Simulated T_max of the Nb tube 4.8 K
(Vc=1.5MV, He flow: 14.4 slm)
4.8 K < 9.3 K
T. Huang et al., AIP Advances 11, 045024 (2021).
Solution 2: Elongate the Nb ext. tube at the coupler port from 80mm to 120mm
After mod. (1.5MV, 14.4 slm)
- 4K heat loss from coupler: 7.7W  1.8W
- T_max of Nb: 11.4K  4.8K

## Slide 14
As the gas helium flow rate increased up to 30 slm, serious frosting observed close to the coupler-cryostat connecting flange
On-cavity test: Frosting issue (CM1: Series design-A)

## Slide 15
Move the fin structure from the sidewall of the OC to the bottom of its warm flange
Move the outlet of the helium gas cooling pipe 113.5 mm away from the frosting area
On-cavity test: Frosting solution (CM1CM2~5)
CM2~CM5: NO frosting

## Slide 16
Rotating the helium inlet pipe 90° sends cold gas to the hottest spot first, which further cools down the interface.
On-cavity test: Overheating further alleviated (CM1CM2~5)
Helium inlet
Helium inlet
Fixing block
Cavity H-end
Cavity H-end
Fixing block
Interference → Bend pipe → Rotate inlet → Cold gas to hottest zone → Lower interface temperature
CM2~CM5
CM1

## Slide 17
Modifications validation
Parameters | Prototype | Series design-A | Series design-B |  |  | 
Modules # | PoP | CM1 | CM2 | CM3 | CM4 | CM5
FPC structures related to main modifications | Nb port: 80mm He outlet: close to the OC warm end | Nb port: 120mm He outlet: close to the OC warm end He inlet: 12 o’clock Fin: on sidewall of the OC | Nb port: 120mm He outlet: in the middle of the OC He inlet: 3 o’clock Fin: on the bottom of OC warm flange |  |  | 
Cavity voltage | 1.0 MV | 1.2 MV | 1.2 MV |  |  | 
T_max on NbTi flange | Not measured | 15.4 K | 10.3 K | 9.8 K | 9.5 K | 10.8 K
T_max on OC cold end | 35.0 K | 14.2 K | 9.6 K | 8.4 K | 9.2 K | 8.9 K
4.2K heat load of FPC | 11.1 W | 3.0 W | 2.0 W | 2.0 W | 0.5 W | 1.4 W
Cavity quench | Quench at 1.5 MV | Not quench at 1.7 MV | Not quench at 1.5 MV |  |  | 
Icing and frosting near window | Icing | Frosting | No frosting |  |  | 

## Slide 18
SRF modules performance improvements
The performance of the 166MHz SRF modules improved significantly benefiting the FPC related modifications.
  Overheating mitigation
  Q0 increased up to 2 times：
  - PoP: 4E8@1.45MV
  - Series: >1.0E9@1.5MV
  On-stand test processed in cleanroom
  Radiation dose decreased:
  - PoP: Several thousands uSv/h
  - Series: Less than 10 uSv/h

## Slide 19: On-line operation: Performance
Five 166 MHz FPCs performed excellently during beam commissioning:
  ✔ ~150 mA beam current reached: 467 kW total RF power;116 kW max per FPC
  ✔ Vacuum <2.5×10⁻⁷ Pa; Temp: Window <29 °C , NbTi flange <9 K; ‘SO’ 5.3~7.4 K
  ✔ No overheating; Rare Multipacting & Genuine Arc

## Slide 20
Each 166 MHz FPC equipped with one AFT dual‑channel arc detector
Suspected False Arc
  Occurred frequently during HEPS commissioning
  Became the dominant interlock type (31/99=31%)
False Arc: Phenomena
False Arc: 31%
Characteristics of the ‘Suspected False Arc’ Events
✔Commonly Preceded by: Beam instability
✘Real Arc Signals NOT Observed:
Outgassing
Reflected power fluctuation
MP-induced e- current
Overheating
Suspected ‘Arc’ events — likely not real FPC arcs.
HEPS RF System Interlock
(202508-202510, 99 events)

## Slide 21
False Arc Confirmed!
Cause: Beam‑loss‑induced X‑rays
Mechanism:
X-rays(beam loss)  Induce light in fiber
 False Arc trigger
False Arc: Identification
Added ‘Tunnel Arc’ system
Fiber path = ‘Coupler Arc’
Viewport not connected to window (5 cm away, shielded)
Experiment Results
‘Tunnel Arc’: triggered frequently
Coincided with:
  ‘Coupler Arc’
  Beam instability
Validation Experiment Setup
Fiber length: 30m

## Slide 22
Solution: Logic-Based Discrimination
Impact of False Arc
✘ RF system trip rate ↑
✘ Optical fiber sensitivity ↓
✘ Fiber complete failure
Logic Discrimination  Reduce ‘Arc’ Frequency
Input signals: ‘Coupler arc’ + ‘Tunnel arc’ (X‑ray monitor)
Logic Rule: ‘Arc’ interlock ONLY triggered when:
‘Coupler arc’ = ‘Yes’ & ‘Tunnel arc’ = ‘No’
 | Before implementation (202508-202510) | After implementation (202601-202605)
Total interlock events (RF) | 99 | 121
Cavity vacuum | 36 (37%) | 68 (56%)
FPC false Arc | 31 (31%) | 22 (18%)
Circulator | 11 (11%) | 18 (15%)
Others | 21 (21%) | 13 (11)
False Arc: 18%
⚠️False arc decreased, but not eliminated
(31%18%)

## Slide 23
We developed the FPC over nine years, from prototype to series, fixing overheating and frosting issues step by step.
All series FPCs passed on‑stand testing up to 250 kW CW (TW) and 150 kW CW (SW). Five are now running stably in HEPS.
During beam operation, a false arc issue caused by X‑ray‑induced fiber light was identified and alleviated by logic‑based discrimination.
Summary

## Slide 24: References of IHEP FPCs
http://dx.doi.org/10.1063/5.0001540
http://dx.doi.org/10.1063/5.0046377
http://dx.doi.org/10.1016/j.nima.2021.165649
http://dx.doi.org/10.1016/j.nima.2010.08.108
http://dx.doi.org/10.1088/1674-1137/32/11/017
http://dx.doi.org/10.1088/1674-1137/32/9/017
http://dx.doi.org/10.1088/1674-1137/36/4/011
http://dx.doi.org/10.1088/1674-1137/41/6/067001
http://dx.doi.org/10.1088/1674-1137/38/11/117002
http://dx.doi.org/10.1088/1674-1137/38/2/027001