## Slide 1
Dr. Pragya Nama
Assistant Professor
KEK
Achievement of CW 100 kW Class Power Transmission by an L-band High-Power Input Coupler for SRF Accelerators

## Slide 2: Contents
CW 100 kW coupler design
Experimental setup
Discussion topics
Summary
RF conditioning
Background

## Slide 3
CW 100 kW coupler design
Conduction cooled by cryocooler
Thermal management strategy
Water cooling for the critical components -> Warm section, Antenna, RF window
Enlarged warm section
Low loss ceramic material

## Slide 4
Background
Burned Inner conductor when 100 kW power in CW mode was applied for one minute
cERL injector coupler (Prototype)
Modified warm inner conductor
Modified warm outer conductor
Pure Cu
Water-cooling jacket
 | cERL injector coupler | Modifed cERL injector coupler
Material (IC) | Cu coated SUS | Pure Cu
Cooling | No cooling | Water cooling for inner and outer conductor
Temperature rise (IC) | 160 oC at CW 20 kW | 4-5 oC at CW 27 kW
Modified cERL injector coupler

## Slide 5
Test stand for high power test
Demountable outer conductor
RF window
Antenna
Coupler Cleaning in class 1000 clean room
Coupler test-stand assembly in class 10 clean room
Warm section assembly and Low power measurement
Adjustment of short plate
Coupler Baking Setup
Modified warm section
Water cooled IC made of OFC
Water cooled OC
Vacuum gauge
Test stand was prepared with a new coupler and modified cERL injector coupler.
New coupler was cleaned in class 1000 CR. Drying and assembly in the class 10 CR. Baked for 48 hours at 120oC.
Measured S1,1 @ 1.3 GHz = -21 dB
Assembled with power source and dummy load for high power test.

## Slide 6
Experiment setup
Vacuum pump,
Chiller for water cooling and Fans for forced air cooling,
Temperature, Arc sensors and Cameras were installed.

## Slide 7
RF conditioning (pulse mode)
Starting RF conditioning in pulse mode (20ms pulse, 5 Hz)

## Slide 8: RF conditioning time
Number of days RF conditioning: 8 days
Total conditioning time: 84.6 hours (Pulse -> 60.6 hours and CW -> 24 hours)

## Slide 9
RF conditioning (CW mode)
Achieved record CW 100 kW RF transmission
No interlock related to the coupler.
Limited by the circulator.

## Slide 10
Suppression of temperature rise
Coupler test-stand during high power test
Water cooling pipes
Fan cooling
Modified warm section
Water cooled IC made of OFC
Water cooled OC
Vacuum gauge
Water cooling at
Warm inner conductor
Warm outer conductor
RF window
Antenna
Fan cooling at
Doorknob
Cold outer conductor
Whole test stand
Flow: 1L/min

## Slide 11
Temperature profile during high power test
Temperature Profile
Simulated temperature rise
(without convection )
New (upstream)
Modified cERL
(downstream)
DK down
(dT = 55 oC)
DK up
(dT = 19oC)
Short (dT = 51 oC)
Short (dT = 18.5 oC)
IC (dT = 18 oC)
IC (dT = 14 oC)
Warm OC (dT = 7 oC)
Warm OC (dT = 4 oC)
RF window
(dT = 9 oC)
RF window
(dT = 0 oC)
Cold OC (dT = 8 oC)
CB up (dT = 19 oC)
CB middle
(dT = 9 oC)
Warm OC jacket
(dT = -1 oC)
Warm OC jacket
(dT = -1.5 oC)
Cold OC (dT = 15 oC)
CB down (dT = 8 oC)
Temperature rise at 100 kW CW power
Doorknob -> 19 oC (max.), Inner conductor -> 14 oC

## Slide 12: Learning
Suppression of temperature rise using water cooling, and enlarged warm section
Water cooling together with the fan cooling was very efficient to suppress temperature rise during high power test in CW mode.
One warm window cooled by water is simple and best solution.
Both simulation and measurement confirmed that the increase in size significantly improve thermal performance.

## Slide 13: Vacuum during RF conditioning in pulse mode
Overall vacuum level decreases with the increase in duty cycle.
Vacuum activity remained power level between 20 kW to 55kW -> Multipacting
New coupler
Blue light
Light from camera
Multipacting light was observed during pulse conditioning
0.25%
1.25%
5%
10%
30%
20%
Note:
No such light was observed for the Modified cERL injector coupler.
RF conditioning for long time -> No multipacting!

## Slide 14: Observation and Simulation
Power 130 kW, Pulse width 20 ms, Repetition rate 5 Hz
Simulated multipacting growth rate along with the measured vacuum level
In simulation, maximum growth rate was found at around 45 kW power -> consistent with the measured power range of vacuum activity.
Does your multipacting simulations are consistent with the measurement of not?
Start of conditioning
End of conditioning
Outgassing or multipacting!
Multipacting
Observed multipacting
Growth rate (Cu 100oC baked)
Growth rate (Cu 200oC baked)
Growth rate (Clean Cu)

## Slide 15: Hysteresis on Vacuum behavior
During power up, vacuum starts increasing around 23 - 55 kW.
Opposite vacuum behavior for power down.
Sharp increase in vacuum at 20 kW during power down.
Reproducible! Reason?
After conditioning, is it possible to completely remove?
During operation, did you observed multipacting? Is it a problem or not?
It is important to increase and decrease the power slowly to prevent the sharp increase in vacuum.
From 20 kW-55 kW, some vacuum activity happens (multipacting region!)
Day 7
Day 8
Power up
Power down

## Slide 16: Summary
Developed CW 100 kW-class 1.3 GHz high power input coupler ->Achieved highest power transmission in CW mode.
In CW mode, 100 kW power transmission was maintained for continuously 10 hours without any interlock.
Published paper:
P. Nama, D. Arakawa, E. Kako, A. Kumar, T. Miura, H. Nakajima, H. Sakai, and K. Umemori, Development of continuous-wave 100 kW-class high power input coupler for conduction-cooled L-band Nb3Sn accelerators, Nucl. Instrum. Methods Phys. Res. Sect. A 1083, 171155 (2025). https://doi.org/10.1016/j.nima.2025.171155

## Slide 17: Discussion topics
1. Multipacting
Consistency of Multipacting simulation and experimental observation.
Complete elimination of multipacting is possible or not after conditioning?
Multipacting during the operation was observed or not? If yes, is it concerning or just avoid it?
2. Issues with higher (>100kW CW) power transmission.
What would be the limiting factor if we increase power level more than CW 100 kW? Multipacting! Or Temperature rise! Or what else?
3. Temperature rise
Consistency of temperature rise simulation and measurment.
How to simulate air cooling?

## Slide 18: Coupler development team
This research was supported by the JST and the establishment of university fellowships for the creation of science and technology innovation (Grant Number JPMJFS2136) and partially supported by the US-Japan Science and Technology Cooperation Program in High Energy Physics and a JSPS Grant-in-Aid for Scientific Research (KAKENHI) Grant No. JP24K03208.

## Slide 19
Thank you