## Slide 1
SRF phase transition at IJCLab
From TEM-cavity specialist to Elliptical cavities
CNRS/IN2P3/IJCLab
Akira Miyazaki on behalf of SRF team

## Slide 2: outline
Introduction
TEM cavities
New activities
Infrastructure update
Fundamental studies
Conclusion

## Slide 3: Introduction : Instances around IJCLab
Credits :
J.L. Biarrotte

## Slide 4: Introduction : History summary and series production @ Supratech
1995
2000
2005
2010
2015
2020
2025
ESS
MYRRHA
PIP2
PIP2
EURISOL
He Liquefier (2008)
SPIRAL2
MYRRHA
Clean-room for cryomodule (2007)
Chemical facility (2008)
SPIRAL2
ESS
Furnace (2016)
New Assembly Hall (2020)
Klystron (2017)
Upgrade CV800 (2018)
First cryogenic test of a cryomodule at Supratech (2007)
Supratech Platform is officially recognized by IN2P3 (2017)
EU-XFEL
MAX
Creation of IJCLab, merging of equipment from LAL and IPNO in Supratech (2020)
TTF3
LHC
First cryogenic test of a Spoke resonator in Europe (2002)
Supratech Platform is created (2004)
Calibration Station (2000)
Vertical cryostat (CV800)
MYRTE
Series production
Prototyping Phase
R&D
ESS : - preparation & testing of cavities, couplers and tuners
- Integration of 14 cryomodules
LHC : Calibration of all Cernox thermal sensors (> 6000 units)
PIP-II : Testing of 33 Spoke cavities
Spiral2 : Integration and test of 7 cryomodules
MYRRHA : - preparation & testing of 60 couplers and tuners
EU-XFEL : Preparation and power testing of 800 couplers

## Slide 5: Our infrastructure: SUPRATech Platform
Zone de montage cryomodule
Hall de test (fosse)
Hall de récupération et compresseurs hélium
Salle de chimie
Four de dégazage
Source RF Klystron 352 MHz
+
+
Hall de test (Cryodrome)
Hall de montage
Station d’étalonnage
+
Hall Lagarrigue
Salle blanche conditionnement coupleurs (XFEL)
Liquéfacteur à hélium
Bâtiment 103
Salle blanche préparation et assemblage coupleurs
Salle blanche cavité
Cryostat de test SAF
Bâtiment 106

## Slide 6: How is SRF organized @IJCLab
MAVERICS team
(~ 8 people involved in SRF activities)
Leading R&D effort in SRF
Driving SRF programs
RF Group
(~ 8 people involved in SRF activities)
Driving SRF programs
RF and mechanical design of SRF components (Cavity, tuner, coupler, LLRF)
Operation and maintenance of RF equipment of Supratech
Cryogenic Group
(~ 6 people involved in SRF activities)
Expertise in design of cryogenic systems
Operation and maintenance of cryogenic facilities of Supratech
VIDE & SURFACES Platform
(Material and surface caracterization)
Material caracterization (SEM, EBSD, EDS, XPS, XRD, SIMS, confocal microscop, …)
Dedicated set-up (SEY, plasma)
SUPRATECH Platform
(Treatment, assembly and test of SRF components)
Cryostats
Dedicated SRF facilities (BCP lab, clean rooms, UHV Furnace)
He Liquefier
Assembly area for cryomodules
3 groups, 2 platforms

## Slide 7: Facts and strategy
IJCLab is a medium size laboratory in the field of fundamental physics
  Mixed CNRS/University but practically VERY university with small non-SRF accelerators
  Not like large accelerator facilities, such as CERN, FNAL, KEK, DESY, etc…
We have certain base funding
  Basic R&D is strongly encouraged
  Somewhat sufficient as a seed funding for small experiments like dark matter, theory, etc…
Superconducting RF studies are enormously demanding even for R&D!
  Material, fabrication, preparation, testing, etc
  Not a typical R&D subject with university-level base funding + external competitive grants
We have focused on TEM-type accelerator projects
  To efficiently profit from the limited resources
  Scientific R&D results have been byproducts of project contributions
    Eg) D. Longuevergne, A. Miyazaki, Phys. Rev. Accel. Beams 24 083101 (2021)
    D. Longuevergne, NIMA, Volume 910, Pages 41-48 (2018)
Our infrastructure has been dedicated to TEM-type cavities for small “mass” production
  Spiral2 (7 cryomodules, 14 QWR), ESS (14 cryomodules, 28 Spokes), PIP-II (test of 30 Spokes),

## Slide 8: IJCLab-SRF has been dedicated to TEM cavities
88 MHz
352 MHz
325 MHz
352 MHz

## Slide 9: Recent TEM-type cavity projects
Requalification of Spiral2 cavity
To validate HPR at GANIL
Cleaning and reassembly of ESS cavities & couplers
MYRRHA prototype CM
MYRRHA tuner
MYRRHA coupler
After accidental venting of one spoke module
PIPII cavity testing 
Two prototype SSR2 cavities
One series SSR1 cavity
PIPII SSR2
IJCLab is actively working on TEM cavity projects
We will keep capability for TEM-type projects
However, new activities are launching 

## Slide 10: New SRF projects in IJCLab  high-b electron beams
Local energy recovery linac PERLE
FCCee for CERN
EIC for BNL/JLAB
1st e- beam
11/05/2026
CW high current  high-Q elliptical cavities!

## Slide 11: Phase transition at IJCLab
Meissner state of TEM

## Slide 12: Phase transition at IJCLab
Meissner state of TEM

## Slide 13: Phase transition at IJCLab
Meissner state of TEM
Mixed state of TEM + elliptical

## Slide 14: New activities with elliptical cavities
1.3 GHz cavities for R&D
PERLE cavities
1DE08
CEA-RI2
JLAB-CRN1
FCC cavities
FCC-UROS2
JLAB-CRN1
VEP
800 MHz b=1 cavities
Under manufacturing
Technical synergy
VEP @ CEA

## Slide 15: 800 MHz is crucial not only for projects but also for basic physics
P. Dhakal et al PRAB 27 062001 (2024)
Q-slope
Anti-Q-slope
750 MHz
650 MHz
Present 800 MHz result from JLAB in 2018
Flash EP + 120C bake surface  Q-slope
Courtesy
Frank Marhauser
Dose N-dope and/or mid-T bake generate anti-Q-slope on 800 MHz cavity?
1.3 GHz

## Slide 16: Infrastructure qualification & development for surface treatment
BCP @ IJCLab
Vacuum furnace @ IJCLab
BCP/30min+120C/12h
Flash EP 30µm +120C/12h
Courtesy Shahnam Gorgi Zadeh and CERN/JLAB SRF team
Courtesy KEK iCASA team
VEP @ CEA
Courtesy Fabien Eozenou and CEA-SRF team
CEA has a VEP setup qualified for 704 MHz 1-cell
IJCLab a furnace qualified for 1.3 GHz 1-cell mid-T
IJCLab and CEA collaborate on 800 MHz Vertical EP
CW machines need high-Q but not super high-G
IJCLab investigates BCP + mid-T
VEP for multi-cell may be OK for 25 MV/m
  Courtesy of Vijay Chouhan

## Slide 17: Infrastructure for vertical tests
VT with CV800
Only for jacketed cavities
PIPII-SSR2
 Demountable He-jacket concept
Successful grant application UPS P2I AAP 2026 « superCav »
  Successful implementation leads to saving LHe amount
The components are under commissioning
1st goal is to reproduce VT results from other labs  exchange cavities within

## Slide 18: Individual R&D subjects
Theory of superconductivity
Carlos’ talk in WG-1 16h00 on Tuesday
HOM damping
See Axel’s talk in WG-4 16h36 on Wednesday
Surface physics and material science
Chahinez’s talk in WG-1 11h36 on Wednesday
COBOT
Nicolas’ talk in WG-4 14h24 Wednesday
Plasma processing
Camille Cheney et al arXiv:2603.04052
Experiment & analysis
A. Bianchi, doi:10.18429/JACoW-SRF2025-THA05
C. Redondo-Herrero, AM arXiv:2604.03702
Martin’s talk in WG-2 11h15 on Wednesday
SRF2025

## Slide 19: IJCLab in TTC
IJCLab
CERN
DESY
INFN
CEA
STFC
KEK
FNAL
JLAB
ANL
ITN
FCC
FCC
PERLE/EIC
PERLE
PERLE
UChicago-CNRS
Cornell
FCC
SLAC
ITN
IITN
ITN
We are 100% benefiting from TTC! + bilateral/multi-labs grants 
FCC
FCC
TYL/FJPPL
TRIUMF
BNL
HZB
EIC
RIKEN
EAJADE
UU
IHEP
SARI
MSU
ORNL
EAJADE
PERLE
PIP-II
NPAT : Nuclear Physics, Nuclear Astrophysics and Accelerator Technologies

## Slide 20: Conclusion
IJCLab is a medium-size laboratory of fundamental physics
  Very large university but still limited resources compared to large accelerator facilities
IJCLab has been working mainly on TEM cavity projects
  Successful contributions to Spiral2, ESS, MYRRHA, PIPII
New project demands lead us to launching multiple R&D projects in elliptical cavities
  Local ERL PERLE
  International colliders FCCee + EIC
800 MHz cavities for PERLE and FCC are of primary interest for R&D
  Cavity manufacturing with industry
  Infrastructure updates and qualification
IJCLab is reinforcing basic R&D activities
  From fundamental theory to robotics
IJCLab profits from the international network thanks to TTC!