## Slide 1
Collective and surface charge effects
in high brightness electron bunch production for FCC-ee
PhASE26| Orsay | 23 September 2026
Anahita Omoumi
A. Latina , S. Doebert, M. Calderon and E. Granados (CERN)
L. Jones (STFC, Daresbury)
S. Bettoni (PSI)
B. O’Shea, R. Loney and C. Emma (SLAC)

## Slide 2
Content:
02 Dynamic Photoemission Model
A. Omoumi | PhASE26 | 23.09.26
03 Experimental Benchmarking
05 Conclusion and Outlook
01 Motivation

## Slide 3
Content:
A. Omoumi | PhASE26 | 23.09.26
01 Motivation

## Slide 4
Motivation — Why collective & surface effects matter
A. Omoumi | PhASE26 | 23.09.26
4
A general challenge for high-brightness photoelectron sources
The high-brightness objective
More charge
+
Shorter bunch
+
Smaller emittance
→ high phase-space density at the cathode
What changes at high charge density?
Why it matters
Extractable charge
saturation / clamping
Temporal dynamic
bunch-shape distortion
Transverse dynamic
emittance growth
At high brightness, photoemission is no longer only a material response to the laser: the emitted bunch modifies the surface and extraction conditions while emission is still occurring.

## Slide 5
Motivation — Why this is critical for FCC-ee
A. Omoumi | PhASE26 | 23.09.26
5
BASELINE OPERATION
Bunch charge
Bunch spacing
Maximum repetition rate
Bunch duration
Energy spread
Bunch per train
5-7 nC
25 ns
2 - 4
≤ 200 Hz
~ 3ps (rms)
390 keV (0.2%)
TOP-UP SCHEME
Dynamic charge range
Response time
Transverse emittance
Transverse profile
0-7 nC
< 25 ms
On-demand
shaping capability
~ 7 mm.mrad*
(depending on the damping ring)
2- FAST AND PRECISE AMPLITUDE MODULATION SCHEME
25 ns
50 ms
The source must combine high charge, fast tunability and controlled phase space
1- TAILORING OF TRANSVERSE BEAM PROFILE

## Slide 6
From source requirements to a predictive photoemission model
A. Omoumi | PhASE26 | 23.09.26
6
Analytical / canonical
models
Fast & interpretable
Microscopic / quantum emission models
Detailed surface physics
PIC / particle tracking
Self-consistent beam dynamics
Our goal: a reduced self-consistent model that couples dynamic surface-barrier physics to collective charge evolution — fast enough for scans, yet rich enough to predict saturation and losses.
State of the art: the relevant physics exists — but usually in separate descriptions
Evolving space-charge fields & transport
Realistic geometries and boundaries
Requires a cathode emission law / closure
Expensive for wide parameter scans and source optimization
Fast, local estimates of emission
Microscopic barrier physics / scaling laws
Typically prescribed or quasi-static fields
No self-consistent collective feedback
Time-dependent emission
Barrier transmission / tunneling
Near-threshold physics
No self-consistent collective feedback

## Slide 7
Content:
02 Dynamic Photoemission Model
A. Omoumi | PhASE26 | 23.09.26
01 Motivation

## Slide 8
From Laser Pulses into Electron Bunches
A. Omoumi | PhASE26 | 23.09.26
8
A
E
T
Absorption
Emission
Transport
Moment Model (MM)
DFT
Dynamic Field
Temperature
,
Relaxation time
e- scattering losses

## Slide 9
A. Omoumi | PhASE26 | 23.09.26
9
T
Absorption
Emission
Transport
Dynamic Field
Temperature
Moment Model (MM)
DFT
,
Relaxation time
e- scattering losses
A
E
From Laser Pulses into Electron Bunches

## Slide 10
A Time-resolved Photoemission Model
A. Omoumi | PhASE26 | 23.09.26
10
CORE PHYSICS
Emission modifies the field that controls subsequent emission.
Fbar(t) = FRF − EIC
Fdyn(t,z) = FRF − ESC
surface barrier
vacuum transport
UV pulse
Emission
IC / SC fields
Barrier
WHY
Top-up injection needs high, tunable bunch charge
At high charge density, the photocathode is no longer a passive emitter.
•
•
The image field affects the barrier. The space charge field affects transport.
FIELD DECOMPOSITION

## Slide 11
Finite Disc Model
A. Omoumi | PhASE26 | 23.09.26
11
𝐹bar (𝑡) = 𝐹RF − 𝐸IC (𝑡)
𝐹dyn (𝑡, 𝑧𝑖) = 𝐹RF − 𝐸SC (𝑡, 𝑧𝑖)
Electron
image
disks
Infinite sheet → Constant field → Overestimates screening → Artificial clamping
We consider instead, finite uniformly charged disks of radius a :
Image Charge
Composite Field at Surface
!

## Slide 12
Time-Resolved Emission Dynamics
A. Omoumi | PhASE26 | 23.09.26
12
For 265 fs:
Rapid image buildup
Mid-pulse suppression
Double emittance peak
For 1.5 ps:
Slower buildup
Smoother emittance evolution
Faster pulses enhance dynamic barrier modulation.

## Slide 13
Content:
02 Dynamic Photoemission Model
A. Omoumi | PhASE26 | 23.09.26
04 Experimental Benchmarking
01 Motivation

## Slide 14
A. Omoumi | PhASE26 | 23.09.26
14
Validation With Experimental Data
Experimental Setup for Charge Production Tests at CTF2

## Slide 15
A. Omoumi | PhASE26 | 23.09.26
15
Charge vs Laser Energy
The model reproduces saturation without invoking ad-hoc limits, it emerges naturally from dynamic field screening.

## Slide 16
Benchmarking the Model: SLAC Results
A. Omoumi | PhASE26 | 23.09.26
16
Cathode
VCCF
FACET-II Injector Parameters:
1.0 | 1.6 | 2.0 | 2.5 | 2.8
56 | 87 | 112 | 145 | 172
5.5 | 5.5 | 5.5 | 5.5 | 5.5
1.2 | 1.2 | 1.2 | 1.2 | 1.2
Charge (nC)
Laser pulse energy (µJ)
Flat-top spot size (mm)
Pulse length (ps rms)

## Slide 17
Benchmarking the Model: SLAC Results
A. Omoumi | PhASE26 | 23.09.26
17
FACET-II Charge vs. UV Pulse Energy | Flat-top 5.5 mm | Pulse RMS 1.2 ps

## Slide 18
From “charge dynamics” to “spatially resolved emission and emittance”
A. Omoumi | PhASE26 | 23.09.26
18
Each cell carries a local emitted charge qᵢ(t)
surrounding cells j
Each surrounding cell contributes according to its charge and relative position.
ESC(xᵢ,yᵢ,t) = Σⱼ Kᵢⱼ(t) qⱼ(t)
Kᵢⱼ : geometrical coupling between source cell j and observation cell i
1
Laser profile
sets qⱼ across the grid
2
Neighbour coupling
each cell feels surrounding charge
3
Local field
E_SC differs from cell to cell
4
3D dynamics
local forces feed transverse phase space
Key idea: the model is cell-to-cell coupling on a 2D transverse grid.
cell i
3D emission grid
Local space-charge field

## Slide 19
For more information…
A. Omoumi | PhASE26 | 23.09.26
19
Read the paper
Example: RF-Track simulation of 5nC bunch in the CLEAR photoinjector using the dynamic photoemission model
RF-Track on Git-Lab

## Slide 20
Content:
02 Dynamic Photoemission Model
A. Omoumi | PhASE26 | 23.09.26
03 Experimental Benchmarking
05 Conclusion and Outlook
01 Motivation

## Slide 21
Motivation — High-brightness beams start at the cathode
A. Omoumi | PhASE26 | 23.09.26
21
Outlook
Charge scaling production is studied for copper-based photoinjectors.
A new model including dynamic field effects on the photocathode surface is presented:
  Sub-ps field dynamics strongly affect the scaling laws
  The real-time QE becomes nonlinear as a function of illumination parameters
The model has been benchmarked with RF guns at CERN and SLAC, showing good agreement.
To deliver up to 7 nC per bunch, several limitations need to be addressed:
  The spot size on the cathode needs to be very large → implications for RF frequency and gun design
  Pulse duration → it can be a knob for changing the extracted charge,
  but also, for charge scaling longer pulses are preferred.
Emittance: Transverse emittance is included, longitudinal emittance coming soon…
We need to:
  Complete the 3D extension of the model
  Enable the capability of simulating arbitrary UV wavepackets → detailed studies of UV shaping techniques
  Explore the modeling of semiconductor photocathodes
  How can we reliably modulate the bunch charge and emittance in a shot-to-shot basis?

## Slide 22
Thank you!