## Slide 1
Verena Kümper, Björn Keune, Michael Hoffmann, and Christoph Quitmann
Photocathodes transfer for PERLE

## Slide 2: RI at a glance
Founded in 1994 as ACCEL Instruments GmbH – since 2009 named RI Research Instruments GmbH
Annual revenue of 90 million EUR in 2024
Majority (52%) owned by Bruker EST, Management team are additional shareholders
Headquarters in Bergisch Gladbach, Germany, very close to Cologne
5 main high-tech business fields (Super conducting and normal conducting particle accelerators, Fusion, Semicon EUV tools, and Semicon supply chain)
More than 150 employees are physicists or engineers (>400 in total)
>400
and growing
Bergisch Gladbach
& Dortmund,
Germany
30 years of innovation
Customers in
>25 countries

## Slide 3: Starting Point
Industrial project for production of radioisotopes (Mo-99)
    Based on electron linac with CsK2Sb-photocathodes
Uptime of the machine 23 h/ 7 days
    1 h time for photocathode exchange
  Suitcase vs. direct transfer
    Visit of some companies and experts
    Suitcase: high risk of degradation or failure scenarios for industrial application
      Decision for linear transfer system directly from PC production to e-gun
  Termination of project and sale of e-gun and photocathode system to PERLE

## Slide 4: PC-Transfer System
Not RIs core business but an interesting challenge
Start of brainstorming and first sketches
Decision: Transfer System shall be part of a test facility
  Find company with experience in MBE and transfer systems to collaborate

## Slide 5: Test Facility
2022 RI built up a test facility with PC production, PC transfer system, e-gun, first part of linac, diagnostic section, beam dump, HV and Laser

## Slide 6: Setup Transfer System
Glovebox, Load Lock, MBE chamber, 2x Transfermodul, gun chamber
All puck/PC transfers automated
Trolley for 5 pucks (size 2”)

## Slide 7: Setup Transfer System
Glovebox and load lock for dust, oxygen and water “free” insertion of fresh pucks
Rail system in linear transfer line
Motorized transfer rods for grabbing pucks and transfer into MBE and gun chamber

## Slide 8: PC/Puck Identification
QR code scanner for puck identification

## Slide 9: Automated Puck Identification
Open “Control System”
Activate the Ident module
Open “Automated Transfer”
Click on “Sample”
Choose one of the pucks and click on “Sample Info”
Click on the grey button next to identification. If this is green the puck identification will start and read out the QR code

## Slide 10: Motion
Software has a button for automated motion
You can choose the puck which should be coated and the position where the puck shall be transferred
Say “Transfer” and the puck will be automatically transferred into the MBE-chamber or into gun if you select “Gun” as final position
Position heater and mask with click on

## Slide 11: Software control for the deposition
Overview of MBE-chamber with
  Evaporators
  Puck heater
  Pumps
  Pressure
  Valve
  Motors

## Slide 12: Software control for the deposition
It was planned to have the deposition completely automatized but project was terminated before it was realized
  Partly automated deposition for each element
You can program different deposition steps with the “Sequencer”
Example:
Heating ramp
Shutter open/close
Set material
Reset quartz

## Slide 13: Summary
One vacuum system from deposition to gun
All steps can be automated individually
  Deposition
  Transfers
  QE measurement
  etc.
Goal: one sequence (one klick) from loading pucks to transfer into gun
Transfer into gun

## Slide 14: Acknowledgement
Thank you for your attention!
and
Thanks to the PERLE and IJC Lab team for the invitation and the good collaboration!

## Slide 15: Thanks for your attention
Questions about the presentation?
Feel free to contact us anytime.
+49-2204-7674-100
sales@research-instruments.de
www.research-instruments.de

## Slide 16: Backup slides
Just in case…