## Slide 1
UHV Transfer Solution for Photocathodes
How we Enable Big Scientific Discoveries with Our UHV Technology
Cyrill Strässle, 2026
Content:
Brief History
UHV Suitcase
SwissFEL Setup
Manipulation of the Cathode
Potential

## Slide 2: Cathode Handling @SwissFEL
Hard X-Ray FEL
740 m Long
Sample Handling System and
Load Lock chamber behind Photoinjector
installed in 2019
Notes: Why am I here? -> Installation and running since 2019
Now we are bulding an additinal system there. With improve ments.
How did we get here?

## Slide 3: Ferrovac - Swiss UHV technology since 1996
Overview Drawing for Patent Application, 1994, ETH
Notes: When starting the company 30 years ago, it all begann with developing a magnetically driven
wobblestick manipulator – at that time such thing did not exist. For Sample Handling!
The Wobblestick remaisn mainly the same ever since.

## Slide 4: The Selection of Components grows
Sample transporters
Wobblestick manipulators
Linear-/Rotary translators
Sample holders and accessories
XYZ Manipulators
Notes: Further Problems arise, enable
However, selection of products grows
Dirfent shape of manipulators,
Also the sample holder it self. In our case of photocathod,

## Slide 5: You name it – we build it
HOENCOL @ Swiss FEL
Energy Collimator for the Swiss Free Electron Laser
SHOM/RECOMEC13
Transferable Sample Holder with 13 electrical contacts
Contract Manufacturing
precision engineering
NPSTAGE @ Ioffe Institute
6 Axis nanopositioning stage for 4 inch wafers
RIXS resonant interference X-ray scattering @ SOLEIL
Design and performance of AERHA, a high acceptance high resolution soft x-ray spectrometer.
Chiuzbăian SG1, Hague CF1, Avila A1, Delaunay R1, Jaouen N2, Sacchi M2, Polack F2, Thomasset M2, Lagarde B2, Nicolaou A2, Brignolo S1, Baumier C1, Lüning J1, Mariot JM1.
Rev Sci Instrum. 2014 Apr;85(4):043108.
Doi: 10.1063/1.4871362.
Notes: Later also System development: Scanning Transmision Microscopy (STM), End Stations, ...
Project for numerous Scientific experiments
Sample Loading and transport allway present! Made us consentrate on Loadlock, Suitcase and Docking Solutions

## Slide 6: How to UHV Transfer
UHV Suitcase p < 1E-10 mbar
Turbo
Docking Station p < 1E-8 mbar Can potentially also serve as Load Lock (Antechamber)
Analytical or Prep System
p < 1E-10 mbar
Notes: Introduce sample through Load Lock, or else Antechamber, place it there
UHV Chamber: remains under Vacuum all the time. Roughing Pump, Trubo-Pump, UHV Pump (ION-Pump).
Docking Station, with rough in Trubo, ponetnially with Cryo UHV Booster. -> 5h to

## Slide 7: The Suitcase as Connecting Link
Selection of standardised Sample Holders and Grippers
Atom Probe Puck
Dovetail
Flag Stlye Plate
Notes: Standart / Compatible asset zu OEM Manufatureres. Example: Cameca, ThermoFisher, ...

## Slide 8: Recap: System @ SwissFEL
Cathode load-lock system (Photo injector)
p < 5E-10 mbar
Docking Station (separate)
NEG/SIP Pump
sample transorter
with bayonet coupling
Carousel for storage of 4 cathodes
linear translator with 2600 N
Cathode preparation system:
Linking chamber (p < 5E-10 mbar)
Carousel for storage of 4 cathodes
Suitcase
Notes: Installation and running since 2019
Non-Evaporable Getter (NEG) Pumpen und Sputter Ion Pumps (SIP) The cathode pressed into the photo-injector gun with ~ 500 N to stabilize the resonant frequency.

## Slide 9: The UHV Suitcase
[Graphic by Romain Ganter]
Cathode Suitcase
p < 5E-10 mbar
DN40CF connecting flange
Notes: Weight closer to 15kg.
Non-Evaporable Getter (NEG) Pumpen und Sputter Ion Pumps (SIP)
NexTorr Z200: 290l/s

## Slide 10: Cathode Handling
Cathode Gripper
The search for a secure gripper
Now compatible with SwissFEL and CERN Cathodes
CERN design:
CLIC Note 303 (1996)
Notes: Aka the Puck
I think the 6th version now

## Slide 11: Operation
The gripper and receiver were just assembled this Monday. This is an initial test for demonstration purposes.
[The video shows the gripper retrieving the cathode from the receiver and placing it back again. The receiver is part of the carousel. The gripper is operated by a dual-shaft, dual-rotary sample transporter.]

## Slide 12: Cathode Handling
Dual Shaft, Dual Rotary Sample Transporter
*contains a special bayonet coupling
Specifications:
linear Travel to 1250 mm
reinforced Teflon
Magnetic coupling: Linear Force: 70N, Torque: 5Nm
Cathode PSI/CERN
Receptor (part of the carousel)
Grabber
Inner Shaft
Outer Shaft
Welded Tube Unit
Notes: lass-fiber-reinforced Teflon (PTFE)

## Slide 13
Ferrovac AG
Thurgauerstrasse 72
CH - 8050 Zürich
+41 44 273 16 38
sales@ferrovac.com
ferrovac.com
Thank you very much for your CONTRIBUTION!
Special thank to Romain Ganter and David Stephan for collaboration on the Project.
Potential
Standardised interfaces enable a unified handling system
Cathode exchange without borders
Notes: Romain instpired me to come here and share the system.