## Slide 1
Laser spectroscopy of radionuclides & development of experimental methods for S3-LEB
V. Marchand1
On behalf of : S3-LEB & FRIENDS3 collaboration
1IJCLab, Université Paris-Saclay & CNRS/IN2P3, 91405 Orsay, France

## Slide 2
Laser spectroscopy of radionuclides & development of experimental methods for S3-LEB
Introduction to laser spectroscopy and links with nuclear physics.
Presentation of the different setups.
Advances made on a CW tunable Ti:sa laser.
Stable Dysprosium spectroscopy with CW tunable Ti:sa laser.

## Slide 3: What is laser spectroscopy ?
A.I (
IP
MCP
Rydberg (
NR.I (

## Slide 4: What is laser spectroscopy ?
A.I (
Laser
MCP
Rydberg (
IP
NR.I (

## Slide 5: What is laser spectroscopy ?
A.I (
Laser
Laser
MCP
Rydberg (
IP
NR.I (

## Slide 6: What is laser spectroscopy ?
A.I (
Laser
Laser
MCP
Rydberg (
+1 counts
+1 counts
+1 counts
+1 counts
+1 counts
+1 counts
+1 counts
+1 counts
+1 counts
+1 counts
IP
NR.I (

## Slide 7: Why laser spectroscopy ?
n=1
1S1/2
F=1
F=0
Fine
structure
Hyperfine structure
Energy of an hyperfine level given by :
With :
F=I+J : total spin
I : nuclear spin
J : electronic spin
The hyperfine coefficients depends on the nuclear properties :
Possible shapes for nuclei,
Image from Iain Moore
X.F. Yang et al., PPNP 129 (2023)

## Slide 8: Where are we performing laser spectroscopy ?
aerial view of GANIL,
image from GANIL
GISELE &
FRIENDS3
S3-LEB@S3
France,
Google maps

## Slide 9: Where are we performing laser spectroscopy ?
Overview of the SPIRAL2 facility

## Slide 10: Where are we performing laser spectroscopy ?
Super Separator Spectrometer S3,
A. Drouart et al., J. Phys, 1643 (2020)

## Slide 11: S3-LEB Overview
S3
exotic ions
S-RFQ
miniRFQ
QMF
Cooler-buncher
Pulse-up
PILGRIM
(MR-TOF-MS)
MagneToF
MCP1
MCP2
S3-Low Energy Branch :
  Goals : probe structure of exotic nuclei
  Technique : In-Gas Laser Ionization Spectroscopy
MCP3
Gas cell
A. Ajayakumar et al., NIMB 539 (2023)

## Slide 12: S3-LEB : Gas cell principle
Characterization of the gas jet,
R. Ferrer et al., Phys. Rev. Research. (2021)
Why a supersonic jet :
  T ↘ ⇒ ↘
  P ↘ ⇒ ↘
Gas cell,
W.Dong., PhD thesis (2024)

## Slide 13: S3-LEB Overview
MagneToF
S3
exotic ions
S-RFQ
miniRFQ
QMF
Cooler-buncher
Pulse-up
MCP1
MCP2
S3-Low Energy Branch :
  Goals : probe structure of exotic nuclei
  Technique : In-Gas Laser Ionization Spectroscopy
MCP3
Gas cell
+1 counts
+1 counts
+1 counts
MCPinj
Ar
He
PILGRIM
(MR-TOF-MS)
A. Ajayakumar et al., NIMB 539 (2023)

## Slide 14: S3-LEB Overview
MagneToF
S3
exotic ions
S-RFQ
miniRFQ
QMF
Cooler-buncher
Pulse-up
MCP1
MCP2
Status :
  S3-LEB fully connected from S3 to PILGRIM.
  Commissioning until deflector done.
  Trapping test in PILGRIM ongoing.
MCP3
Gas cell
+1 counts
+1 counts
+1 counts
MCPinj
Ar
He
PILGRIM
(MR-TOF-MS)
Towards SEASON
A. Ajayakumar et al., NIMB 539 (2023)

## Slide 15: S3-LEB Overview

## Slide 16: GISELE Laboratory

## Slide 17: GISELE Laboratory
Goals :
Development of new laser/laser system.
Development of ionization scheme.
Send beam towards off-line experimental area such as FRIENDS3 & LRC.
Laser layout at GISELE,

## Slide 18: GISELE Laboratory
Lasers systems :
1 Nd:YAG pulsed pump laser (532nm, 60 W)
2 pulsed broadband Ti:sa laser (650-1100 nm, 2W)
1 pulsed narrowband Injection-Locked (ILC) Ti:sa laser (650-1100nm, 2W)
1 Narrowband diode to seed the ILC.
Frequency doubling achieve via BBO/BiBO crystals
  ⇒ 390-450 nm

## Slide 19: GISELE Laboratory
Atomic Beam Unit (ABU) :
Goal : Laser spectroscopy
How ?
  Evaporation of the atomic sample.
  2-steps ionization.
  Accélération via 2 electrodes ⇒ MCP

## Slide 20: FRIENDS3 setup
3D drawing of FRIENDS3 experimental setup,
E. Morin et al., NIMB 573 (2026).

## Slide 21: FRIENDS3 setup
Fast
Radioactive
Ion
Extraction
Neutralization
Device
S3
3D drawing of FRIENDS3 experimental setup,
E. Morin et al., NIMB 573 (2026).

## Slide 22: FRIENDS3 setup
Gas-cell @ S3-LEB :
  Extraction time 600 ms [1].
  ⇒ Limit the exotic nuclei studies.
  FRIENDS3 goal :
    Fast extraction
    Fast neutralization
3D drawing of FRIENDS3 experimental setup,
E. Morin et al., NIMB 573 (2026).
[1] W. Dong et al., arXiv:2601.12009 [physics.ins-det] (2026)

## Slide 23: FRIENDS3 setup IRL

## Slide 24: FRIENDS3 setup IRL

## Slide 25: My work : CW Ti:sa
CW Ti:sa laser
ABU
Seeding diode
Injection-Locked Cavity:
  Needing seeding to achieve narrowband.
  Seeding diode limited in tuning range.
Goal :
  Replace it by a continuous wave Ti:sa laser with a high tunable range.

## Slide 26: CW Ti:sa : IRL layout
Pump :
  CW Nd:YAG (532 nm)
Optics :
  Wavelength selection :
    BRF
    Air-spaced etalon
    Direction of emission :
      TGG crystal
CW Ti:sa cavity
Millennia eV
pump laser (CW 532 nm)

## Slide 27: CW Ti:sa : simplified layout
Pump :
  CW Nd:YAG (532 nm)
Optics :
  Wavelength selection :
    BRF
    Air-spaced etalon
    Direction of emission :
      TGG crystal

## Slide 28: Wavelength selection theory
Cavity design & Ti:sa specs :
Discrete spectrum of emission.
650-1100 nm range.
Solution :
  ⇒ introduction of losses via etalon & BRF.
Spectroscopy requirements :
Need for a continuous scan.
How ? :
  Change size of cavity via OC.
    ⇒ Translation of .
FSR

## Slide 29: Wavelength selection theory
Mode position at rest (t) :
  centered.
  Mode position if :
    not centered.
    Not ideal but ok !

## Slide 30: Wavelength selection theory
  Mode position if :
    not centered.
    Not ideal but ok !
    Mode position if :
      « Mode Jumps »

## Slide 31: Wavelength selection theory
    Mode position if :
      « Mode Jumps »

## Slide 32: Wavelength selection theory
    Mode position if :
      « Mode Jumps »
      Solution :
        Translate the gain curve.
          ⇒ Change length of the etalon via piezo.
    Mode position after correction of the etalon :
      (t+1) centered with (t+1).
      « Etalon locked to the OC »

## Slide 33: Wavelength selection in practice, 1st step : OC scan
    Locking of the OC, 1st method :
      Simple feedback loop.
      User set .
      Labview use its P-loop, & to drive the OC.

## Slide 34: Wavelength selection in practice, 1st step : OC scan
Conclusion :
  Frequency variation below wavemeter relative accuracy (3MHz).
  OC locking works !

## Slide 35: Wavelength selection in practice, 2nd step : etalon locking
    Etalon locking :
      Laser sampled by photodiode.
      Use of the Dither-locking technique via LaseLock device.
      LaseLock PID loop drive the etalon piezo to bring the error signal at 0.

## Slide 36: Wavelength selection in practice, 2nd step : etalon locking
    Etalon locking :
      Laser sampled by photodiode.
      Use of the Dither-locking technique via LaseLock device.
      LaseLock PID loop drive the etalon piezo to bring the error signal at 0.

## Slide 37: Wavelength scan
    Conclusion :
    Scanning range is relatively low, 5 GHz would be better for laser spectroscopy.
    With frequency doubling, possible to scan for 7 GHz, which make laser spectroscopy possible for low isotope shift.

## Slide 38: Proof-of concept : Seeding CW Ti:sa
    Injection-Locked Ti:sa Cavity (ILC) :
      Realized that optic fiber generates huge losses via s-polarisation.
      But seeding work perfectly.

## Slide 39: Proof-of concept : Stable Dysprosium spectroscopy
23 877,739 cm-1
0 cm-1
47 900,5 cm-1
48 343,96 cm-1
418,8 nm
408,727 nm, 24 466,221 cm-1
A.I

## Slide 40: Proof-of concept : Stable Dysprosium spectroscopy
Natural abundances :
156Dy : 0,056 %
158Dy : 0,095 %
160Dy : 2,329 %
161Dy : 18,889 %
162Dy : 25,475 %
163Dy : 24,896 %
164Dy : 28,260 %

## Slide 41: Proof-of concept : Stable Dysprosium spectroscopy
Natural abundances :
156Dy : 0,056 %
158Dy : 0,095 %
160Dy : 2,329 %
161Dy : 18,889 %
162Dy : 25,475 %
163Dy : 24,896 %
164Dy : 28,260 %

## Slide 42: Proof-of concept : Stable Dysprosium spectroscopy

## Slide 43: Proof-of concept : Stable Dysprosium spectroscopy
PRELIMINARY RESULTS
    Isotope shift :
    Isotope shift in bibliography :
      MHz
      In John S. Ross, J. Opt. Soc. Am. 62, 548-554 (1972)

## Slide 44: Proof-of concept : Stable Dysprosium spectroscopy
PRELIMINARY RESULTS
    King-Plot :
    ⇒ allow to determine

## Slide 45: Conclusions
    S3-LEB :
      Installation is finished.
      Commissioning nearing completion.
    FRIENDS3 :
      1st off-line tests soon.
    GISELE :
      New seeding laser for narrowband laser spectroscopy.

## Slide 46: Perspectives
    CW Ti:sa :
      Solve scanning & stability problems.
      ⇒ Change OC, eventually study real behaviour
      of etalon/BRF.
    2nd part of my PhD - FRIENDS3 :
      Commissioning of the setup.
      In-gas jet spectroscopy of Dy with CW Ti:sa.
    Spectroscopy :
      Finish analysis for odd-even isotopes.

## Slide 47: The S3-LEB collaboration & FRIENDS3 project team
GANIL:
Anjali Ajayakumar; Dieter Ackermann; Alexandre Brizard; Lucia Caceres; Samuel Damoy; Pierre Delahaye; Hemanth Dinesan;
Sai Kumar Chinthakayala; Patrice Gangnant; Sarina Geldhof; Johan Goupil; Nathalie Lecesne; Andrés Lopez;
Thierry Lefrou; Renan Leroy; Franck Lutton; Alejandro Ortiz; Benoit Osmond; Julien Piot;
Blaise-Maël Retailleau; Hervé Savajols; Gilles Sénécal; Tudor Stefan
LPC:
Frédéric Boumard; Maylis Brun; Jean-François Cam; Hugues de Préaumont; Antoine de Roubin;
Philippe Desrues; Xavier Fléchard; Clément Gautier; Pierre Lassegues
Julien Lory ; Yvan Merrer; Skyy Pineda; Christophe Vandamme
IJCLab:
Wenling Dong; Patricia Duchesne; Serge Franchoo; Vladimir Manea; Valentin Marchand;
Elodie Morin; Olivier Pochon; Afonso Vicente
KU Leuven:
Arno Claessens; Ruben de Groote; Rafael Ferrer; Mark Huyse; Fedor Ivandikov; Sandro Kraemer ; Yuri Kudriavtsev;
Jekabs Romans; Simon Sels; Paul Van den Bergh; Piet Van Duppen; Matthias Verlinde ; Elise Verstraelen
JGU:
Sebastian Raeder; Dominik Studer; Klaus Wendt
JYU:
Iain Moore; Michael Reponen; Juha Uusitalo
IPHC:
Emil Traykov
IRFU:
Martial Authier; Olivier Cloué; Antoine Drouard; Thomas Goigoux;
Mathilde Ragot; Emmanuel Rey-Herme; Damien Thisse; Marine Vandebrouck
and the RESIST network in ENSAR2