## Slide 1: Direct Dark Matter Research : The Damic-M* experiment
MELLOUKI Issam-Eddine
* DArk Matter In CCDs at Modane

## Slide 2
T. Lin, arxiv:1904.07915
Detection of particles produced by the annihilation of SM particles
Detection of electronic/nuclear recoils
Search for missing transverse energy
WIMP Waning, Nearly Excluded

## Slide 3: Dark Matter production scenarios
Production scenarios :
  Freeze-in/out
  Gravitational
  Etc.
Freeze-out :
  Dark Matter in thermal equilibrium in early universe
Freeze-in assumption :
  No Dark Matter in the primordial plasma
  Production from thermal bath species over time
Freeze-out
Freeze-in
arXiv:0911.1120

## Slide 4: Damic-M in Dark Matter research
Direct Dark Matter experiment
Skipper-CCD detectors
Single electron detection capability
  For low-mass dark matter :
Sub-electron readout noise
World-leading limits on hidden sector Dark Matter
Alvaro E. Chavarria, “The search for dark matterwith DAMIC-M”

## Slide 5: Dark Sector Theory
The SM is not complete (neutrino, dark matter, …)
New Interactions may exist !
Simple natural extension of the Standard Model : new U(1) symmetry
New gauge boson which can be :
  Analogous to the photon
  Analogous to the Z boson with V-A structure
Leads to MeV-scale Dark Matter
Pierre FAYET, “The U BOSON as a generalized DARK PHOTON”
arXiv:2005.01515

## Slide 6
T. Lin, arxiv:1904.07915
DAMIC-M
Max Planck Institute for Nuclear Physics
MeV
Alvaro E. Chavarria, “The search for dark matter with DAMIC-M”

## Slide 7: Classical CCDs
interaction ionizes the medium and generates charges
Charges are trapped in potential wells
Then, the charges are moved line by line, pixel by pixel, toward the serial register
Measurment of the charge on each pixel in the sens node

## Slide 8: Skipper-CCD
Multiple non-destructive charge measurments
Readout noise divided by
  Sub-electron reading noise
Allows us to explore small energy deposits
arxiv:1706.00028

## Slide 10: Some informations
CCD mass : ~4g
Images of 6300×1600 pixels taken every 1668 seconds
Pixel size :
  15 μm ×15 μm
  675 μm thick
DAMIC-M readout noise :
In comparison :
  Euclid space telescope :
  3.2-Gigapixel LSST :
DAMIC-M LBC (2025):
  4 CCDs for ~1.3 kg-day exposure
DAMIC-M (2026-202X)
  ~80 CCDs with better bkg/noise

## Slide 11: Data Analysis
Contamination sources :
  Astroparticles
  Radioactivity
  Defects generating charges continuously
  Charge transfer inneficiency (CTI)
  Infrared light
  Etc.
Pixel selection :
  Hot region (large rate)
  Clusters of high-charge pixels ( )
  Line/column multiplicity
  Etc.
  ~90% of data are kept

## Slide 12: Pattern Event Research: Predictions vs Observations for DAMIC-M LBC
The Dark Current (DC) is poissonian
Need to find the for the Dark Current to calculate the expected number of events (, )
Comparison with observed events ():
  Background is compatible with observations
  No evidence for Dark Matter
arXiv:2503.14617

## Slide 13
arXiv:2503.14617 : Probing Benchmark Models of Hidden-Sector Dark Matter with DAMIC-M (2025)

## Slide 14: Daily Modulation
Attenuation of the event rate while crossing the Earth
Signal modulated by Earth’s rotation
Can be used to improve the constraints
arXiv:2511.13962

## Slide 15: Skipper-CMOS
Taking images with Skipper-CCD can be long
Skipper-CMOS are times faster !
In developpement here at IJCLab !

## Slide 16: Conclusion
The DAMIC-M experiment allows us, for the first time, to probe MeV-scale Dark Matter with remarkable sensitivity
Skipper technology is a powerful tool and may have other interesting applications in physics
Charge-coupled devices are currently among the best detectors for MeV-scale direct Dark Matter searches
Current DAMIC-M LBC limits challenge hidden-sector benchmark models
The upcoming full-scale experiment may achieve the first detection of Dark Matter

## Slide 17: Annex

## Slide 18: Skipper technology for other fields
A Cosmological examples

## Slide 21
Euclid: Early Release Observations – A glance at free-floating new-born planets in the σ Orionis cluster

## Slide 22
Euclid Quick Data Release (Q1) : An investigation of optically faint, red objects in the Euclid Deep Fields (https://arxiv.org/abs/2503.15322)
From left to right: IE, YE, JE, HE,
IRAC1, and IRAC2.

## Slide 25
Crystal form factor calculated in QEDark
Dark matter form factor :
Dark matter velocity distribution
Differential event rate
Dark matter–electron cross section