## Slide 1: Status of iCASA activity at KEK
Hiroshi Sakai
Innovation Center for Applied Superconducting Accelerators (iCASA), Accelerator Laboratory
High Energy Accelerator Research Organization (KEK)
IJClab visiting 2026.June.8
Contents :
Introduction KEK & iCASA
The latest SRF activities in iCASA at KEK (mainly cERL & ITN )
Summary
52 pages
After cERL explanation (end of 24page), it is better to make discussion time. And other R&D and ITN will be quickly explained (or skip).

## Slide 2: My Research History (Brief introduction）
1997 – 2002 | Kyoto University Master's/Ph.D. student
& KEK and Postdoctoral Fellow.
  Development of the laser wire beam profile monitor for KEK-ATF damping ring:
  Successfully measure the 7um vertical beam size in KEK-ATF damping by laser-wire.
2002 – 2009 | The University of Tokyo (ISSP) assistant professor
  3rd-generation VUV-SX light source design and.
  injector, vacuum & 、x-ray beam profile monitor with FZPs (for KEK-ATF）
  ERL (Energy Recovery Linac) (2006-2009.5)
    Development of cERL SRF cavity (with KEK,JAEA)、VT on KEK-STF.
2009 – Present | KEK Accelerator Laboratory
  Continue development of cERL SRF cavity. Achieve 1mA energy recovery in cERL。
  One-year stay in 2016 to join EURO-XFEL(DESY) for cryomodule construction with 800 cavities in DESY.
  2017- High-Q, High-G for KEK-STF cryomodule with 31.5MV/m and beam acceleration.
  2018- Team leader of application of SRF GRP.by using cERL. Development of Nb3Sn cavity.
  2024-now: Head of iCASA. TTC(Tesla Technology Collaboration) Technical-Board co-chair.
ATF Laser wire
EURO-XFEL
cERL Main linac
Around 20 years of dedicated experience in the development of superconducting accelerator cavities.
Engaged in cutting-edge low-emittance electron beam accelerator R&D (e.g., ILC) since graduate studies.
Currently driving advanced industrial applications and global research collaborations.
H：50μm
V: 6μm
ATF XSR monitor
Clean assembly
STF cryomodule

## Slide 3: A)
Contents :
Introduction KEK & iCASA
The latest SRF activities in iCASA at KEK (ITN & mainly cERL)
Summary

## Slide 4: Past & present SRF development in KEK
Super KEKB
(circumference 3km)
STF
cERL
CFF
CFF
EBW & deep drawing of cavity
(Cavity fabrication)
COI building
(for new furnace)
& Nb3Sn cavities
For industrial application with CW beam
508MHz TRISTAN (1989)
STF (2005-)
Cavity R&D, electro-polish, vertical test and cryomodule test
Long-pulse beam for ILC
508MHz KEKB (1998)
SRF cavity R&D since 1980s
Experiences at TRISTAN/KEKB/SuperKEKB
KEK has the long experience for the development of SRF accelerator since TRISTAN (1980s) to present (2025).
New R&D of cavity fabrication was doen in CFF building and High-Q R&D & new material like Nb3Sn was proceeded on COI building
iCASA
iCASA
Compact ERL (cERL)
(2013-)
Cryomodule test
KEK Tsukuba campus

## Slide 5: Innovation Center for Applied Superconducting Accelerator （iCASA)
ATF
STF
CFF
（mechanical center）
cERL
Acc. 1st Div.
Innovation Center for Applied Superconducting Accelerator (iCASA)
Director
Acc. 2nd Div.
Acc. 3rd Div.
Acc. 4th Div.
Acc. 5th Div.
Acc. 6th Div.
Accelerator Lab.
J-PARC
SuperKEKB
Linac
PF
Established in 2022
And, iBNCT, etc
Experience of large accelerator
Applied research
For LC, cavity R&D
For ILC
cavity R&D
iCASA is developing a linear collider (LC) accelerator for particle experiments using a superconducting RF cavity, which capable of high-intensity beam acceleration, as well as developing applications of superconducting accelerator technology for industrial and medical applications.
Positron source

## Slide 6: B)
Contents :
Introduction KEK & iCASA
The latest SRF activities in iCASA at KEK (mainly cERL & ITN)
  cERL status (toward 1 mA operation and latest brief status)  and question time (Alex Fomin &..)
  SRF application (Nb3Sn & EUV-FEL based on cERL )
  ITN activities concerning SRF work and briefly show nanobeam and positron
Summary
Quick
explanation
Today’s main
After cERL explanation (end of 24page), it is better to make discussion time. And other R&D and ITN will be quickly explained (or skip).

## Slide 7: 1. Compact ERL (cERL) in KEK
cERL developed the following key technologies and was constructed in 2013.
High current and high brightness photo cathode DC gun.
CW superconducting cavity for the high current beam operation.
High current CW energy recovery operation achieved 1 mA ERL operation in 2016.
©Rey.Hori/KEK
Circumference ~ 90m
Marger
Beam Dump
9-cell SC cavity x 2
2-cell SC cavity x 3
Buncher
Photocathode DC gun
(Not SRF gun)
RF frequency= 1.3 GHz
Compact ERL (cERL)
Nominal beam energy | 35 MeV  20MeV
Nominal Injector energy | 5 MeV 2.9MeV
Beam current | 10 mA (initial goal) 100mA (final)
Normalized emittance | 0.1 ‒ 1 mmmrad
Bunch length (bunch compressed) | 1-3ps (usual) 100fs (short bunch)
Design parameters of the cERL
17.7 MeV
500kV DC Gun (highest DC voltage in the world)
Injector LINAC
Main LINAC
Now cERL was used for industrial application by using stable high current beam.
CW laser
These activities were done by
iCASA (previous CASA) from 2018.
Irradiation beam line with CW beam (2019)
THz “test beam line” (2020)
Two undulator for IR-FEL (2020)
Max 26 MeV 10mA

## Slide 8: History of construction and Commissioning of cERL
Now we continue the beam operation under ERL operation with 1mA .  next 10mA
8
2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026
Refurbishment
of building
Clearing radioactive
materials
Construction of
radiation shielding
Commissioning of injector
Commissioning of cERL (with loop)
Commissioning/Operation
Construction/Maintenance
Construction of recirculation loop
Increasing the beam current
Commissioning of LCS system
Construction of
injector
Construction of LCS system
High bunch charge
& THz study
1mA again
T. Akagi, et., al. “Narrow-band photon beam via laser Compton scattering in an energy recovery linac” Phys. Rev. Accel. Beams 19, 114701 (2016)
R&D for Industrial application
Laser Compton scattering experiment in ERL
Commissioning started
(Published) M. Akemoto et al., “Construction and commissioning of the compact energy-recovery linac at KEK” Nucl. Instrum. Method A 877 p.197-219 (2018).
Construction of RI beamline
RI beam test & production
Beam operation
Construction of IR-FEL
FEL produced
here
0.3 mA CW beam with undulator
1mA CW ERL achieved
DC gun and cryogenic maintenance
1mA CW ERL with undulator
R&D for industrial SRF application
(1) RI manufacturing facility for nuclear medical examination and irradiation to wood by using irradiation beam line
(2) IR-FEL experiment with high current ERL beam  toward the EUV-FEL development (later).
(3) Intense THz light generation with ERL
(Published) H.Sakai et al. “Stable operation of a fully energy-recovered 1-mA-class electron beam at a compact energy-recovery linac“ , Phys. Rev. Accel, Beams 28, 091603 (2025).
https://doi.org/10.1103/qvpb-jsqx
EUV-FEL project start
4mA DC gun
Y. Honda et al. “Construction and Commissioning of Mid-Infrared SASE FEL at cERL“ Review of Scientific Instruments, (11) Vol.92 (2021)
DC gun
Power supply replacement

## Slide 9: DC Gun status & how to make CW beam
Strategy for reaching beam current higher
  Sophisticated beam tuning (optics matching) by Burst beam and sometimes use collimator at injector point to reduce halo of beam.
  After changing CW mode, we increase the beam current by changing laser power under monitoring the beam loss by loss monitor.
Expand
st = 1-3 ps
CW beam
(for high currents)
1.3 GHz
Peak current
1.3 GHz
Bunch charge: 7.7 pC  average current: 10 mA
9
Photocathode DC gun
Initial conditions are determined by the gun-drive laser.
For LCS experiment or high charge operation, not 1.3 GHz but 162.5 MHz beam operation was used
 | condition | Parameters
Beam Repetition | Standard | 1300 MHz
 | LCS | 162.5 MHz
Bunch Length | Standard | 1 – 3 ps
 | Compressed | 0.15 ps
Total path length | Gun to Dump | 120 m
Two ceramics for DC 500 kV in 2016
Cathode #2 QE after installation
Total extracted charge of cathode in Mar/2016
#1 : 14.2 [C], #2 : 25.6 [C]
No critical issues on vacuum design of the gun.
We successfully extract 500 keV electron from gun to dump (previous 390~450keV).
Prepare to submit paper
cathod

## Slide 10: Comact ERL (cERL) in KEK & cERL cryomodules
Injector-linac
Dump
Recirculation (return) loop
Injector diagnostic line
Merger
Compact ERL Layout
Photocathode DC gun
(Not SRF Gun)
Main linac module
Main-linac
Input couplers
Cryostat
Tuner
HOM absorber
Two 9-cell SC cavities
e-
HOM damped (for 100mA circulation to suppress HOM-BBU in design)
9-cell cavity (ERL-model2)× 2
Requirement was satisfied at V.T. Issue: Heavy F.E was met @9-10MV/m after string assembly. & met quench shown later In detail
3MeV
20MeV
Input Coupler
HOM Coupler &
RF Feedthrough
2-cell Cavity
Tuner
Cryostat
e-
Injector module
2-cell cavity × 3
Double coupler
RF frequency: 1.3 GHz
Input power :
10kW/coupler (10mA, 5MeV)
180kW/coupler (100mA, 10MeV)
Eacc: 7.6MV/m（5MeV）
15MV/m (10MeV)
Unloaded-Q: Q0 > 11010
Target Energy : 35MeV
 Change 20MeV due to field emission
RF frequency: 1.3 GHz
Input power : 20kW CW (SW)
Eacc: 15 MV/m（design）
Unloaded-Q: Q0 > 11010
Issue: We met the HOM coupler heating if field inceased more than 7MV/m. It is the reason for heating not perfectly to be filiterd in HOM coupler iand results in lower Q0 than 1x1010.
Nominal beam energy | 35 MeV  20MeV 17.5MeV
Nominal Injector energy | 5 MeV 2.9MeV
Beam current | 10 mA (initial goal) 100mA (final)
Normalized emittance | 0.1 ‒ 1 mmmrad
Bunch length (bunch compressed) | 1-3ps (usual) 100fs (short bunch)
Design parameters of the cERL
17.5 MeV
Tuner
Irradiation beam
Line (IR) (2019)
K. Watanabe, et al. “Development of the superconducting rf 2-cell cavity for cERL injector at KEK” Nucl. Instru. Meth. A Vol. 714, p67-82 (2013)
H.Sakai et al. “Field emission studies in vertical test and during cryomodule operation using precise x-ray mapping system”. Phys. Rev. Accel. Beams 22, 022002 (2019)

## Slide 11: Power & LLRF stability in cERL beam operation
Present (2022) | Inj1(2cell) | Inj2(2cell) | Inj3(2cell) | ML1(9cell) | ML2(9cell)
Acc. Field | 3.4 MV/m | 3.6 MV/m | 3.2 MV/m | 5.2 MV/m | 8.2 MV/m
power | 0.6 kW | 1.4 kW | 1.1 kW | 0.7 kW | 2kW
Power source | 25 kW klystron | 300kW klystron (Vector sum) |  | 16 kW solid state Amp | 8kW solid state Amp
QL | 1.2e6 | 5.8e5 | 4.8e5 | 1.3e7 | 1.0e7
DA/A(% rms) | 0.014% | 0.011% |  | 0.016% | 0.011%
Dq(deg rms) | 0.023deg | 0.025deg |  | 0.027deg | 0.015deg
Data taken in 2021.Feb.5. Basically suppress michrophonics and almost close our requirements of DA/A ~ 0.01% , Dq ~ 0.01 deg.
FPGA
Virtex5-FX
Beam stability was also achieved about 0.01% by measuring momentum jitter at screen monitor on arc section thanks to LLRF optimization
Hz
dBc/Hz
T. Miura, IPAC2014 @Dresden
Phase noise by Microphonics was suppressed well by RF FB.
Phase noise of Vc with FB was almost the same as that of Master Oscillator.
Microphonics suppression in ML
(Up to now, we keep the RF stability after ML1 field reduced 8.3 MV/m  5.2 MV/m in 2017 )
Inj1
Inj2,3
ML1
ML2
Total beam energy 17.5 MeV
Injector gain : 3.0 MV
Main linac gain : 14.0 MV

## Slide 12
(ref) M. Shimada, “Operation and plans for cERL”, PERLE Collaboration Meeting, CERN, October 13-14, 2025

## Slide 13
Optics matching and halo collimation
Beam optics (assume 0.5 mm mrad) & beam profile after matching (2016)
CAM8 before inserting collimator
H. Sakai, et al., Phys. Rev. Accel. Beams 28, 091603 (2025)
FIG 6. (Top) Beam profile on a screen monitor, where the dispersion is approximately 0.23 m after the COL1 position just before entering the merger section and be-fore inserting the collimator (COL1). (Bottom) Beam profile on the same screen monitor after inserting collimator (COL1). In both figures, the beam intensities in the core of the measured beam profile are saturated to emphasize the beam halo.
CAM8 after inserting collimator
GPT
elegant
Optimization of collimator
Position of collimator and dispersion function
CAM8 (screen)

## Slide 14: Successful ~ 1mA CW beam operation with energy recovery
Δptotal=Δ(Pin1+Pin2-Pref1-Pref2)
red : Difference between an input (Pin) and a reflected (Pref) power of the ML. Energy loss measured from the graph = 4 W. (error +-4W)
Required power without recovery is :
17.14 MV x 900 uA = 15.4 kW
Energy Recovery is almost 100.0% (error +-0.04%)
Beam current (CW)
（upper） ML1
8.57MV
（lower）ML2
8.57MV
e-
Pin
Pref
Main linac
Change CW mode and increase the beam current :
Reach 0.9 mA after the 1mA approval from the government at 8th/Mar/2016.
Details will be explain in next page
H. Sakai, et al., Phys. Rev. Accel. Beams 28, 091603 (2025)

## Slide 15
FIG 11. Power variation (Pin-Pref) (Run1) with respect to the beam current. The horizontal axis shows the beam current(I). The vertical axis shows the variation of Pin-Pref from the zero-beam current. The Pin,cav-Pref,cav variations in each cavity (ML1 and ML2) are shown in red and blue, respectively. The Pin-Pref variation for the sum of ML1 and ML2 is shown in green.
where the beam power is expressed as Prf,acc = (Vc1+Vc2)x I, with the ML1 cavity voltage (Vc1), ML2 cavity (Vc2), and Pin (Pref) expressed as the sum of the Pin,cav (Pref,cav) of the ML1 and ML2 cavities, respectively.
Summary of parameters of Energy recovery of 1mA in cERL on 3 run
Main linac
Due to the low-energy beam acceleration of the 2.9 MeV injection beam and deceleration of the 2.9 MeV beam to the damp, phase slip occurred despite maintaining a 100% energy recovery condition.
H. Sakai, et al., Phys. Rev. Accel. Beams 28, 091603 (2025)
We tried three times 1mA operation as follows (2016-2018)

## Slide 16
Discussion about beam loss with measured radiation under 1mA operation
simulation
Measurement
Enegy recovery ratio is consistent with our beam loss estimation
H. Sakai, et al., Phys. Rev. Accel. Beams 28, 091603 (2025)

## Slide 17: Heat load of HOM beam of ML
Temperature rise at 162.5MHz x 0.9mA
Parameter | Value
Current | 900 µA
Repetition | 162.5 MHz
Bunch length | 3ps
No temperature rise of HOM damper
Expected heat load of ML : Loss Factror 10[V/pC]@3ps
Cavity Loss Power=7.7pC x 900µA x10V/pC x 2= 140 mW
2K
900µA
LBP HOM2
SBP HOM
LBP HOM1
Temp
Temp
Temp
Temp
Temp
Temp
Not different w w/o beam
Also
No HOM-BBU
was observed.
H. Sakai, et al., Phys. Rev. Accel. Beams 28, 091603 (2025)
This small HOM head load will not affect energy recovery ratio of 100.0%

## Slide 18
Faraday cup
Screen monitor in front of Gun
screen
Add SS
shield
Unexpected discharge(1)
Unexpected discharge(2)
Field emitted electron induce a charge up of Faraday cup.
⇒Discharge lead to vacuum deterioration and increase of radiation.
Improvement on Faraday cup solved problem.
Field emitted electron hit photocathode → Secondary electron extracted by DC voltage and accelerated by injector cavities. Finally collide with the screen monitor.
⇒ Lead to vacuum spike and increase of radiation.
Both case, interaction of F.E. and surrounding components.
2015, June 16
INJ

## Slide 19: Injector performance from Oct. 2019 to Feb. 2022
We once met the sudden severe X-ray increase during beam operation in Jun. 2020.
F.E onset reduced from 8 MV/m to 5 MV/m in Inj #2 cavity. We do not know the reason.
After pulse processing, F.E onset recovered at normal level.  kept 7 MV/m operation
final
Suddenly x-ray onset reduced
2020.Jun.18
X-ray onset before and after pulse processing、
Pulse duty (0.5ms 10Hz)
18 MV/m (~2 hours)
Pulse duty (5ms 10Hz)
12 MV/m (~1 hours)
(Before pulse processing)
CW = 8MV/m (onset 5MV/m)
(After Pulse processing)
CW = 8MV/m (onset 8MV/m)
2020.Jun.19

## Slide 20: Main linac performance (long-time Q-value history (2012.Dec – 2023.Dec))
Before the beam operation, we could keep 1x1010 at 10MV on both cavities in 2012.
Main degradation of ML1 is thermal breakdown from 2017.
After that, quench limit and Q-values gradually reduced.
Cavity performance is suffered from field emission. In the latest four years, we kept the same Q-values in both cavities by applying the pulse processing on every cERL operational phase.
Kept same level of
Q-values on 4years
Chart: ML2 Vc (MV)
| 3 | 4 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5
Rad6(lower) (mSv/h) (before pulse aging) (2022/2/8) | 0.0003 | 0.0003 | 0.0015 | 0.024 | 0.1113 | 0.8396 | 6.722 | 33.04 | 121.5 | 353.9 | 844.8 | 1781
Rad6(lower) (mSv/h) (after pulse aging) (2022/2/8) | 0.0005 | 0.0005 | 0.0003 | 0.009 | 0.0188 | 0.4099 | 3.257 | 17.93 | 65.6 | 211.1 | 496.8 | 1156
ML Pulse processing (peak 11.7MV)
Vc = 8.8MV(CW) + 2.9MV(pulse 10Hz 4ms) (3 hours apply)
After pulse processing, 0.5 MV onset of x-ray was increased. X-ray monitor was set at the downstream of cryomodule.
Kept same level of
Q-values on 4years
ML1
ML2
Before
Beam operation
Before
Beam operation

## Slide 21: Latest CW ~1mA beam operation with undulator (2023.Nov  now)
Trend of the beam current during CW operation
Machine learning(ML) tuning of the collimators to reduce beam loss by 16 loss monitors
~1mA (952μA) CW ERL beam operation was done with undulator.
Beam loss was drastically reduced by using collimator in injector part. And we tried beam tuning with machine learning. 100.0 % +- 0.2 % (preliminary) was achieved under ERL operation.
These results of ~1mA operation with energy recovery will push higher current ERL operation of more than 10 mA in cERL under extremely small beam loss.
M.Kurata et al, “Recent studies on high current operation at the compact ERL”, IPAC 24 proceesings.
Good lifetime of GaAs cathode
Collimator
20 min.

## Slide 22
latest cERL operation in FY2025 concerning about IJClab
High charge operation was conducted with IJClab. Please see the above results for injector study.
higher current operation than 1mA in this operation we will present in ERL2026. (with upgrade status of DC gun for 10mA)

## Slide 23
Question from Alex Fomin about our cERL beam operation and design (1)
1. In your most recent paper, you achieved 100% energy recovery while operating on crest. Looking toward future applications, you mention moving to off-crest operation. How much do you expect the energy-recovery efficiency to decrease under these conditions, and what specific methods will you use to try and maintain 100% recovery?
within +-10% off phase is expected to make FEL operation, energy recovery efficiency seems OK under our brief experiment. but beam current was reduced in one trial. We need to survey more.
2. Is the initial collimator design, in terms of dimensions, location, and shielding, based on simulation or on early commissioning data? Was it upgraded later?
--> No. it is better to optimize. At least, in our design we will increase (upgrade?) up to 10 mA to cover Pb block more in COL1 and COL2.
3. Did you choose the collimator locations using phase advance? For the two collimators, did you study the optimal phase advance between them? Is it possible to adjust the phase advance?
-->I'm not sure that we care the phase advance on designing phase about high energy region of COL3,4,5. We only assume where is the loss point for our operation, for example arc section and injector part. And we set collimators before the arc section and injector part.

## Slide 24
Question from Alex Fomin about our cERL beam operation and design (2)
4. Did you observe any effect of collimation on emittance growth or secondary halo in some cases?
--> Once we tried measuring the emittance growth with/without collimator (COL1) and measure the emittance on south straight section. we see the same emittance of 0.5 mm mrad of both with and without collimator. At least we found that wake field effect of our collimator is negligible. We have no secondary halo because halo is very low current.
5. During CW high-current operation, can the collimators be adjusted to compensate for beam-loading effects, or are the collimation settings fixed during high-current operation?
--> Please see the 4 about wake field effect. during 1mA operation, collimation setting is fixed. if we need feedback for long term operation. Now we have no method. But need to investigate to operate for long time.
6. Do you use kickers with the feedback loop system from BPMs to correct trajectory instabilities?
--> No. it is also important to keep good beam operation for a long time and need to study. Thank you for your suggestion.
We need more question time more at this timing ? (5min. ?)

## Slide 25: 2. SRF application (Nb3Sn & EUV-FEL based on cERL )
The ERL-type EUV-FEL is the only solution to realize a high-intensity EUV light source we think. From April.2025, we got new funding for Economic Security Critical Technology Development Program (so called “K program” ) Next-generation semiconductor microfabrication process technology on JST (MEXT) for 5 years
A compact superconducting accelerator will be realized using recent superconducting technology.  keyword is “without He plant by Nb3Sn cavity”  Compact high-intensity electron beam irradiation facility for various applications.
Scientific significance & impact
High quality
High intensity
Electron beam irradiation facility
ERL-type
EUV-FEL
❶
❷
Ultra-fast electron microscopy
❸
Compact ERL (KEK)
Development for EUV-FEL light source
Achieve 10mA ERL operation with SASE-FEL
furnace for Nb3Sn coating (KEK)
Development of compact high current Nb3Sn superconducting RF accelerator
High current beam for irradiation
Irradiation material study at cERL
High current high quality beam
ERL study at cERL
10kW EUV-FEL

## Slide 26
Mo-99 (medical diagnostics) production and technetium extraction at cERL (2019.10 KEK news）
ERL based SASE-IR-FEL
(NEDO)
~10-kW EUV source
by ERL based FEL (EUV-FEL)
High efficiency and low cost of nanocellulose production by electron beam irradiation (collaboration with AIST) .
Water purification by electron beam irradiation
Electron beam irradiation onto asphalt to extend its life.
Applications of SRF accelerator
JLAB
cERL (CW and SRF accelerator) is the key to applied research on accelerators.
Key technologies
High brightness gun
SRF cavity
Energy recovery technique on high current beam
THz beam

## Slide 27: (ERL-FEL technology) cERL  EUV-FEL
Development of a high-intensity EUV light source for EUV lithography is next main issue.
It is possible to realize 10 kW level EUV light source based on ERL-FEL technology.
Present LPP source for EUV-lithography
LPP(Laser Produced Plasma)
Wavelength: 13.5nm(EUV)
 A few100W level
>1kW：need breakthrough
10kW
EUV
Most promising next generation EUV light source (recently xlight Inc. plan to develop EUV-FEL)
Superconducting cavities
Achieve IR-FEL generation at cERL in 2021
Feature of ERL
・ Energy recovery linac→ can reduce beam power and radiation at beam dump ８MW100kW , Damp energy 10MeV (very small)
We aim to realize 10kW EUV light source by establishing the accelerator core technologies at cERL.
Necessary with ERL
Proposed EUV-FEL
800MeV 10mA
cERL
Next target : 10mA ERL-SASE-FEL
Norio Nakamura et al 2023 Jpn. J. Appl. Phys. 62 SG0809
In Apr.2025, we started Economic Security Critical Technology Development Program (so called “K program” ) Next-generation semiconductor microfabrication process technology on JST (MEXT)

## Slide 28
Y. Honda, ”FEL Development Status Update” EUVL and source workshop 2026, 2026.6.8, Berkeley
“K program”

## Slide 29
Y. Honda, ”FEL Development Status Update” EUVL and source workshop 2026, 2026.6.8, Berkeley
“K program”

## Slide 30: Toward more reliable operation for SRF cryomdule for high current beam on cERL & future EUV-FEL
 | ERL Model 2 | EUV
Rsh/Q | 897 Ω | ~1000 Ω
Ep/Eacc | 3.0 | ~ 2.0
Iris diameter | 80 mm | 70 mm
Hp/Eacc | 42.5 Oe/(MV/m) | ～42.0 Oe/(MV/m)
Field emission & crack of HOM damper are main issues for reliable operation.  How to overcome field emission
cERL HOM damper
Ferrite with HIP bonding
T. Ota, et. al. SRF workshop 2019
AlN cylinder
Fragile under thermal cyle
C-shaped waveguide
M.Sawamura, “Development of HOM coupler with C-shaped waveguidefor ERL operation” ERL2019
R&D for Clean assembly work
Open clean bench
KOACH (ISO class 1) for local clean bench
Slow pumping/venting system with vacuum particle sensor.
Both were already applied for STF cryomodule assembly work.
H. Sakai, et. al. SRF workshop 2019
EUV cavity – TESLA-type 9-cell cavity + Large beam pipes(100f & 110f)
Stable operation at 12.5 MV/m and more seems achievable due to reduced Ep/Eacc.
Satisfy the HOM-BBU threshold of more than 100mA by EUV cavity.
EUV cavity design
H. Sakai, et., al. “SUPERCONDUCTING ACCELERATOR FOR ERL BASED FEL EUV LIGHT SOURCE AT KEK ” Porc, of SRF2017, Lanzhou, China, MOXA04, p13 (2017)
Done by T.Konomi
Taro Konomi at al.
PHYS. REV. ACCEL. BEAMS 26, 121601 (2023)

## Slide 31: Development of SRF components for High-Q
Standard recipe (120deg,48h), 200deg,3h
300 ~ 400deg,3h
600 ~ 800deg,3h
Mid-T furnace baking is good approach for producing Higher-Q cavity
T. Ito et al, “Influence of furnace baking on Q–E behavior of superconducting accelerating cavities”
https://doi.org/10.1093/ptep/ptab056
Mid-T furnace baking
Surface condition was changed
High-Q (low cryogenic loss) technology can largely reduce operation cost of EUV-FEL accelerator (15-20MV/m).
~ 300C heat treatment in the vacuum furnace improves Q-value 2~3 times or more.
Cryogenic loss is inverse of Q-value.
Notes: 理由（仮説）：
１．従来から実はMulti-layer構造(Nb2O5 , NbO, NbH(tc = 1.4K), Nb(bulk))になっているのだが、この構造が変わって、従来よりhigh-Qが出ているかもしれない。(酸化ニオブがlossy、
2. 空洞側の処理でn-dopingの場合は窒素の拡散でdirtyにしている。  furnace bakingでは酸素に置き換えている。これでN-dopingと同等のHigh-Qが出ているのではないか？

## Slide 32
A. Miyazaki et al., “Beyond the-state-of-the-art SRF cavities with advanced surface preparation” in Joint Workshop of TYL/FJPPN and FKPPN in Hamamatsu Japan (2026.May18-21)
SRF collaboration between IJClab and KEK for High-Q (synergy for CW machine and FCC-ee)
Works well both cavities of KEK and IJClab with mid-T baking for more than 3x10^10 of Q0 and >20 MV/m
Continue this work under FJPPN and global collaboration

## Slide 33: The latest superconducting RF (SRF) technology (Nb3Sn cavity)
Nb cavity
High Tc can operate 4.2K
Nb3Sn cavity (coating by Vaper deposition)
S Posen et al 2021 Supercond. Sci. Technol. 34 025007
Nb3Sn > 20 MV/m Q0~1e10
By vaper deposition
S. Posen and D. L. Hall. Superconductor Science and Technology, 30(3):033004, 2017
Reduce heat load lower than 1/5. Can conduction cooling by small refrigerator.
Nb3Sn cavity will be without He tank.
Many R&D were conducted all over the world.
Realization of Nb3Sn cavity- based accelerator is a major step toward compact accelerators for many application uses.
Recently beam acceleration based on Nb3Sn cavity with conduction cooling started.
https://doi.org/10.48550/arXiv.2404.09187 (Z.Yang et al.)

## Slide 34: Nb3Sn cavity R&D at KEK
Nb3Sn furnace replacement & VT results
  Restart Nb3Sn cavity coating and measure the cavity performance.  Q0 was improved at 10 MV/m.
Nb3Sn cryomodule development by conduction cooling
  Preparation for horizontal test by using conduction cooling with tuner. done making stand
1.3GHz CW power coupler for Nb3Sn cryomodule
  We develop 1.3 GHz 100kW CW coupler transmission.
   Results of highest performance in the world [2].
Nb3Sn furnace replacement in COI building and restart Nb3Sn cavity coating
Nb3Sn cavity VT results
Preparation for horizontal test by using conduction cooling
High power coupler development (100 kW CW coupler)
1e10
10MV/m
4.2K
VT
Done 9th VT after replacement
[2] (Published) Pragya Nama et al., “Development of continuous-wave 100 kW-class high power input coupler for conduction-cooled L-band Nb3Sn accelerators”, Nucl. Instrum. and Methods in Physics Research Section A 1083 171155-171155 (2025).
T. Ito et. al. “Progress in Nb3Sn vapor diffusion method for single-cell cavities at KEK” in SRF2025, MOP22 (2025)
Pragya Nama of Sokendai got Doctoral thesis.

## Slide 35: More than 10 MeV proposal for compact SRF linac based on Nb3Sn
At present
Rhodtron is powerful
Electron beam source
Max 10MeV x 35mA available
Normal commercial :
7MeV x 80mA = 560kW
Good efficiency :
50% (AC power  beam)
Against Rhodtron
More than 10MeV
High power
High efficiency
Ref：Rad. Phys and Chemistry 71 (2004) 285-288
FERMILAB-PUB-21-701-DI-TD
https://arxiv.org/abs/2112.09233
10MeV, 100mA.650MHz 5cell Nb3Sn
Water purification
Many Nb3Sn based compact SRF accelerator were proposed and developed.
H Sakai et al 2024 J. Phys.: Conf. Ser. 2687 092013 (IPAC23)
10MeV, 50mA.1.3GHz 2cell Nb3Sn x5
10MeV, ??mA.650MHz 4.5cell Nb3Sn
extended
35MeV, 10mA.1.3GHz 3cell Nb3Sn x13
nanocellose
For RI production
S Kashiwagi et al 2024 J. LINAC2024 Chicago p797-800 (THPB085)

## Slide 36
Nb3Sn latest results (cryomodule with beam operation) from SRF2025
~3MV/m,4.6MeV CW, transmission 40%, conduction cooling 4.2K,
IMP
4~7MV/m,4.6MeV CW, transmission 100%, Liq. He 4.2K,
Beam operation with Nb3Sn cavity w w/o Liq. He was started.  We plan to beam operation by using Nb3Sn cavity in KEK.
Jlab
Rong-Li Geng (JLAB)/ Beam acceleration with a Nb3Sn cryomodule at JLAB in SRF2025
Supercond. Sci. Technol. 38 (2025) 015009 (11pp)
Ziqin Yang (IMP-CAS)/ First beam acceleration using cryo-cooled Nb3Sn coated cavity at IMP in SRF2025

## Slide 37: 3. ILC and the Accelerator Technology
Parameters | Value
Beam Energy | 125 + 125 GeV
Luminosity | 1.35 / 2.7 x 1034 cm2/s
Beam rep. rate | 5 Hz
Pulse duration | 0.73 / 0.961 ms
# bunch / pulse | 1312 / 2625
Beam Current | 5.8 / 8.8 mA
Beam size (y) at FF | 7.7 nm
SRF Field gradient | < 31.5 > MV/m (+/-20%) Q0 = 1x1010
#SRF 9-cell cavities (CM) | ~ 8,000 (~ 900)
AC-plug Power | 111 / 138 MW
SRF Technology
Nano-Beam Technology
e- Source
e+ Main Liinac
e+ Source
e- Main Linac
Detectors
Damping Ring
Interaction point
e-
e+
（ILC key technologies) done under ITN
1. SRF cavities of 9000 numbers
2. Nanobeam production and stability。
3. Huge electron and positrons production
From 2023, key technologies of WPPs are developed under ILC Technology Network(ITN)

## Slide 38: ITN contribution and Japanese contribution under MEXT-ATD program
 | Goals of MEXT-ATD (2023-2027)
SRF | Evaluation of one cryomodule (CM)(including fabrication of CM components such as cavity and couplers）
Positron | Evaluation of target, flux concentrator (FC) and cavity
Nanobeam | Demonstration of long-term stability in ATF
In Japan, Accelerator technologies are conducted by the approved budget from 2023-2027 as “Advanced Accelerator element Technology Development” by Ministry of Education, Culture, Sports, Science and Technology (MEXT)” in Japan (called MEXT-ATD program)
Evaluation of one CM
(At least one in Europe and in the US commercially manufactured cavity should be included.)
WPP-1
WPP-2
WPP-3
・・・
Subsidy (MEXT/ATD) in Japan
ITN：
WPP's overseas share
KEK's involvement will be necessary for any WPP
But some WPPs have a higher overseas share
Development of infrastructure related to SRF, centered on the COI building
MEXT-ATD activities are broadly classified into
(1) Superconducting radio-frequency (SRF)
(2) Positron
(3) nanobeam
ITN is the global collaboration program from 2023
(7 Oku-yen(~5M$)/year)
Shared development under these contries to study critical accelerator technologies called as Work Package Program (WPP) for ITN.

## Slide 39
Design of CM and ancillaries
↓
Production of components
↓
Cavity string assembly
↓
CM assembly
↓
CM test
(a) Latest SRF development under ITN (from 2023)
Cavity fabrication
↓
Surface treatment
↓
Performance test （cavity only）
(called as vertical test)
↓
(WPP-2: to cryomodule)
WPP-1: cavity surface treatment
Freqency Tuner
Supercondcuting magnet
Input coupler
cavity
design ILC-CM under ITN
WPP-2: Cryomodule test
Magnetic shield
Build high performance SRF cryomodule
We perform the cryomodule test by gathering Japan and other countries (EU and so on) (under ITN collaboration)
39
Target values of cavity performance
Vertical test (cavity only):
Eacc = <35.0 MV/m >, Q0 = 1.0 x 1010
Cryomodule test :
Eacc = <31.5 MV/m >, Q0 = 1.0 x 1010
8 cavities will be delivered globally and assembled to one CM, and tested
Under WPP-2, we only need to design the ITN cryomodule. However, the cavity performance test is also important after cryomodule assembly to fulfill our target of ILC.
(WPP-1 ; normal surface treatment of TDR for ILC)
electrochemical polishing (EP), outgassing at 800◦C in a furnace under high vacuum, HPR, and vacuum baking at 120◦C.  change 2-step baking
H.Sakai et al., “ILC Accelerator status”, Proc. of IPAC’25, p24 (2025).
2step-baking will be applied(shown later)
Assembly by Robotics

## Slide 40
(FY2025) (1)WPP1: Results of surface treatment by 2-step baking
Based on the results of past R&D, we chose 2-step baking for this project.
VT for six 1-cell cavities was successfully done, going to 9-cell cavities in KEK.
Cold EP
2 step Baking
Heat treatment
VT
KEK’s recipe
(FY2025) All 6 cavities passed the spec
Kensei Umemori/Ryo Katayama
35 MV/m
Q0 = 1x1010
All 6 cavities reached 35 MV/m and 1x1010 of Q0
75 C, 4h + 120 C, 48h
In a clean room
in next TTC meeting (9-12 June) Eric Viklund (KEK) ”Recent result of 2-step baking at KEK “

## Slide 41
(FY2025) (1)WPP1: Progress of Cavity production at CFF/oversea
Six 1-cell cavities produced
Five 9-cell cavity produced
Takayuki Saeki/Takeshi Dohmae/Kensei Umemori
The world’s first MG cavity!
These cavities are made by RI!
(for the first time at KEK)
Categories related to HPGS
(results of FY2025)
World’s first MG 9cell cavity was fabricated.
2 oversea 9-cell cavities are under fabrication.
Pass HPGS regulation of KEK cavity.
The last few year one-cell MG Nb cavity reached more than 35 MV/m.
Ingot
Slicing image by wire-saw
A New Approach:
Medium Grain (MG) Disc
Grain Size < 1 mm
MG Nb
Fine Grain (FG) Disc
Grain Size: 50 - 100 um
FG Nb
Nb Ingot
Rolling
Forging
MG can reduce the cost
Change FC05

## Slide 42: ITN 5yeas plan (FY2023～2027)(about SRF) under MEXT/ATD program at KEK
In 2027, we plan to complete ITN cryomodule in KEK (COI building)
Clean Assembly
by robot
Cryomodule design for ITN
4 Input couplers done
Tuner test with cavity
4 cavities (2 MG and 2 FG ) are under fabrication at KEK
2 step-baking will be applied.

## Slide 43: Requirement of positron source
Chart: e- beam power (kW)
| 8.9999999999999993E-3 | 1.52E-2 | 4.2999999999999997E-2 | 0.125 | 4 | 0.91200000000000003 | 1 | 3.5 | 4 | 13.32 | 27 | 56.32 | 62.9 | 73.260000000000005
Ne+/Ne-/GeV | 0.073 | 0.063 | 0.05 | 0.014 | 0.0375 | 0.013 | 0.03 | 0.114 | 0.025 | 0.11667 | 0.036 | 0.28 | 0 | 0.43
●past
▲present
◆future
ILC e-driven
High power
High efficiency
SLC
SuperKEKB
FCCee
ILC undulator
CLIC
CEPC
KEKB
BEPC
DAFNE
VEPP-5
Linear collider need many positrons compared with Circular collider due to only one collision
experience from Linear collider of SLC
highest e-beam power for positron source.
Luminosity ~x5000 of SLC
  bunchesｘrepetition ~ x50  source
  Vertical beam size ~ x80  nanobeam
  Need both development
We will develop a positron source that is more efficient than Super KEKB. We will use our experience in particle production with Super KEKB, which is currently the world's largest positron source
Super-KEKB
Fixed target
To reduce heat load of target to stand under high electron beam
Fixed target  rotating target (one of the key development )
Undulator method (baseline) developed in mainly EU. on the other hand, Electron driven method developed in Japan.

## Slide 44
Made test stand to evaluate the following items
  Evaluation of rotating target is in progress
    Thermal test by adding heat load of 20 kW
    Continuous operation of rotating for more than one Start to fabricate accelerator structure
  Test cell and all cells of Acc structure under fabrication and test of brazing.
  Test of power supply of solenoid
  Start to fabrication of power supply of Flux Concentrator .
Tracking simulation is in progress.
Positron source in KEK
Build these parts
& test them
Under fabrication In FY2025-FY2026
Accelerator structure under fabrication of each cell & brazing. continue to FY2026.
Plan view of our test stand
About 200 r p m with water cooling. Vacuum is around 10^-6 Pa level. (FY2024-2025). Now continue long-term operation.
rotating target.
Acc. cell
Stable rotating target was produced under good vacuum condition.  impressive progress for future e+e- colliders

## Slide 45: WPP-15: Final focus at ATF in KEK
Goal 1: Establish the ILC final focus method with same optics and comparable beamline tolerances
ATF2 Goal : 37 nm  ILC 7.7 nm (ILC250); achieved 41 nm (2016)
Goal 2: Develop the position stabilization for the ILC collision
FB latency 133 nsec achieved (target: < 366 nsec)
positon jitter at IP: 106  41 nm (2018) (limited by the BPM resolution)
History of ATF2 small beam
Nano-meter stabilization at IP
FB off
FB on
Long-term (a few days) stabilization is the goal of WPP-15
Damping ring
FFS
1.28 GeV
On November 2025, we held ATF project meeting under our international collaboration to focus nanobeam operation https://agenda.linearcollider.org/event/10859/
(2018)
Including IJClab
(Angelas)

## Slide 46
Large beam
Small beam
By comparing the beam
with the laser interference pattern,
the beam size can be evaluated.
2-8 deg. mode
30 deg. mode
174 deg. mode
The accuracy of the beam size monitor improved after the laser was replaced.
With the hardware upgrade, preparations for beam adjustment starting in fiscal year 2026 are now complete.
Advancing of the IP beam size measurement after the IP-BSM laser renewal
ATF IP beam size monitor
Dynamic range of ATF IP-BSM
The same beam size was measured in different cross angle modes, the modulation in each mode was as expected.
It became possible to generate ideal interference fringes at ATF IP after the laser was replaced, .
66nm beam size measurement stably was done in 2026.Mar.
JFY2026-2027 is very important to fulfill nanobeam generation (<37nm) and stabilization (for a few days)
(important message)

## Slide 47
Shoji Asai “Collaborations for Future” in Joint Workshop of TYL/FJPPN and FKPPN in Hamamatsu Japan (2026.May18-21)
Korea Univ.

## Slide 48
European ITN related studies (dedicated funding from Japan combined with European resources) are distributed over five main activity areas:
ML related tasks
SRF and ML elements: Cavities and Cryo Module,
Crab-cavities, ML quads and cold BPMs
Sources
Pulsed magnet and wheel/target for undulator scheme
Damping Ring including kickers
Low Emittance Rings
ATF activities, final focus and nanobeams
ATS and MDI
Implementation
CE, Cryogenics
Sustainability, Life Cycle Assessments
EAJADE (EU funding) for training of young scientists (linear and circular machines)
Studies in labs distributed across CERN, UK, Germany, France, Italy, Spain
On-going technical studies in Europe – the ILC technology network topics
See more details in the Venice presentation of Peter McIntosh (LINK)
and
Angeles Faus-Golfe on ATF2-3 (LINK)
Steinar Stapnes & Hiroshi Sakai

## Slide 49
(already explain about our collaboration)
Shoji Asai “Collaborations for Future” in Joint Workshop of TYL/FJPPN and FKPPN in Hamamatsu Japan (2026.May18-21)
(explained with high-Q activities)
A. Faus Golfe (IJCLab) / KEK – T. Okugi
A. Martens (IJCLab), D. Charlet(IJCLab) / KEK – A. Aryshev
I. Chaikovska (IJCLab) / KEK - Y. Enomoto
A. Faus Golfe (IJCLab) / KEK – N. Terunuma, A. Aryshev
A. Miyazaki (IJCLab), D. Longuevergne (IJCLab) / KEK - K. Umemori
W. Kaabi (IJCLab), M. Baylac (LPSC) / KEK- M. Yamamoto, K. Umemori

## Slide 50: C)
Contents :
Introduction KEK & iCASA
The latest SRF activities in iCASA at KEK
Summary

## Slide 51: Summary
iCASA was established in 2022 to develop ILC technologies and SRF applications.
ILC accelerator development is on-going under the framework of ITN and mainly supported on MEXT-ATD program, JFY2023-2027 in Japan.
Until JFY2024, we conducted 3 critical accelerator technologies, such as SRF, nanobeam and positron under MEXT-ATD program.
We continuously keep cERL beam operation for more than 10 years since 2013. and cERL now move to use for the various application by using SCRF technology.
We plan to increase cERL beam current from 1 mA to 10 mA for POC of EUV-FEL by using ERL-SASE-FEL scheme.
We also plan to make more compact accelerator based on Nb3Sn for irradiator. Nb3Sn SRF cavity developments are under way.
Thank you.

## Slide 52: Acknowledgements
This work was supported by “MEXT Development of key element technologies to improve the performance of future accelerators Program”, Japan Grant Number JPMXP1423812204
This work was partially supported by U.S.-Japan Science and Technology Cooperation Program in High Energy Physics (2022-19-3) (2025-04-3).
This works was partially supported by JST K-Program Japan Grant Number JPMJKP24M2
We would like to express our gratitude all cERL members and iCASA members for these studies.
KEK iCASA members (+α) contribute to ITN accelerator development and SRF application (picture on 2026.April)
cERL development members In cERL (2023)

## Slide 53: backup

## Slide 54: ILC Technology Network (ITN)
e- Source
e+ Main Liinac
e+ Source
e- Main Linac
Damping Ring
Beam dump
Interaction point
Physics Detectors
WPP | 1 | Cavity production
WPP | 2 | CM design
WPP | 3 | Crab cavity
WPP | 4 | E- source
WPP | 6 | Undulator target
WPP | 7 | Undulator focusing
WPP | 8 | E-driven target
WPP | 9 | E-driven focusing
WPP | 10 | E-driven capture
WPP | 11 | Target replacement
WPP | 12 | DR System design
WPP | 14 | DR Injection/extraction
WPP | 15 | Final focus
WPP | 16 | Final doublet
WPP | 17 | Main dump
SRF
e-, e+
Sources
Nano-
Beam
Creating particles Sources
  polarized elections / positrons
High quality beams Damping ring
  Low emittance beams
    Small beam size (small beam spread)
    Parallel beam (small momentum spread)
Acceleration Main linac
  superconducting radio frequency (SRF)
Getting them collided Final focus
  nano-meter beams
Go to Beam dumps
Not only for the ILC but also
for various application
“Work Package Prime (WPP)” is critical technologies to realize ILC under ITN.
ITN is global program to focus to develop accelerator technology of ILC determined under IDT .

## Slide 55
Worldwide ITN activity
For WPP-1&2 (SRF cavity, CM), single cell cavity production in Korea/Europe started.
U. Hamburg is working for WPP-6/7 (undulator scheme).
JAI (UK) started WPP-14 (DR Injection/extraction, synergy with Diamond Light Source upgrade)
For WPP-15 (Final Focus System), European and Korean researchers have joined to the ATF experiments since 2023.
WPP-1/2 in Asia
WPP-1 in Europe
WPP-2 in Europe
WPP-6 in Europe
WPP-8 in Japan
WPP-14 in Europe
WPP-15 (ATF in KEK)
WPP-9 in Japan
WPP-10 in Japan
WPP-11 in Japan
WPP-17 in Japan
WPP-7 in Europe
The recent status will be reported at the ITN information meeting this week!
Important contribution to ITN from ATF

## Slide 56
(FY2025) (2)WPP2: Ancillaries
First set (two power couplers) assembled for high power test, waiting for preparation of RF system After coupler test, we saw the bad transmission (detailed written in page 8) | Cold test for each component under progress Procurement of real tuners under progress Some simulation works under progress
Prototype magnetic shield was manufactured and delivered. Performance test of the prototype magnetic shield was completed. (After a minor design change) One real magnetic shield is scheduled for delivery in this FY. | Real magnet under production to be completed in this FY Test cryostat produced and under preparation for cold test Simulation for leak field under progress

## Slide 57
(FY2025) (2)WPP2: Progress of Cryomodule design
Specifications
Type | B
Thermal shield | Single
Vacuum vessel length | 12,652 m
Vacuum vessel diameter | OD965mm, ID946mm
Coupler pitch distance | 1326.7 mm
Cavity length | 1247.4 mm
Takeshi Dohmae/Tomohiro Yamada/Takafumi Hara
3D model of CM with waveguide system
Thermal analysis for 40K shield
ILC “Type B” CM chosen (eight cavities + one SC magnet/BPM)
Single thermal shield @40K (5K dropped)
Tuner access available
3D model completed
Heat load simulation done (dynamic under progress)
Waveguide support frame designed
Total cost for contract under estimation
A. Kumar

## Slide 58
Cryogenics TRT under production, to be installed in next FY Design of 2K cold box finished High pressure gas safety act Control system under updating | RF system RF components under production/testing Resonant ring system ready for high power test Design of waveguide system attached to CM Design of long-distance waveguide system from STF to COI | Cryomodule Test Bunker Floor reinforcement work was complete (750t) Design of concrete shielding Consideration on CM transport
(FY2025) (2)WPP2: Progress of infrastructure in COI building
Toshihiro Matsumoto/Kota Nakanishi/Kirk Yamamoto

## Slide 59: (b) Positron source development
Undulator method (baseline): 125 GeV electrons are passed through a helical undulator, and the produced gamma rays hit the target to produce electron-positron pairs. Polarized positrons (30%) are obtained. Need 125 GeV electron beam.
Electron driven method：3GeV electrons hit the target to produce electron-positron pairs. High-energy electrons are not required, and the commissioning of the positron production is independent from electron beam commissioning.
Developed mainly in Japan.
Developed in mainly EU.
Both needs strong target and sophisticated design of Flux concentrator and capture section (cavity and solenoid)  In KEK, prototype of positron source based on e-driven method start to develop.
H.Sakai at al
IPAC25

## Slide 60
Fabrication of Target disk (W-Cu)
Install Flux Concentrator (FC)
Fabrication of collimator with pillow seal
Fabrication of solenoid
The latest development of positron source (in KEK)
The infrastructure for positron test stand was developed until JFY2024, including a cold fit test of the W-Cu target. From 2025, we will conduct the accelerator structure fabrication.
Build these parts
Until FY2024
About 200 r p m
with water cooling.
Vacuum is around 10^-6 Pa level. (last year & this year)
rotating target.
Flux concentrator
Movie
Stable rotating target was produced under good vacuum condition.  impressive progress for future e+e- colliders
H.Sakai at al
IPAC25

## Slide 61
Positron source (rotating target heat load) FY2025
2026.Mar.3-5 Advisory board
Temperature distribution and thermal conductivity of target disk were evaluated.
This test was done two times and finally in Jan. 2026.
Increase input power to the target up to 20 kW and temperature is less than 200 deg. (see the following figure)
No drastic temperature increase was found  W/Cu smoothly contact and can cooled via the shrink fit of W/Cu.
We think that this target will satisfy our requirement of 27 kW beam deposit for positron production.

## Slide 62: (c) Nanobeam development
Goal 1:
Establish the ILC final focus method with same optics and comparable beamline tolerances (design optics for ILC and learn precise tuning of nanobeam operation)
ATF2 Goal : 37 nm @1.28 GeV ILC 7.7 nm @ 125 GeV beam
  Achieved 41 nm (2016)  more smaller
Goal 2:
Develop a few nm position stabilization for the ILC collision by feedback
FB latency 133 nsec achieved (target: < 300 nsec)
positon jitter at IP: 410  67 nm (2015) (limited by the BPM resolution)  to be confirmed and need to be more stabilized
T. Okugi,
ECFA-LCW, June, 2016
K. Kubo
Stability on final focus
FB on
https://agenda.linearcollider.org/event/7371/contributions/38027/attachments/30831/46133/LCWS_FONT_presentation.pdf
From 2017 (intensity dependence) like wake field effect and so on
Damping ring
FFS
presented by Y. Kano and T. Okugi
at ECFA LC workshop 2016.
Learn from SLC experience for feedback system. Stability drastically improved in IP then previous SLC and could collide e+e- beam in IP on ILC.
H.Sakai at al
IPAC25

## Slide 63
The latest activities for Nanobeams (ATF)
FFS
1.28 GeV
We have two doctoral thesis in ATF ( Y. Abe (2024) and K. Popov (2023) at SOKENDAI).
  Beam instrumentation for extremely small vertical emittance beams
  Extremely small vertical beam size realization
we carried out nanobeam generation in ATF at KEK under international collaboration.
ATF2 final focus magnet installed in beam line
Wakefield effect for nanobeam (see next)
Improvement of nano Beam measurement Systems by using laser interference
Beam size measurement by laser interference pattern
Test chamber prepared.
Stabilization beam size by optics tuning and machine learning.
63
ATF collaboration
H.Sakai at al
IPAC25

## Slide 64
Mitigation of wake field effect on final focus points in ATF2
ICT70 flange, bellows, screen monitor and so on are arranged in beamline.
ICF70 flange, bellows are the major wakefield sources in ATF2 beamline.
ATF2
JFY2023 : The effect of wakefield on ICF70 flange and the effect of RF mask to reduce it were tested with test chamber.
JFY2024 : Based on the results, low impedance flanges, bellows were designed and fabricated, and beamline was updated.
JFY2025: The effectiveness of the vacuum components in reducing the wakefield effect on the nano-beam will be tested.
Wake function of each components
Test chamber for evaluation of wake field
Results of test chamber
Replacement of bellows and flange
Test chamber

## Slide 65
Future R&Ds for applications of SRF accelerators
Compact high-power accelerator using
SRF gun
& high-performance cavity
& beam target (very important)
ELBE(Dresden）
4MeV,20uA operation
（goal:1mA）
SRF application study
High efficient RF power source (SSA)
High efficeint cryocooler are important.
Important is not only high power beam
But also target to be stood high power beam
～a few MW、a few 10 MeV
RI production、small acc.
800 MeV 10 mA
EUV-FEL light source(~10kW)
200 W
20 MeV 10uA
Window, target, etc. for high power beam
~10 years
Other material
Like high Tc and
thin film
Nb3Sn/Nb
De-(High Pressure Gas Safety Act & Large-scale cryo-plant)
High performance cav.
~5 years
~10 years
~20 years
Large cryogenic plant
Small cryogenics
Conduction cooling
Past：Nb Q~1x1010 @2K
Now：N dope Q~3x1010 @2K
Future：Nb3Sn Q~3x1010 @~5K
Nb3Sn/Cu
Low-cost cav.