## Slide 1: iSAS WP5.4: iSAS from a beam dynamics perspective
Supervisors: Mike Seidel and Tatiana Pieloni
Acknowledgements: Andrea Latina, Carmelo Barbagallo, Julien Michaud, Alex Fomin, Akira Miyazaki, David Amorim, Elias Métral
Funded by the European Union. Views and opinions expressed are however those of the authors only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the granting authority can be held responsible for them.
April 22th 2026

## Slide 2: Research goals
Beam Dynamics for ERL-based accelerators with energy-efficient cryomodules
Single- and multi-bunch instability studies in the iSAS/PERLE cryomodules
  Development of simulation tools
    Multi-pass recirculation model
    Wake field model
  Single- and multi-bunch beam breakup and beam loading studies
Energy-recovery efficiency studies

## Slide 3: Benchmarking cavity fields
Figure 1: Comparison of the evolution of the transverse beta functions and beam size of a bunch through the PERLE cryomodule between Bmad/Tao, BDSIM, RF-Track, and the PERLE RF field map simulated in RF-Track; the grey rectangles on top indicate the location of the 5-cell standing-wave cavities.
Notes: bmad is used at PERLE

## Slide 4
Model of recirculating linac
Multi-pass recirculation model
  Lattice is split up separate beamlines and connected by spreader and recombiner sections
  Beam is split up separate bunches
    Each bunch is assigned a global time value in the heap queue (0, bunch spacing, 2*bunch spacing, 3*bunch spacing etc.)
    Pop bunch with lowest the global time value out of the heap queue
    Determine the beamline depending on bunch location and bunch parameters
    Track bunch individually in a separate beamline
    Bunch and global time are updated and pushed into the heap queue
    Repeat until all bunches reach the dump
    Stich all simulation together into one simulation
Figure 2: Schematic overview of the PERLE 250 MeV lattice in the BDSIM/Geant4 visualiser.

## Slide 5: Recirculation model of 250 MeV PERLE
Recirculation model implemented Python package (PyERL) interfaced with RF-Track
250 MeV PERLE MAD-X lattice (v2.4.250) [A. Fomin] :
  Split up in different Twiss files  imported into model
  Simulate each individual element in the lattice
  Very good agreement (2% error); Discrepancy in cavities due no proper focussing in Mad-X (approached focussing using thin/thick matrices and cavity elements (Rosenzweig-Serafini [1]))
Figure 3: Comparison of the horizontal beta function through the PERLE 250 MeV lattice.

## Slide 6: Recirculation model of 250 MeV PERLE
Figure 4: Maximum horizontal radius of 10k bunches passing through the PERLE 250 MeV lattice at an operating beam current of 120 mA.

## Slide 7: Research goals
Beam Dynamics for ERL-based accelerators with energy-efficient cryomodules
Single- and multi-bunch instability studies in the iSAS/PERLE cryomodules
  Development of simulation tools
    Multi-pass recirculation model
    Wake field model
  Single- and multi-bunch beam breakup and beam loading studies
Energy-recovery efficiency studies

## Slide 8: Wake field model for recirculating lattices
What do we need to simulate wake fields in the recirculating model to study HOM instabilities?:
  RF-Track’s current wake field model only works for “linear lattices”
  Wake fields need to excite, accumulate and be evaluated for each bunch/slice
  Wake fields need to be “remembered” by the element across simulations
  Wake fields for asymmetric structures
    “Dressed cavity”: HOM couplers, fundamental power coupler etc.
    Asymmetric excitation of HOM’s
Figure 5: 5-half-wave-cell standing wave dressed cavity with 2H2P HOM-damping scheme and fundamental power coupler [P. Duchesne].

## Slide 9: Higher-order mode parameters
HOM parameters from an EM field solver like CST or Wakis
HOM’s (m, n) are defined by:
  Order of the mode m (m=0: monopole, m=1: dipole, m=2: quadrupole etc.)
  Mode number n
  Resonant angular frequency:
  Loaded quality factor: ; with average dissipated power loss and the stored energy
  Shunt impedance:
  Effective voltage: ; with the transit time factor
  Effective shunt impedance:
  over :

## Slide 10: Model of wake fields
Model wake fields impedance (frequency domain) as RLC circuit resonators
Fourier transform to get wake functions (time domain): only structure dependent
Solve EM equations according to wave equation to solve for wake potentials: structure AND source/test particle dependent
Developed both transverse and longitudinal symmetric wakes and asymmetric wakes:
  Symmetric: up to the n-th order
  Asymmetric: up to quadrupolar modes
For derivation see additional slides and consult [2-8]
Implemented as an RF-Track “UserEffect” (see RF-Track manual) into PyERL:
  Create user defined collective effects as Python class that links to RF-Track
  Attached to a beamline element of length
  Set number of kicks  gauge inside element

## Slide 11: Longitudinal wake function benchmark
New wakes vs Xwakes: ; New wakes vs RF-Track beam loading:
Figure 6: Longitudinal wake function comparison with , , and .

## Slide 12: Transverse wake function benchmark
New wakes vs Xwakes: ; New wakes vs RF-Track dipolar wakes:
Figure 7: Transverse wake function comparison with , , and .

## Slide 13: Longitudinal monopole kick benchmark
New wakes vs Xwakes: difference of order
Figure 8: Longitudinal monopole kick comparison with , , and .

## Slide 14: Transverse dipole kick benchmark
New wakes vs Xwakes: difference of order
Figure 9: Horizontal transverse dipole kick comparison with , , and .

## Slide 15: Transverse quadrupole kick benchmark
New wakes vs Xwakes: difference of order
Figure 10: Horizontal transverse quadrupole kick comparison with , , and .

## Slide 16: What has been developed?
Recirculation model that works for arbitrary recirculating lattices
General axisymmetric and two-fold symmetric wake field model that works in RF-Track and in recirculating lattices
Benchmarked wake field model against Xwakes (PyHEADTAIL)
  Xwakes: good agreement
  Small differences are due to different integration methods (thin kick vs integrated kick)
  RF-Track: Not very good agreement
  Intrinsic differences in wake field models
What is next?
Extend model for non-ultra-relativistic regimes
Extend model for travelling wave structures
Implement both recirculation and wake field models in C++ into RF-Track for significant speed increase
General optimisations

## Slide 17: Research goals
Beam Dynamics for ERL-based accelerators with energy-efficient cryomodules
Single- and multi-bunch instability studies in the iSAS/PERLE cryomodules
  Development of simulation tools
    Multi-pass recirculation model
    Wake field model
  Single- and multi-bunch beam breakup and beam loading studies
Energy-recovery efficiency studies

## Slide 18: First study: search for current threshold
Current threshold: maximum current that can circulate before an instability appears due to HOM
(Regenerative) multi-pass beam breakup:
Search for the current threshold
  Updated PERLE lattices ()
  General ERL using iSAS technology
Compare threshold current with analytical regenerative multi-pass MBBU formula [C. Barbagallo]

## Slide 19: Simulation setup
Full recirculation in 250 MeV PERLE lattice (v2.4.250) [A. Fomin]
30 dipole HOM modes in iSAS/PERLE dressed cold cavity [P. Duchesne]
Bunches are injected at normal distributed transverse offsets (sigma is of the beam size ())
Since dipole wake field wavelengths are at least
Bunch length is about of wavelength
Rigid-bunch as first approximation: one macroparticle per bunch (similar to BBU codes such ERLBBU, TDBBU, bi, BBU-R)
Decouple short-range and long-range wake field regimes
Figure 11: Schematic overview of the PERLE 250 MeV lattice in the BDSIM/Geant4 visualiser.

## Slide 20: End-to-end simulation of PERLE at 20 mA
Full recirculation of 25k bunches (25k particles)
Stable at design injection beam current of 20 mA  operating beam current of 120 mA
Figure 12: Horizontal bunch position of 25k bunches passing through the PERLE 250 MeV lattice at 20 mA.

## Slide 21: Dipole HOM voltage in cavities at 20 mA
Figure 13: The average evolution of individual horizontal and vertical dipole HOM voltages experienced by a test particle at a 1 mm offset inside the 4th PERLE dressed 5-cell half-wave cavity excited by 25k bunches passing through the PERLE 250 MeV lattice at 20 mA.
No instability

## Slide 22: Average horizontal position at 20 mA
Figure 14: Average horizontal position of 25k bunches at the exit of the 250 MeV PERLE linac after the last decelerating pass at 20 mA.

## Slide 23: Average vertical position at 20 mA
Figure 15: Average vertical position of 25k bunches at the exit of the 250 MeV PERLE linac after the last decelerating pass at 20 mA.
Horizontal bands? Artifact of rigid-bunch?

## Slide 24: Dipole HOM voltage in cavities at 435 mA
Figure 16: The average evolution of individual horizontal and vertical dipole HOM voltages experienced by a test particle at a 1 mm offset inside the 4th PERLE dressed 5-cell half-wave cavity excited by 25k bunches passing through the PERLE 250 MeV lattice at 435 mA.
No instability
Instability appears

## Slide 25: Average horizontal position at 435 mA
Figure 17: Average horizontal position of 25k bunches at the exit of the 250 MeV PERLE linac after the last decelerating pass at 435 mA.

## Slide 26: Average vertical position at 435 mA
Figure 18: Average vertical position of 25k bunches at the exit of the 250 MeV PERLE linac after the last decelerating pass at 435 mA.

## Slide 27: Dipole HOM voltage in cavities at 430 mA
Figure 19: The average evolution of individual horizontal and vertical dipole HOM voltages experienced by a test particle at a 1 mm offset inside the 4th PERLE dressed 5-cell half-wave cavity excited by 25k bunches passing through the PERLE 250 MeV lattice at 430 mA.
No instability;
“battle” between decay and excitation
No instability

## Slide 28: Average horizontal position at 430 mA
Figure 20: Average horizontal position of 25k bunches at the exit of the 250 MeV PERLE linac after the last decelerating pass at 430 mA.

## Slide 29: Average vertical position at 430 mA
Figure 21: Average vertical position of 25k bunches at the exit of the 250 MeV PERLE linac after the last decelerating pass at 430 mA.

## Slide 30: First results for threshold current
At a first glance threshold current found at injection current of 430 mA
Operating Beam current of 2.50 A in the linac
21.5 times the nominal current of 20 mA / 120 mA
Instability seems to appear first on the vertical axis before appearing on the horizontal axis
Dominant dipole HOM in -plane has a shunt impedance of while the dominant dipole HOM in -plane has a shunt impedance of (same HOM degenerate pair ())
More than larger shunt impedance
Further investigate and search for the dominant modes

## Slide 31: Caveats
Threshold current is dependent on offsets lower or higher threshold current
25k bunches HOM decay time
  However, to ensure stability: at least check for  Lower threshold current
Rigid-bunch approximation does not allow to evaluate statistical bunch parameters such as emittance, beam size, etc.
Threshold current search  rigid-bunch approximation becomes invalid at larger bunch charges
 The approximation does not capture short-range effects which can influence the long-range regime
 Bunch from Twiss parameters at injector:
  Quasi-random distributed particles (error decreases with instead of )
  Less artificial wake field blow-up due to noise
With higher macroparticle count  more slices per bunch  short-range effects  lower threshold current
Threshold will depend on bunch parameters
Testing different setups: balance accuracy vs computational resources
 Memory optimisation of recirculation and wake field model!

## Slide 32: Second study: effect of beam loading
Figure 23: Average vertical position of 25k bunches at the exit of the 250 MeV PERLE linac after the last acceelrating pass at 20 mA.
Beam energy is not nominal  Implement LLRF system to feedback on phase and amplitude
Transient beam loading bunches
Steady-state beam loading

## Slide 33: What next?
For PERLE and general ERL:
  Continue dipole current threshold study
    Continue rigid-bunch + extend to full bunch
    Dependency on beam parameters, filling patterns, misalignments
    Develop BBU instability recognition routine
  Determine HOM thresholds
    Critical impedance, quality factor
  Effect of fundamental/monopole modes on beam loading AND beam breakup
    Introduce LLRF system to mitigate beam loading in transient regime
  Investigate mitigation techniques
    Introduce frequency jitter by machine errors
Energy recovery efficiency in PERLE
Energy recovery efficiency in ERL collider
  General collider study
  Still decide on optimal option for study on specific ERL-based collider project:
    ERLC with assistance of Kaoru Yokoya and Tatsuya Nakada
    erc@CERN with assistance of Andrew Hutton
    LHeC, FCC-ee ERL, and more….

## Slide 34: Bibliography
[1] J. Rosenzweig and L. Serafini, “Transverse particle motion in radio-frequency linear accelerators,” Phys. Rev. E, vol. 49, no. 2, pp. 1599–1602, Feb. 1994, doi: 10.1103/physreve.49.1599.
[2] T. P. Wangler, RF linear accelerators, 2nd completely rev. and enl. Ed. in Physics textbook. Weinheim: Wiley-VCH, 2008.
[3] A. W. Chao, Ed., Handbook of accelerator physics and engineering, Second edition. Hackensack, New Jersey: World Scientific, 2013.
[4] A. W. Chao, Physics of collective beam instabilities in high energy accelerators. in Wiley series in beam physics and accelerator technology. New York: Wiley, 1993.
[5] T. Weiland and R. Wanzenberg, “Wake fields and impedances,” in Lecture Notes in Physics, vol. 400, Berlin, Heidelberg: Springer Berlin Heidelberg, 1992, pp. 39–79. doi: 10.1007/3-540-55250-2_26.
[6] K. L. F. Bane, P. B. Wilson, and T. Weiland, “Wake fields and wake field acceleration,” in AIP Conference Proceedings, AIP, 1985, pp. 875–928. doi: 10.1063/1.35182.
[7] C. Barbagallo, “Design and optimization of higher order mode couplers for the superconducting cavities of the PERLE energy recovery linac”.
[8] S. Heifets, A. Wagner, and B. Zotter, “Generalized impedances and wakes in asymmetric structures,” SLAC/AP--110, 663316, Jan. 1998. doi: 10.2172/663316.

## Slide 35: Additional slides

## Slide 36: HOM’s in a cylindrical symmetric structure
Derivation setup:
  Source bunch/slice: (to axis),
  Test bunch/slice : ,
  Assume ultra-relativistic regime:
    Wakes can only effect trailing particles
  Assume perfect vacuum:
  Cylindrical symmetric standing wave structure of length
    Bare structure, without any mode couplers
Figure 25: Normalised axial electric field amplitude of the TM010-π mode at 801.58 MHz in the 5 half-wave cell bare cavity for PERLE, with an energy gain of 20.5 MeV [7].

## Slide 37: Higher-order mode parameters
HOM parameters from an EM field solver like CST or Wakis
HOM’s (m, n) are defined by:
  Order of the mode m (m=0: monopole, m=1: dipole, m=2: quadrupole etc.)
  Mode number n
  Resonant angular frequency:
  Quality factor: ; with average dissipated power loss and the stored energy
  Shunt impedance:
  Effective voltage: ; with the transit time factor
  Effective shunt impedance:
  over :

## Slide 38: Higher-order mode parameters
There are various conventions and definitions for shunt impedance:
  Linac vs circuit definitions: 
Longitudinal:
  Loss factor:
Transverse:
  Panofsky-Wenzel theorem: , with
  Kick factor:

## Slide 39: Analytic resonator impedance
Higher-order modes can be represented as analytical resonator impedances
  , with the resistance and the reactance of the system
RLC resonator impedance (resistor (R), inductor (L), capacitor (C)):
Total impedance:
Figure 26: LRC circuit [2].

## Slide 40: Analytic resonator impedance
Figure 27: Real and imaginary part of a narrow-band resonator impedance with , , and .

## Slide 41: Single-mode resonator wake function
Impedance (frequency domain)  Fourier transform  Wake function (time domain, we represent )
Wake functions:
  with
Damped oscillator
Property of the structure only!

## Slide 42: Wake function properties
Wake function ():
Properties:
  (Beam loading theorem)
Figure 28: Left: Shape of the longitudinal wake function. Right: Shape of the transverse wake function [4].
Wake function ():
Properties:

## Slide 43: Single-mode axisymmetric wake potential
Wakefields in cylindrically symmetric structures of length :
  Source bunch/slice: (to axis),
  Test bunch/slice : ,
Synchronous EM field must follow wave equation:
 Wake potential [5,8]:
Property of the structure, source bunch/slice, and test bunch/slice!

## Slide 44: Single-mode axisymmetric wake potential
Define a cartesian system:
  Source bunch/slice: , y’
  Test bunch/slice: , y
  Each bunch/slice now has two components of distribution moments:
    Normal:
    Skewed:
Wake potential (decompose in and ):

## Slide 45: Axisymmetric wake potential phasor representation
Euler’s formula:
Longitudinal wake potential:
Transverse wake potential:

## Slide 46: Axisymmetric wake potential phasor representation
Wake potential excited by l number of source bunches/slices with index ( (derivation for but similar for and ):
Split up in “source part“ and “test part”:
    and depends only on the structure and source bunches/slices
Represent excitations as a sum of normal complex phasors and skew complex phasors
Using distribution moments and complex phasors
No need to remember the details about the source bunches/slices!

## Slide 47: Total axisymmetric wake potential
Total wake potential:
Total wake force:
  Divide by the length of the structure
  , ,
  Integrate over length of the structure
  , ,
This model is valid in cylindrically symmetric structures up to the m-th mode
Even longitudinal wake fields  Handels energy loss due to HOM excitation
How do we upgrade to asymmetric structures?

## Slide 48: Single-mode asymmetric wake potential
Asymmetric structure  different transverse shunt impedances for and
Following [8], we can write the general asymmetric wake potential as two power series in and in , with ; is the source particle order and is test particle order:
For axisymmetric:
Asymmetry  Approximate by two-fold rotational symmetry
  Symmetry around -plane and around -plane
    even in and
    odd in and even
    even in and odd
    and have the same parity
    Higher multipole components are much smaller, and can be neglected
    becomes the lowest allowed value

## Slide 49: Single-mode asymmetric wake potential
Loss and kick factor now have units and
Monopole modes (, ):
Dipole modes (, ):
Quadrupole modes (, ):

## Slide 50: Total asymmetric wake potential
Again, wake potentials are excited by l number of source bunches/slices
Total wake potential:
Total wake force:
  Divide by the length of the structure
  , ,
  Integrate over length of the structure
  , ,
This model is valid in asymmetric structures (two-fold rotational symmetry) up to quadrupole modes

## Slide 51: Kick benchmark setup
Bunch properties:
  1000 macro particles
  total particles= 1e14,
  particle type = electrons
  beam energy = 500 MeV
  bunch length = 1 mm
  horizontal and vertical transverse offset = 1 mm
RF-Track/New wakes:
  ; ;
  Drift element:
Xwakes:
  Thin kick
Differences between Xsuite and RF-Track:
  Thin kick vs integrated kick
  Even though  kick is still divided by two: one in the beginning and one in the end
  Even though  There will be a small degree of bunch lengthening happening due to the kick in the beginning  Final kick will be different