## Slide 1: PHENIICS Fest
Supervisors: Esther Ferrer Ribas Thomas Papaevangelou
09/06/2026
Fasoula Elisavet Irfu, Cea, Universite Paris-Saclay
Imaging with Micromegas detector with optical readout

## Slide 2: Contents
Part 1: Introduction
  Optical Micromegas: Concept
  Light detection
  Charge and light gain for different gas mixtures
Part 2: X-ray Imaging
  Test with X-ray generator (resolution)
  Contribution of optics on resolution
  Part 3: Application β-Imaging
  Concept
  samples
  samples
Part 4: Application Neutron Imaging
  Concept
  Degradation of TPB (WLS)
  Resolution
Conclusions/Next steps
Notes: On the first part we will discuss about the light production mechanisms (in other words: how does the Micromegas work) and about the light detection devices (lens and the camera)

## Slide 3: Introduction
  Optical Micromegas: Concept
  Light Detection
  Charge and light gain for different gas mixtures
1

## Slide 4: Optical Micromegas: Concept
Anode
GAS
Optical Micromegas: Standard Micromegas with glass substrate and transparent anode
Amplification region
Mesh|Pillars
Active area:
Electric field lines
Animation: Antoine Cools
Notes: The Micromegas detector consists in three parallel electrodes and two regions separated by a micro-mesh. The conversion gap is defined between the cathode and the mesh while amplification occurs in a gap ranging from 50 µm to 150 µm between the micro-mesh and the anode. 150nm of ITO layer

## Slide 5: Light detection: Camera
Hamamatsu ORCA Quest qCMOS
https://camera.hamamatsu.com/content/dam/hamamatsu-photonics/sites/documents/99_SALES_LIBRARY/sys/SCAS0154E_C15550-20UP_tec.pdf
Readout Noise
Ultra quiet scan: 0.3 electrons rms
Standard scan: 0.44 electrons rms
Minimum exposure time
Ultra quiet scan: 199.9 ms/frame
Standard scan: 7.2 µs/frame
Pixels
Number:
Size:
9.4 Mpixels
Sampling and quantization
Pixels
Dark Noise
Sensor Temperature -: 0.016e/p/s
Notes: one camera pixel corresponds to a 50 µm × 50 µm square on the object.

## Slide 6: Factors which affect our results
Source/Beam
Light Cone
Lens Camera
Chamber
Micromegas Detector
Gas mixture
Stability
Gain
Diffusion
Track length
Electric field
Gain
Lens
Focal length
Focus
Aperture
Camera
Exposure time per frame
Total number of frames
Hamamatsu ORCA Quest qCMOS

## Slide 7: Optimization of gas mixtures for charge and light gain Setup
55Fe source
Central circle: d=5 cm
4 circles: d=0.5 cm

## Slide 8: Light gain Vs charge gain for different gas mixtures

## Slide 9: X-ray Imaging
  Test with X-ray generator (resolution)
  Contribution of optics on resolution
2

## Slide 10: X-ray generator: Setup and Goal
~100cm
Xray generator
Energy: 15 kV-50 kV
Current: 0-40 mA
Operate @ 15 kV, 10 mA
Copper frame & Lead target
Chamber
Lens & Camera
Schneider onyx fast lens
Hamamatsu Orca Quest qCMOS
How??
Relative comparison of different detectors types in terms of the spatial resolution
Different detectors (black mesh, std, WLS)
Different parameters (gain, drift, aperture etc)

## Slide 11: How: Lead target
Target
Pb 0.05 mm
Plexiglass 2 mm
Dimensions:
Lines: 0.6-10 lp/mm
Groups: 26
Object
Image
Black_Tn
Exp: 10 sec
Total acq: 120 sec
Preliminary!
Image Processing
, where N = Total number of frames
x,y = Pixel coordinates
Data Acquisition
Pedestal Images: Dark images, no detector (-> Calculation of the mean intensity per pixel)
Raw Images: Detector & beam/source
Notes: Ed = 750V/cm
Ea = 37 kV/cm

## Slide 12: How: Analysis
Analysis for the resolution
Contrast Transfer Function (CTF)
Edge Spread Function (ESF)
Step function
Edge Spread Function
Two approaches:
  Analytic
    Assume Gaussian blur
    Fit with error function
    FFT-Fourier Transformation
    MTF-Modulation Transfer Function
  Numeric
    LSF (derivative of ESF)
    FFT-Fourier Transformation
    MTF-Modulation Transfer Function
Contrast:
  ROI & projection
  Peaks & minima
  Contrast calculation
Notes: The Modulation Transfer Function (MTF) quantifies the imaging performance of an optical system by analyzing its ability to resolve detail and maintain contrast.
MTF of a System = MTF of Lens × MTF of Camera

## Slide 13: Results: All detectors
All detectors exhibit similar behavior
The black mesh does not provide significant improvement
The WLS performs better than initially expected
Preliminary!

## Slide 14: Factors affecting resolution
Detectors
Optical part: lens, camera
Aperture
Focus
Old lens
Criterion
CTF @ 10%
lp/mm = 1.67
Resolution ~ 600 μm Vs 926 μm
Preliminary!
Lens: Ricoh FL-CC5028
  Focal length: 50 mm
  Aperture: F2.8-F22

## Slide 15: β-Imaging
  Concept
  samples
  samples
3

## Slide 16: Applications: β-Imaging
QuantiCell Project Objective: Characterization of how Antibody-Drug Conjugates (ADCs) distribute and accumulate at the single-cell level inside tumors, using dual radioactive labeling ( and ) and beta detection with Micromegas detectors.
Chemotherapy everywhere in the body Guided drug directly to the cancer cells Targeted therapy
Radio- active
labelling
¹⁴C signal = how much antibody reached the cell.
³H signal = how much drug reached the cell.
=> Detection of the ADC via their β-decay
→ ADC reached the cell as a whole or if the drug separated off.
What is the ADC?
“Smart bomb”:
  Antibody →”GPS tracker”
  Linker → chemical connector
  Drug (payload) →killer of cancer cells
Trace the track of the ADC
What happened with the ADC?
Did it enter the tumor?
Did it go inside the cancer cells?
How much accumulated inside each cell?
Single-cells Samples
Notes:   Antibody →finds and binds to a specific target on cancer cells|| : the “GPS tracker” that binds a specific protein on the surface of the cancer cell (e.g. HER2 receptor).
  Linker → connects antibody and drug- chemical connector.
  Drug (payload) → a highly potent toxin that kills cancer cells once delivered.
  Healthy cells usually don’t express that protein (or do so at low levels), so the ADC does not target them efficiently. That is the principle of targeted therapy.
atoms into the Antibody
atoms into the Drug
-------
Why radioactive isotopes?
³H (tritium) and ¹⁴C (carbon-14) emit beta particles (electrons).
They’re low-energy beta emitters, which:
  Don’t travel far → suitable for cellular-level measurements.
  Don’t significantly damage the ADC structure → maintain normal biological behavior.
  perfect for single-cell measurements without huge radiation hazard.
Radioactive signals are quantitative:
  We can directly count how many decays occur → how much drug or antibody is there.
--------------------------
Ideally, you want:
Both ¹⁴C and ³H in the same cells:
  ¹⁴C → confirms that the antibody arrived.
  ³H → confirms that the drug was retained.
Therefore:
Cells with both ¹⁴C and ³H → likely internalized ADC.
Cells with only ¹⁴C → probably surface-bound ADC. If the antibody stays on the surface, the drug may not be released inside the cell.
Cells with only ³H → free drug uptake.
This is why combining fluorescence imaging (antibody internalization assays) with beta imaging is powerful.
🤔 Visualization inside tumors
Imagine:
A tumor like a big city.
ADCs are delivery trucks carrying toxins.
¹⁴C tells you whether the truck arrived at a house (cell).
³H tells you whether the toxin was dropped off inside the house.
Micromegas is your city surveillance system, watching every block to see which houses received deliveries!
  Antibody →finds and binds to a specific target on cancer cells|| : the “GPS tracker” that binds a specific protein on the surface of the cancer cell (e.g. HER2 receptor).
  Linker → connects antibody and drug- chemical connector.
  Drug (payload) → a highly potent toxin that kills cancer cells once delivered.
  Healthy cells usually don’t express that protein (or do so at low levels), so the ADC does not target them efficiently. That is the principle of targeted therapy.
(_^𝟏𝟒)𝐂 atoms into the Antibody
(_^𝟑)𝚮 atoms into the Drug
-------
Why radioactive isotopes?
³H (tritium) and ¹⁴C (carbon-14) emit beta particles (electrons).
They’re low-energy beta emitters, which:
  Don’t travel far → suitable for cellular-level measurements.
  Don’t significantly damage the ADC structure → maintain normal biological behavior.
  perfect for single-cell measurements without huge radiation hazard.
Radioactive signals are quantitative:
  We can directly count how many decays occur → how much drug or antibody is there.
--------------------------
Ideally, you want:
Both ¹⁴C and ³H in the same cells:
  ¹⁴C → confirms that the antibody arrived.
  ³H → confirms that the drug was retained.
Therefore:
Cells with both ¹⁴C and ³H → likely internalized ADC.
Cells with only ¹⁴C → probably surface-bound ADC. If the antibody stays on the surface, the drug may not be released inside the cell.
Cells with only ³H → free drug uptake.
This is why combining fluorescence imaging (antibody internalization assays) with beta imaging is powerful.
🤔 Visualization inside tumors
Imagine:
A tumor like a big city.
ADCs are delivery trucks carrying toxins.
¹⁴C tells you whether the truck arrived at a house (cell).
³H tells you whether the toxin was dropped off inside the house.
Micromegas is your city surveillance system, watching every block to see which houses received deliveries!

## Slide 17: Applications: β-Imaging
Liquid scintillation measurement
Micromegas autoradiography
Industrial β imager autoradiography
100 µL
1 µL
Reference
Tritiated glucose solutions
Autoradiography
What do we need?
A Micromegas detector which can:
Detect and quantify the activity of sub-Bq activity samples
Separate different radioactive isotopes (like 3H and 14C)
Separate low signal from the background noise
Tritiated samples
    Validation and characterization of our detector using simple, well-characterized drops
chemical incorporation into glucose molecules = > solution of Tritiated glucose with 1μL volume each drop
Notes: AS we do not have single-cells until now, we have to test also the Micromegas sensitivity, that’s why we proceed with tritiated glucose samples

## Slide 18: Setup and Acquisition: samples
Acquisition:
Gas Mixture: : 90/10, 85/15, 80/20 : 2% or 3% Isobutane!
Drift and Amplification Field:
Exposure Time & Number of frames:
  30s, 120 frames -> Total acq. 1hour
7 samples of 10 Bq
12 samples of 1 Bq
12 samples of 0.1 Bq
12 samples of 0.01 Bq
10Bq
1Bq
0.1Bq
0.01Bq
Notes:   Antibody →finds and binds to a specific target on cancer cells|| : the “GPS tracker” that binds a specific protein on the surface of the cancer cell (e.g. HER2 receptor).
  Linker → connects antibody and drug- chemical connector.
  Drug (payload) → a highly potent toxin that kills cancer cells once delivered.
  Healthy cells usually don’t express that protein (or do so at low levels), so the ADC does not target them efficiently. That is the principle of targeted therapy.
(_^𝟏𝟒)𝐂 atoms into the Antibody
(_^𝟑)𝚮 atoms into the Drug
-------
Why radioactive isotopes?
³H (tritium) and ¹⁴C (carbon-14) emit beta particles (electrons).
They’re low-energy beta emitters, which:
  Don’t travel far → suitable for cellular-level measurements.
  Don’t significantly damage the ADC structure → maintain normal biological behavior.
  perfect for single-cell measurements without huge radiation hazard.
Radioactive signals are quantitative:
  We can directly count how many decays occur → how much drug or antibody is there.
--------------------------
Ideally, you want:
Both ¹⁴C and ³H in the same cells:
  ¹⁴C → confirms that the antibody arrived.
  ³H → confirms that the drug was retained.
Therefore:
Cells with both ¹⁴C and ³H → likely internalized ADC.
Cells with only ¹⁴C → probably surface-bound ADC. If the antibody stays on the surface, the drug may not be released inside the cell.
Cells with only ³H → free drug uptake.
This is why combining fluorescence imaging (antibody internalization assays) with beta imaging is powerful.
🤔 Visualization inside tumors
Imagine:
A tumor like a big city.
ADCs are delivery trucks carrying toxins.
¹⁴C tells you whether the truck arrived at a house (cell).
³H tells you whether the toxin was dropped off inside the house.
Micromegas is your city surveillance system, watching every block to see which houses received deliveries!

## Slide 19: Poisson Statistics
, where λ=expected decays per frame
eg 0.01Bq & 30sec per frame:
λ=0.01decays/sec * 30sec = 0.3 decays per frame
=> 1 decay per 3 frames
P(0) = 0.74 => 74% probability to not see signal

## Slide 20: Setup, Acquisition & Results: samples
7 samples of 10 Bq
18 samples of ~9 Bq
18 samples of ~5 Bq
Beta spectrum for the and
14C: 10Bq
3H: ~9Bq
3H: 5Bq
Notes:   Antibody →finds and binds to a specific target on cancer cells|| : the “GPS tracker” that binds a specific protein on the surface of the cancer cell (e.g. HER2 receptor).
  Linker → connects antibody and drug- chemical connector.
  Drug (payload) → a highly potent toxin that kills cancer cells once delivered.
  Healthy cells usually don’t express that protein (or do so at low levels), so the ADC does not target them efficiently. That is the principle of targeted therapy.
(_^𝟏𝟒)𝐂 atoms into the Antibody
(_^𝟑)𝚮 atoms into the Drug
-------
Why radioactive isotopes?
³H (tritium) and ¹⁴C (carbon-14) emit beta particles (electrons).
They’re low-energy beta emitters, which:
  Don’t travel far → suitable for cellular-level measurements.
  Don’t significantly damage the ADC structure → maintain normal biological behavior.
  perfect for single-cell measurements without huge radiation hazard.
Radioactive signals are quantitative:
  We can directly count how many decays occur → how much drug or antibody is there.
--------------------------
Ideally, you want:
Both ¹⁴C and ³H in the same cells:
  ¹⁴C → confirms that the antibody arrived.
  ³H → confirms that the drug was retained.
Therefore:
Cells with both ¹⁴C and ³H → likely internalized ADC.
Cells with only ¹⁴C → probably surface-bound ADC. If the antibody stays on the surface, the drug may not be released inside the cell.
Cells with only ³H → free drug uptake.
This is why combining fluorescence imaging (antibody internalization assays) with beta imaging is powerful.
🤔 Visualization inside tumors
Imagine:
A tumor like a big city.
ADCs are delivery trucks carrying toxins.
¹⁴C tells you whether the truck arrived at a house (cell).
³H tells you whether the toxin was dropped off inside the house.
Micromegas is your city surveillance system, watching every block to see which houses received deliveries!

## Slide 21: Neutron Imaging
  Concept
  Degradation of TPB (WLS)
  Resolution
4

## Slide 22: Applications: neutron-Imaging
From (thermal) neutrons to charge particles:
  layer on the cathode ~2um
  Efficiency ~ 5%
α and Li: Heavy fragments
Dense Ionization
Tracks up to ~10 mm in gas => resolution ↓
Minimization of the drift gap (<1 mm) & use of high electric field (ionization near the converter)
Notes: B₄C (boron carbide)
->Fast neutrons:
  -Test aluminized polypropylene or Mylar (0.1–1 mm) to generate recoil protons.
  -Less efficient, worse resolution, but still feasible.

## Slide 23: Neutron test beam @ ISIS, UK Setup
Detectors:
  W014: 5 mm quartz with WLS
Drift gap ~ 200 um
Amplification gap 150 um
Gas: He/CO2 87/13 (86/14) → W014
Beam: Fast and thermal neutrons
Beam
Micromegas detector

## Slide 24: Targets
Circle
Diameter 2 mm
Slit
Width 2 mm
Homemade Target
Plastic + Aluminium

## Slide 25: Ageing of WLS: W014 1st and 24th (last) acquisition
Beam 3cm X 3cm
1st acquisition
Beam 6cm X 6cm
Last acquisition
Beam 6cmX6cm
Beam 3cmX3cm
Slit 2mm

## Slide 26: Slit: MTF, ROIs selection

## Slide 27: Beam: MTF, ESF

## Slide 28: Beam: MTF, Resolution (mm) | all acquisitions
noCd→Fast+Thermal
Cd → Thermal

## Slide 29: Conclusions/Next steps
Conclusions:
  Optimization of gas mixtures for charge & light gain:
    Best gas mixture for charge and light gain: Ar/CF4/Isob (95/3/2)
  X-ray imaging, spatial resolution:
    Detectors with black mesh present better resolution.
  Beta-Imaging:
    Detection of sub-Bq activities ~0.1Bq of Tritiated glucose samples
    Detection of samples and discrimination of
  Neutron-Imaging:
    Degradation of TPB(WLS) within 5min
Next steps:
  X-ray imaging, spatial resolution:
    Finalizing the analysis of SOLEIL test beam campaing: comparison of spatial resolution for different detectors, lens and gases.
  Beta-Imaging:
    Finalize the discrimination of , and estimation of the activity
    Envisage of new depositions : different activities, different pattern
  Neutron-Imaging:
    Data taking campaign in neutron facility
  Simulations:
    Simulations of transverse diffusion for different gas mixtures and charge gain for different detectors & gas mixtures

## Slide 30
Merci! 
29/07/2025
SPAD Image

## Slide 31: Backup slides
3

## Slide 32: Light detection: Scintillation Spectrum
Layer of Indium Tin Oxide (ITO) on the glass substrate
    Electrically conductive
    Optically transparent
    Simple deposited of thin films by evaporation
Key point: Match the light wavelength and the QE of the imaging sensor
  Use of Quenchers, like CF4 or Ethane with a noble gas i.e. Argon/CF4
  Use of Wavelength Shifter Shifts UV light to visible light i.e. Tetraphenyl Butadience (TPB) +Argon/C4H10
Transparent window
Lens
Notes: The TPB is used to shift scintillation light spectrum to visible range with peak around 425nm, This corresponds to ~85% QE of the ORCA camera

## Slide 33: Readout
Recording induced electronic signals with readout electronics
Electronic Readout
WHY?
Optical readout Vs charge readout
  2D images on real time, without the need of extensive track reconstruction
  High granularity (e.g. 40962306)
  Bigger active area & lower cost per pixel
  Better spatial resolution?
Disadvantages:
Limited frame rate
Sensitive only to a part of the spectrum (Need of CF4- based gas mixtures or Wavelength shifters)
Radiation hardness
Optical Readout
Recording scintillation light with imaging sensors

## Slide 34: Diffusion of the different gases, Magboltz

## Slide 36: Charge and optical gain

## Slide 37: Gases
Gas mixture | Gas Percentage
 | 90/10
 | 85/15
 | 80/20
 | 88/10/2
 | 87/10/3
 | 78/20/2
 | 77/20/3
 | 95/3/2
 | 96/4
 | 95/5
 | 93/5/2
 | 88/10/2
 | 90/10
 | 85/15
 | 80/20
 | 90/10
 | 86/10/4
Gas mixture | Gas Percentage
 | 90/10
 | 85/15
 | 80/20
 | 88/10/2
 | 87/10/3
 | 78/20/2
 | 77/20/3
 | 95/3/2
 | 96/4
 | 95/5
 | 93/5/2
 | 88/10/2
 | 90/10
 | 85/15
 | 80/20
 | 90/10
 | 86/10/4

## Slide 38: Charge Gain: Ar, He and Ne based mixtures

## Slide 39: Light Gain: Ar/CF4 (90/10) ROIs selection

## Slide 40
Ar/CF4/Isob (95/3/2)
Ar/CF4 (90/10)
Ar/CF4 (95/15)
Ar/CF4 (80/20)
Ne/CF4 (90/10)
He/CF4 (80/20)

## Slide 41: Light gain
Calculation of light gain:
, where i=Pixel-i inside the ROI
What about noise that does not exist at all spectrums? (first channels)
Calculation of error:
, where
and (poisson)

## Slide 42
Ar/CF4/Isob (95/3/2)
Ar/CF4 (90/10)
Ar/CF4 (95/15)
Ar/CF4 (80/20)
Ne/CF4 (90/10)
He/CF4 (80/20)
Ar/CF4/Isob (78/20/2)

## Slide 43: beta-Imaging

## Slide 44: How could we detect the lowest activity?
Mask the noisy pixel
  Two different methods for the declaration of noisy pixel
    Two parameters (threshold & occupancy)
Gas Mixture (detector gain)
  90% Ar + 10%
  85% Ar + 15%
  80% Ar + 20%
  Triple gas:
    Ar + 10% + 2% Isob
    Ar + 10% + 3% Isob
    Ar + 15% + 2% Isob
    Ar + 15% + 3% Isob
    Ar + 20% + 2% Isob
    Ar + 20% + 3% Isob
No significant change!
Preliminary!

## Slide 45: Pedestal, Raw and Signal image
Raw Image
Pedestal Image
Signal Image
10Bq
1Bq
0.1Bq
0.01Bq

## Slide 46: Different gas mixtures
1Bq
0.1Bq
Ar + 20% CF4 + 3% Isobutane
Ar + 20% CF4 + 2% Isobutane
Ar + 10% CF4 + 2% Isobutane
Ar + 15% CF4 + 2% Isobutane
Ar + 15% CF4 + 3% Isobutane
10Bq
Preliminary!

## Slide 47: neutron-Imaging

## Slide 48: Slit: Size 2mm

## Slide 49: Slit: Size, All acquisitions
noCd→Fast+Thermal
Cd → Thermal

## Slide 50: 1st Acquisition: Degradation with time (frame by frame) Beam 3cmX3cm
5min
5min
5min