## Slide 1
Advanced concept for a fast breeder reactor based on the phenomenon of nuclear deflagration
French-Ukrainian Workshop 2026
“Instrumentation Developments for High Energy Physics”
dedicated to the blessed memory of Nikolai F. Shul’ga
October 12-14, 2026, IJCLab, University Paris-Saclay, Orsay
Sergii FOMIN
Leading researcher at the Akhiezer Institute for Theoretical Physics
National Science Center "Kharkiv Institute of Physics and Technology"
e-mail: spfomin@gmail.com
15.09.1947 - 23.01.2024

## Slide 2: Outlook:
Introduction
Nuclear deflagration phenomenon
Mathematical approach & results of calculations
Our achievements in the study of the Nuclear Burning Wave
Stability study and intrinsic safety of FR in NBW mode
Transient processes & power control of the NBW reactor
Main features of the NBW reactor & unsolved problems

## Slide 3: Different kinds of “Energy sources”
- Gravitational interaction: hydroelectric power plant
- Electromagnetic interaction: burning of organic fuels (coal, oil, gas)
- Strong interaction: “Nuclear power” is the binding energy
of the nucleons in the nucleus
Fission of 1 atomic nuclear of Uranium releases ~ 200 MeV,
i.e. 108 times more !!! than at oxidation of 1 carbon atom
To boil 1 liter of water ~ 0.1 kWh
~ to drop 40 t٠m of water
~ to burn 10 g of gasoline
~ to split 1016 nuclei of 235U
1 cm3 contains 1022 of 235U atoms that allows to boil 1 million liters of water

## Slide 4
Key parameters of a chain nuclear reaction
1939: Leo Szilárd and Enrico Fermi
Delayed neutrons
< 1%, ∆t ~ 10 s
~ 0.6% (235U)
~ 0.2% (239Pu)
Neutron multiplication factor keff = 1 !!!
Reactivity
Neutron lifetime
~ 10-7s – fast n
~ 10-4 s – thermal n
r << b !!!
Reactivity margin !!!
Neutron mean free pass l ~ 3 cm

## Slide 5
Safety !!! (Chernobyl accident -> Radiophobia)
Limited fuel resources (0.7% of U-235 & 99% of U-238)
Ecological problems (nuclear waste utilization – mainly MA)
Nonproliferation of fissile materials (nuclear terrorism)
Nuclear Power Challenges
Atomic Bomb House, Hiroshima

## Slide 6
232Th
233Th
233Pa
233U
234U
235U
236U
237U
T½ = 22.2 min
T½ = 27 days
237Np
T½ = 6.75 days
238U
239U
239Np
239Pu
240Pu
241Pu
242Pu
243Pu
T½ = 23.5 min
T½ = 2,35 days
243Am
T½ = 4.98 hours
241Am
T½ = 14,3 years
Th-U fuel cycle
U-Pu fuel cycle
Nuclear fuel reproduction
(n, g)
(n, g)
b
b

## Slide 7
Open and closed nuclear fuel cycles

## Slide 8: 1988: Lev Feoktistov (IAE, USSR): Nuclear Burning Wave concept
238U (n,g) ® 239U (b) ® 239Np (b) ® 239Pu (n,fission) ...
T1/2 » 2.35 days
Concept & Analytical approach
Feoktistov
criterion
L.P. Feoktistov. Preprint IAE-4605/4, 1988.
L.P. Feoktistov. Sov. Phys. Doklady, 34 (1989) 1071.
Neutron balance equation
Set of burnup equations
n(z,t) = ? – one-dimensional problem

## Slide 9
L
z
r
R
L ign
j ext
Breeding zone
Ignition zone
238 U 100 %
238 U
90 %
239 Pu
10 %
S. Fomin, et al. - 1st IC “Global 2009”, Paris, paper 9456.
Nuclear Burning Wave
Non-Stationary Nonlinear Multi-Group Diffusion Equation of Neutron Transport
Together with Fuel Burn-up Equations and Equations of Nuclear Kinetics
of Precursor Nuclei of Delayed Neutrons
Metal fuel (44%)
Pb-Bi coolant (36%)
CM - Fe (20%)
jext ~ 1015 cm‑2 s‑1
toff = 400 days
2D Non-Stationary Theory of Nuclear Burning Wave

## Slide 10
FANTENS-2D computing code
(FAst Neutron Transport in Evolving Nuclear Systems)
A two-dimensional pattern of a rectangular grid in a cylindrical coordinate system (z, r) with steps h and t (uniform steps for (z, r) and with variable step for t ) was used. The solutions of the set of the algebraic equations were obtained by finite-difference technique using the implicit difference Crank-Nicolson scheme.
This symmetric-in-time scheme has an unconditional stability at any relation between space and time steps.
It is the unique implicit scheme that has approximation of the second order of accuracy in h and t.
S. Fomin et al., Annals of Nuclear Energy, 148 (2020) 107699.

## Slide 11: S.P. Fomin, M.S. Malovytsia - IAEA Research Agreement No: 22942/R0 (2018-2022)
Neutronics simulations of CEFR Start-up Tests using deterministic code FANTENS-2D
IAEA CRP: Neutronics Benchmark of CEFR Start-Up Tests
The results of keff calculations for fuel loading into the core of the CEFR reactor, performed using
the FANTENS-2D code, showed good agreement with the results obtained by other research groups.
China Experimental Fast Reactor (CEFR) 65MW(th) pool-type sodium cooled fast-spectrum reactor core
Results of keff calculations for the sequential loading of fuel assemblies into the core of a CEFR reactor, performed by representatives of different groups using various deterministic computer codes

## Slide 12
,1017 cм‑2 с‑1
,1021 cм‑3
2D Non-Stationary Theory of Nuclear Burning Wave
NBW Reactor : R=117 cm, L = 500 cm
S. Fomin, et al. - 1st IC “Global 2009”, Paris, paper 9456.

## Slide 13
    Fuel burn-up
238U
239Pu
Fission
products
(Results of calculation in buckling approximation)

## Slide 14: Fuel burn-up for mixed Th-U-Pu cycle
S. Fomin et al., ICAPP 2010 (San Diego, USA) paper 10302.
S. Fomin et al., Progress in Nuclear Energy, 52 (2011) 800-805.

## Slide 15
Perturbation of integral neutron flux Fint (´1022 cm/s) caused by an external neutron source
via time t (days). The source with intensity Qext = 2´1011 (cm-3 s‑1) starts at t0 = 3650 days,
lasts during 1 hour and is situated at 160 < z < 170 cm
Stability study of the NBW mode
R = 230 cm
t ≈ 2.5 days
S. Fomin et al., IC “Fast Reactors 2013“ (Paris, France) paper CN-199-457.

## Slide 16
Evolution of the volume-averaged neutron flux Fav (´1015 cм‑2 с‑1) and concentrations Nav (´1017 cm‑3) of the main fissile and intermediate nuclides in the fuel of mixed Th­-U-­Pu cycle with time t (days) at the initial stage of the neutron flux perturbation t0 = 3650 days. The averaged nuclide concentrations: NNp is for 239Np, NPa = NPa - 53.1·1017 cm‑3, is for 239Pu is for 233U.
Negative Reactivity Feedback inherent to the NBW mode
t ≈ 2.5 days
S. Fomin et al., IC “Fast Reactors 2013“ (Paris, France) paper CN-199-457.

## Slide 17
Variation of the reactivity ρ ($) with time t (days) along the variation of the volume-averaged neutron flux Fav (´1015 cм‑2 с‑1)
Negative Reactivity Feedback
S. Fomin et al., IC “Fast Reactors 2013“ (Paris, France) paper CN-199-457.

## Slide 18
Shutdown and Restart of the NBW Reactor with U-Pu fuel
S. Fomin et al., IC Global 2015 (Paris, France) paper 5254.

## Slide 19
Radial reflector Pb-Bi
Breeding zone 238U
Ignition zone 238U + 239Pu (10%)
2D Non-Stationary Theory of Nuclear Burning Wave
Radial reflector effect study
S. Fomin et al., Annals of Nuclear Energy, 148 (2020) 107699.

## Slide 20
20
Malovytsia M.S., “Power control of an advanced fast reactor operating in a self-sustained Nuclear Burning Wave mode”, PhD thesis, 2021,
V.N. Karazin Kharkiv National University,
Kharkiv, Ukraine.
S.P. Fomin et al., Annals of Nuclear Energy, 148 (2020) 107699.
Reactor Power Control by Reflector Efficiency

## Slide 21
Malovytsia M.S., PhD thesis, 30 June 2021, Kharkiv, Ukraine.
S. Fomin et al., IC “Fast Reactors 2022“, IAEA, Vienna, Austria, paper CN- 291-365.
Reactor Power Control by Reflector Efficiency

## Slide 22
- negative feedback on reactivity - intrinsic safety (!!!) - long-term (decades!!) operation without refuelling and external control
- possibility of 232Th and 238U utilization as a fuel
- fuel burn-up depth for both 238U and 232Th ≈ 50% (one through cycle !) - neutron flux in active zone ≈ 2·1015 n/сm2s
- neutron fluence during the whole reactor campaign ≈ 3·1024 n/сm2
- energy production density in active zone ≈ 200 W/сm3 - total power at the steady-state regime ≈ 1.2 GWt
- wave velocity at the steady-state regime ≈ 2 сm/year
- possibility of nuclear waste burn out (expected)
Main features of NBW reactor with mixed Th-U-Pu fuel cycle
Reactor composition (vol. frac.):
Fuel = 55% (FTh = 62%, p = 0.20), Coolant = 30%, CM = 15%, R = 215 cm

## Slide 24
Neutron flux Ф
238U concentration
239Pu concentration
Fission products concentration
Radial (along r) and axial (along z) distributions of flux and components of the cylindrical NBW reactor core of radius R = 126 cm with the radial reflector of thickness Wref = 71 cm
ALLEGRO type helium-cooled
fast reactor with metal fuel
UZr (10% wt) in the NBW mode
The volume fraction ratio:
- fuel (20% porosity) - 42%
- He coolant (7 MPa) - 38%
- SM (Zircaloy-4) - 20%
Wave velocity –
V ≈ 10 cm/year
Thermal power – PTh ≈ 3.6 GW
Radial reflector SiC :
- 78 % silicon carbide
- 22 % He coolant (1 MPa)
EURATOM program
project # 101164616
(2024-2028) 18 groups
Work Package 1, Task 1.1

## Slide 25
List of our publications on the NBW reactor :
S. Fomin et al., Annals of Nuclear Energy, 32 (2005) 1435-1456.
S. Fomin et al., Problems of Atomic Science & Technology, 6 (2005) 106-113.
S. Fomin et al., ICENES (2005) (Brussels, Belgium) paper IC058.
S. Fomin et al., Nuclear Science & Safety in Europe. Springer (2006) 239-251.
S. Fomin et al., ICAPP’06 (2006) (Reno, USA) paper 6157.
S. Fomin et al., Problems of Atomic Science & Technology, 3 (2007) 156–163.
S. Fomin et al., ICAPP’07 (2007) (Nice, France) paper 7499.
S. Fomin et al., Progress in Nuclear Energy, 50 (2008) 163-169.
Yu.Mel’nik et al., Atomic Energy, 107 (2009) 288-295.
S. Fomin et al., Global 2009 (Paris, France) paper 9456.
S. Fomin et al., ICAPP 2010 (San Diego, USA) paper 10302.
S. Fomin et al., Progress in Nuclear Energy, 52 (2011) 800-805.
O. Fomin et al., Journal of KNU, #104, «Nuclei, Particles, Fields», issue 2 /58/ (2013) 49-56.
S. Fomin et al., IC “Fast Reactors 2013“ (Paris, France) paper CN-199-457.
S. Fomin et al., IC “Global 2015” (Paris, France) paper 5254.
S. Fomin et al., Problems of Atomic Science & Technology, 3 /121/ (2019) 80–85.
S. Fomin et al., Annals of Nuclear Energy, 148 (2020) 107699.
S. Fomin et al., IC “Fast Reactors 2022“ (Vienna, Austria) paper CN- 291-365.

## Slide 26
Conclusion
Advantages of the Burning Wave Reactor
No reactivity margin required during operation
Inherent safety due to negative reactivity feedback
Use of natural/depleted uranium and thorium as fuel
Decades of operation without refuelling
Potential transmutation of long-lived radioactive waste
Main Results
Physical justification of inherent safety
Application of thorium–uranium fuel
Smooth reactor start-up methodology
Safe shutdown and restart capability
Power control via radial reflector efficiency
Remaining Challenge
Neutron fluence remains too high for currently available structural materials

## Slide 27
THANK YOU FOR ATTENTION!

## Slide 30
Institute of Solid-state Physics, Materials Science and Technologies
Various nuclear concepts require low void swelling of structural materials at very high exposures (>200 dpa), high temperatures (7000C) and at super high levels of helium and hydrogen.
Due to high swelling of austenitic steels (life-limited by swelling to 150 dpa) the nuclear materials community has moved toward ferritic and ferritic/martensitic alloys and ODS - Oxide dispersion-strengthened alloys.