## Slide 1: Evolution of Neutron-Capture Cross Sections of Fission Products Under High-Neutron-Fluence Irradiation
Maksym MALOVYTSIA
researcher at NSC Kharkiv Institute of Physics and Technology
mmalovytsia@gmail.com
French-Ukrainian Workshop 2026

## Slide 2: Motivation of study
Strong influence on the neutron absorption by fission products at high burnup levels (= high fluence)
Change of the fission product composition with time and fluence
Challenge of accounting for all of the possible fission products ~1000 nuclides
Developing a fast method for accounting for fission product evolution

## Slide 3: Methods for accounting for fission products
Full vector of fission products. Around 1000 nuclides + the transmutation chains which are influenced by the neutron flux
  - Very time consuming
Accounting only for “important” nuclides, which are considered strong neutron absorbers (e. g. Xe-135, Sm-149, Gd-157 etc.)
  Less time consuming, still requires full transmutation chains that result in production of the “important” nuclides
One-lump lumped fission product model
  - Simplest model, usually independent from time and fluence
  4. Two-lump lumped fission product model
  - Accounting for even- odd- A lumps, with transmutation between them

## Slide 4: Accounting for important fission products
Hiroshi Sekimoto, Kouichi Ryu & Yoshikane Yoshimura (2001) CANDLE: The New Burnup Strategy, Nuclear Science and Engineering, 139:3, 306-317, DOI: 10.13182/NSE01-01

## Slide 5: Calculating nuclide evolution
Mass conservation law for nuclide transmutation chain
– i-th nuclide concentration
– nuclide disappearance ratio
– nuclide production ratio (from decay/neutron capture/fission or other reaction)
For the system of equations can be solved analytically for nuclide n :
If the time interval can be split into a set of smaller intervals, at which the flux can be considered relatively constant

## Slide 6: Methodology of research
Consider an elementary volume initially filled with U-238
The volume is then irradiated by the neutron flux
Three variants of fluxes considered: constant fluxes = 2.5e+16 cm-2s-1 and = 2.5e+14 cm-2s-1 , and the flux that changes similar to the flux in nuclear burning wave.
For the three variants, the final fluence is approximately Ψ = 4 barn-1, which roughly corresponds to a burnup level of 500 GWd/t.
U-238 due to the neutron capture and two beta decays transforms into Pu-239 (and further into other fissile nuclides). Fission of fissile products produces fission products.

## Slide 7: Methodology of research
For all of the possible nuclear transmutation chains that started originally from U-238 we calculate concentrations at different moments of time/burnup/fluence.
For each moment an average neutron capture microscopic cross-section is calculated:
  ,
  where is a sum over all fissile products.

## Slide 8: Results

## Slide 9: Results
a = 0.1290 barn, b = 0.00454 barn2

## Slide 10: Conclusions
Nuclear fission products have a strong influence on neutron absorption ratio at high burnup levels
Taking into account all of the fission products in the neutron absorption calculation can become a time-consuming operation
One lumped fission product model is a fast method to account for the presence of fission products, however, and additional consideration is required to account for evolution of the fission products.
An approximation is proposed to account for fission product evolution in the one-lump fission product model

## Slide 11: Acknowledgements
This work was partially supported by the EURATOM research project "TREASURE," project number 101164616.

## Slide 12: Thank you!
contacts:
Maksym MALOVYTSIA
mmalovytsia@gmail.com

## Slide 13: Change in the group structure of cross-sections

## Slide 14: Fuel transformation cyce