## Slide 1: PALLAS
Jana Serhal. 13/10/2026
A Laser Plasma Accelerator at IJCLab : the beamline and status
FRENCH–UKRAINIAN WORKSHOP ·

## Slide 2
Gradient: ~100 GV/m → 1000× conventional accelerators.
Laser Plasma Acceleration:
Concept and Mechanism
High-intensity laser beam (≅ )
Drives a plasma wakefield in a gas target.
Electrons can be trapped and accelerated in this wake.

## Slide 3
How to Inject Electrons into the Wakefield?
N6+,N7+ trapped electrons
Only electrons moving close to the wake’s phase velocity can be trapped and accelerated.

## Slide 4
How to Inject Electrons into the Wakefield?
Ionization injection: high-Z dopant (N₂) in low-Z gas (He).
Electrons born inside the wake are automatically trapped and accelerated to high energies.

## Slide 5: PALLAS: Laser-Plasma Injector
⚡️ Precision Laser Control
Improve beam stability: pointing, energy, wavefront
Increase system uptime and reduce operator dependence
⚙️ Target Systems
Develop structured gas cells for reliable electron injection
Focus on material robustness and power handling at 10 Hz operation
💥 Electron Beam Studies
Baseline beam characterisation and first control tests
🎯 Core Objectives:
Aiming for “high-quality beam” laser-plasma injector (LPI) facility working in continuous 10 Hz operation

## Slide 6
Focusing
quadrupoles

## Slide 7: PALLAS: Laser-Plasma Injector
Ultimately the goal is to go to 10 Hz within 3 years and have a stability <1 µrad
Current Laser System:
3J, 45 fs
1 Hz rep rate
Stability: 11–13 µrad (PV)
Focusing
quadrupoles

## Slide 8: The Setup
PALLAS: Laser-Plasma Injector
Notes: Generated notes (Beta). Check for accuracy.
Here is a look at the actual physical setup of the PALLAS injector inside the lab
We have a highly integrated layout with the laser focusing, the plasma gas target, and the diagnostics aligned in sequence
Key elements like the beam position monitors and spectrometers are highlighted here to show the compact footprint
This is where the magic happens and where we capture all our diagnostic data shot-to-shot

## Slide 9: Two-Chamber Gas Cell: Injection & Acceleration
• Injection chamber (blue): N₂/He mixture → ionisation injection
• Acceleration chamber (orange): pure He for energy gain
• Gas profiles: validated with computational fluid dynamics simulations
Plasma diagnostics:
• Probe beam for electron density
• Spectral diagnostics for dopant localisation via spectral emission lines
1 cm

## Slide 10: February Campaign
Run overview, Feb 10 - 13 · all shots: charge (ICT), laser energy, N₂ concentration and mean pressure across ~7500 shots, colour-coded by day.

## Slide 11: Electron Beam : Spectra
Spectra averaged over groups of 10 shots, from a ~350-shot long run of the February campaign.

## Slide 12: Glimpse into Some Experimental Results

## Slide 13: Laser and Target Conditions

## Slide 14: Laser and Target Conditions
Stable gas target
Pressure in both chambers held to 0.6 % over 300 shots.
Charge follows the vacuum.
Laser pointing matters:
Horizontal laser pointing correlates with charge.

## Slide 15: Glimpse into Some Experimental Results
29.5 pC
Charge
187 MeV
Peak energy

## Slide 16: Conclusion
            Laser
Further stabilisation; reduce horizontal pointing jitter, which correlates with charge
PALLAS was able to deliver 185 MeV electron beams on a compact <5 m beamline.
Main influences on charge identified. From laser pointing to vacuum stability.
Next Step
1
            New Plasma Cells
Commission and test cells with further dopant localisation.
2
            Beamline Upgrade
Installation of the focusing quadruples
3
Beam time restarts mid-November 2026

## Slide 17: Electron Beam
16 pC
Charge
180 MeV
Peak energy

## Slide 18: Next Step
Further stabilisation of the laser and improvement on the laser side.
Commissioning and testing of new plasma cells that offer further dopant localisation.
Redemarer en mi-November

## Slide 19: The Team
Baynard, Elsa
Beck, Arnaud
Cassou, Kevin
Cayla, Jean Noel
Coacolo, Jean Louis
Douillet, Denis
Gonnin, Alexandre
Huber Arnaud
Iaquaniello, Gregory
Kane, Gueladio
Kazamias, Sophie
Lenivenko, Mykyta
Lucas, Bruno
Malkinski Konrad
Neveu, Olivier
Peinaud, Yann
Pintonato Marceau
Pittman, Moana
Serhal, Jana
Specka, Arnd
Swain, Kalyani
Smartsev, Slava