## Slide 1: Laser source for ThomX Optical R&D for Laser beam - electron beam Compton scattering Technology
Interest for Compton scattering
Laser beam for ThomX
Technical solution
   Fabry-Perot optical resonator
R&D on optical cavities
F. Zomer, 8, juin, 2011

## Slide 2: Some interest in Compton scattering
electron
Laser
wlaser
photon : wf
(scattered electron)
g=Eelectron/mec2
q
We are interested by using the scattered photon
Tolhoek, Rev.Mod.Phys.28(1956)277
Energy distribution ~flat with
wf,max=4g2 wlaser
with g~100 (Eelectron=50MeV)
wf,max=40000ev if wlaser  1eV
Compton scattering is the most powerful mechanism to boost photon energies
2 body process  wf=f(q)
wf (keV)
q (mrad)
Eelectron=50MeV
collimator
 ~monoenergétic beam by selecting Backscattered photons at wf,max
Sprangle et al. JAP72(1992)5032

## Slide 3
Cavité optique
Size ~10mx7m
Optical resonator
X rays
The compact Compton X-ray machine (museum , medical applications)
~50MeV electrons ring
Photo gun
S-band (3GHz) LINAC

## Slide 4: Technical solution to reach high laser average power: Fabry-Perot cavity
One needs 100-500kW laser beam average power
 at present

## Slide 5
Fabry-Perot cavity:
Principle with continous wave
e beam
When nLaser  c/2L  résonance
But: Dn/nLaser = 10-11  STRONG & ROBUST laser/cavity feedback needed…
Gain=F/p=1/(1-R)
isolateur
LASER
~1W
~1W
~10kW
JLAB/Saclay Polarimeter, NIMA459(2001)412 HERA /Orsay Polarimeter, JINST 5(2010)P06005

## Slide 6
1ps
Mode lock
oscillator
Fabry-Perot cavity
with Super mirrors
Electron beam
Fabry-Perot cavity in pulsed regime
Same feedback technics (more complexe) is used in cw & pulsed regime
State of the art (Garching MPI) : ~70kW, 2ps pulses @78MHz, stored in a cavity (O.L.35(2010)2052) ~20kW, 200fs pulses @78MHz

## Slide 7
Issue for the laser cavity feedback
Laser incident average power 50W
Cavity finesse : F=4000xp
To reach ~100kW in cavity
ThomX Optical path length : L~16m
Cavity resonance frequency linewidth Dn=c/(LF)~1.5kHz !
Dn/n=l/(LF)~5x10-12
Same numbers as in metrology !!!
M. Oxborrow

## Slide 8
From a feedback point of view:
Locking a ‘16m’ cavity to finesse~ 4000 (‘gain’~1300) is equivalent to Lock a 0.2m cavity to 300000 finesse ! BUT
The hyper stable small cavity is ‘hyper’ temperature stabilised
Put on an hyper stabilised optical table
Into an hyper isolated room
And an hyper stable cw laser is used, linewidth 1kHz
http://www.innolight.de/index.php?id=mephisto
In the case of ThomX
‘Huge’ laser beam average power
  Larger frequency/amplitude noise
  ‘Bad’ beam profile quality
‘Giant’ cavity geometry
  Uneasy isolation from noisy accelerator environment
R&D required
~100mW power
M. Oxborrow

## Slide 9: Four-mirror Fabry-Perot cavity R&D at ATF (MightyLaser-ANR-08-BLAN-0280-01)
R&D context
Starting point : ILC polarised positron source (2005):
>10MW cavity average power needed for ILC/CLIC
Now : fundings for compact X-ray sources projects
Quantum beam/Japan; ThomX/France
100kW-1MW average power needed

## Slide 10
French Japanese Collaboration
Araki-san
+I. Chaikovska, N. Delerue, R. Marie LAL/France

## Slide 11
Oscillator (customize commercial)
=0.2W, 1030nm
Dt~0.2ps frep=178.5MHz
Amplifier
photonic fiber Yb Doped
4-mirror
Fabry-Perot cavity
Gain~1000
~5W
Numerical feedback
Final goal: to reach the MW average power (~5mJ/pulse but @178.5MHz…)
STEP ONE: commissioning a 4-mirror cavity at ATF, done end 2010
ATF clock
2 steps R&D
STEP ONE (done end 2010)
With cavity laser/coupling ~50% Power_cavity~2.5kW
STEP TWO: upgrade mirrors & laser power
100W
~10000
STEP TWO (with sapphire mirror substrates)
With cavity laser/coupling ~50% Power_cavity~250kW
1 piezo
2 piezos 1 temp. Ctrl.

## Slide 12
Cavity
~30MeV g
BaF2 calo
Cavity installation on the Accelerator Test Facility (ATF) at KEK

## Slide 13
BUT linearly polarised eigen-modes which are instable because of vibrations at very high finesse (KEK geometry)
Stable solution: 4-mirror cavity as in Femto laser technology
Non-planar 4-mirror cavity
Stable & circularly polarised eigenmodes (AO48(2009)6651) as needed for an CLIC/ILC polarised positron source
Small laser beam size +stable resonator  2-mirror cavity
e- beam
Laser input

## Slide 14
ATF e- beam
Injection laser
2 flat mirrors
2 spherical mirrors
laser/beam
Interaction point
Angle laser / e- beam= 8°
Non planar 4-mirror compact cavity design for an accelerator (ATF)
ATF beam pipe: 5mm slit…
~50cm

## Slide 15
2 flat mirrors
2 spherical mirrors
e-
laser
Mirror positioning system
Invar base to ensure length stability
12 encapsulated Motors
Vacuum inside ~3x10-8mbar
without baking
(in situ)

## Slide 16
Gimbal θx θy
Actuator
Piezo Mounting
Z Translation on 3 balls
Details
θx
θy
Ring Piezo
Spring ring
Mirror

## Slide 17
Implementation at ATF
Pulse Motor Port
for
Up-Down Move
Pulse Motor Port
for
Horizontal Move
From Hirotaka-san
Assumed ATF Beam Line
ATF table mount system (~1µm precision) used for spatial laser and e- beam matching
Electron beam pipe
Class 100 air flow
KEK 2-mirror cavity

## Slide 18
Feedback
system
The optical scheme
Signal reflected by the cavity used to build the laser/cavity feedback signal:
  interference between the modulated incident laser beam AND the leackage on the beam circulating inside the cavity

## Slide 19
19
Ø core = 40 µm
Ø cladding = 200 µm
We obtained 60W average power ~stable thanks to connectorisation R&D
800W (11µJ/pulse) demonstrated with the same technique Limpert,OL35(2010)94
The laser amplification R&D
We use Ytterbium doped photonic cristal fiber as amplifier
laser
Fiber amplifier
Toward cavity

## Slide 20
technological R&D to reach long term stability and reliability …
additive phase noise also an issue…
But we broke, burnt many fibres
Using 100W pumping diode (focused on 400µm)…

## Slide 21: Laser/cavity numerical feedback development
Clk = 100 MHz
8x ADC 14 bits
8x DAC 14 bits
FPGA Virtex II
  Filtering => algo. To reach 18 bits / 400 kHz
  Modulation/demodulation made inside the FPGA
  Feedback Identification procedure included ‘in the FPGA’

## Slide 22
With a feedback developped for a Ti:sapph oscillator / 2 mirror cavity (MIRA : 800nm, 2ps@76MHz, pumped with a green laser beam)
It took only ~ an hour to lock an Yb amplified doped oscillator to the KEK 4-mirror cavity (ONEFIVE : 1032nm, 200fs@178.5MHz, diode pumped)
But it takes some time to optimise the feedback…
amplifier

## Slide 23
Results before the earth quake
Power stacked inside the cavity
Before optimising the feedback filters
After an optimisation of the feedback

## Slide 24
Results before the earth quake
One very short run before ATF breakdown (modulator on fire 3 week before the earth quake…)
Laser power ~10W (we had ~60W aside)
Cavity laser/coupling ~30% (best obtained~60%) Power_cavity~3kW
Max : ~25/g/bunch-Xsing (Emax=28MeV)
Average: ~3/g/bunch-Xsing107/s (full spectrum)
PM Waveform

## Slide 26: Summary
We build & installed a tetrahedron cavity at ATF
  Stable circularely polarised eigen modes
  Commisisoning ok in 2010 with at most in 2011
    ~10W laser power, 60% coupling & cavity gain ~1000 (6kW inside the cavity)
Restart in july 2011…
  Goal: to reach 100kW by end 2011
  Cavity mirror change
    Higer finesse
    sapphire substrates to limit thermal load effects