## Slide 1: UA9 instrumentation
G.Cavoto
INFN Roma
Seminar
Jan 24th 2011
LAL - Orsay

## Slide 2: Outline
Description of what we have now in SPS
  Layout
  Detectors
    Beam Loss Monitor, direct beam imaging,…
  Performances
Ideas for a possible layout for LHC
Current layout in SPS:
  W. Scandale et al., JINST 6 T10002 (2011)

## Slide 3: What we measure
Detect inelastic interaction secondary products
  Instrument region close to crystal or to the absorbers/secondary collimator where no other BLM available (or BLM dynamic range is not appropriate)
  External to vacuum chamber
Detect channeled beam
  Measure ch. beam profile
    Check crystal torsional effect, axial channeling…
  Count channeled particles
  Possibly without absorbing the beam or just before beam dump
  Either in vacuum or in secondary vacuum (Roman Pot)
Detect leakage around the ring
  Use accelerator BLM distributed over the whole ring
Measure beam parameters (current, emittance, orbits, …)
  Use accelerator devices
SPS BLM are difficult to use in our experiment (old instrumentation, insensitive to low current)
LHC BLM are modern and reliable

## Slide 4: Collimation region
Protons
hitting
the crystal
✖
Intercepted by LHC collimator
Imaged by Medipix
Absorbed
by secondary collimator (TAL)
BLM Cerenkov
BLM Scint
BLM Scint
65 m
Inelastic interaction of protons
in the crystal
BLM GEM
Deflected beam

## Slide 5: UA9 devices
Tanks with goniometers
2 Triple GEM detector
at large angle
Active area 10x10 cm2
128 pads 6x12 mm2
3 Medipix
in roman pot
Active area 1.4x1.4 cm2
65536 pads 55x55 mm2
scintillators

## Slide 6: Dispersive region
TAL2 Al scatterer
New scatterer + BLM (scint, Cerenkov, ionization ch.) in highly dispersive region to detect
1) off-momentum particles (produced in the crystals) which are displaced lateraly
2) any not absorbed secondary halo
Observe the spray rate as a function of scatterer lateral position

## Slide 7: SPS UA9 devices
Strip crystal in IHEP tank
TAL absorber & Quartz Cerenkov detector
TAL2 Al scatterer
High quality mechanical devices, accurate motion system

## Slide 8: Alignment procedure
Crystal and all UA9 movable devices are aligned during each fill.
Standard and fast procedure to find channeling configuration and collimation!
1) Search of the closed orbit, 2) redefine the beam at how many sigma we want.
Same distance from closed orbit
Alignment position
BLM rate
Collimator jaws positions
1
2

## Slide 9: Roman pots
      Movable device housing detectors in secondary vacuum
        Used to acquire images of channeled beam
          Very important to confirm channeling online
        Relevant to measure channeled beam direction (from centroid) and flux of proton of channeled beam
Online picture
with Medipix
Horizontal displacement
Vertical displacement

## Slide 10: LHC collimator scans
      Measurement of channeled beam position and width
        sbeam ~0.6mm
      Comparison of plateau with core beam
        Deflection efficiency ~80%,
      Close to expectation (92% and 0.33mm)
Protons
Moving jaw!
No particles
Channeled beam
Core
beam
dechanneled

## Slide 11: Rotating crystal in the beam
Appearance of 120 GeV/c proton beam deflected by crystal channeling
Periphery of circulating beam
BLM rate close to crystal
Crystal angle (around a vertical axis)

## Slide 12: GEM on SPS
      Two GEM mounted on Ex-RD22 tank since 2009
      Operate during UA9 MD, data synchronized with other UA9 BLM
GEM2
Downstream CERN tank
Electronics to control thresholds and LV PS
Carioca chip on board DAQ crate remote
HV to power GEM
foils.
128 pads 6x12 mm2
vertical
10x10 cm2 active area

## Slide 13: Gas Electron Multiplier
70 µm
140 µm
A Gas Electron Multiplier (F.Sauli, NIM A386 531 1997) is made by 50 m thick kapton foil, copper clad on each side and perforated by an high surface-density of bi-conical channels;
50 µm
Triple GEM
Gain
~20
~20
~20
~8000

## Slide 14: Monitoring with GEMs
The GEM are acquired every second getting an online image of inelastic scattering at large angle
When an angular scan is performed on crystal, a drop appear on the total rate measured by the downstream GEM
during the channeling time period.
Also the total current drawn by the GEM chamber is a good measurement of the flux of particles from inelastic interactions.
Very large dynamic range
Current vs time.

## Slide 15: Data Synchronization
Use of middleware accelerator infrastructure to save data
Every subsystem provide a “measurement” every second
Data are partially available online
More refined analysis can be made offline

## Slide 16: Basic layout for LHC
  Goniometer
  Special beam line monitor
    Close to goniometer ahd absorber
    Sensitive to secondaries
  Micro-RomanPot
    Intercept channeled particles
Gonio
BLM
Micro RP
BLM
From SPS UA9 layout experience
Absorber
I assume standard LHC BLM are much better than standard SPS

## Slide 17: Goniometer spec for LHC
Total angular range : >10 mrad
“Resolution”: <0.1 µrad
  Minimum step of motor
“Accuracy”: < 1 µrad
  How precisely the motor goes to a given ang. position
  Related to channeling critical angle scale
Maximum tilt inaccuracy: < 1 µrad
  Linear-angular coupling,…
Linear resolution: 5 µm
Total linear range: 40 mm

## Slide 18: Goniometer from CINEL srl (Italy)
To be built in the next weeks and to be tested on SPS at first
This will be the first critical device for the UA9 LHC setup
Mechanical devices (motors, encoder, etc.) are a very delicate element

## Slide 19: BLM close to crystals
LUMI GEM detector Dafne (LNF) luminometer
LHC close-to-crystal can be modeled on this

## Slide 20: Details on LUMI GEM
places for 2 FEE cards
PAD PCB
Back side
Each pad can count number of m.i.p.’s crossing it. [threshold well know ]
20 cm diameter
GEM principle:
Localized electron multiplication
can sustain large rate (MHz/cm2)
Instrinsically radiation hard detector (No flammable gas)

## Slide 21: More on GEM BLM
      Electronics Radiation Hard (Carioca chip, used for LHCb)
  Can be made in several modules (put at different distances in coincidence)
  Can be made movable
    (to scan different angles)
  Addition of degrader can make them sensitive to neutron
  Electronics (hit definition) and slow control (thresholds and FE LV PS) in compact FPGA (to be tested in SPS this year)
x
1
4

## Slide 22: Relavant facts for BLM
  Sensitive to secondaries (inelastic interaction)
    Should be able to detect mips with full efficiency
  On SPS doing test with one bucket filled
    Bunch length few ns
    Revol. Frequency 43 MHz
    Secondary particles arrives “bunched” on the BLM
  Scint BLM are NOT counting secondary
    If one or more mips crossing scint ALWAYS count one
    Fully efficient (it is sensitive at low flux ) but saturates at rev.freq.
    Linearity guaranteed for low flux
  Gate with RF signal
    Very important to reject out of filled bunch particle
    Need < ns time resolution to distinguish among close bunch (5ns)

## Slide 23: Example of different BLMs
Ionization chamber rate
Scints rate

## Slide 24: Detector for RP
    Intercept channeled protons.
      O(100 proton) in few ns [SPS] on a fraction of mm^2 every 43 MHz
    Should give a signal proportional to crossing protons
      Good knowledge of calibration and efficiency
      Not saturate
    Spatial resolution
      “image” of beam (shape). Not critical
      If two RP at different machine azimuth: beam direction
    Trigger from machine timing
Test a scint fiber odoscope in SPS
Positive experience with Medipix
Very good spatial resolution
But calibration is not totally understood
Timing is possible but…
Not clear if it can stand high dose
Other more robust Si
Pixel/strip ?

## Slide 25: Roman pot (sec. vacuum)
Thin window (200 mm Al thick) where the detector
active region should be placed
Add scintillating fibers in front of Medipix device
(calibration, trigger,…)

## Slide 26: Detector concept
One or more layers of fibers:
Plastic (PMMA, polystyrene) fibers:
  scintillation (blue)
  ncore≅1.6, ncladding≅1.4
  Round or square fibers
  Diameter/side from 250 mm to few mm
Quartz (SiO2) fibers: Cerenkov emission
  Different cladding materials (silica, hard plastic, PMMA)
  Core diameter from 100 mm to 2 mm
Directly coupled to multi-channel photodetector (e.g. multi-anode PMT)

## Slide 27: Scintillating fiber detector
Single particle sensitivity, response proportional to number of electrons in beam
≈1 photo-electrons/mm at 50 cm from PMT, 20% quantum efficiency
From LNF BTF test
On similar detectors

## Slide 28: Profilometer
16 mm
Two layers 32X4 0.5mm fibers
Project at INFN RM, in construction
Two layers of 32x4 0.5 mm fibers
Fibers routed to vacuum-air interface
Hamamatsu MA 64 ch H7546 PMT coupled directly on to vacuum-air interface
Four fiber coupled to a signal photocathode pixel
Need advanced electronics to acquire the signals!!!
Measure pulse height and timing

## Slide 29: Some comments
    UA9 devices must reliable
      Position in high rad. environment
      Few and short accesses during the year
    In LHC devices must comply with strict regulation
      Cables, HV PS, gases, etc.
      Accelerator safety
    We never achieved a satisfactory system able to count incoming (to crystal) particles and channeled particles
      Fast electronics to digitize each pulse of a detector would be an important step

## Slide 30: Backup slides

## Slide 31: Possible readout
MAROC2 chip, developed for scintillating fiber detector for ATLAS luminosity measurement (ALFA)

## Slide 32: Another possibility…
Particle
v>c/ncore
ncore
ncladding
cosq=(ncore(v/c))-1
Quartz fibers:
Cerenkov emission in place of scintillation
lower light yield
Better radiation resistance

## Slide 33: Angular scans
    Reduction factor of the inelastic losses due to inelastic interactions in channeling versus amorphous orientations.
      Measured with LHC-BLM and GEM detectors
      Very reproducible in several scans and fills
Losses in amorphous regime
channeling
channeling
Volume
reflection
Volume reflection
Depending on crystals 5 – 9 reduction factor (protons)
NEW: measurement also with Pb ions: 2-4 factor
Still off with respect to simulation

## Slide 34: Tools to make progress
Simulation.
  Proton Tracking
  Aperture model
    Inelastic interaction
  Crystal simulation
  Detector simulation (GEANT4,FLUKA,…)
Use of mixed tool
  ICOSIM
Obviously we need this to make a conceptual design (next months?)
A detailed simulation can come later

## Slide 35: Scintillating fiber detector
Fiber detectors (x and y views, 4 layers, 1 mm diameter fibers)
Working since 2003 at Frascati BTF

## Slide 36: BLM based on GEM
    Sustain high rate (100 KHz/cm2)
      Limit given by spacing of GEM foil holes
    Linear (sensitive to mip)
    Measure rate on small element (0.5x1cm2 pads)
    Already used in LHCb
New compact DAQ board (see F.Murtas) can avoid
problem with long cable
SPS 2010 shows they reproduce standard SPS BLMs.

## Slide 37: Road-map for a test in LHC
Parameters | Obtained in 2009 | Obtained in 2010 | Required for LHC | 
Channeling efficiency | 75 | 80 | 90÷95 | ★★
Nuclear loss reduction | 5 | 5-10 | 20÷30 | ★★
Goniometer: angular accuracy [µrad] | 30÷40 | 10 | 1÷2 | ★
Crystal bend [µrad] | 140÷150 | 150÷170 | 50÷100 | ★★★
Crystal torsion [µrad] | 20÷30 | 0.1÷1 (*) | 0.1÷1 | ★★★
Amorphous layer on crystal | About zero | About zero | About zero | ★★
Collimation leakage reduction | - | 5 | Should be analyzed | ★★
(*) On external beam test