        Pattern recognition in new generation
        highly granular calorimeters
LHC
       Roman Pöschl
Siminole Meeting 26/1/2010

---
Where do we stand today?
Standard Model of Particle Physics
  All matter is composed of 12 Fermions
        'Lepton and Quarks'
  Interactions are mediated by Vector Bosons
        'Force Carriers'
- All matter which surrounds us is composed
  by the particles of the Generation I
  The other generations contain particles
  observed in the accelerators
  of the 20th century
e+e- → γ/Z → hadrons
e quark scattering at HERA

---
Beyond (?) the Standard Model of particle physics
        SM explains elements of ordinary matter as
        quarks and leptons – fermions with spin 1/2
        interacting via force carriers – bosons with spin 1
Simulation of Higgs signal at
International Linear Collider
Higgs Boson is missing piece of Standard Model
Chase for Higgs Boson is at full swing at the LHC
Elementary spin 0 particle – Portal to New Physics?
LC would allow complete tomography of Higgs

---
The International Linear Collider ILC
Linear Electron-Positron Collider
Main parameters
√s adjustable from 200 – 500 GeV
Luminosity  ∫Ldt = 500 fb-1 in 4 years
Ability to scan between 200 and 500 GeV
Energy stability and precision below 0.1%
Electron polarisation of at least 80% Option: Polarised Positrons
The machine must be upgradeable to 1 TeV
Total Footprint 31 km
Technology for Main Linac
Superconductive RF cavity
ITRP Recommendation 2004
Technical design report 2012
 R&D Project for higher Energies CLIC
Present outlook

---
Why Electron Positron Machine?
Note: ILC will probably be put into operation after major
LHC discoveries. Why is the ILC still needed?
p = composite particle:
unknown √s of IS partons,
parasitic collisions
p = strongly interacting:
huge SM backgrounds,
highly selective trigger needed,
radiation hard detectors needed
e = pointlike particle:
known and tunable √s of IS particles,
polarisation of IS particles possible,
kinematic contraints can be used
e = electroweakly interacting
low SM backgrounds,
no trigger needed,
Electron Positron Collider – Best premises for precision measurements
p
p
e+
e-

---
Detector Requirements
Track Momentum:	σ1/p < 5 x 10-5/GeV	(1/10 x LEP)
        ( e.g. Z-Mass Measurement with charged Leptons)
Impactparameter: σd0 < 5 ⊕ 10/(p[GeV]sin3/2) m (1/3 x SLD)
        (c/b-tagging)
Jetenergy :	dE/E = 3-4%
        (Measurement of W/Z Mass with Jets)
Hermeticity :	θmin = 5 mrad
      (to detect of events with missing energy e.g. SUSY)
Events with large track multiplicity and a large number of Jets (6+) are expected.
Therefore:
high Granularity
good track Measurement
good Track Separation

---
The ILD Detector
Return Yoke
ETD
Coil
VTX
SIT
FTD
Forward components
(QD0 magnet – FCals)
SET
TPC
HCal
ECal
Letter of Intent in 2009 – Based on full detector simulation
Beam line

---
Hadronic final states at the ILC
e.g. Boson Boson Scattering
W, Z separation in the ILD detector
Jet
Jet
Jet
Jet
Remember: MZ-mW ≈ 10 GeV
- Need excellent jet energy resolution to separate W and Z bosons
  in their hadronic decays

---
Jet Energy Resolution
Final state contains high energetic jets from e.g. Z,W decays
Need to reconstruct the jet energy to the utmost precision !
Jet energy carried by …
- Charged particles (e±, h±,μ±)): ‏65%
   Most precise measurement by Tracker
   Up to 100 GeV
- Photons: 25%
  Measurement by Electromagnetic
   Calorimeter (ECAL)
- Neutral Hadrons: 10%
  Measurement by Hadronic
  Calorimeter (HCAL) and ECAL
%sigma_{Jet}=sqrt{%sigma^2_{Track}+%sigma^2_{Had.}+%sigma^2_{elm.}+%sigma^2_{Confusion}}
Tracker Momentum Resolution GeV/c

---
Confusion Term
- Base measurement as much as possible on measurement of charged particles
   in tracking devices
 - Separate of signals by charged and neutral particles in calorimeter
- Complicated topology
  by (hadronic) showers
- Correct assignment
  of energy nearly impossible
⇒ Confusion Term
Need to minimize the confusion
term as much as possible !!!

---
Detector and Calorimeter Concept – Particle Flow
Jet energy measurement by measurement of individual particles
    Maximal exploitation of precise tracking measurement
large radius and length
  - to separate the particles
large magnetic field
  - to sweep out charged tracks
“no” material in front of calorimeters
  - stay inside coil
small Molière radius of calorimeters
  - to minimize shower overlap
high granularity of calorimeters
  - to separate overlapping showers
Physics Goals at the ILC demand the
Construction of Highly Granular Calorimeters!!!
Emphasis on tracking capabilities of calorimeters

---
R&D for an Electromagnetic Silicon Tungsten Calorimeter – SiW Ecal
Basic Requirements
The SiW Ecal in the ILD Detector
- Extreme high granularity
- Compact and hermetic
Basic Choices
- Tungsten as absorber material
   - X0=3.5mm, RM=9mm, I=96mm
   - Narrow showers
   - Assures compact design
- Silicon as active material
  - Support compact design
  - Allows for pixelisation
  - Large signal/noise ratio
SiW Ecal designed as Particle Flow Calorimeter

---
The Collaboration
Calorimeter R&D for the
~300 physicists/engineers from >50 institutes
   and 16 countries from 4 continents
- Integrated R&D effort
- Benefit/Accelerate detector development due
  to common approach

---
The Calice Mission
Final goal:
A highly granular calorimeter optimised for the Particle Flow measurement of multi-jets final state at the International Linear Collider
Intermediate task:
Build prototype calorimeters to
Establish the technology
Collect hadronic showers data with unprecedented granularity to
- tune clustering algorithms
- validate existing MC models
E. Garutti
Si-W ECAL
Scint. Tiles-Fe AHCAL
Scint. Strips-Fe TCMT
Imaging
calorimeter

---
SiW Ecal Physics Prototype
30 layers of Tungsten:
• 10 x 1.4 mm (0.4 X0)‏
• 10 x 2.8 mm (0.8 X0)‏
• 10 x 4.2 mm (1.2 X0)‏
‣ 24 X0 total
½ integrated in detector housing
⇒ Compact and self-supporting detector design
        6x6 PIN Diode Matrix
   Resistivity: 5kcm - 80 (e/hole pairs)/µm
Shielding
PCB
Tungsten: H structure
Thickness:
 525µm
Front End
electronics zone
62 mm
Total: 9720 Pixels/Channels
Silicon wafer
62 mm

---
Large Scale Beam Tests
     Experimental Setup
Particle Distance~ 5 cm
 No Confusion !!!
Zoom into Ecal
Two electrons
- Beam tests at DESY, CERN and FNAL
- Beam tests provide well defined initial conditions
  i.e. energy and type of particle is well known as well as impact point and
  impact angle
- Large statistics accumulated in past years by (to e.g. train algorithms)
- Large statistics to come in coming years

---
Exploiting the high granularity – Particle separation
High granularity allows for application of advanced imaging processing techniques
E.g. Hough transformation
Events recorded in test beam
Two pions entering
the SiW Ecal
Secondary muon within
electron shower

---
Particle separation – cont'd
Efficiency of particle separation
Separation MIP <-> Electron
1
1
10 MIP Hits
20 MIP Hits
30 MIP Hits
Fraction of common cells
Distance MIP shower axis [mm]
E -> 100% for up to 50% shared hits
Independent of hits generated
by MIP
Full separation for
distances > 2.5 cm
Detection efficiency
Detection efficiency

---
Granularity and hadronic cascades
(Start of) Hadronic showers in the SiW Ecal
Simple but nice
Complex and impressive
Scattered Pion
Initial Pion
Interaction
Ejected Nucleon
Outgoing
Fragments
Short truncated showers
Inelastic reaction in SiW Ecal
High granularity permits detailed view into hadronic shower

---
Hadronic showers extend well beyond the Ecal
Primary particle
Secondaries
First interaction
Second interaction
The goal must be to identify the interaction points and to associate the
secondaries correctly to the promary particle

---
Hadronic showers come in various forms

---
Event reconstruction with particle flow algorithm
Reconstruction of a Particle Flow Calorimeter:
Avoid double counting of energy from same particle
Separate energy deposits from different particles
e.g.
If these hits are clustered together with
these, lose energy deposit from this neutral
hadron (now part of track particle) and ruin
energy measurement for this jet.
Level of mistakes, “confusion”, determines jet energy resolution
not the intrinsic calorimetric performance of ECAL/HCAL
Three types of confusion:
i) Photons
ii) Neutral Hadrons
iii) Fragments
Failure to resolve
neutral hadron
Reconstruct fragment as
separate neutral hadron
Failure to resolve photon
M. Thomson Cambridge

---
Particle Flow Algorithms in practice
Highly non-trivial !
e.g. PandoraPFA consists of a number complex steps (not all shown)
Iterative Reclustering
Fragment ID
Photon ID
More on Pandora PFA see: M. Thomson, NIM A 611 (2009) 25
Clustering
Topological Association
30 GeV
12 GeV
18 GeV
9 GeV
9 GeV
6 GeV

---
Application of Pandora to real (beam test) data
Advantage: Hadron showers not well modelled by simulation
Simple configuration: Two particles in detector
10 GeV 'charged particle'
10 (30) GeV 'neutral' particle in neighbourhood
CALICE Collaboration, JINST 3 (2008) P08001
Already remarkable performance
        but
still room for improvement!!!!

---
Summary
- ILC is essential to understand the physics at the TeV scale
  Decision on realisation depends crucially on first LHC results
- Detector concept is built on Particle Flow
  Successful particle Particle flow requires highly granular
  calorimeters
- Already considerable results with existing algorithms
  However clear room for improvement
- High granularity provides new quality for particle reconstruction
  Search for fresh ideas to fully exploit the potential of the
  Calorimeters
  Which algorithms could be adequate?
  Where are limits?
  Synergies with other fields of science in which pattern recognition
  And (non trivial) separation of objects is of interest.
  See also at seminar of Manqi Ruan (LLR) on 14/2/12, approach
  with fractal dimensions
- Existing data sets and competences in detector simulation

---
Backup Slides

---
SiW Ecal Optimisation
Optimisation using Jet Events and Pandora Particle Flow Algorithm
Interplay B-Field and inner radius of Ecal
Radius more
important
than B-Field
Lateral granularity of Ecal
Jet Energy resolution strongly
sensitive on cell dimensions
- Better separation power
- Importance grows towards higher
  energies
High granularity of Ecal is crucial for
precision measurements