Test beam (DESY – July 2012)
DQ checks
Analysis status

---
Setup
- wafer 9x9 cm2, 324 pixels 5x5 mm2
- 6 FEV8 (4 SKIROCs per FEV)
  - 4 SKIROCs x 64 channels = 256 channels
    (2 channels with 2 pixels and 22 channels with 4 pixels)
    Total = 1536 channels
    PreAmplifiers of noisy channels are switched off
    total active channels = 1278
- PVC structure with position for tungsten plates (2.1 mm)

---
Beam spot
    Layer 1 Layer 2 Layer 3
    Layer 4 Layer 5 Layer 6

---
Goals of the test beam(from Roman's talk)
- Main goal: Determine signal over noise ratio of the detector
  Remember: R&D target is 10:1
- Establishment of calibration procedure for a larger number of cells
- Homogeneity of response (x,y scan of detector)
- Small physics program
  Electrons between 1-6 GeV

---
Data taking
- Trigger threshold calibration (no beam)
  gain, comp. Capa.
- Hold scan (beam)
  trigger threshold calibration
- Data taking (beam or cosmic)

---
Data (July 2012)
- Trigger threshold calibration
  - 1 gain, all channels = ~1-5 Go, ~30 min
  - Jérémy: DONE
- Hold scan
  - Need stat: 30-60 min/delay
  - Elmaddin: DONE (low stat)
- XY scan
  - Energy calibration: DONE (Jérémy)
  - Detection efficiency
  - Beam studies
  - Correlations...
- Showers
  - 4 energies
  - 3 config
- Others (3 gains, some chips/channels OFF)

---
Some events
Event with a lot of hits in 1 layer
e- 3 GeV, no tungsten
e- 3 GeV
3X0 in front of the detector + 5 W plates between layers
e- 1 GeV
5 W plates between layers

---
Memory occupancy (1)
Data: 3GeV – No W – beam centered

---
Memory occupancy – BCID +1
Data: 3GeV – No W – beam centered
~50%
~30%
Seen on test bench, cut on BCID + 1

---
Memory occupancy (3)
Data: 3GeV – No W – beam centered
Not seen on test bench

---
Events with a lot of hits
Data: 3GeV – No W – XY scan
All layers
Total number of events: 2,3.106

---
Events with a lot of hits (2)
Data: 3GeV – No W – XY scan
All layers
Total number of events: 2,3.106
After single hits
After single hits
After single hits
Is it just a map of noisy channels?
Is some channels induced events with a lot of hits?

---
MIP studies (1)
Data: 3GeV – No W – XY scan
All layers
Total number of events: 2,3.106
MIP selection:
At least 3 layers with hits
5 hits in the same XY region (+- 1 pad)
Nhits<10

---
MIP studies (2)
Data: 3GeV – No W – XY scan
All layers
Total number of events: 2,3.106
MIP selection:
At least 3 layers with hits
5 hits in the same XY region (+- 1 pad)
Nhits<10

---
MIP studies (3)
Data: 3GeV – No W – beam centered
All layers
pre-selection:
3<Nhits<10
Fit function:
x = x0 + k.ux
y = y0 + k.uy
z = k.uz
Other method: Hough transform (CPU time) → check results
Use the result to improve simulations

---
Efficiencies
Data: 3GeV – No W – XY scan
All layers
Total number of events: 2,3.106
MIP selection:
At least 3 layers with hits
5 hits in the same XY region (+- 1 pad)
Nhits<10
Efficiency of 1 layer:
1 MIP using the 5 others layers
Simulation: 99.999%
Better MIP selection (previous slide)?

---
Summary
Analysis in progress:
Determine signal over noise ratio of the detector (in progress: 3 gains)
S/N = ~10-20 in function of the gain (min to max)
Energy calibration + Homogeneity of response (DONE)
Trigger threshold calibration (DONE)
Hold scan (DONE)
Efficiency (in progress)
Study of showers (in progress ??)
Crosstalk (in progress)
events with a lot of hits (DONE)
Pedestals (in progress)
Noise (in progress)
Beam study (in progress)