Analysis Meeting – 08/10/2012
T. Frisson (LAL)

---
Software status
https://forge.in2p3.fr/projects/calice/wiki/DESY_2012-07_Analysis
(installed on LLR DAQ PC since June, on forge since August !!)
- Raw files conversion: Raw2Root.C
  - 1 ROOT file per layer
  - No cut (Keep all informations)
  - Flag BCID+1 events
- ROOT files Merging: mergeRootFiles.C
  - Keep all informations
- Reconstruction: ObjectBuilder.C
  - Group hits with the same BCID (tolerance +1 in others chips)
  - Cut BCID+1 events
  - Flag plane events (Nhits in 1 chip > 20)
  - File content:
    - Hit: energy, position (pad position, channel number, chip number)
    - Time (spill number + BCID)
    - Nhits
    - EventType
- Event Display: Plot3D_Obj.C
To do: pedestal substraction

---
Simulation Status
- Geometry:
  - Detailed description of the detector geometry
  - Simple script to modify configuration
- Beam:
  - Direction: almost OK
  - To do : check position
  - Correlation between particle position and beam direction?
- Output: same root file structure (1 chip, 1 column, 324 channels)
    ==> same analysis tools
- Simple digitization
  ==> waiting for feedback

---
Energy measurement in simulation - Digitization
Keep all informations in the ROOT file!!
- Total energy deposited in one pixel (in keV)
- Gemetrical cuts (inter-pixel gap) (in keV)
- Electron-hole prair production fluctuation (in keV)
- Electron-hole transport diffusion (in keV)
- Scaling using the landau MPV (1/1.27 -> in ADC)
  + Add PA noise (sigma from 2 to 4 ADC)
  - Apply trigger threshold (scan trigger threshold -> detection efficiency...)
- Add SS noise (sigma = 1.4 ADC)
- Add pedestal (+300 ADC)
Total energy (scaled)
Energy with PA noise

---
Data quality

---
Plane events
Is it just a map of noisy channels?
Is some channels induced plane events?
Need further investigations!
# plane event
RMS

---
BCID+1 and Plane events
BCID+1
Plane Evts
- 2 acquisitions, centered, no W
  0: chip M1: 30% – 20-25% , others chips 10-15% – 6-9%
  1: chip M1: 40% – 25-30% , others chips 10-15% – 6-9%
  2: chip M1: 43% – 30% , others chips 12-20% – 10-15%
  3: chip M1: 45% – 40% , others chips 30-40% – 20-30%
  4: chip M1: 53% – 20-25% , others chips 20-30% – 15-18%
  5: chip M1: 52% – 20-25% , others chips 20-30% – 15-18%
  ==> increase from 0 to 4, 1 ~ 2, 5 ~ 3 or 4
- % of bad events compared with Nevt in the chip
    --> not appropriated (plane events does not occur in the same chip than previous hits)
  - chip= 1 Evt= 17475 - 39.6% - 26.9%
  - chip= 2 Evt= 125130 - 9.6% - 3.1%
  - chip=3 Evt= 17325 - 40.7% - 26.6%
  - chip= 4 Evt= 121305 - 8.9% - 4.0%
More bad events
Some events are plane and BCID+1

---
BCID+1 and Plane events
BCID+1
Plane Evts
- Increase with shower developpement
  - Ex: 5 GeV – 6X0 in front of the detector + W plates - layer 4
    - chip= 1 Evt= 240300 - 71.7% - 43.2%
    - chip= 2 Evt= 244185 - 57.7% - 64.7%
    - chip= 3 Evt= 246015 - 72.8% - 53.8%
    - chip= 4 Evt= 231495 - 66.0% - 64.8%
Some events are plane and BCID+1

---
Isolated hits
Signal?
Cosmic?
- Reconstructed events with only 1 layer with hits:
  - No W: ~30%
  - Shower: ~10%
Pedestal?
Huge tails

---
Pedestal filtering
Same channel
Red: all events
Blue: remove all events of the spill if 1 plane event in the spill
==> Plane event at BCID=1000 correlated with bad pedestal at BCID 500 ???

---
MIP Reconstruction – Beam studies

---
MIP reconstruction - Beam studies
Fit function:
x = x0 + k.ux
y = y0 + k.uy
z = k.uz
==> spherical coordinates
D = distance (Track – hit) ==> minimize: Sum(D x Exp(D-pixelEdge)

---
MIP reconstruction - Beam studies
Beam reconstruction
Theta:
beam slightly deflected in X direction
=> detector alignment?, fake effect due to layer alignment?
4 part ellipse:
Construct using main axis
Randomly choosen using area
Data
Simulation
Typo in code
Log scales !!
To do trigger scan!

---
MIP reconstruction - Beam studies
Beam reconstruction
Phi: gaussian distribution, sigma = 1°
To do trigger scan!

---
Detection efficiency
Data
Simulation
Low efficiency close to switched off channels
But some isolated low efficiency channels (to be investigated)
Efficiency depends on the beam parameters (angle)
Need real beam parameters in simulation --> DONE
Some effects not yet in the simulation (noise, trigger...)
To do trigger scan!
On going analysis!

---
Number of hits around MIP
Data
Simulation
Some effects not yet in the simulation (noise, trigger...)
Check correlation between the number of hits around MIP and the trigger threshold
To do trigger scan!
On going analysis!
Number of hits at distance < 1.5 cm

---
Correlation studies

---
Correlation studies
- Extract coherent noise source + intensity
  Chip M1: Sigma total ~ 3.5 ADC
    ==> 1 source for all layers (<sigma> ~ 2.3 – 2.5)
To do: check fluctuations with XY channel position

---
Correlation studies
- Chip M1: Sigma total ~ 3.5 ADC
    ==> Layer 2
Channel 32
Channel 33

---
Correlation studies
Chip M2: Sigma total ~ 4-5 ADC
    ==> 3 sources for all layers
Channel 59
Channel 54
To do:	check intensity varaitions with XY channel position
Is higher sigma total only due to higher coherent noise?

---
Event display

---
Event display

---
Event display
g
e+
e-
g

---
Summary
Analysis in progress:
Beam reconstruction
MIP studies --> Trigger threshold scan: efficiency
Crosstalk --> on going, to be check with special runs
BCID+1, plane events.... on going
Energy calibration + Homogeneity of response : DONE
Determine signal over noise ratio of the detector: DONE
Study of showers
See Jeremy's talk
See Elmaddin's talk

---
Back up

---
Setup
- wafer 9x9 cm2, 324 pixels 5x5 mm2
- 6 FEV8 (4 SKIROCs per FEV)
  - 4 SKIROCs x 64 channels = 256 channels
    (2 channels with 2 pixels and 22 channels with 4 pixels)
    Total = 1536 channels
    PreAmplifiers of noisy channels are switched off
    total active channels = 1278
- PVC structure with position for tungsten plates (2.1 mm)