## Slide 1
LEETECH
experimental platform
Oleg Bezshyyko
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 2
Outline
LEETECH facility at PHIL
Goals and applications
Simulations in GEANT4 (I stage, II stage)
Design and production (in Kyiv University, TSNUK) of vacuum chamber and collimator system (mechanical part and electronics)
Design and production of Dipole Magnet (in CERN)
Status
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 3
PHIL - PHoto-Injecteur au LAL
LEETECH – Low Energy Electron Technology –
facility at the PHIL to obtain quasi monochromatic electrons of variable low energy
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay
Collaboration with: LAL (PHIL, general management and many other…); CERN (dipole magnet), Kiev U - TSNUK (collimators, vacuum chamber, simulation), IRFU (gas system, setup calibration)

## Slide 4
Goals and applications
extension
PHIL
Using of electrons provided by PHIL with momentum 5-8 MeV/c and (108 now) 109 particles per bunch, 5 bunches per second
Timing: laser pulse with 7 ps FWHM
Goal: obtain samples of “quasi-monochromatic” electrons:
with adjustable energy between 1 MeV (is desirable a few 100 keV) and 5 MeV
energy spread of better than 10 %
with adjustable intensity down to 104 and less electrons per sample (ideal case is 1 electron on bunch)
Specific advantage – good time resolution (<300 ps)
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 5
Goals and applications
Test bench:
Gaseous detectors tests, e.g. routine Micromegas/InGrid performance tests
to optimize the protection layer.
Generic R & D
Applications: LCTPC with Micromegas/InGrid option, CAST
Studies of the crystal properties and prototypes for UA9 project
FTOF: time-of-flight particle identification detector based on DIRC technique
Measurements of scintillators for SuperNEMO experiment
Tests of diamond sensors (profile monitor, tracking, …)
Physics measurements:
E.g. non-relativistic electron energy losses with Micromegas/TIMEPIX
Students hands-on:
All above + track reconstruction, gaseous detector edge effects
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 6
Use of electrons from PHIL
Reduce energy/intensity using Al plug
Beam vacuum
e-
Al Plug
Initial flight direction of electrons
Capture the electrons with the angle from the plateau
Different plug thickness favours different energy samples, so that it is advantageous to produce several plugs of different thickness
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay
GEANT4 Simulations
L.Burmistrov (LAL)
Active participation of students: O.Fedorchuk, V. Krylov, M. Haranko

## Slide 7
Use electrons from PHIL
Reduce energy/intensity using Al plug
Select optimal direction for electrons passing the plug with collimator 1
Select required energy by half-turn of electron in the magnetic field
Beam vacuum
e-
Al Plug
Magnet with adjustable field In range 100(50?)-2000 gauss
Vacuum
Collimator1
Magnet
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 8
Use electrons from PHIL
Reduce energy/intensity using Al plug
Select unique direction for electrons passing the plug with collimator 1
Select required energy by half-turn of electron in the magnetic field (position of collimator 2 or field value)
Adjust intensity/energy spread using collimator 2, positioned in front of tested detector
Electron counting at low fluxes: Micromegas to calibrate detector settings (magnetic field and collimator positions) or count electrons on individual bunch basis
Beam vacuum
e-
Al Plug
Magnet with adjustable field
Vacuum
Detector to be tested
(Micromegas, …)
Collimator1
Collimator2
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 9
Simulations in GEANT4 (I stage), geometry
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 10
First collimator 0.2cm
Second collimator 0.6cm
First collimator 1cm
Second collimator 1cm
First collimator 0.4cm
Second collimator 1.2cm
First collimator 1cm
Second collimator 1.6cm
Simulations in GEANT4 (I stage), typical spectra
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 11
Simulations in GEANT4 (I stage), time resolution
Collimators 0.8x1cm
Sigma 78ps
Collimators 0.4x0.8cm
Sigma 48ps
Collimators 1x1.4cm
Sigma 96ps
Real Settings
Collimators 1x1.4cm
Sigma 110ps
Gamma
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 12
This picture shows all tracks which hit the detector and with momentum less than 0.9 MeV and more than 1.1 MeV (image only for background particles).
2
3
4
Source of the noise
1
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 13
Simulations in GEANT4 (II stage), geometry
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 14
Simulations in GEANT4 (II stage), typical spectra
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 15
Simulations in GEANT4 (II stage),
Quasi-monoergetic positron source
Resulting spectrum at the detector.
1.5 mm lead cup
Resulting spectrum at the detector
(only positrons). 1.5 mm cup
General Particle Source technique had been used to create distributions (in GEANT4 ) - to simulate 10 billion of electron events, we need to run only 1.42 million of positrons (for 1.5 mm cup).
Only one positron per 7000 of electrons (for 1.5 mm lead cup)
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 16: Engineering design of the system (mechanical part )
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 17: Manufacturing of vacuum chamber and 3 boxes for collimators
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 18: Collimator systems
Three similar collimator systems with piezomotors were produced and verified
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 19: Control electronics for collimator system Active participation of students: V. Krylov, T. Patlatiuk
Computer
Master Board
3 Slave Boards
CAN bus
interface
CAN
CAN
Ethernet
Feedback
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 20: Feedback
Hall effect position sensor
A specific magnet strip needs to be placed above the chip
Characteristics
Coordinate value is stored in 12-bit register
This register value becomes to zero every 2mm.
Resolution: 2mm/212 = 0,488 um
Access interface: I2C
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 21: Test assembly
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 22: Test assembly
Master board
Slave
board
Test collimator motor
Auxiliary board
HDMI
connector
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 24
produced at CERN, and delivered to LAL
Dipole magnet
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 25
Dipole magnet
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 26
Status
Magnet, vacuum chamber and three collimator subsystems are produced and delivered to LAL. Electronic, mechanical, vacuum tests of these components are performed and now tests of all LEETECH system are starting at the PHIL facility
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 27
Vacuum chamber and collimators were produced in Kyiv University (TSNUK, Ukraine), delivered to LAL and have tested here
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 28
Vacuum chamber and collimators were produced in Kyiv University (TSNUK, Ukraine), delivered to LAL and have tested here
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 29
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay

## Slide 30
Conclusions
Tasks for LEETECH facility at PHIL and its general design were considered
Simulation of LEETECH facility in GEANT4 was performed
Design and production (in Kyiv University) of vacuum chamber and collimator system (mechanical part and electronics) was carried out
Design and production of Dipole Magnet (in CERN) was carried out
All LEETECH components were delivered in LAL and tested here
Testing of whole system and studies at the PHIL in the schedule
O.Bezshyyko, 2-nd French-Ukrainian workshop on the instrumentation developments for HEP, October 1-3, Orsay